## Slide 1
Particle tracking with the beam tracker
Paolo Maestro
University of Siena
Beam Test F2F Meeting
CERN March 15-17, 2012

## Slide 2: Outline
Detector configuration
Beam profiles
Track reconstruction with Si-strips
Si-strip sensors “internal” alignment
Alignment of the Beam Tracker and IMC/TASC
Measurement of the attenuation length of the IMC fibers using the Beam Tracker
Charge ID with Si array

## Slide 3
Top Tracker
2 Pairs of X-Y Strip sensors
9.4cm x 9.4cm
strip pitch 183 μm
128 channels. Readout pitch 732μm
(Ganging of 4 strips)
4 Matrices (8 x 8 Pixel Array)
9.0 cm x 9.0 cm
1.125 cm x 1.125 cm pixel area
Interpixel distance 80 μm
Bottom Tracker
2 Pairs of X-Y Strip sensors
Tracker configuration

## Slide 4
Si-strip
x1
x2
Si-strip
Si-matrix
Si-strip
Si-strip
y1
y2
35.3 cm
9.4 cm
6.1 cm
7.5 cm
x3
x4
y3
y4
Si-strip
Si-strip
Si-strip
Si-strip
Trigger
Scintillators
Beam
z
y
x
Beam test layout

## Slide 5
Protons @ 350 GeV run 328-334 BEAM PROFILES
YZ view
XZ view

## Slide 6
e+ 30 GeV run 280-284 BEAM PROFILES
YZ view
XZ view

## Slide 7
p @ 350 GeV run 328-334
Average beam particle trajectory
e+ 30 GeV run 280-284
Strip# | D (mm) p | D (mm) e+
0Y | -0.40 | -0.44
1X | 1.35 | 1.27
2X | -0.28 | -0.35
3Y | -0.69 | -0.71
4Y | 1.62 | 1.68
5X | 1.10 | 1.14
6Y | -0.53 | -0.54
7X | -2.18 | -2.06
XZ view
YZ view
Need to correct for:
Si strips misalignment
Beam tracker tilt angle
qy ~12 mrad
qx ~16 mrad

## Slide 8: Si strips tracking algorithm
Clusters of adjacent Si-strips with energy deposit > 12 ADC (hits) are identified in each layer.
Each cluster defines a candidate track point, with X(Y) coordinate equals to the COG (center of gravity) of the cluster and Z coordinate equals to the position of the sensor.
Candidate tracks are built by scanning all the possible combinations of candidate track points in each view (XZ and YZ).
Ensemble of candidate tracks with at least 3 points (per view).
The parameters of each track in the ensemble are calculated by a c2 fit.
The track with minimum c2 is selected as the beam particle trajectory.
Pulse height distribution
of the hits associated to the
reconstructed trajectories

## Slide 9
XZ VIEW
YZ VIEW
Scintillator
Top Tracker
x1
x2
x3
x4
y1
y2
y3
y4
Bottom Tracker
Matrix

## Slide 10
Si strip alignment
SCIFI2
SCIFI3
STR5
STR7
zoom
S7
S5
Find the offset Sj (j=1,…,Nlayer) to be applied to the nominal strip coordinate (xstripj) to get the best alignment of the sensors
Iterative procedure in each view (XZ/YZ) based on a c2 minimization
Free parameters : 4 Sj shifts, one per layer in that view
xtrackj is the intercept of the fitted track with the layer j

## Slide 11
YZ view: distribution of the residuals ystrip - ytrack before alignment

## Slide 12
YZ view: distribution of the residuals ystrip - ytrack AFTER alignment
Resolution on impact
point ~50-60 mm

## Slide 13
Si strip layer 0
Si strip layer 3
Si strip layer 6
Si strip layer 6
ystrip – ytrack < 0
ystrip – ytrack > 0
ystrip – ytrack < 0
ystrip – ytrack > 0

## Slide 14
XZ view: distribution of the residuals xstrip - xtrack before alignment

## Slide 15
XZ view: distribution of the residuals xstrip - xtrack AFTER alignment
Resolution on impact
point ~50-60 mm

## Slide 16
65 cm
18.5 cm
9.4 cm
6 cm
Beam Tracker
IMC
TASC

## Slide 17
65 cm
18.5 cm
9.4 cm
6 cm
Beam Tracker
IMC
TASC
Beam Tracker
qy ~12 mrad

## Slide 18
Find the tilt angle of the BT w.r.t. IMC/TASC
Iterative procedure based on a c2 minimization
yIMC is the intercept of the IMC reconstructed trajectory with the first IMC layer, i.e. the beam particle impact point on IMC
yBT is the impact point on IMC of the BT reconstructed trajectory, rotated in the IMC reference frame according to equation
q , Oy , Oz are the free parameters in the fit.
y’z’ are the coordinate in the BT reference frame
Si strip-IMC alignment

## Slide 19
YZ view: distribution of the residuals yBT - yIMC
BEFORE alignment
AFTER alignment
RMS of impact
point on IMC ~ 1 mm
BT too far from IMC !

## Slide 20
Measurement of the fiber signal as a function of the x-coordinate of the impact point reconstructed with the beam tracker.
Fit the attenuation curve with
Attenuation lenght from the fit ~ 300 cm
muon run 154-184
muon run 186
muon run 189
l = 299 ± 25
l = 324 ± 36
l = 273 ± 27
Measurement of the attenuation length of IMC fibers
Layer 3
Layer 0
Layer 5

## Slide 21: CHARGE ID with the Si array
The intersection of the reconstructed trajectory with the Matrix sensors is used to identify the
pixel hit by the beam particle.
Four independent samples of dE/dx of the primary particle  Charge ID

## Slide 22
Muons pulse height distribution
in Si-array
Heavy ion spectra at GSI

## Slide 23: Conclusions
Tracking algorithm is fast and efficient and allows to reach a spatial resolution of the impact point ~50 mm
Beam tracker alignment in two steps: 1. internal alignment among the Si strip sensors;
2. alignment with IMC/TASC.
Procedure based on c2 minimizations work fine. They have been applied to different runs and produce stable results (in terms of correction factors).
Critical issue: BT and IMC at the beam test were placed too far ~ 1 m.
That amplifies the effect of small rotations <1° between the two systems, degrading the fine
spatial resolution of the reconstructed impact point achievable with BT.
Nevertheless we use the BT to measure the x-coordinate (not readable by the IMC
prototype) and study the response of fiber and crystals as a function of the impinging point
of the particles.
Lesson learnt for the next beam test:
- BT should be placed as close as possible to IMC to provide a fine tracking.
- Si array can be used to determine the particle charge with a fragmented ion beam.
FUTURE PLAN FOR THIS ANALYSIS
Write the BT reconstructed particle track parameters in the ntuples, in TParticleIncident class of the CALET MC unified format (equivalent to LEVEL-2 data)