## Slide 1: Status of Vacuum System and near future plan
Junichiro KAMIYA
J-PARC/Japan Atomic Energy Agency

## Slide 2
Linac
3GeV RCS
MLF
50-GeV MR
Hadron
Japan
J-PARC,
Tokai-mura, Ibaraki-ken
Tokyo
Japan Proton Accelerator Research Complex (J-PARC)

## Slide 3
J-PARC RCS(rapid cycling synchrotron) design:
Beam power 1MW= 3GeV, 8.3x1013 protons, 25Hz
Challenge to vacuum components
Small residual radio activity: Titanium ducts & bellows
Resistance to radiation: TMP with high radioactive resistance
Suppression of eddy current
& low impedance
: Ceramic ducts with RF shield
Components with low outgassing
: Ferrite cores of kicker magnet
: Cu block of beam collimator
N.Ogiwara, Vacuum 84(2010)
M. Kinsho, Vacuum 81(2007)
J. Kamiya, J. Vac. Soc. Jpn(2007)
K. Yamamoto, Phys. Rev. ST-AB 11(2008)

## Slide 4
From Linac
To neutron source (Hg target)
& 30GeV Synchrotoron
181MeV
3GeV
Vacuum chambers
108 Ceramic ducts
186 Ti ducts & bellows
Pumps
24 Turbo molecular pumps
(20 Spattering ion pumps)
Gauges
44 Cold cathode gages
17 BA gages
44 Pirani gauges (beam line and back line of TMP)
Collimators
Kicker magnet
Charge exchange foil …..
Other vacuum components
Vacuum system
Circumference 348.3m
1st arc
2nd arc
3rd arc
RCS Vacuum System

## Slide 5
Vacuum Performance ~static pressure distribution
Beam off, All magnet are excited.
Pressure of less than 10-5 Pa is stably maintained.

## Slide 6
Source of Dynamical pressure change in high intensity accelerator
~Mechanism is similar to plasma-surface interactions in nuclear fusion machines.
G. M. McRACKEN, P.E. SCOTT, Nuclear Fusion, Vol.19, No.7(1979)
1) Thermal desorption of gas adsorbed on the vacuum walls
2) Desorption due to bombardment by ions, electrons, and photons
3) Chemical reactions which release gaseous contaminants such as H2O and CH4.
We are seeing the combination of those interactions.

## Slide 7
Dynamic Pressure in RCS (2) ~ gas analysis
gaseous molecule
+
+
proton beam
ion
desorption
H2
CH4
H2O
CO
C2H4 etc.
300kW beam
Beam off
Beam on
Ion bombardment ~one of the process of dynamic pressure change
Especially in the beam operation just after a maintenance, we see the large pressure increase.

## Slide 8
Dynamic Pressure in RCS (2)~ conditioning effect
There is a conditioning effect by the beam during a continuous beam operation.
There is no pressure increase after long term beam operation.
-> After molecules on the surface are desorbed by the particle hit, a clean surface is obtained.
For higher power beam?
No one knows. We will see.
Pressure distribution
after long beam operation.
Pressure history (on beam)
maintenance
maintenance
Chart: 
| C02CCG01 | C02CCG02 | C03CCG01 | C03CCG02 | C03CCG03 | C03CCG04 | C04CCG01 | C04BAG01 | C05CCG01 | C06CCG01 | C07CCG01 | C07BAG01 | C08CCG01 | C08BAG01 | C09CCG01 | C10CCG01 | C10CCG02 | C10CCG03 | C10BAG01 | C11CCG01 | C11CCG02 | C11BAG01 | C12CCG01 | C12CCG02 | C13CCG01 | C13BAG01 | C14CCG01 | C14BAG01 | C15CCG01 | C16CCG01 | C16BAG01 | C17CCG01 | C17BAG01 | C18CCG01 | C18BAG01 | C19CCG01 | C19CCG02 | C20CCG01 | C20BAG01 | C21CCG01 | C21CCG02 | C22CCG01 | C22BAG01 | C23CCG01 | C24CCG01 | C24BAG01 | C25CCG01 | C25BAG01 | C26CCG01 | C27CCG01 | C27BAG01
Off beam | 0 | 2.2e-07 | 2.9e-07 | 2.9e-07 | 3.1e-07 | 3.2e-07 | 1e-06 | 2.95e-06 | 1.2e-06 | 4.3e-06 | 5.3e-06 | 9.2e-06 | 2.4e-06 | 5.67e-06 | 3.7e-06 | 4.7e-06 | 3.1e-06 | 2.8e-06 | 5.51e-06 | 2.6e-06 | 8.2e-07 | 2.87e-06 | 4.7e-07 | 4.5e-07 | 2.6e-06 | 2.17e-06 | 1.1e-06 | 3.7e-06 | 4.1e-06 | 7e-06 | 6.88e-06 | 1.6e-06 | 4.45e-06 | 4.4e-06 | 7.79e-06 | 3.6e-06 | 2.5e-06 | 1.8e-06 | 4.65e-06 | 2.5e-06 | 2.9e-06 | 5.5e-06 | 8.5e-06 | 1.3e-06 | 2.5e-06 | 6.83e-06 | 3e-06 | 7.91e-06 | 1.5e-06 | 2.4e-06 | 4.05e-06
220kW on beam | 0 | 2.5e-07 | 3.4e-07 | 3.3e-07 | 3.5e-07 | 3.7e-07 | 1.3e-06 | 3.36e-06 | 1.4e-06 | 4.9e-06 | 5.8e-06 | 1.01e-05 | 2.6e-06 | 6.01e-06 | 4e-06 | 4.9e-06 | 3.2e-06 | 3e-06 | 5.66e-06 | 2.8e-06 | 8.8e-07 | 2.97e-06 | 5.2e-07 | 5.3e-07 | 2.8e-06 | 2.35e-06 | 1.2e-06 | 4.07e-06 | 4.7e-06 | 7.7e-06 | 7.53e-06 | 2e-06 | 4.96e-06 | 5.1e-06 | 9.07e-06 | 4.5e-06 | 3.4e-06 | 2.4e-06 | 5.4e-06 | 3.3e-06 | 3.6e-06 | 6.5e-06 | 9.9e-06 | 1.5e-06 | 2.9e-06 | 7.57e-06 | 3.5e-06 | 8.75e-06 | 1.8e-06 | 2.9e-06 | 4.66e-06

## Slide 9
Development of the vacuum component
Vacuum chamber and bellows of
magnetic material with high permeability
2. In-situ bake out for kicker magnets

## Slide 10
1. Magnetic field shielding by vacuum chambers of magnetic material
Bellows
Beam ducts
Turbo molecular pumps
Request from beam commissioning group
Magnetic field in the area (~10gauss) must be 1/10 at beam position.
Beam ducts, bellows, turbo molecular pumps of magnetic materials.
Leakage field from a magnet in the extraction line distort the beam orbit in RCS.
Most effective way to shield such field is to cover the beam by the magnetic materials at the nearest space.
=Vacuum wall
These components are made of magnetic alloys.

## Slide 11
SUS430(ferritic stainless steel):
○Ready availability: easy
△magnetic permeability (μ): 500~1000
Enough field shielding characteristic with a thickness of more than 10mm
-> Enable for flanges(t30mm) and outer case of TMP (t10~20mm)
Permalloy (Ni base alloy with very high permeability)
○ magnetic permeability (μ): >10000
△ Ready availability: difficult especially for thick alloy
-> Enable for bellows (t0.2mm) and ducts (t3mm)
bellow
Permalloy
SUS316L
SUS430
SUS430
Permalloy
Beam duct
Selection of magnetic alloy

## Slide 12
Conditions for magnetic annealing
Mechanical stress = Decrease of magnetic permeability
→ Magnetic annealing(=heat treatment) is necessary after cutting, bending, pressing etc..
Dependence of magnetic shielding characteristic on annealing temperature
External field (Bout)
Gauss meter
(Measure of Bin)
Bellow of permalloy
Good shielding characteristic for the annealing temperature with more than 850 degC(10H).

## Slide 13
Magnetic field shielding
x
z
0
+500
-500
-750
External field Bx_out=20gauss
Chart: Position Z（mm）
| -200 | -220 | -240 | -260 | -280 | -300 | -320 | -340 | -360 | -380 | -400 | -420 | -440 | -460 | -480 | -500 | -520 | -540 | -560 | -580 | -600 | -620 | -640 | -660 | -680 | -700 | -720 | -740
Bout=20Gauss | 0.46 | 0.45 | 0.45 | 0.46 | 0.46 | 0.47 | 0.49 | 0.5 | 0.52 | 0.55 | 0.58 | 0.62 | 0.67 | 0.73 | 0.8 | 0.87 | 0.96 | 1.06 | 1.15 | 1.24 | 1.31 | 1.35 | 1.36 | 1.33 | 1.27 | 1.19 | 1.09 | 1
Bellows
Ducts
B_in/B_out<1/10 is achieved.

## Slide 14
Vacuum fire
Before vacuum fire: 1.e-8 Pam/s
Outgassing rate of permalloy
After vacuum fire: 3.e-9Pam/s
TDS spectrum(H2O)
Chart: time(min)
Temperature | 7.5 | 109.5 | 179.3 | 286.9 | 432.2 | 589.6 | 710.4 | 807.5 | 855.3 | 861.6 | 861.8 | 861.6 | 861.6 | 861.6 | 861.6 | 861.6 | 661.2 | 458.6 | 287.8 | 237.7 | 209.9 | 191.9 | 188.7
Temperature [degC]
850degC 10H
If we work annealing in good vacuum, it can combine with vacuum fire.

## Slide 15
2. In-situ bake out for kicker magnets
The usual way= bake-out the whole vacuum chamber
x huge heater capacity
x heat expansion of the chamber (Critical to the accelerator, which have many components in small area.)
Raise the temperature of the structure inside without heating the vacuum chamber.
Kicker : Outgassing from ferrite cores
= Water is a main component due to the porosity of ferrites.
Concept of setup.
Relative position of kicker and heaters.

## Slide 16
Heater power at this measurement 1.6kW << Former heater power 10kW
(heaters are put onto the outer surface.)
Temperature of ferrite cores and vacuum chamber.
Temperature of ferrite cores due to the in-situ method
Required heater power to reach
a kicker temperature up to 100 oC.
Effective and “eco” way for outgassing reduction!
Install heaters directly into vacuum＋Heat shield panels to direct the radiated heat to kicker
=

## Slide 17
Summery
Status of vacuum system
Development of vacuum components
Dynamical pressure change due to high power beam has been observed.
After molecules on the surface are desorbed by several mechanisms, pressure is stable even during high power beam operation up to 200kW.
What will happen in higher beam power?
Vacuum chambers and bellows of magnetic alloy with high permeability
In-situ outgassing reduction method for kicker magnets
We are developing vacuum components such as
We desire the continuous collaboration about information exchange, development of vacuum components, and scientific research about accelerator vacuum.