## Slide 1: LHeC Linac-ring Beamdynamics
D. Schulte

## Slide 2: LHeC Layout

## Slide 3: Reasoning
Reacceleration after turn-arounds
  With no synchrotron radiation energies of beam before and after collision can be matched pair-wise
  Does not work with uncompensated synchrotron radiation
  Compensation at last 60GeV arc would be more efficient before arc, but space constraints need to be addressed
Dedicated reacceleration sectors
  Using the linacs for compensation does not save power because real reacceleration is affected
    Off-phase acceleration creates beamloading
    There is no perpetuum mobile
  Dedicated sectors allow simple tuning, coupling only two turns not all of them
    E.g. easier energy ramping
  But some additional cost
Circumference choice is CLHC/n with n=3
  Explained later

## Slide 4: Note: Reacceleration Frequency Choice
Reacceleration at 60GeV turn-around can be fundamental frequency
  Only one beam
Other compensation stations require other frequency
  Rule:
    Linac frequency = n (2m+1) f0
      Create n buckets for accelerated beam
      And n for decelerated beam
    Compensation frequency = n (2k) f0
      Will accelerate both beams
  Baseline are 721.42 and 1442.84 MHz
  But could use 721.42 and 801.58 MHz (50ns spacing)
  Or 721.42 and 961.89 MHz (25ns spacing)
  Or …

## Slide 5: Energy Loss in Arcs
Incoherent synchrotron radiation in arcs (ρ=764m)
Total loss about 2GeV
i.e. 12.2MW beam power
Impact of energy spread and tail at dump needs to be studies
increase of injection energy would help
Baseline Arc designs from A. Bogacz
Alternative design by V. Litvinenko et al.

## Slide 6: Coherent Synchrotron Radiation
Use simple one-dimensional free space model leads (Ch. Mayes, G. Hoffstaetter)
  Assume same effect in drifts as in magnets
  Should be conservative
  A. Latina did similar calculation using other derivation
For a bunch length of 600μm, N=2x109
  RMS energy spread at dump of ~5MeV
  Average energy loss for all turns of ~8MeV
  Much smaller than incoherent radiation
Combination of wakefields and coherent synchrotron radiation not studied

## Slide 7: Emittance Growth in Arcs
Incoherent synchrotron radiation only
Growth before the interaction point: 7μm
Total growth: 26μm
Numbers should be fine

## Slide 8: Linac Design
8 1.06m long cavities per module, 2 modules per quadrupole pack
Quadrupole spacing 33m
60 modules per 990m-long linac (480 cavities)
Beam physicists assumed slightly different parameters (576 cavities at 18MV/m, quadrupole spacing of 28m and 72 modules)
Results are only slightly affected by the difference

## Slide 9: Linac Lattice
Optimised for beam stability by minimising
Alternative optics exists with no focusing in linac (V. Litvinenko et al.)
Lattice from A. Bogacz used

## Slide 10: Short-range Wakefields
Difficult to compute
Hence use scaled ILC wakefields (from RDR studies)
Simple scaling with aperture:
Transverse
Longitudinal

## Slide 11: Wakefield-induced Energy Spread
Simple PLACET simulation
Arcs are not included
Fine, somewhat large at dump

## Slide 12: Single-bunch Emittance Growth
Emittance growth due to initial offset Δx=σx
PLACET simulation, arcs are not included
Fine

## Slide 13: Long-range Wakefields
Thanks to M. Schuh for the modes
Q=105 assumed (consistent with ILC cavities)
0.1% mode detuning
Longitudinal modes need also to be studied

## Slide 14: Multi-bunch Beam Break-up
New code developed
Point-like bunches
Impact of single offset bunch on other studied
Beam is stable

## Slide 15: Multi-bunch Beam Break-up
Damping and detuning are essential

## Slide 16: ILC Cavities
f [GHz] | k [V/(pCm^2)] | Q
1.6506 | 19.98 | 7e4
1.6991 | 301.86 | 5e4
1.7252 | 423.41 | 2e4
1.7545 | 59.86 | 2e4
1.7831 | 49.2 | 7.5e3
1.7949 | 21.70 | 1e4
1.8342 | 13.28 | 5e4
1.8509 | 11.26 | 2.5e4
1.8643 | 191.56 | 5e4
1.8731 | 255.71 | 7e4
1.8795 | 50.8 | 1e5
2.5630 | 42.41 | 1e5
2.5704 | 20.05 | 1e5
2.5751 | 961.28 | 5e4
Beam is stable
Note: A translation error in one cell
of the the lattice file from excel to RTF
led to different results in the past
TESLA TDR

## Slide 17: Static Imperfections
Can assume the same tolerances as for ILC
ILC achieves nm emittance growth using complex beam-based
alignment, see below
Need BPMs that can resolve the bunches from the different turns
-> Do not expect any issue

## Slide 18: Cavity Tilts
The combination of cavity tilt and gradient jitter leads to transverse deflection of the beam
Approximate estimate using the simple formula (assuming averaging over beam phase):
For
a reasonable RMS tilt of 300μradian
a not so small 1% RMS gradient jitter
one obtains RMS beam jitter of O(5%σy) at the interaction point

## Slide 19: Fast Beam-ion Instability
Positive ions that are trapped in the beam can
  Change the phase advance of the different bunches
  Can lead to a multi-bunch instability
Studies need to
  Check whether ions are trapped
    Bunch to bunch and turn to turn
  How much damage they do while being trapped

## Slide 20: Fast Beam-ion Instability
Ions are trapped from bunch to bunch if fc<flimit
Frequency fc is shown for continuous train
-> All gases are trapped
-> likely will need to add a gap in the train

## Slide 21: Beam Pulse
Could use 20μs trains and 10μs gaps
  Beam loading in injectors 0.6% for 720MHz cavities
  Increase bunch charge by 50%
  This fixes LHeC circumference to be 1/n of LHC
    Each LHC bunch always or never collides with electron bunches
Need to study consequences on RF
Still need good vacuum (O(10-11hPa)) in linacs, more study needed

## Slide 22: Clearing of Ions in the Gap
Replace many thin focusing lenses of beam by a thick long lens:
Ions will be cleared if this long lens is over-focusing
Note: derivation differs from what I found in literature

## Slide 23: Ion Clearing
Longitudinal drift will get rid of remaining ions
Ions are cleared almost everywhere

## Slide 24: Phase Advance Error
The relative phase advance error can be approximated for
round beams as (G. Hoffstaetter, M. Liepe, NIM A 557 (2006) 205–212):
With no clearing ions will accumulate until the beam is neutralised:
i.e. ϑ=1 -> Δϕ/ϕ=16 -> not acceptable
With gap one finds for p=10-9hPa (warm) and p=10-11hPa (cold):
ϑ=3.3x10-5 -> Δϕ/ϕ=7x10-4 -> acceptable
Assume ions are lost in first gap passage (optimistic)
Ions are trapped within each train, look at last bunch before the gap

## Slide 25: Multi-bunch Instability
Can calculate the instability rise time for the nth bunch in a train
(F. Zimmermann et al., SLAC-PUB-7617)
Average the rise time along the machine
Pessimistic: detuning ignored
Assume beam to be stable if instability rise length L=τcc is longer than
beam travel length

## Slide 26: Rise Length
Note: the rise length
Is proportional to the
Pressure, here 10-11hPa
Rise length for
CH4+: 14km
H2+: 25km
Total length of travel in
linacs is 12km
p=10-11hPa is marginally OK
Measurements show 6x10-11,1x10-11, 0.05x10-11 hPa
for LEP (N. Hilleret), HERA (B. Holzer), LHC (V. Baglin)

## Slide 27: Rise Length in the Arcs
For p=10-9hPa
H2+: 70km
N2+,CO+:50km
CO2+: 60km
Calculation is similar than in the linac
But only two beams in each arc
Total length in arcs is 33km
p=10-9hPa is marginally OK

## Slide 28: Beam-beam Effects
Electron bunch changes size during the collision
Luminosity is slightly above target
L~1.35x1033 cm-2s-1
Emittance growth is not large
But strong mismatch, so need
Average energy loss ~0.2MeV
GUINEA-PIG simulation

## Slide 29: Beam-beam Offsets
Deflection of electron beam centroid
Maximum deflection is about 300μradian
Maximum deflection of proton centroid is about 30nradian
(=4x10-4σ’)
GUINEA-PIG simulation

## Slide 30: Some Things To Do
Include the beam-beam effects and arcs in the main linac stability studies
Study the impact of energy spread/tail at the dump
Study the fast beam-ion instability
Protection of linac from arc synchrotron radiation
Study of imperfections and mitigation in presence of different energy beams

## Slide 31: Simulation Tools
Focus is usually either on rings or transfer lines
  Few turns with interleaving bunches is normally not simulated
Currently use dedicated code for multi-bunch studies
  Point-like bunches
  No beam-beam interaction
PLACET for single bunch studies
  Has multi-bunch wakefields, coherent synchrotron radiation, imperfections, correction techniques, can call beam-beam, is fully programmable
  Cannot handle interleaved trains
  Will have to add this for the CLIC drive beam in the combiner rings
GUINEA-PIG for beam-beam interaction
  Easily integrated in PLACET
  But takes some seconds per collision
FASTION (G. Rumolo)
  Can simulate fast beam-ion instability in transfer lines
  Planned to be integrated into PLACET
  Does currently not allow to use interleaved trains

## Slide 32: Conclusion
Did not find any show stopper
Do not expect to find a show stopper
But a number of studies remain to be done
  Requires some resource
  Some synergy with CLIC studies

## Slide 33: Reserve

## Slide 34: Beam-loading in the Gap
In the linacs no basic beam loading exists
  All gaps fall on top of each other
For the control RF and the injector one can estimate
-> Variation is about 0.6%