## Slide 1: Beam-Beam dynamics in the LHeC T.Pieloni with help from W. Herr, Y. Hao and W. Fischer (BNL)

## Slide 2: Beam-Beam interactions in the LHeC
Head-On
Long Range
Hadron Colliders:
  Beam Losses (dynamic aperture )
  Beam Lifetime
  External noise very important
  Landau damping properties
  Coherent modes
  …
  IR: 3 Head-on collisions
  30 long-range interaction

## Slide 3: Beam-beam interactions in the LHeC options
  Crossing angle needed (S factor 86-75%)
  One head-on interaction at IP
  Long range encounters every 3.75 m in IR
  e-beam acts as noise source
  No crossing angle
  One head-on interaction at IP
  No Long-range encounters
  e-beam noise source
  No worry of stability of e-beam
  LHC pp Beam-beam effects:
  2 Head-on collisions & 60 Long-range interactions at least
RING-RING Option
LINAC-RING Option

## Slide 4: LHeC Beam-beam complications:
Large Number of bunches in both beams (2808)
Simultaneous collisions of ep and pp of one proton beam
  pp collisions in IR1 and IR5
  ep collisions at another IR
Long term stability of
proton beams:
dominated by non linear effects
Long term stability of RR e-beam
and mismatch of e-beam in LR
Different beam-beam properties

## Slide 5: Known performance issues :
Optical matching (SPS, Hera and Tevatron experience)
  sxe = sxp
  sye = syp
Since different emittances for p and e then the beta functions at IP have to be different for the two beams (Hourglass effect)
  Restricts choice on be
Electron emittance must be controlled (coupling H/V ):
  Might be ok for RR option
  Not obvious for LR option
ep collision introduces asymmetry HV in Hadrons beam-beam effects

## Slide 6: Beam-Beam effects
Tune shift/spread
Mismatch
Disruption
Tune shifts/spread
Long Range interaction effects
Noise
Tune shifts/spread
Landau Damping properties
Long Range interaction effects
Noise from ep collisions
e-beam
e-beam
p-beam

## Slide 7: Beam-beam parameter:
ep tune shift goes opposite direction respect to pp collisions
ep Tune shift 1e-4 on proton beam less than 1% of pp collision effect
(LR CdR D. Schulte & Co)
Could become important ingredient to consider when lack of Landau Damping or when pinch effect considered in the e-beam

## Slide 8: BB parameter and Tune Shifts:
From Experience | LHC pp collisions | LEP (90 GeV) electron
xx,y | 0.07 - 0.017 /IP | 0.03 – 0.07 /IP
Head-on beam-beam parameter achieved so far:
  Electrons higher than what achieved in LEP (tune shifts of 0.04):
  1 degree option optimistic but significant reduction from dynamic
  beta and small number of IP can make it feasible
  10 degree option too high tune shift for the electrons
  Protons tune shift from e-beam in shadow of head-on pp collisions and opposite direction (decreases pp tune spread) assuming designed transverse size 0.0001.
    Pinch Effect can enhance the compensating effect and/or will act differently on particles
Electron effect on protons tune spread is an important ingredient for Landau Damping even if small should be studied in details!

## Slide 9: Tune spread and Landau Damping
Head-on beam-beam only sufficient to provide tune spread for Landau Damping at collision energy
If a head-on collision is not guaranteed then lack of Landau damping drives the beam unstable as observed in the LHC 2012 operation
ep collisions compensate a fraction of the spread of pp collisions (as e-lenses)
Cortesy of X. Buffat

## Slide 10: Experimental studies: e-lenses in RHIC
e-lenses at RHIC perfect test bench for studying experimentally the dynamics of
ep collisions with pp collisions
Perfect test bench to study:
the interplay between pp and ep collision dynamics
compensation of tune spread
effect of transverse mismatch between p and e beams
Curtesy of W. Fischer
e−
e−
e−
p
p

## Slide 11: Parasitic Encounters Separation
Electron Beam
Proton Beam
d
a
3.75 m
Long range encounters every 3.75m in IR
1 degree option preferable due to larger separation
10 degree option separation smaller, important the interplay with many other LRs
Dynamic Aperture studies define the effects of the long-range encounters and an optimum set of parameters for the LHeC operation

## Slide 12: Increase d or crab cavities?
  Increase further the crossing angle and crab cross
  Crab cavities could an option to gain luminosity geometrical reduction due to crossing angle and reduce bb long-range effects
Full study of the effects of crab cavities deflection on the proton beams should be performed

## Slide 13
Hadron colliders performances/luminosity deteriorates in the presence of transverse noise as known from past experience in Spps, Tevatron, RHIC
A source of noise (as the e-beam in LHeC RR or LR options, crab cavities, the 2nd proton beam etc) can lead to:
Emittance increase
Reduced tune shifts achievable
Analytical models: simple case cannot describe the LHC/LHeC configurations
Numerical models could have all ingredients (head-on, long-range effects etc) but detailed study does not exist yet (PhD thesis on-going for LHC X. Buffat)
Main components to be addressed:
  Any excitation of one beam will give  dipolar kicks to the other beam
  Jitter of e-beam intensity and/or sizes  quadrupolar error for the proton beam
  Crab cavities (if an option)
  Any other unavoidable source of noise
Noise on pp collisions
Detail study is fundamental by use of numerical models for all colliders
Luminosity deterioration

## Slide 14
Curtesy of W. Fischer
e−
e−
e−
p
p
  e-lenses give the possibility to test in controlled way also effects of electron intensity and/or sizes jitters on proton-proton collisions
LHeC case e-beam is a noise generator for the protons
Experimental benchmark of existing models in the LHC or at RHIC with the e-lenses is a key ingredient to define predictive power of numerical tools
Installation foreseen summer 2012 then commissioning in 2013 run

## Slide 15: Beam-beam issues to be addressed
Dynamic of pp and ep collisions to be studied self consistently with numerical tools and where possible with experimental studies (RHIC e-lenses)
Dynamic aperture tracking studies (define best WP and parameters) for the two options
Detail study on noise effects on the protons by numerical models and where possible experimental benchmark
Long Range beam-beam effects from RR option
Multiple bunch effects (colliding with same bunches)
Long term stability of e-beam
Effect of pinched e-beam on proton dynamics (tune shift and spread, etc)
e-beam deflection on p-beam

## Slide 16
Thank you