## Slide 1: LHeC Accelerator Overview
Frank Zimmermann
LHeC Workshop 2012
Chavannes-de-Bogis
Many contributors:
Jose Abelleira, Chris Adolphsen, Husnu Aksakal, Rob Appleby, Mei Bai, Desmond Barber Nathan Bernard, Alex Bogacz, Luca Bottura, Chiara Bracco, Hans Braun, Oliver Brüning, Eugene Bulyak, Helmut Burkhardt, Swapan Chattopadhyay, Ed Ciapala, Kenan Ciftci, Reina Ciftci, John Dainton, Anders Eide, Emre Eroglu, Miriam Fitterer, Hector Garcia, Brennan Goddard, Yue Hao, Friedrich Haug, Bernhard Holzer, Erk Jensen, Miguel Jimenez, John Jowett, Dmitry Kayran, Max Klein, Peter Kostka, Vladimir Litvinenko, Karl Hubert Mess, Zafer Nergiz, John Osborne, Tatiana Pieloni, Alessandro Polini, Vadim Ptitsin, Louis Rinolfi, Lucio Rossi, Stephan Russenschuck, Daniel Schulte, Ilkyoung Shin, Peter Sievers, Mike Sullivan, Saleh Sutansoy, Hugues Thiesen, Luke Thompson, Rogelio Tomas, Davide Tommasini, Dejan Trbojevic, Joachim Tückmantel, Alessandro Variola, Ferdinand Willeke, Vitaly Yakimenko, Fabian Zomer, … ++

## Slide 2
LHeC CDR completed (~600 pages);
Large Hadron electron Collider (LHeC)

## Slide 3
LHeC CDR
Accelerator
Part:
table of
contents;
4 chapters;
226 pages

## Slide 4
RR LHeC:
new ring
in LHC tunnel,
with bypasses
around
experiments
RR LHeC
e-/e+ injector
10 GeV,
10 min. filling time
LR LHeC:
recirculating
linac with
energy
recovery
Large Hadron electron Collider

## Slide 5: performance targets
e- energy ≥60 GeV
luminosity ~1033 cm-2s-1
total electrical power for e-: ≤100 MW
e+p collisions with similar luminosity
simultaneous with LHC pp physics
e-/e+ polarization
detector acceptance down to 1o

## Slide 6: colliding unequal beams
ring-ring
ee>>ep
ring-linac
ee≈ep
minimum beta function
and beam size
limited by hourglass effect;
small crossing angle acceptable;
little disruption
smaller beta function
and beam size possible;
head-on collision required;
significant disruption
;

## Slide 7
R-R LHeC road map to 1033 cm-2s-1
luminosity of RR collider:
highest proton
beam brightness “permitted”
(ultimate LHC values)
ge=3.75 mm
Nb=1.7x1011
bunch spacing
25 or 50 ns
maximize
geometric
factor with nonzero
crossing angle
and hourglass
effect (small be*)
b*x,y (p)=4, 1 m
(flat beams)
average e-
current
limited by SR
Ie=100 mA
HD~1

## Slide 8
L-R LHeC road map to 1033 cm-2s-1
luminosity of LR collider:
highest proton
beam brightness “permitted”
(ultimate LHC values)
ge=3.75 mm
Nb=1.7x1011
bunch spacing
25 or 50 ns
smallest conceivable
proton b* function:
reduced l* (23 m → 10 m)
squeeze only one p beam
new magnet technology Nb3Sn
b*p=0.1 m
maximize geometric
overlap factor
head-on collision
small e- emittance
qc=0
Hhg≥0.9
(round beams)
average e-
current
limited by
energy
recovery
efficiency
Ie=6.4 mA
HD~1.3
D. Schulte
LHeC2010

## Slide 9: LHeC design parameters
electron beam | RR | LR | LR*
e- energy at IP[GeV] | 60 | 60 | 140
ep luminosity [1032 cm-2s-1] | 8 | 10 | 0.4
eN luminosity [1032 cm-2s-1] | 0.45 | 1 | 0.04
polarization for e- (e+) [%] | 40 (40) | 90 (0) | 90 (0)
bunch population [109] | 20 | 1.0 | 0.8
e- bunch length [mm] | 6 | 0.3 | 0.3
bunch interval [ns] | 25 | 25 | 25
transv. emit. gex,y [mm] | 0.59, 0.29 | 0.05 | 0.1
rms IP beam size sx,y [mm] | 45, 22 | 7 | 7
e- IP beta funct. b*x,y [m] | 0.4, 0.2 | 0.12 | 0.14
full crossing angle [mrad] | 0.93 | 0 | 0
geometric reduction Hhg | 0.87 | 0.91 | 0.94
disruption enhancement | 1.0 | 1.3 | ~1.0
repetition rate [Hz] | N/A | N/A | 10
beam pulse length [ms] | N/A | N/A | 5
ER efficiency | N/A | 94% | N/A
average current [mA] | 100 | 6.4 | 5.4
tot. wall plug power[MW] | 100 | 100 | 100
proton beam | RR | LR
bunch pop. [1011] | 1.7 | 1.7
tr.emit.gex,y [mm] | 3.75 | 3.75
spot size sx,y [mm] | 30, 16 | 7
b*x,y [m] | 4.0,1.0 | 0.1
bunch spacing [ns] | 25 | 25
RR= Ring – Ring
LR =Linac –Ring
50 ns & Nb=1.7x1011
probably conservative
design also for deuterons
(new) and lead (exists)
*) pulsed, but high energy ERL not impossible
b*~0.025 m possible in IP3 or 7
using ATS optics (S. Fartoukh);
+ also going to 2 mm emittance
(H. Damerau, W. Herr),
→L~1034 cm-2s-1 within reach!
higher-L
design exists

## Slide 10: LHeC Ring-Ring Layout
Two LHeC bypasses shown in blue - each 1.3 km long. RF in the central straight sections of the two bypasses (<500 m total). The bypass around Point 1 also hosts the injection.
H. Burkhardt,
M. Fitterer, B. Holzer,
J. Jowett

## Slide 11
LHeC Ring-Ring Arc Optics
2 LHeC FODO cells = 1 LHC FODO cell
even IR
odd IR
H. Burkhardt,
M. Fitterer,
B. Holzer,
J. Jowett
ex,LHeC<1/3 ex,LEP1.5

## Slide 12: LHeC R-R: Bypassing LHC detectors
For the CDR the
bypass concepts
were decided to be confined to
ATLAS and CMS
Without using the survey gallery the ATLAS bypass would need to be 100m away from the IP or on the inside of the tunnel!
ca. 1.3 km long bypass
ca. 170m long dispersion free area for RF
Oliver Brüning,
ED 20 March 12

## Slide 13: LHeC R-R: Integration in LHC tunnel
RF Installation in IR4
Cryo link in IR3
Oliver Brüning,
ED 20 March 12

## Slide 14: LHeC R-R: Matching LHC circumference
requires:
support
structure
with
efficient
montage
and
compact
magnets
to transport LHC cryo equipment e- ring may need to be
shifted 30 cm to the outside ; semi-automatic movement
& expansion joints

## Slide 15: LHeC R-R dipole magnets: 400 mm long CERN model
interleaved ferromagnetic laminations
air cooled
two turns only, bolted bars
0.4 m models with different types of iron
30 cm
Magnet Parameters of the full length magnet | 
Beam Energy [GeV] | 70
Magnetic Length [m] | 5.45
Magnetic field [Gauss] | 127-763
Number of magnets | 3080
Vertical aperture [mm] | 40
Pole width [mm] | 150
Number of coils | 2
Number of turns/coil | 1
Current [A] | 1500
Conductor section [mmxmm] | 92x43
Conductor material | aluminum
Magnet Inductance [mH] | 0.15
Magnet Resistance [m] | 0.2
Power per magnet [W] | 450
Cooling | air
Weight [tons] | 1.5
Manufacture & tests of 3 models
[Davide Tommasini]

## Slide 16: LHeC Ring-Ring Challenges
bypassing the main LHC detectors
  CMS: 20 cm distance to cavern, 1.3 km bypass, 300 m for RF installation
  ATLAS: using the survey gallery, 1.3 km bypass, 170 m for RF installation; similar schemes for LHCb & ALICE
integration into the LHC tunnel
  cryo jumpers taken into account in arc-cell design
installation matching LHC circumference
  avoiding Hirata-Keil resonances, arcs ~4000 magnets
  no show stopper found; 3D integration needed
  compact magnet design & prototypes (BINP & CERN)
  installation within LHC shutdown schedule

## Slide 17: LHeC Ring-Ring Conclusions
Low-emittance optics compatible with LHC
Light arc magnet prototypes from Novosibirsk and CERN show that required field quality and reproducibility is achievable
No fundamental problem found for R-R LHeC
But RR still needs a full 3-D integration study!
Planning integration into LS2 and LS3 might be challenging!
40% polarization to be demonstrated
Oliver Brüning,
ED 20 March 12

## Slide 18: LHeC Linac-Ring Option: ERL layout
two 10-GeV SC linacs, 3-pass up, 3-pass down; 6.4 mA, 60 GeV e-’s collide w. LHC protons/ions
(C=1/3 LHC allows for ion clearing gaps)
A. Bogacz, O. Brüning,
M. Klein, D. Schulte,
F. Zimmermann, et al

## Slide 19
Alice
LHeC RL option: underground layout / integration with LHC;
example: Point 2
J.Osborne / A.Kosmicki CERN/GS
Prevessin site
LHC
TI2

## Slide 20
J.Osborne / A.Kosmicki CERN/GS
underground layout / integration with LHC;
example: Point 2
Alice
TI2

## Slide 21: LHeC L-R Option: ERL Linac Optics

## Slide 22: LHeC L-R: Vertical Separation of Arcs & Spreader Optics
Arc 1 (10 GeV)
Arc 3 (30 GeV)
Arc 5 (50 GeV)
Alex Bogacz

## Slide 23
flexible momentum compaction cell; tuned for small beam size (low energy) or low De (high energy)
A. Bogacz
LHeC L-R Option: ERL Arc Optics

## Slide 24
BBU: beam stability requires both damping (Q~105) & detuning (Df/frms~0.1%) , 720 MHz
LHeC L-R Option: ERL Beam Dynamics
D. Schulte
(no focusing)

## Slide 25: LHeC Linac-Ring Challenges
2 x 10 GeV SC Energy Recovery Linacs
  SC linac: synergies with ESS, SPL, XFEL, JLAB, ILC, eRHIC
  linac size similar to XFEL at DESY; cryo power ~1/2 LHC
  less current than other ERL designs (CESR-ERL, eRHIC)
return arcs
  total circumference ~ 9 km, 3 passes
  same magnet design as for RR option, >4500 magnets
  installation fully decoupled from LHC operation
e+p luminosity: e+ production & recycling
  IP e+ rate ~100 times higher than for CLIC or ILC
  several schemes proposed to achieve this

## Slide 26
L-L&R-L LHeC arc magnets & RF cavities

## Slide 27: electrical power
 | ring-ring | linac-ring
cryogenics | 1 MW | 21 MW
RF (microphonics + SR) | 79 MW | 58-80 MW*
injector | ? | 7 MW
magnets | 2 MW | 4 MW
total | 82 MW | 91-113 MW
*Erk Jensen, Chamonix’12

## Slide 28: LHeC L-R & R-R Joint IR Challenges
interaction region layout for 3 beams
  exit holes & optics, R-L: detector integrated dipole
final quadrupole design
  Q1 half quadrupole design
  synergy with HL-LHC developments (Nb3Sn)
IR synchrotron radiation shielding
  IR SR ~50 kW for both; Ec~163 (R-R) or 718 keV (R-L)
  minimize backscattering into detector
  shielding of SC quadrupoles
  SC masking to be further optimized (vac & det. bkgd)
  spin rotator (including SR)

## Slide 29: LR LHeC IR layout & SC IR quadrupoles
Non-colliding proton beam
colliding proton beam
Electron beam
Synchrotron radiation
High-gradient SC IR quadrupoles based on Nb3Sn for colliding proton beam with common low-field exit hole for electron beam and non-colliding proton beam
detector integrated dipole: 0.3 T over +/- 9 m
S. Russenschuck
Inner triplets
Exit hole for electrons & non-colliding protons
Inner triplets
Q1
Q2
Q2
Q1
R. Tomas
Nb3Sn (HFM46): 5700 A, 175 T/m, 4.7 T at 82% on LL (4 layers), 4.2 K | Nb3Sn (HFM46): 8600 A, 311 T/m, at 83% LL, 4.2 K
46 mm (half) ap., 63 mm beam sep. | 23 mm ap.. 87 mm beam sep.
0.5 T, 25 T/m | 0.09 T, 9 T/m

## Slide 30
 | SLC | CLIC (3 TeV) | ILC (RDR) | LHeC
Energy | 1.19 GeV | 2.86 GeV | 5 GeV | 60 GeV
e+/ bunch at IP | 40 x 109 | 3.72x109 | 20 x 109 | 2x109
e+/ bunch before DR inj. | 50 x 109 | 7.6x109 | 30 x 109 | N/A
Bunches / macropulse | 1 | 312 | 2625 | N/A
Macropulse repet. rate | 120 | 50 | 5 | CW
Bunches / second | 120 | 15600 | 13125 | 20x106
e+ / second | 0.06 x 1014 | 1.1 x 1014 | 3.9 x 1014 | 400 x 1014
LHeC Linac-Ring e+ source
X 18
X 65
X 6666
L. Rinolfi

## Slide 31: linac e+ source options
recycle e+ together with energy, multiple use,
  damping ring in SPS tunnel w t~2 ms
Compton ring, Compton ERL, coherent pair production, or undulator for high-energy beam
3-ring transformer & cooling scheme
accumulator ring (N turns)
fast cooling ring (N turns)
extraction ring (N turns)
(Y. Papaphilippou)
(E. Bulyak)
(H. Braun,
E. Bulyak,
T. Omori,
V. Yakimenko)
(D. Schulte)

## Slide 32: some arguments for linac or ring
energy-recovery linac
    novel far-reaching energy-efficient technology
    no interference with LHC operation & HL-LHC work
    synergies w SPL, CEBAF+, ESS, XFEL, eRHIC, SPL, ILC, …
    new technology, great investment for future (e.g. neutrino factory, linear collider, muon collider, 20-GeV SC proton linac, HE-LHC injector, higher-energy LHeC, proton-driven plasma acceleration,…)
ring
    conventional, little risk, less demanding p optics
    synergies with LEP3 Higgs factory in LHC tunnel

## Slide 33
draft LHeC time schedule (11/2011)
O. Brüning, ECFA meeting, 25 November 2011
-Only 2 long shutdowns planned before 2022
-Only 10 years for the LHeC from CDR to project start.
LS3 --- HL LHC

## Slide 34: LHeC Priority R&D
R&D activities:
-Superconducting RF with high Q & strategic partnerships  1.3 GHz versus 720 MHz
-Normal conducting compact magnet design ✔
-Superconducting 3-beam IR magnet design
 synergy with HL-LHC triplet magnet R&D
-Test facility for Energy Recovery operation and/or for compact injector complex
- R&D on high intensity polarized positron sources

## Slide 35: LHeC IR quad R&D work ?
Half-quad with field-free region, assembled using MQXC coils
  2.5 FTE
  500 kCHF
  approx. 2 years till test
Large resultants on the magnetic wedge (> 50 tons/m)
Luca Bottura @
Chamonix 2012

## Slide 36: ERL Test Facility at CERN
ERL demonstrator
e-cooling (@PS/SPS energies)
ultra-short electron bunches
strong synergy with SPL-ESS & BNL activities
High energies & CW (100 – 400 MeV)
Multi-cavity cryomodule layout (validation + gymnastics)
MW class power coupler tests in non-ERL mode (vector feedback?)
Complete HOM characterization and instability studies
FEL & gamma-ray source
R. Calaga,
E. Ciapala,
E. Jensen,
J. Tückmantel

## Slide 37: ERL Test Facility at CERN
Potential layout:
Erk Jensen

## Slide 38: LHeC key decision points
2012: choice of IR: Point 2 (or 7 or 3?)
2012: choice between linac and ring
20xx: decision to go ahead with production
2012: choice of IR: Point 2 (or 7 or 3?)

## Slide 39
thank you for your attention!
“LHeC” in google scholar / year