## Slide 1: ERL and Frequency Choice
Rama Calaga, Ed Ciapala, Erk Jensen, Joachim Tückmantel (CERN)

## Slide 2: ERL overview
Part 1

## Slide 3: Assumptions for LHeC
LHeC with Linac-Ring Option
Linac with Energy Recovery
LHeC parameters:
 | Units | Protons | RR e- | LR e-
Energy | [GeV] | 7000 | 60 | 60
Frequency | [MHz] | 400.79 | 721.42 or 1322.6 | 
Norm. ε | [mm] | 3.75 | 50 | 50
Ibeam | [mA] | >500 | 100 | 6.6
Bunch spacing | [ns] | 25, 50 | 50 | 50
Bunch population |  | 1.7· 1011 | 3.1· 1010 | 2.1· 109
Bunch length | [mm] | 75.5 | 0.3 | 0.3

## Slide 4: Low Energy ERL’s and ERL test facilities
3 x 7 cell cavities, 1.3 GHz
100mA, 50MeV, 1 mm mrad (norm), 2ps
BERLinPro
ALICE, Daresbury
2 x 9 cell, 1.3 GHz
100 pC, 10 MeV, 100 µs bunch train
Peking ERL-FEL
1 x 9 cell, 1.3 GHz
60 pC, 30 MeV, 2 ms bunch train
2 x 7 cell 1.3 GHz + DC Gun
10mA, 35MeV, 2ps
IHEP ERL, Beijing
2loop-CERL, KEK
9 cell, 1.3 GHz cavities, 4 modules
77 pC, 245 MeV, 1-3 ps
Brookhaven ERL
1 x 5 cell, 704 MHz
0.7-5 nC, 20 MeV, CW

## Slide 5: Low Energy ERL’s and ERL test facilities (contd.)
500 MHz + DC Gun
5 mA, 17 MeV, 12 ps
JAERI, Tokai
Normal Conducting 180 MHz + DC Gun
30 mA, 11 MeV, 70-100 ps
BINP, Novosibirsk

## Slide 6: Low Energy ERL’s and ERL test facilities (contd.)
IHEP ERL-TF | HZB BERLinPro | BINP | Peking FEL | BNL ERL-TF | KEK cERL | Daresbury ALICE | JAERI
35 MeV | 100 MeV | 11-40 MeV | 30 MeV | 20 MeV | 245 MeV | 10 MeV | 17 MeV
1.3 GHz 9 cell | 1.3 GHz | 180 MHz | 1.3 GHz 9-cell | 704 MHz 5-cell | 1.3 GHz 9-cell | 1.3 GHz 9-cell | 500 MHz
10 mA | 100 mA | 30 mA | 50 mA | 50-500 mA | 10-100 mA | 13 µA | 5-40 mA
60 pC | 10-77 pC | 0.9-2.2 nC | 60 pC | 0.5-5 nC | 77 pC | 80 pC | 400 pC
2-6 ps | 2 ps | 70-100ps | 1-2 ps | 18-31 ps | 1-3 ps | ~10 ps | 12 ps
1 pass | 1-2 pass | 4 passes | 1 pass | 1 pass | 2-passes | 1-pass | 1-pass
Under construction | Planned / construction | operating |  | Under construction | Under construction | operating | operating

## Slide 7: High Energy ERL’s, EIC’s (election-ion)
JLab MEIC | BNL eRHIC | CERN LHeC
5-10 GeV | 20 GeV | 60 GeV
750 MHz ? passes | 704 MHz 6 passes | 704 MHz 3-passes
3 A | 50 mA | 6.4 mA
4 nC | 3.5 nC | 0.3 nC
7.5 mm | 2 mm | 0.3 mm
Planned | Planned | Planned
JLAB, MEIC
BNL, eRHIC
CERN, LHeC

## Slide 8: High Energy ERL’s, Light sources, FEL
7GeV
Double Acc.
3GeV ERL
First Stage
XFEL-O 2nd Phase
JLAB, FEL, 160 MeV
KEK-JAEA
APS-ERL Upgrade
5 GeV, 1-2 passes
APS
Cornell ERL Light Source, 5 GeV
Beijing Advanced
Photon Complex

## Slide 9: High Energy ERL’s, Light sources, FEL’s
JLab FEL (IR, UV) | Argonne Light Source | Cornell Light source | Mainz, MESA ERL | KEK-JAEA Light Source | Beijing Photon Source
160 GeV | 7 GeV | 5 GeV | 100-200 MeV | 3 GeV | 5 GeV
1.5 GHz | 1.4 GHz 1-2 passes | 1.3 GHz | ? 2 passes | 1.3 GHz | 1.3 GHz 9 cell
10 mA | 25-100 mA | 100 mA | 0.15-10 mA | 0.01-100 mA | 10 mA
135 pC | 77 pC | 77pC | 7.7 pC | 7.7-77 pC | 77 pC
0.045-0.15 mm |  | 0.6 mm | - ps | 2 ps | 2 ps
Operating | Planned | Planned | ? | Planned | Planned
CEBAF not in the list since it is not normally operated in ER mode.
(Is this so? – Please correct me if wrong! – and help fill my other blanks!)

## Slide 10: Choice of frequency
Part 2

## Slide 11: Which frequency? 700 MHz vs. 1300 MHz
Synergy SPL, ESS, JLAB, eRHIC
Smaller BCS resistance
Less trapped modes
Smaller HOM power
Beam stability
Smaller cryo power
Power couplers easier
Synergy ILC, X-FEL
Cavity smaller
Larger R/Q
Smaller RF power (assuming same Qext)
Less Nb material needed
Advantages 700 MHz
Advantages 1300 MHz

## Slide 12: Scaling 700 MHz  1400 MHz (J. Tückmantel, 2008 for SPL)
Start with simple geometric scaling (with constant local fields):
Length, beam pipe diameter:
Surface area(s):
Volume, stored energy:
Voltage:
:
Loss factor:

## Slide 13: Scaling 700 MHz  1400 MHz (continued)
Power (input, HOM losses, main coupler): all would scale as an area
How would scale?
  but please note: is a choice
Wakefields:
  longitudinal short range wakes:
  longitudinal impedance:
  longitudinal long range wakes:
  dipole wakes: (at same offset!)

## Slide 14: Scaling 700 MHz  1400 MHz (continued)
Meaning of this latter scaling : the beam break-up threshold scales as !
Beam spectrum (multiples of 40 MHz, plus betatron and synchrotron sidebands)

## Slide 15: Scaling 700 MHz  1400 MHz (continued)
But at higher f you have also to increase the number of cells!
n cells – n modes!
2 cells
3 cells
4 cells
6 cells
10 cells

## Slide 16: Scaling 700 MHz  1400 MHz (continued)
  With (at same offset!) plus the increased number of cells per cavity:
  Beam break-up threshold current decreases with !

## Slide 17: Lower f, larger currents possible
Stable beam current limit

## Slide 18: 721 MHz much larger stable beam current limit than 1323 MHz!
My main message is this:
… but also:

## Slide 19: Dynamic wall losses
T [K]
Rs = RBCS + Rres
For small Rres, this clearly favours smaller f.

## Slide 20: One should aim for very large Q0
ILC Cavities 1.3 GHz, BCP + EP (R. Geng SRF2009)
BNL 704 MHz test cavity, BCP only! (A. Burill, AP Note 376)
first cavities – large potential
More in Ed Ciapala’s talk!

## Slide 21: ERL-TF @ CERN
Part 3: - some initial thoughts on
very sketchy and preliminary …
You are invited to contribute!

## Slide 22: ERL-TF @ CERN
5 MeV Injector
SCL1
200-400 MeV ERL Layout
4 x 5 cell, 721 MHz
~6.5 m
SCL2
Dump
 | units | 1-CM | 2-CM
Energy | [MeV] | 100 | 200-400
Frequency | [MHz] | 721 | 721
Charge | [pC] | ~500 | ~500
Rep. rate |  | CW | CW

## Slide 23: Why ERL TF @ CERN?
Physics motivation:
  ERL demonstration, FEL, γ-ray source, e-cooling demo!
  Ultra-short electron bunches
One of the 1st low-frequency, multi-pass SC-ERL
  synergy with SPL/ESS and BNL activities
High energies (200 … 400 MeV) & CW
Multi-cavity cryomodule layout – validation and gymnastics
Two-Linac layout (similar to LHeC)
  …could test CLIC-type energy recovery from SCL2  SCL1
MW class power coupler tests in non-ER mode
Complete HOM characterization and instability studies
Cryogenics & instrumentation test bed
Could this become the LHeC ERL injector (see next page)?
…

## Slide 24: Could the TF later become the LHeC ERL injector ERL?
very preliminary – just an idea by Rama and me yesterday.

## Slide 25: HOM Measurements
1.3 GHz, M. Liepe et al., IPAC2011
N. Baboi et al. (FLASH)
Complete characterization of HOM
Benchmark simulations
Improvements on damping schemes
Precision measurement of orbit
Cavity & CM alignment

## Slide 26: Injector R&D (~700 MHz)
DC Gun + SRF CM (JLAB-AES)
NC Gun (LANL-AES)
SRF Gun (FZR-AES-BNL)
SRF Gun (BNL-AES)
 | DC+SRF-CM | NC | SRF
Energy | 2-5 MeV | ? | 2 MeV
Current | 100 mA | 100 mA | 1000 mA
Long. Emit | 45 keV-ps | 200 keV-ps | -
Trans. Emit | 1.2 mm | 7 mm | < 1 mm

## Slide 27: RF Power
Main LINAC
(zero beam loading)
 | 721 MHz
Q=1 x 106 | 250 kW
Q=5 x 106 | 50 kW
Q=1 x 107 | 25 kW
Commercial television
IOT @700 MHz
Peak detuning
5 MeV injector → Pbeam ~ 50 kW (10 mA)
Will need higher powers if we go to 100 mA+
Reach steady state with increasing beam current

## Slide 28: RF Power
Use of IOTs ~ 50-100 kW at 700 MHz
High efficiency, low cost
Amplitude and phase stability
50 kW TV Amplifier, BNL
At 700 MHz

## Slide 29: Cryogenic System
Phase separator
To cryo distribution
Cryo fill line
Can use the SPL like cryo distribution system
No slope at the C-TF → the distribution line can be in center ?
V. Parma, Design review of short cryomodule

## Slide 30: RF Controls
Development of digital LLRF system (Cornell type ?)
Amplitude and phase stability at high Q0 ~ 1 x 108
Reliable operation with high beam currents + piezo tuners
In case of failure scenarios: cavity trips, arcs etc..
9-cell cavities at HoBiCaT, Liepe et al.
Rms amplitude stability
10-4
10-3
10-2
10-1
Propotional Gain

## Slide 31: RF Failures
Slow failures (for example: power cut)
Qext is very high → perhaps need to do nothing
Fast failures (coupler arc)
If single cavity → additional RF power maybe ok
Reduce beam currents or cav gradients gradually
If entire LINAC → lot of RF power
Perhaps play with 2-LINAC configuration for safe extraction of high energy beam

## Slide 32: Timeline & Costs
If:
SPL R&D CM can be used, then very fast turn-around (cheap option)
Else:
3-4 years of engineering & development (SRF + beam line)
The costs should be directly derived from SPL CM construction (< 5 MCHF ?)
Do we need high power couplers ?
R&D of HOM couplers
Will be needed for probing high current & CW
Key question: where to place the ERL-TF to have maximum flexibility ?

## Slide 33: Conclusions
We are beginners (well, I am) – but there are many ERL’s and ERL TF’s out there
… and of course expertise which will help us with the LHeC ERL
We need you!
I very strongly recommend the lower frequency (721 MHz) for transverse beam stability!
There is interesting R&D – synergetic with other activities.
A dedicated ERL-TF dedicated looks attractive, serves many purposes and is complementary to other facilities.
Thank you very much!