LHeC interaction region
R. Tomas
Many thanks for contributions to J. Abelleira,
N. Bernard, O. Bruning, Y.I. Levinsen, H. Garcia,
M. Klein, P. Kostka, S. Russenschuck, D. Schulte, L. Thompson and F. Zimmermann

---
Status and DIS12 feedback
- Concept OK
- IR synchrotron radiation scary
- Detector solenoid to be considered
- B field in e- Q1 aperture to be considered
- e-/e+ compatibility
- Chromaticity correction and FFS synchrotron radiation to be balanced (3 e- optics designs)

---
LHeC in IP2...
IR3?
IR7?
LR LHeC
recirculating
linac with
energy
recovery

---
performance targets
LHeC targets
e- energy ≥60 GeV
luminosity ~1033 cm-2s-1 or higher !
total electrical power for e-: ≤100 MW
e+p collisions with similar luminosity
simultaneous with LHC pp physics
e-/e+ polarization
detector acceptance down to 1 deg

---
	RR / HL/HA	LR
Luminosity [1033cm-2s-1]	1.3/0.7	0.4
Detector acceptance [deg]	10/1	1
Polarization [%]	40	90
IP beam sizes [μm]	30, 16	7
Crossing angle [mrad]	1	0
e- L* [m]	1.2/6.2	30
Proton L* [m]	23	10
e- beta*x,y [m]	0.2,0.1/0.4,0.2	0.12
Proton beta*x,y [m]	1.8, 0.5	0.1
Synchrotron power [kW]	33/51	50

---
LHeC Linac-Ring IR layout
D1
D1
D2
γ
D2
γ

---
Beamstrahlung photons at the entrance of D1

---
Zooming around the IP

---
Linac-Ring IR magnets
-High-gradient SC IR quadrupoles based on Nb3Sn for colliding proton beam with common low-field exit hole for electron beam and non-colliding proton beam
-Detector integrated dipole: 0.3 T over +/- 9 m
Nb3Sn (HFM46): 5700 A, 175 T/m, 4.7 T at 82% on LL (4 layers), 4.2 K	Nb3Sn (HFM46): 8600 A, 311 T/m, at 83% LL, 4.2 K
46 mm (half) ap., 63 mm beam sep.	23 mm ap.. 87 mm beam sep.
0.5 T, 25 T/m	0.09 T, 9 T/m

---
IR magnets
Bz=3.5 T, By=+/- 0.3 T
Stolen from A. Polini, DIS12

---
SR photon density at different locations

---
Linac-Ring IP Beam pipe
Inner Dimensions:
Circular(x)=2.2cm; Elliptical(-x)=-10., y=2.2cm
x=2.2cm
x= -10cm
y=2.2cm

---
LR: Power on absorber surface
e-
aperture
Proton
aperture

---
Approximation of solenoid field to the ILD case

---
Effect of ILD solenoid in the e- vertical orbit
0.5mm max excursion, 50μrad at the IP
        (few % lumi loss, correctable)

---
Fields in Q1
Poor quality in p aperture
strong field and gradient in e- aperture

---
Fields in Q1 with larger beam separation
Larger separation helps a lot for field quality

---
Larger beam separation
- Best way is to increase also L*
- L*=20 m and B=0.15T:
  - Beam separation = 130 mm
  - Photon critical energy = 360 keV
  - IR synchrotron power = 25 kW (factor 2 lower!)
  - Half quadrupole might not be necessary anymore
- This introduces larger chromaticity in LHC → larger beta* → lower luminosity
- Unless the LHeC IP could be IP3 or IP7 to adopt ATS optics-like approach

---
e-/e+ compatibility
- All e- IR and FFS dipoles and quadrupoles should be bipolar
- The solenoid polarity can stay unchanged, the orbit correction system should do
- The field in the Q1 e- aperture should be negligible → another motivation for larger beam separation

---
e- FFS optics I: Triplet

---
e- FFS optics II: Doublet, local chromaticity correction

---
e- FFS optics III: Doublet, trad. chromaticity correction

---
e- FFS quadrupoles

---
e- FFS options: performance comparison
	Triplet	doublet-local	doublet-trad.
Length [m]	90	150	260
Δσx/σx (no SR) [%]	9	1.5	5.7
Δσy/σy (no SR) [%]	21	1.7	14.1
Δσx/σx (with SR)[%]	10	141	39.3
Δσy/σy (with SR)[%]	21	1.9	14.3
ΔL/L with SR [%]	-14	-46	-23
Chromaticity correction requires a long FFS and
introduces significant emittance growth due to SR

---
Conclusions
- SR and back shining from absorber is the largest concern (lower bend/SR welcome), followed by SR power in the spin rotator
- Solenoid effects are reasonably small
- Q1 field quality might impose larger beam separation and longer L* (→reduce By/SR)
- Optimization of L* and β* within the LHC
- e- FFS optics: balance between chromaticity correction, SR and length
- Common effort needed for the global optimization → study group

---
Ring-Ring HA & HL layouts

---
Ring-Ring proton quadrupoles
Standard tech: NbTi