## Slide 1: Computing Resources Requirements 2013-2017
September 18, 2012

## Slide 2: ForEword
Computing Resources requirements estimated for the period 2013-2017
To be discussed by WLCG in September 2012 (now)
To be presented to the RRB in October 2012

## Slide 3: LHC Schedule

## Slide 4: LHC schedule
… our guess for pa
2012-2013
 | Effective time (s) | Number of events | Effective trigger rate (Hz)
pp (2012) | 3.4×106 | 1.2×109 | 314
pA (2013) | 5.1×105 | 3.0×108 | 800

## Slide 5: LHC schedule
… our guess
2014: no data

## Slide 6: LHC schedule
… our guess
2015-2017: standard years
 | Effective time (s) | Number of events | Effective trigger rate (Hz)
pp | 3.4×106 | 1.7×109 | 500
AA | 4.6×105 | 4.2×108 | 925

## Slide 7: Computing Model parameters

## Slide 8: Computing model parameters
… from 2012 data processing
CPU power
kHEP06×s/event | Reconstruction | Analysis Train | End Users Analysis | Monte-Carlo
pp | 0.08 | 0.13 | 0.01 | 1.14
AA | 2.00 | 1.99 | 0.14 | 90.00

## Slide 9: Computing model parameters
… from 2012 data processing
Data size
MBytes/event | Raw | ESD | AOD | Monte-Carlo
pp | 0.41 | 0.23 | 0.01 | 0.37
AA | 5.59 | 5.26 | 1.10 | 20.00

## Slide 10: Requirements

## Slide 11: Requirements
CPU
Chart: 
| 2013.0 | 2014.0 | 2015.0 | 2016.0 | 2017.0
T0 | 91 | 100 | 100 | 120 | 120
CAF | 35 | 35 | 45 | 55 | 55
T1s | 98.4 | 151.2 | 151.2 | 174 | 174
T2s | 166 | 211 | 211 | 216 | 216
KHEP06
+10%
+20%
+56%
+16%
+20%
+8%

## Slide 12: Requirements
Tape
Chart: 
| 2013.0 | 2014.0 | 2015.0 | 2016.0 | 2017.0
T0 | 22.8 | 26.1 | 30.3 | 42.7 | 57.3
T1s | 19.6 | 23.9 | 26.8 | 37 | 49
PBytes
+20%
+9%
+35%

## Slide 13: Requirements
Chart: 
| 2013.0 | 2014.0 | 2015.0 | 2016.0 | 2017.0
T0 | 10.8 | 10.8 | 13.8 | 16.7 | 19.5
CAF | 0.24 | 0.24 | 0.34 | 0.44 | 0.54
T1s | 8.9 | 8.9 | 11.3 | 13.5 | 16
T2s | 15.8 | 15.8 | 20.1 | 24 | 27.8
Disk
PBytes
+20%
+28%
+20%

## Slide 14: Beyond 2017
After LS2 :
  Tape +163 PB (× 3)
  Disk +125 PB (× 2)