## Slide 1: A TPC for High-Rate Experiments: Towards an Upgrade of the ALICE TPC
Bernhard Ketzer
Technische Universität München
On behalf of the GEM-TPC Collaboration and the ALICE TPC Collaboration
11 February 2013
Vienna Conference on Instrumentation 2013

## Slide 2: Time Projection Chamber
Combination of MWPC and Drift Chamber: 3-D tracking device
  long drift path (~m) in gas-filled volume  z coordinate
  MWPC + pads perpendicular to drift path  x,y coordinates
Time Projection Chamber [D.R. Nygren et al., Phys. Today 31, 46 (1978)]

## Slide 3: Advantages and Limitations of a TPC
An (almost) ideal tracking detector:
Large acceptance
Large active volume
Low material budget
3D hits  simple pattern recognition
Extremely high particle densities
 heavy ion experiments
Good momentum resolution
Particle identification
Examples:
STAR (420 cm × 400 cm)
ALICE (500 cm × 500 cm)
Limitations:
Calibration very demanding
Drift distortions due to ion backflow
Gating  low trigger rates

## Slide 4: Advantages and Limitations of a TPC
Limitations:
Calibration very demanding
Drift distortions due to ion backflow
Gating  low trigger rates
Examples:
STAR (420 cm × 400 cm)
ALICE (500 cm × 500 cm)

## Slide 5: The ALICE Detector
e ALICE Detector
TPC Parameters:
Ne/CO2(90/10)
18 sectors per readout plane
557568 pads
IROC: pads
OROC: pads
TPC performance:
at 10 GeV
(159 clusters)
Readout rate: 500 Hz (Pb-Pb)

## Slide 6: ALICE Upgrade
- Small diameter beam pipe
Talk by Serhiy SENYUKOV on 13 Feb 2013 at 11:30 AM

## Slide 7: Operation at High Rates
  Goal: operate ALICE at high luminosity )
    Record all minimum bias events:
      50 kHz in Pb-Pb collisions  100× higher than present
  ~ 5 overlapping events
  no gating and continuous readout: TPC as analog event pipeline
Event from
2013 p-Pb
Run
Notes: Preserve tracking and PID preformance
Enhance secondary vertex capability and tracking at low pT

## Slide 8: Outline
Introduction
Ion Backflow and Distortions
Prototype Detectors
  GEM-TPC in FOPI
  ALICE IROC with GEM amplification
Conclusions and Outlook

## Slide 9: Ion Backflow Suppression in GEM
Low ion density in drift region requires
  low primary ionization
  low gain
  low ion backflow

## Slide 10: Space Charge Effects
e = 5
e = 10
[S. Rossegger, CERN, F. Böhmer, TUM]
Goal: IB = 0.55%, e = 10 at G = 2000
 Resulting distortions can be corrected

## Slide 11: Ion Backflow - Measurements
 Issues concerning:
  diffusion, e− transparency
  energy resolution
  stability
Low ion backflow requires
    low drift field
    very asymmetric transfer fields
    highest amplification in 3rd GEM
Ar/CO2 (70/30)
[T. Huber, TUM]
TUM

## Slide 12: Ion Backflow - Measurements
TUM
Ar/CO2 (70/30)
Ar/CO2 (70/30)
Rate dependence
 Space charge effect?
Low ion backflow requires
    low drift field
    very asymmetric transfer fields
    highest amplification in 3rd GEM
[C. Garabatos, Y. Yamaguchi, CERN]
CERN
[T. Huber, TUM]

## Slide 13: Ion Backflow - Measurements
Ne/CO2 (90/10)
Ion backflow in Ne/CO2 higher:
Higher drift field:
Keep to avoid amplification in transfer gap
Solutions under study:
Add N2 to gas
Tolerate small amplification in transfer gap
Add 4th GEM
[A. Hönle, K. Eckstein, TUM]

## Slide 14: Ion Backflow - Simulations
ANSYS + GARFIELD/MAGBOLTZ: Systematic scan of parameter space
    Gas composition
    Three / four GEMs
[T. Gunji, Univ. Tokyo]
4 GEM configuration

## Slide 15: Ion Backflow - Simulations
ANSYS + GARFIELD/MAGBOLTZ: Systematic scan of parameter space
    Gas composition
    Three / four GEMs
    Hole geometry, aspect ratio
  Explore more exotic configurations
    Hole alignment
    Cobra GEM
[A. Lyashenko et al., NIM A 598 (2009) 116]
[F. Sauli et al., NIM A 560 (2006) 269]

## Slide 16: Outline
Introduction
Ion Backflow and Distortions
Prototype Detectors
  GEM-TPC in FOPI
  ALICE IROC with GEM amplification
Conclusions and Outlook

## Slide 17: FOPI GEM-TPC
Light-weight field cage
Drift length 725 mm
Ø 105-300 mm
Triple GEM amplification
10254 ch., AFTER ASIC
Gas: Ar (Ne)/CO2 (90/10)
[L. Fabbietti et al., NIM A 628, 204 (2011),
M. Ball et al., arXiv1207.0013, 2012]

## Slide 18: Installation in FOPI
Al target (x/lI = 2%) at z=0 and -34 cm
  84Kr beam, 1.4 AGeV, 40·104 / 10s
  197Au beam, 1.2 AGeV, 40·103 / 10s
  22Ne beam, 1.7 AGeV, 1·106 / 10s
Physics run, p beam, 1.7 GeV/c, C, Cu, Pb targets

## Slide 19: Gain Calibration with 83mKr
Equalization of gain for each pad
Resolution before correction:
  Main peak 6.9%
After correction:
  Main peak 5.1%
Results similar for Ne/CO2 (90/10)
[R. Schmitz, D. Kaiser, HISKP Bonn]

## Slide 20: Position and Momentum Resolution
Track reconstruction in TPC:
Riemann pattern recognition
[J. Rauch, TUM]
Track fitting: GENFIT
[C. Höppner et al., NIM A 620, 518 (2010)]
s = 230 mm
Spatial Resolution vs z
Momentum Resolution
[M. Berger, TUM]
[F. Cusanno, TUM]

## Slide 21: Vertex Resolution
Vertex reconstruction
using GENFIT / RAVE
Considerable improvement in z-direction
[J. Rauch, TUM]

## Slide 22: Energy Resolution
PID using dE/dx:
  Resolution ~ 18%
  No density correction yet
First dE/dx measurement
with GEM-TPC!
Sum up charge in 5 mm steps
Truncated mean: 0-70%
Momentum from TPC + CDC
p-p separation
[F. Böhmer, M. Ball, TUM]
K
p
p
d

## Slide 23: ALICE IROC Prototype
[P. Gasik, M. Berger, TUM]
3 large-size GEM foils: single-mask
18 sectors (top side), ~ 100cm2 each
bias resistors 10 / 1MW
2mm frames glued on bottom side
spacer grid: 400mm thickness
additional frame for induction gap: 4mm

## Slide 24: IROC Beam Test at CERN PS
p, p±, e± beam, 1/2/3/6 GeV/c
2000 particles / 0.5s
Cherenkov and Pb glass detectors for PID
Electronics: PCA16 / ALTRO (LCTPC)
Goal: measure separation power for different voltage settings

## Slide 25: IROC Beam Test at CERN PS
Gain equalization using tracks
No temperature/pressure correction yet
Truncated mean of cluster charge: 5 – 70%
for pions at 1 GeV
For comparison: IROC in ALICE TPC:
electrons
pions
p=1 GeV/c
G=5000
[J. Wiechula, Tübingen]

## Slide 26: Test in ALICE with p-Pb 2013
Chamber installed underneath LHC beam pipe
Standalone readout: signals, discharges, trips
Run still ongoing

## Slide 27: Conclusions
GEM-TPC:
  Opens possibility to use TPC in high-rate environments without gate
  Large GEM-TPC fully operational in FOPI
  Performance: improvement of vertex/momentum resolution, forward
  First dE/dx measurement with GEM-TPC
  Physics analysis ongoing
ALICE TPC:
  Plan to upgrade TPC with GEM endorsed by LHCC
  Prototype IROC equipped with GEMs
  Successful beam test at CERN PS
  Stability test in ALICE cavern during p-Pb run in 2013
  Issues under study:
    ion backflow
    front-end electronics and readout

## Slide 28: Experiments with GEM-TPCs
CB-ELSA (Bonn)
DarkLight (JLAB)
ALICE (CERN)
FOPI (GSI)
ILC

## Slide 29: Thanks to
GEM-TPC Collaboration
R. Arora, M. Ball, R. Beck, M. Berger, J.-C. Berger-Chen, F.V. Böhmer, P. Bühler, F. Cusanno, S. Dørheim, K. Eckstein, L. Fabbietti, J. Frühauf , J. Hehner , N. Herrmann, A. Hönle, C. Höppner, D. Kaiser, B. Ketzer, M. Kis, V. Kleipa, I. Konorov, J. Kunkel, N. Kurz, M. Lang, Y. Leifels, P. Müllner, R. Münzer, S. Neubert, S. Paul, K. Peters, J. Rauch, H. Risch, C.J. Schmidt, L. Schmitt, S. Schwab, R. Schmitz, D. Soyk, S. Uhl, M. Vandenbroucke, B. Voss, J. D. Walther, J. Weinert, J. Zmeskal
ALICE TPC Upgrade Team
H. Appelshaeuser, M. Ball, E. Bartsch, G. Bencze, M. Berger, P. Braun-Munzinger, J.-C. Berger-Chen, S. Dorheim, K. Eckstein, I. Erdemir, L. Fabbietti, C. Garabatos, P. Gasik, T. Gunji, A. Hoenle, B. Ketzer, G. Hamar, C. Lippmann, M. Ljunggren, S. Masciocchi, T. Morhardt, E. Oliveri, A. Oskarsson, M. Ozdemir, G. Paic, V. Peskov, N. Pitz, L. Ropelewski, K. Teresaki, D. Vranic, J. Wiechula, Y. Yamaguchi

## Slide 30
Thank you for your attention!

## Slide 31: Spare Slides

## Slide 32: Signal-to-Noise Ratio
Ne/CO2 (90/10)
Edrift = 360 V/cm
B = 0.6 T

## Slide 33: Spatial Resolution
GEM pad response function smaller than MWPC  pad size adequate?
Resolution diffusion-dominated for z<200 cm
Increasing number of single-pad clusters for shorter drift length,
but partially outside barrel acceptance (|h|<0.9)
[H. Appelshäuser]

## Slide 34: Momentum Resolution
[H. Appelshäuser]

## Slide 35: Cobra
reached
problem of IB completely eliminated!
to be studied: e- transparency, size
[A. Lyashenko et al., NIM A 598 (2009) 116–120]

## Slide 36: FEE Specifications
 | TPC | 
 | Now | Upgrade
Polarity | Pos | Neg
Detector capacitance | 12 – 28 pF | 12 – 28 pF
Peaking time | 160ns | 160ns
Shaping | 4th order | 4th order
Sensitivity (mV/fC) | 12 | 12
Gas gain | ~4000 | 1,000-2,000
Noise (electrons) | 700e–@25pF | <700e-@25pF
Linear Range (V) | 2V | 2V
Linear Range (fC) | 170fC | 170fC
Signal coding | 10 bits | 10 bits
Power consumption (per ch) | ~32mW (PASA+ALTRO) | ≤ 32mW
Channel per chip | 16 | 16 – 32
Chan per readout link | 2,304 – 3,200 | 80 – 400
Aim: Common FE chip for different ALICE subdetectors
Based on S-ALTRO
  Programmable polarities and frontend peaking times,
  DSP: Signal processing etc.
10 bit SAR ADC; power consumption only 1-2 mW per channel

## Slide 37: Readout Architecture
Readout architecture has to support
  Continuous (trigger-less) readout for physics data taking
  Triggered readout (for calibration runs, e.g. pedestal)
Two options under study:
  CERN GBT (radiation hard ASIC, 4.8 Gb/s versatile links)
  DDL3: Custom optical link with radiation-tolerant smartfusion2 FPGA as readout unit close to the Front-End (10 Gb/s)
FTP
LTU
DCS Server
DAQ/HLT EPN
DCS Server
Data traffic
GBT: Trigger & Data & Control
Monitoring & Control
Trigger
& Busy
Front-End
DAQ/HLT FLP
DAQ/HLT
Network
DCS
Network
Option 1

## Slide 38: Electronics
+ ASIC for ATLAS muon upgrade (BNL)
Performance of present FE electronics satisfactory for final detector
Self-triggering capability  several solutions being developed