## Slide 1
On behalf of the LCTPC collaboration
VCI13, February 12th, 2013
Large Prototype TPC using Micro-Pattern Gaseous Detectors
 David Attié 
Notes: I’m here to present a TPC review

## Slide 2: Overview
Introduction: Physics case at International Linear Collider (ILC)
Large Prototype Time Projection Chamber for ILC
TPC Readout using Micro-Pattern Gaseous Detectors:
  GEM module with ALTRO electronics
  Integrated AFTER-based electronics and resistive Micromegas detector module
Latest results
  Time information
  Spatial resolution
  Alignment
  Field distorsions
Conclusion

## Slide 3: Introduction: Physics Case at ILC
Identify the particle of cosmic dark matter
Find the origin of the masses of elementary particles
  precision of Higgs coupling to each particle mass
  sensitivity of the ILC experiments to Higgs boson couplings in a model-independent analysis
Higgs recoil mass: e+e- → ZH (Z→μ+μ-/e+e-) + X
Next collider: linear e+e– collider, length: ~ 31km
Tunable center of mass energy of 200-500 GeV
Two detectors with push-pull concept
Need to to fit into Particle Flow* concept [*] Particle flow: the aim to reconstruct every particle in the best suited sub detector

## Slide 4: Time Projection Chamber for ILD
TPC is the central tracker for International Linear Detector
– Large number of 3D points  continuous tracking
– Good track separation and pattern recognition
• Low material budget inside the calorimeters important for PFA
– Barrel: ~5% X0 – Endplates: ~25% X0
• Two options for endplate readout:
    – GEM: 1.2×5.8 mm² pads using ALTRO electronics
    – Resistive Micromegas: 3×7 mm²pads using AFTER electronics
• Alternative: pixel readout with pixel size ~55×55 μm²
ILD
TPC Requirements :
Momentum resolution:
(1/pT) < 9×10-5 GeV-1
Spatial resolution at 3.5T:
(r) < 100 m
(z) < 500 m
Tracking eff. for pT>1 GeV: 97%
dE/dx resolution ~5%
4.3m
3.6m
Cathode membrane
Endplate
MPGD
Large Prototype
TPC

## Slide 5: Large Prototype TPC for ILC
Built by the LCTPC collaboration
Financed by EUDET & AIDA
Located at DESY: 6 GeV e- beam
Sharing out :
- magnet: KEK, Japan
- field cage: DESY, Germany
- lifting stage: DESY, Germany
- cosmic trigger: Saclay, France
- beam trigger: Nikhef, Netherlands
- endplate: Cornell, USA
- Resistive Micromegas: Irfu, France, Carleton/Montreal, Canada
- Double GEMs with 100m laser-etched crystal polymer, Saga, Japan
- Triple standard 50m GEMs: Germany
- TimePix pixel: F, G, NL<
1T PCMagnet on lifting stage
Large Prototype TPC
Endplate + 7 Micromegas modules

## Slide 6: Micro-Pattern Gaseous Detectors: Micromegas & GEM
50-100 µm
40 kV/cm
~1000 µm
1 kV/cm
GEM
~100 µm
80 kV/cm
Micromegas
Technology choice for TPC readout: Micro Pattern Gaseous Detector
more robust than wires
no E×B effect
better ageing properties
easier to manufacture
Avalanche
fast signal & high gain
low ion backdrift
Gas Electron Multiplier (F. Sauli, 1997)
2 copper foils separated by kapton
multiplication takes place in holes
use of 2 or 3 stages
MICROMEsh GAseous Structure (Y. Giomataris et al., 1996)
metallic micromesh (typical pitch 50μm)
supported by 50μm pillars, multiplication between anode and mesh, high gain
Gas Electron Multiplier (F. Sauli, 1997)
2 copper foils separated by kapton
multiplication takes place in holes
2-3 layers needed

## Slide 7: DESY GEM: Module Design
Triple GEM stack
Grid support structure
Top GEM electrode not segmented Bottom segmented into 4 sectors
4829 channels (pad size: 1.26×5.85 mm2) read out by ALTRO electronics
HV line for each GEM side
Protection resistors very close to GEM

## Slide 8: DESY GEM: Simulations of Field Distorsions
Simulation of electric field at module borders
Using a field shaping wire improves field
homogeneity
Better charge collection efficiency
Measurements
Simulations

## Slide 9: DESY GEM: Single Point Resolution
Without magnetic field using a single module
1 module data from 2011 in 5 GeV electron beam

## Slide 10: Resistive Micromegas: Module Design
Pads PCB
+
Micromegas
Cooling system
Front-End Mezzanine
Front-End Card (FEC)
Fully integrated Module
Resistive Micromegas Detector
FEC
FEM

## Slide 11: Resistive Micromegas: spread charge technology
Specific Pad Response Function (PRF) needed
PRF parameters determined by fitting data
Use material properties and geometry to spread charge over pads
Diffusion equation on the 2D continuous RC network:
Resistive foil
Isolated layer
Pads
PCB
Micromegas mesh
See Dixit et.al., NIM A518 (2004) 721
left
Pads
middle
right
Pad pulses
Pulse height scatter

## Slide 12: Resistive Micromegas: 7-Module Beam Tests
t = 1 s
t = 7.2 s
Zbeam=2.5 cm
Zbeam=50 cm
5 GeV electron beam
Gas: Argon/CF4/Isobutane (95/3/2)
Edrift = 230 V/cm
B = 1 T
Micromegas gain (380V): ~5000
pads
Row
12 000 channels in 7 modules
24
72

## Slide 13: Resistive Micromegas: ILC Software analysis
Analysis done using ILCSoft framework:
  Find the pulses in the detector
  Obtain hit with PRF fit
   (r, , z[t])
  Tracks are reconstructed used a Kalman filter processor
  Resolution, momentum, …
No telescope was used to determined the position of the tracks

## Slide 14: Resistive Micromegas: Time Zero and Drift Velocity
Bfield (T) | Edrift (V/cm) | Drift Velocity (cm/s) | 
 |  | Measured | Simulated
1 | 230 | 7.50±0.07 | 7,6
1 | 140 | 5.83±0.03 | 5,91
0 | 230 | 7.63±0.04 | 7,6
0 | 140 | 5.94±0.04 | 5,91
t0 = 0.66 ± 0.04 s

## Slide 15: Resistive Micromegas: Space resolution studies
Edrift = 230 V/cm
Bfield=1T
Vmesh = 380 V
Beam energy = 5 GeV
Preliminary
7 modules with pad size 3×7 mm²

## Slide 16: Resistive Micromegas: Alignment
Bfield=0T
After alignement
Before alignment
Row Number
Row Number
Displacement (mm)
Displacement (mm)
Module # (rows #) | 1 (0-23) | 3 (24-47) | 5 (48-71)
df (mrad) | -3.0 | -2.6-1 | -1.4
dx (m) | -23 | 14 | 17

## Slide 17: Resistive Micromegas: Field Distorsions
Bfield=1T  E×B effect observed
After alignement
Before alignment
Row Number
Row Number
Displacement (mm)
Displacement (mm)
Module # (rows #) | 1 (0-23) | 3 (24-47) | 5 (48-71)
df (mrad) | 2.9 | 2.1 | 2.2
dx (m) | 47 | -43 | -52

## Slide 18: Summary
The LCTPC collaboration have been working since many years on a Large Prototype of a TPC
The performance of two MPGD technology reached the requirements of the ILD detector
The readout technology has to be chosen (GEM or Micromegas)
Ion back drift, electronics, mechanical integration, ... are under study waiting for the approval of the ILC project

## Slide 19: Thank you

## Slide 20: Backup slides

## Slide 21: Pad Response Function PRF
PRF function:
Only two parameters
Easier to work with
Better fits to data

## Slide 22: Old PRF – Ratio of two symmetric quartics