## Slide 1: R&D for THE upgrade of the high momentum particle identification detector for ALICE at LHC
A. Di Mauro
(CERN - Geneva, Switzerland)
on behalf of the ALICE/VHMPID collaboration

## Slide 2: Outline
Physics motivation for a Very High Momentum PID upgrade
New design specifications and related R&D
Expected performance
Testbeam studies
Summary

## Slide 3: PID in ALICE
ALICE specifically designed to study Quark-Gluon Plasma in “heavy ion collisions” at LHC, pp studies relevant part of the physics program
Excellent PID capabilities by combining different techniques over a large momentum range
ALICE: P.P.R., vol. I”, J.Phys.G30:1517-1763,2004

## Slide 4: Physics motivation
The Very High Momentum PID (VHMPID) RICH has been proposed as additional detector to extend charged hadron track-by-track PID capability up to 25 GeV/c and complement the existing measurements based on statistical methods (dE/dx), addressing specifically the study of jets properties
The latest proposal foresees the combined integration of an EMCAL and a RICH in the same acceptance to achieve direct reconstruction of the full jet and its energy, thus significantly improving the track-by-track physics and correlation measurements (jet-hadron, di-hadron)
Such an integrated detector system will provide major contribution in the determination of particle identified fragmentation functions both in pp and in heavy ion physics

## Slide 5: Design specifications and R&D issues I.
First VHMPID proposal in 2006, various layouts studied; after first LHC results at the end of 2011, new specifications requiring further R&D:
Charged hadrons (p, K, p) identification in 5 -25 GeV/c and combined integration with EMCAL extension (DCAL) -> Cherenkov radiator
  K identification starting at 5 GeV/c not possible with any gaseous radiator at atmospheric pressure: increase radiator gas pressure to lower Cherenkov threshold
  After discontinuing of production by 3M, poor UV transparency and larger cost of C4F10 available on the market: new radiator gas C4F8O, tested for BTeV RICH in the visible, first use in UV. 2nd option: C5F12.
  Max detector depth ~70 cm (limited “free” space) pushes for a compact detector
  Focusing RICH with pressurized C4F8O gaseous radiator

## Slide 6: Cherenkov radiator gas pressurization
Refractive index optimization
@ 3.5 bar and L= 50 cm: excellent photon yield and ring radius (5 cm) suitable for pattern recognition
PID range can be extended by lowering P
@ 3.5 bar C4F8O needs heating at ~ 40 oC to prevent condensation
Using C5F12 : P ~ 2.8 bar, T~ 60 oC
P [bar] | Refr. ind.@ 175 nm | Momentum threshold [GeV/c] |  |  | Nph cm-1 eV-1 at saturation
 |  | p | K | p | 
1 | 1.00153 | 2.5 | 9 | 17 | 1.1
1.5 | 1.002295 | 2.1 | 7.3 | 13.5 | 1.7
2 | 1.00306 | 1.8 | 6.4 | 12 | 2.2
2.5 | 1.00383 | 1.6 | 5.6 | 10.7 | 2.9
3 | 1.0046 | 1.5 | 5.1 | 9.8 | 3.4
3.5 | 1.00535 | 1.3 | 4.8 | 9.1 | 3.9
liquid
gas

## Slide 7: Design specifications and R&D issues II.
Large acceptance (up to 60 m2, ~ 30% of the barrel) and large photosensitive area (up to 8 m2) + B=0.5 T -> photon detector
  ALICE HMPID ( 11 m2 of CsI-MWPC) know-how, CsI-based photo-detector is the most cost effective solution
  Modified MWPC with reduced CsI PC pad size and anode-cathode gap: improved spatial resolution + smaller induction spread (5 cm ring radius wrt 12 cm in HMPID)
  CsI-based TGEM photon detector
  Photonis Planacon XP85012Q with bialkali PC to work in the visible
High luminosity ALICE upgrade (pp: up to 2 MHz, Pb-Pb: 50 KHz)
  Front-end and readout electronics
Other topics
  Radiator vessel and mirror system engineering studies
  Radiator gas cleaning and UV transparency measurement systems
  Tracking detector based on CCC (Close-Cathode Chamber)

## Slide 8: Baseline detector principle scheme
Focusing RICH, C4F8O gaseous radiator L~ 50 cm, operated at 1-3.5 bar
Al honeycomb radiator vessel, 4 mm sapphire window with A/R coating
HMPID-like photon detector: MWPC with CsI pad segmented photocathode, operated with CH4 ; pad size 4x8 mm2 , 20 mm anode wires, 0.8 mm gap, 4 mm pitch
50x50 cm2 spherical mirror, light C-fiber substrate, Al/MgF2 coating
CCC tracking layers with strip chambers
FEE with analogue readout for centroid measurement, three options:
  HMPID Gassiplex chip with T/H, modified version from COMPASS RICH (max 500 KHz trigger rate)
  APV25 with continuous sampling at 40 MHz, as used in COMPASS RICH and HADES RICH upgrades
  new common FEE developments for ALICE high-lumi upgrade
phi cross section

## Slide 9: Detector layout and integration in ALICE
VHMPID
DCAL
Module arrangement under study
5 Central modules, size ~ 1.4x1.7x0.7 m3
10 Side modules, size: ~ 2.7x1.7x0.7 m3

## Slide 10: Mirror layout studies with ZEMAX
CsI photocathode
IP
Focal point for mirror 1
Focal point for mirror 2
3-D View
217

## Slide 11: Detector figure of merit N0
MC simulation: 15 GeV/c p, C4F8O @ 3.5 bar
Single photoelectrons overlap within a pad cluster: number of reconstructed photons
Nrp < Npe .
Npe
Nrp
 | UV | Visible
N0 [cm-1] | 60 | 130
Npe | 24 | 45
Lab measurements

## Slide 12: Angular resolution and particle separation
12/30
 | UV | Visible
sq chromatic | 2.7 mrad | 5.3 mrad (!)
sq emission | 0.5 mrad | 0.5 mrad
sq granularity | 1.7 mrad | 1.7 mrad
sq tracking | 1.6 mrad | 1.6 mrad
sq total | 3.6 mrad | 5.8 mrad
Nrp | ~ 13 | ~ 30
sq track | ~ 1 mrad | ~ 1.1 mrad
Theoretical estimation
C4F8O @ 3.5 bar
PID ranges
- Lower limit: cut Nrp >2
- Upper limit: 3s separation
 | Signal (GeV/c) | Absence of signal (GeV/c)
p | 2-16 | 
K | 5-16 | 
p | 10-25 | 5-10
assuming sqtrack ~ 1.5 mrad

## Slide 13: MC studies of PID performance
Events from single particles gun embedded in HIJING generated background (ALIROOT framework)

## Slide 14: MC studies of PID performance
Events from single particles gun embedded in HIJING generated background (ALIROOT framework)
Probability of identification for p, K, p
PID algorithm based on HMPID pattern recognition (Hough transform)
Further tuning/optimization in progress for VHMPID ring patterns

## Slide 15: Testbeam studies at CERN PS/T10
Prototypes using liquid C6F14 radiator (in proximity focusing, HMPID-like), and C4F10 or C4F8O at atmospheric pressure with mirror focusing
MWPC prototype with adjustable anode-cathode gap (0.8-2 mm), smaller pad
Prototype with C4F8O radiator pressurization and heating
CsI-TGEM and -RETGEM as photon-detector in RICH prototype with C6F14 radiator (see V. Peskov’s talk)

## Slide 16: Prototype with two Cherenkov radiators (Nov 2011)
C4F10 or C4F8O radiator gas at atmospheric pressure
(L = 100 cm)
C6F14 liquid radiator
Achieved HMPID benchmark performance
CsI PC, 8x8 mm2 pads
Gaseous radiator
Liquid radiator
SiO2 windows
Spherical mirror
MWPC
20 mm anode wires,
2 mm gap, 4 mm pitch
beam
Spherical mirror

## Slide 17: Comparison C6F14 /C4F10 /C4F8O
C6F14 thickness : 6 mm, to obtain same photon yield as 100 cm gaseous radiator
First tests with radiator gas, C4F10 and C4F8O used w/o cleaning or filtering
Simulation with
full absorption
for l < 175 nm
Simulation with
full absorption
for l < 175 nm
C6F14
<10>
C4F10
<2.9>
C4F8O
<4.4>

## Slide 18: Variable-gap chamber tests (June 2012)
Refurbished old prototype (F. Piuz, RD26), anode-pad cathode gap adjustable in 0.8-2 mm (100 mm steps), anode -wire cathode 2 mm, 20 mm anode wires, pitch 4 mm
Basic performance studies using liquid C6F14 radiator, 3 mm thick: HV scan, gap scan
Pad cathode before CsI coating
60x16 pads, 4x8 mm2
C6F14 liquid radiator
RICH prototype with variable-gap
MWPC photon-detector

## Slide 19: Variable-gap chamber tests (June 2012)
Single e- PH spectrum
Gain vs HV at various gaps
Equal amount of photons seen @ various gaps
slope-> gain A0

## Slide 20: Variable-gap chamber tests (June 2012)
Cluster size proportional to gap
No. of raw clusters increases by reducing the gap

## Slide 21: Testbeam with pressurized C4F8O radiator (Oct 2012)
Radiator equipped with heating tape and P, T probes
Safety pressure test (@ 5 bar for 5 h)
Heating studies with Fluent 6.0 to optimize insulation and ensure radiator temperature uniformity
51
IN
OUT
Sapphire window
C4F8O
radiator

## Slide 22: Testbeam with pressurized C4F8O radiator (Oct 2012)
P, T monitoring and control panel
Gas system, piping and detector heated and insulated

## Slide 23
The first 15 events for C4F8O at 3.5 bara with 6 GeV/c p- beam
Testbeam with pressurized C4F8O radiator (Oct 2012)

## Slide 24: Testbeam with pressurized C4F8O radiator (Oct 2012)

## Slide 25: Testbeam with pressurized C4F8O radiator (Oct 2012)
Few % K’s contamination: detected and identified
C4F8O refractive index in UV ~ C4F10 , simulation are in progress to deduce exact parameterization

## Slide 26: Testbeam of CsI-TGEM photon detector with C6F14 liquid radiator (2011)
6 TGEM stack layout
Observed detection efficiency ~ 60% of HMPID, Gassiplex not optimized for TGEM
First tests performed with APV25 and in progress
New tests planned with larger TGEM

## Slide 27: Photonis Planacon XP85012
Due to delay on electronics production, it could not be tested before the end of testbeam at CERN/PS in 2012
Planned lab tests with LED source
Pro’s | Con’s
Larger photon yield (larger bandwidth in visible), intrinsically faster | Cost (~ 8.8 K$ /piece) and timescale for full production
No issues from radiator gas transparency (purity, O2 and H2O contamination), less demanding systems | Chromatic error due to larger bandwidth, (compensated by photon yield, final performance similar to UV)
Can be mounted inside radiator vessel, sapphire windows not needed | Detection efficiency losses due to 80% packing factor
Commercial device, savings on work for photon detector, no CH4 gas system | 
LAPPD ALD-MCP (A. Elagin’s talk) could be a further option depending on R&D timescale

## Slide 28: Summary and outlook
Intense R&D campaign has been performed in 2011/12 to meet new design requirements
Successful tests of C4F8O as Cherenkov radiator in UV, proven preliminary design concepts for pressurization/heating
Baseline solution for photon-detector: CsI-MWPC with thin gap; new prototype with final layout successfully tested in Dec ‘12
Further activities
  continue tests on CsI-TGEM and Planacon, for “faster” detector option
  FEE and readout electronics development
  engineering studies on vessel structure and mirror system
LoI submitted this week to the ALICE Collaboration, final decision in March

## Slide 31: BACK-UP SLIDES

## Slide 32: Material budget
Detector component | X/X0
Bottom+top radiator vessel sandwich panel | 7%
Photon detector + tracking layers | 3%
C-fiber mirror substrate | 2%
Radiator gas at 3.5 bar | 4%
Sapphire window | 6%
total | 22%
For comparison:
- ITS + TPC ~ 15% X0
- TRD ~ 26% X0
- TOF ~ 20% X0

## Slide 33: Radiator refractive index and QE curves
C4F8O cutoff
sapphire cutoff