The Spectrometer Telescope for Imaging X-Rays
on-board the ESA Solar Orbiter satellite
Oliver Grimm
Institute for Particle Physics, ETH Zürich
—— for the STIX collaboration ——
13th Vienna Conference on Instrumentation
12 February 2013, Vienna

---
ESA Solar Orbiter
“How does the Sun create and control the heliosphere?”
● Sun-heliosphere interaction	● Solar wind accelerating mechanisms
● Energetic solar phenomena	● Solar wind plasma, coronal magnetic fields
● Solar transients, heliospheric variability	● Solar dynamo working principle
10 instruments
(remote-sensing and in-situ)
Mass 1.8 t (payload 180 kg)
Power 180 W
Telemetry 150 kbps (@ 1 AU)
Launch January 2017
Mission duration 4+3 years
Resonance orbit with Venus
Currently in realization phase C
STIX
~2 m

---
STIX Science Goal
Imaging 4-150 keV x-rays
determines intensity, spectrum, timing and location	of accelerated electrons near the Sun.
Study	● acceleration mechanism of electrons at the Sun
● electron transport into interplanetary space
UV image
X-ray source structures
are not very complex
SDO AIA image

---
STIX Design
Instrument allocation is 4 W power, 7 kg mass and 700 bits/s telemetry.
→ only indirect Fourier imaging feasable at X-ray energies for required parameters
Imager tube
X-Ray windows
Detector Electronics
Module
Energy range	4-150 keV
Energy resolution	1 keV (FWHM @5 keV)
Effective area	6 cm2
Angular resolution	7 arcsec
Pointing accuracy	4 arcsec
Field of view	2°
Time resolution	0.1s (statistics limited)
~20 cm

---
STIX imaging: Basic principle
2 grids with slightly different pitch
Illuminated by point source at large distrance
→ Moire transmission pattern
Large-scale Moire structure encodes direction to point source
One grid shifted by ½ period
→ Large-scale pattern moved by ½ period
Shift equivalent to source moved in angle by
→	Coarsly pixelized detector sufficient
for high angular resolution
(if fine grids with large separation used)
  ½ grid pitch
grid separation

---
Number of grid pairs determines allowable source complexity
Slightly different angles on grids generates Moire pattern
→ orientation of Fourier component and Moire pattern decoupled
Grid
Pitch 666 / 690 μm
Angle 60° / 64°
Vertically impinging x-rays
→ Large scale Moire pattern period 10 mm
CdTe
sensor
Pixel count rate differences encode source direction

---
Imaging in STIX
32 Tungsten grid-pairs
Pitch 38 μm – 1 mm
400 μm thick
30 Fourier components in three directions
2 special counters
32 CdTe semiconductor sensors
10x10x1 mm3
Sensors from Acrorad (Japan)
Pattering and testing at PSI, Switzerland
32 Caliste-SO hybrids
ASIC, voltage filtering and bias routing
ASIC and hybrid developed at CEA Saclay, France

---
Beryllium X-ray windows
Rear window
1 mm thick
Al-SiOx coating
Redundant against failure of
one window (e.g. micrometerorite)
Mass 360 g (without feedthrough)
Temperatures at perihelion
• 300°C front
• 180°C rear
Central hole for
aspect system
Space-craft
feed-through
Front window
2 mm thick
Courtesy

---
Imager
Read grid
+ aspect apertures + diodes
Tube supports front and
rear grid assembly
Prevents twisting of grids
Mass ~1.6 kg
Aspect system to establish
line of sight
Front grid
+ aspect lens
Diode and temperature
sensor read-out
Stiffener
plate

---
400 μm thick Tungsten grids
32 subcollimators
Pitch 38 μm to 1 mm
Mounting & alignment apertures
Produced from etched and
stacked Tungsten foils
Front grid copper dummy

---
Aspect system
Lens in front grid casts
solar image on rear grid
Linear photodiodes illuminated
through holes in rear grid
Step-wise change in diode signal
when solar limb crosses hole
Signal decrease due to diode aging
not signficant for limb detection
3 points define solar disk
4th point for redundancy/error determination
Imager line-of-sight determined to 4 arcsec
→ X-ray images can be accurately placed on Sun
55 cm

---
Detector Electronics Module (DEM)
PCB and cold plate
transparent to show
50 cm cables behind
Data
processing
unit
Cold element
interface
Cold unit -20°C
with multi-layer
thermal insulation
Case +50°C
Caliste-SO
CdTe bonded to top
Ba-133 calibration
sources above
Mechanical
attenuator
20 cm

---
CdTe semiconductor sensors
X-ray absorption
Guard ring
1 mm thick CdTe
Pixilized Au-Ti-Al Schottky electrode
(connected to ASIC inputs)
X-rays
Monolithic Platinum Electrode
(-300 V)
Pair creation energy	4.43 eV (870 pairs at 4 keV)
Leakage current (large pixel)	<60 pA (-20ºC, 300 V)
Charge absorption length	10 cm / 0.6 cm (electron/hole)
Non-ionizing dose (NIEL) will degrade charge collection over mission duration
Total ionizing dose of 30 krad otherwise not severe
10 mm

---
Caliste-SO read-out hybrid / ASIC
Caliste-SO hybrid contains	CdTe bonded to top
IDeF-X HD ASIC
bias routing, filtering
ASIC	32 charge-sensitive amplifiers, ENC ~80 e-
multiplexed readout (~6.6 μs per hit @ 20 MHz clock)
~1 mW/active channel
Americium-241 spectrum
Resolution FWHM < 1.2 keV @ 14 keV
1 cm

---
Thermal simulation
Temperatures (hot operational case)
ESATAN model
Test unit
Model predicts heat flux to cold element of 2.5 W
→ above current space-craft allocation
→ under study with a bread board

---
Simplified STIX block diagram
Detector Front-End
Instrument Data
Processing Unit
Quarter 1
Caliste-SO
(4 groups à 2 each)
Buffers, filtering
Temperature sensor
-20°C
4 ADCs
4 diff./single-ended converters
Voltage regulator
Test pulse generator
Filtering	+50°C
Low-voltage
supplies*
House keeping*
FPGA*
Q 2
Bias voltage 1
max. 1 kV
Q 3
Bias voltage 2
max. 1 kV
Q 4
*Replicated in cold redundancy
Imager
Temperature sensors
Aspect system ADCs
50 cm
SpaceWire
Main + Red.
28 V from
spacecraft

---
Instrument Data Processing Unit
Event rates up to 105 s-1 during strong Solar flares (all Caliste simultaneously)
Autonomous operation up to 80 days
Several month of science data can be stored on-board
→ provides telemetry flexibility by allowing off line data selection and downlinking

---
Outlook
STIX currently in realization phase C
ESA critical design review in 2013
Industrial prime contractor will oversee instrument construction in phase D
Flight instrument delivery to ESA January 2015
Launch January 2017

---
Extra slides

---
In-flight energy calibration
ADC count to x-ray energy has to be established over 10-year mission duration
CdTe charge collection degrades due to displacement damage from protons
Changing leakage current will alter response of ASIC
ASIC gain / offset have small dependence on temperature
Requirements on calibration
Steep spectra	→	100 eVrms precision for each pixel
Low background	→	Source strength must be low
Technical realization
Barium-133 (t½=10.5 years)
Ø1 mm dots (<1 Bq activity)
wedged between plastic foils
Mounted on support of
multilayer insulation

---
Barium-133 spectrum
ASIC channel number
31 keV
Small pixel
Large pixels
Cd/Te
escape
peaks
35 keV
81 keV
53.1 keV
Bias 300 V, temperature -20ºC

---
Radiation damage of CdTe
Before irradiation
20°C, 300 V
After irradiation
20°C, 300 V
After irradiation
-20°C, 500 V
200 MeV protons
Fluence 3.6·1010 p/cm2
approx. 1.4 krad
STIX worst-case ~20 krad
Duration 10 hours
133Ba spectra