## Slide 1
ESS Target Options
ESS Target Division
Pb/Bi loop target for EURISOL
May 10th 2012, CERN

## Slide 2: Outline
ESS general project status
Target concept selection
ESS TSDU project
Baseline tungsten target
Comparative LBE target

## Slide 3: Discovery of neutrons

p
neutrons

## Slide 4: Neutrons 80 yrs ON
Materials science Bio-technology Nano science
Energy Technology Hardware for IT Engineering science
Neutrons can provide unique information on almost all materials.
Information on both structure and dynamics simultaneously. ”Where are the atoms and how do they behave?”
5000 users in Europe today.
- Science with neutrons is limited by the performance of today’s neutron sources. ESS performance will open new frontiers.

## Slide 5: Motivation for ESS
Many research reactors in Europe are aging and will be closed before 2020:
  Up to 90% of the use is with cold neutrons
There is an urgent need for a new high flux cold neutron source in Europe:
  The vast majority of users will profit from a pulsed structure
  A large fraction of the users are fully satisfied by a long pulse source (approx 2 ms, 20 Hz)
  Existing short pulse sources (ISIS, JPARC and SNS) can supply the present and imminent future need of short pulse users
  Construction must start now for use in 2018-2019

## Slide 6: Motivation for ESS (2)
Berkeley 37-inch cyclotron
350 mCi
Ra-Be source
Chadwick
1930
1970
1980
1990
2000
2010
2020
105
1010
1015
1020
1
ISIS
Pulsed Sources
ZINP-P
ZINP-P/
KENS
WNR
IPNS
ILL
X-10
CP-2
Steady State Sources
HFBR
HFIR
NRU
MTR
NRX
CP-1
1940
1950
1960
Effective thermal neutron flux n/cm2-s
(Updated from Neutron Scattering, K. Skold and D. L. Price, eds., Academic Press, 1986)
Evolution of the performance of neutron sources
FRM-II
SINQ
SNS
ESS
J-PARC

## Slide 7: Motivation for long pulse
ESS
SNS

## Slide 8: Lund: host site for ESS
Neutrons and SR at the same site
  MAX-IV and ESS
A World-leading cluster of science facilities
  XFEL, ESS, PETRA and MAX-IV
Excellent Communications
  33 minutes to airport
  125 direct destinations
  A cross-roads for 10 European countries
Intellectual capital
  10,000 scientists - 140,000 students
  3rd biopole in Europe
  Lund University 3rd largest attractor of EU R&D funds
  IDEON - MEDICON Village

## Slide 9
Sweden, Denmark and Norway
50% of construction costs
ESS partner countries
17 Partners
today

## Slide 10: ESS partner institutes
Map of possible partner labs. Under construction!
  Collaboration partners for work-packages and in-kind contributions:
  Instruments and use: Networks involving ILL, RAL, FRMII, HMI, FZJ, CTH, UU, LU LLB, …
  Target: PSI, FZJ, KTH, CERN, IDOM, KIT, CEA …
  Accelerator: CEA/IN2P3, INFN, UU, Århus U, TEKNIKER, CERN, ….
  Systems Integration, Project management, Safety, Data handling, Construction : ESS central team

## Slide 11: ESS baseline parameters
Proton beam
2.5 GeV proton linac
2 mA average beam current
2.86 ms pulse length
14 Hz rep. frequency
Target options:
Baseline: Solid Tungsten (or W alloy)
Comparative: Molten LBE

## Slide 12: ESS main elements
Proton linac (~400 M€) - Cavities, cryomodules - High power RF - Cryogenics, vaccuum, cooling - Shielding
Target station (~200 M€) - Nuclear tech/safety systems - Hot cell / remote handling - Cooling & Cryogenics - Shielding – Steel & Concrete
Instruments (~250 M€) - Shielding - Detectors - Neutron guides, choppers - Electronics - …
Conventional facilities (~400 M€) - Buildings – labs & offices - Cooling, heating, electric systems (energy) - Computers & Controls

## Slide 13: ESS Project Timeline

## Slide 14: Accelerator - progress
Accelerator Design Update is launched – kick off meeting in Lund 24/3
WP1 Management - ESS AB work funded & started
WP2 Accelerator Science - ESS AB work funded & started
WP3 Infrastructure - TEKNIKER – contract signed, but made void since funding was not yet received
WP4 & WP5 Elliptical & Spokes - CEA, CNRS contracts signed, work started
WP6 Front end - INFN – contract agreed, awaiting signature and funding in weeks, work started
WP7 HEBT & Magnets - Aarhus University – contracts signed and funding is there, work started
WP8 RF - Uppsala University – Contract agreed – only about 1 M€ missing for complete funding
Important to secure funding so contracts can be signed, not to loose coherence.

## Slide 15: Conventional facilities - progress
Project plan, organisation, contract forms
Refined site layout with zones for buildings and activity types
Takes elaborated requests from science directorate into account

## Slide 16: Licensing - progress
General Safety Objectives
PSAR – work is ongoing, focusing on Target Design Concepts
EIA – work is ongoing
Safety Advisory Committee set up
  Required by authorities
  Foreign and domestic experts. Some cross membership with TAC.
The required licenses are foreseen to be available by early 2013, with a slight reservation for the time needed by the Environmental Court. Risks are mitigated by Swedish government permissibility right.

## Slide 17: Staff numbers – pre-construction phase
Chart: 
| 2010 In | 2010 Average | 2010 Out/2011 In | 2011 Average | 2011 Out/2012 In | 2012 Average | 2012 Out
Staff numbers | 35 | 45 | 70 | 90 | 110 | 120 | 125

## Slide 18: Target concept – decision process
Target Station Concept Selection Completed end 2010 as a European collaboration
Target baseline and fallback internal decision May 16, 2011 ESS Lund ( CCB & EPG)
Workshop to discuss decision Lund May 31st, 2011 Collaboration on Target
Review by Technical Advisory Committee July 11-12 TAC
Endorsement by Steering Committee October 2011 STC

## Slide 19: Target Station Design Update Project
The TSDU project aims at integrating most recent worldwide knowledge, experience and state-of-the-art technology into an updated target design for ESS. Its main goals are:
  Providing information needed for the environmental licensing of the ESS Target Station on two design options.
  Producing a Technical Design Report for the ESS Target Station by end 2012.

## Slide 20: TSDU Work Packages
  WP1: Project Management, Coordination of Global Design Effort and overall system integration
  WP2: Target Performance Modelling and Optimisation
  WP3: Material Properties
  WP4: The RoTHeTa Concept – Replaceable systems
  WP5: The RoTHeTa Concept – Permanent systems
  WP6: Liquid Metal Target
  WP7: Premoderator, Moderator and Reflector Engineering Design
  WP8: Shielded Target Monolith System and Beam Extraction
  WP9: Infrastructure Services and Utilities
  WP10: Hot cell, Handling of used Targets, Moderators, Reflectors outside Target Shielding Monolith – Beam dumps
  WP11: Waste Disposal, Emissions, Dismantling and Decommissioning
  WP12: Control Systems for Target Station

## Slide 21: Some Recent ESS Documentation
 | Date issued/due | Completed? | LBE?
Evaluation of ESS safety relevant concerns assuming two basic target concepts for the target station | September 2011 | Yes | Yes
Target Station Design Update Baseline | December 2011 | Yes | No
Project specification for the ESS Target Station Design Update Project | February 2012 | Yes | Yes
TAC4 documentation | February 2012 | Yes | No
ESS Conceptual Design Report | February 2012 | Yes | Yes
ESS Technical Design Report | December 2012 | No | Yes

## Slide 22: The RoTHeTa Concept
  ø2.5m
  33 sectors
  Tungsten vertical plates with cooling channels in between

## Slide 23: RoTHeTa Wheel Velocity
33 slices in total
Beam repetition rate is 14Hz
Angular velocity should be 0.42Hz, 25.45rpm
Each section sees on average 1/33 of the beam.

## Slide 24: RoTHeTa Flow Pattern
S-channel: Lower W max. temperature

## Slide 25: RoTHeTa Helium Loop

## Slide 26: RoTHeTa Helium Loop Parameters

## Slide 27: Target Station For a Rotating Target

## Slide 28: Total activity: W vs LBE
D. Ene

## Slide 29: Hazard index for different options
Most active isotopes at shutdown
D. Ene

## Slide 30: LBE META:LIC Layout
pump module
heat exchanger module
target module
pool
A. Class

## Slide 31: Pressure pulse issue
J. Wolters

## Slide 32: Pressure pulse problem
t = 40 µs
t = 15 µs
t = 60 µs
t = 85 µs
Pressure [MPa]
J. Wolters

## Slide 33: Effect of pulse ramp
J. Wolters

## Slide 34: Time dependent stresses in container
To avoid accumulation of stresses for transient events like a beam trip, an additional spillway can be used. Dimensioning and demonstration of the effectiveness is one of the next tasks.
after first pulse
prior to second pulse
after second pulse
J. Wolters

## Slide 35: Bypass to diffuse stresses
J. Wolters
additional spillway
(bypass)

## Slide 36: Dealing with beam trips I/II
Water hammer beam trip on → off
time for the cavitation bubble to be neutralized at the free surfaces: approx. 2 pulses
A. Class

## Slide 37: Dealing with beam trips II/II
Modified design to account for LBE expansion:
  expansion volume
  2 internal free surfaces
„expansion volume“
„spoiler for forced detachment“
A. Class

## Slide 38: Free surfaces
Internal free surfaces at t = 1.75 s
A. Class

## Slide 39: Velocity distribution
Velocity distribution at t= 1. 76s
Velocities at t = 1.76 s
A. Class

## Slide 40: Pressure distribution
Pressures at t = 1.76 s
A. Class

## Slide 41: META:LIC Test Stand at IPUL
1-Module of Target body;
2-PbBi loop (diameter 108 x 4.0; SS316L);
3-Channel of EMP;
4-Valve;
5-Venturi tube;
6-Electromagnetic Q-meter
Operating parameters:
Temperature, 0C up to 400;
Flowrate, L/S up to 11;
Pressure, bars 4
Expansion tank, supply vessel, heaters etc. are not showed
E. Platacis

## Slide 42: Instrumentation
Differential pressure across circular to rectangluar transition
temperature ahead & after pump
Temperature >3 ahead of the test section
CIFT inflow channel?
bulk velocity
  EHM
  Venturi

## Slide 43: LBE ESS TDR Contributions
Introduction (C. Fazio)
Design requirements and configuration selection (A. Class, U. Fischer)
Neutronic design (U. Fischer)
Engineering design (A. Class with input from FZJ J. Wolters)
Instrumentation of liquid metal flow (S. Eckert, F. Stefani and K. Thomsen PSI)
Trolley design and interface to monolith (J. Fetzer, A. Class)
Needed ancillary systems (K. Thomsen – include here experience from MEGAPIE)
Target module validation (E. Platacis, A. Class with input from all involved partners in the experiment)
Corrosion and erosion properties of structural steels in contact with liquid metal coolant (A. Weisenburger)
Potential needs for licensing, dismantling and final disposal (K. Thomsen PSI taken from the MEGAPIE experience – calculation of spallation products is done by Dana (ESS))

## Slide 44
Thank you for your attention!