## Slide 1: CERN targetry activities
A non-exhaustive review

## Slide 2: Outline
CNGS
  Development, Design tools, Manufacturing, Installation, Operation
nTof
  Target history, Design tools, New cooling and moderator circuits, Operation
ISOLDE
  Target concepts and strengths, Installation & Operation, Storage
  Static molten Pb/Bi bath
Molten metal target activities
  MERIT free Hg jet target
  Offline molten Pb loop

## Slide 3: CNGS
Development
Design tools
Manufacturing
Installation
Operation
Thanks to R. Losito, D. Grenier

## Slide 4: CNGS
Design development
  Target rod: C (2020PT), SC24 & CC Aerolor A035
  Vacuum / 0.5bar He
  4.3kW avg / 750kW peak
  Dedicated Target WG
  Collaborations with several institutes
  Development 2001-2006

## Slide 5: CNGS
Design tools
  Monte-Carlo analysis (FLUKA)
  Modal and dynamic analyses (Spectral Element Method and explicit FEM)
  Thermo-structural analyses (implicit FEM)

## Slide 6: CNGS
In-house manufacturing and assembly

## Slide 7: CNGS
Alignment
Motorization and Rotation precision

## Slide 8: CNGS
Installation in TT40

## Slide 9: CNGS
Operation
  1st run 2007 – today
  Issues in rotating the target (ball bearing corrosion @ 450 MGray)
  Estimated production of H inside the target inert atmosphere
  Spare target modification ongoing to substitute the target in case of problems

## Slide 10: nTof
Target history
Design tools
New cooling and moderator circuits
Operation
Thanks to M. Calviani

## Slide 11: nTof
Target history
  1st run 2000-2004
  Inspection 2007/08
  Update and restart (2nd run) in 2008
  Power: 6.5kW avg / 22kW max avg

## Slide 12: nTof
Design tools:
  External collaboration
  Monte Carlo (Fluka) analyses
  CFD analysis of cooling circuit
  Elastic wave propagation in Pb core (Explicit FEM)

## Slide 13: nTof
Design tools:
  Neutron fluence (FLUKA)
  RP studies (FLUKA)
http://pceet075.cern.ch/Meetings/TB2006/index.html
https://edms.cern.ch/cedar/plsql/project.info?cookie=10315092&proj_id=1064549944&p_tab=TAB3
Non-borated water

## Slide 14: nTof
Design tools:
  Beam window modal analysis and fatigue life assessment (FEM)
  CFD analysis of the moderator circuit

## Slide 15: nTof
  New cooling circuit:
  Water flow ~5-6 m3/h (0.5 m3/h at proton face)
New (separated) moderator circuit:
  B-water, reduction of in-beam g-rays & thermal fluence
https://ntofdaq.cern.ch/Cooling.php
Cooling circuit
Moderator circuit

## Slide 16: nTof
Operation
  Monitoring O2 content, pH and conductivity (both circuits)
  Degassing device via N2 flush in cooling circuit
  Moderator circuit with saturated 10B-water (~90 litres) at 20 °C
  ~constant boron concentration
https://ntofdaq.cern.ch/Cooling.php
x18
~x10
https://edms.cern.ch/document/1105710/6

## Slide 17: ISOLDE
Target concepts and strengths
Solid target
Installation & operation
Storage
Static molten Pb/Bi bath
Thanks to T. Stora

## Slide 18: ISOLDE
Established Solid target concept
  UCx but also CeO, SiC, Sn, Pb, Ta, Ti, MgO
  Also used Al2O3 , Y2O3 , hBN, ZrO2 , …
  Power: 3kW avg/10 GW peak
Strengths
  Remote handling and monitoring
  Well Defined beam-time schedule
  Target unit tracking system
  In-house target unit production and assembly (few weeks)
  PIE (@ PSI) and ALARA

## Slide 19: ISOLDE
Proven solid target design
  Concept in use since the late 60’s
1967

## Slide 20: ISOLDE
Operation
  Transfer to target station : trained operators
  Operation for 3 days- 4 weeks on target station
  Recuperation and short-term storage in primary area
https://ab-dep-op-elogbook.web.cern.ch/ab-dep-op-elogbook/elogbook/eLogbook.php?shiftId=1039819

## Slide 21: ISOLDE
Storage
  Recuperation and short-term storage in primary area
  Intermediate storage at CERN (DIMR/ALARA procedure )
  Dismantling/shipping to PSI
https://edms.cern.ch/file/857363/1/ISL-T-ES-003-00-10.pdf

## Slide 22: ISOLDE
Proven design of the static Pb/Bi molten bath
  High purity Pb(44.5%) / Bi(55.5%) eutectic alloy, used in 2004/05
  Molten Pb used for 1 week/year
Notes: Correlation between the thermal shock and release of radioisotopes

## Slide 23: ISOLDE
Proven design of the static Pb/Bi molten bath
  Thermal shock enhance the release of radioisotopes
  Thermal shock weaken the target container (pitting corrosion on window)
Exemple_movie
Notes: Correlation between the thermal shock and release of radioisotopes

## Slide 24: Molten metal target activities
MERIT free Hg jet target
Offline molten Pb loop
Thanks to T. Stora, E. Noah

## Slide 25: Molten metal target activities
MERIT free Hg jet target
  International collaboration
  2001/02 small-scale validating experiments
  2007 experiment with full-scale target in TT2A gallery (nTof)
  14 and 24 GeV. 1cm-dia, 20m/s Hg jet
  Proof of principle of Hg jet in 0-15T solenoid field

## Slide 26: Molten metal target activities
Offline molten Pb loop
  600 °C pressurized Pb droplets trough diffusion chamber (DC)
  Tests at IPUL during EURISOL Design Study by E. Noah (CERN-ISOLDE)
  Proof of principle for the feasibility of film/droplets and operation of the loop

## Slide 27: Thank You
C. Maglioni, CERN EN-STI-TCD

## Slide 28: Spare slides
NA
  4 targets (T2,T4,T6,T10) built in the 70s & running since then – consolidation in LS1
  Forced air cooled 2mm-thickness Be plates
  Forced air cooled 2mm-dia Be rods
AD
  Same configuration as from the 80’s
  8-100W avg power on target
T2, T4, T6
  https://edms.cern.ch/document/1146356/
AD pbar production target
T10