## Slide 1: MINING FOR WIMPS: THE LUX-ZEPLIN (LZ) EXPERIMENT
Henrique Araújo
Imperial College London
On behalf of the LZ Collaboration
TIPP 2014, Amsterdam, The Netherlands, 2-6 June 2014

## Slide 2: HOW TO CATCH A WIMP
Direct detection (scattering XS)
  Nuclear (atomic) recoils from elastic scattering
  (annual modulation, directionality, A- & J-dependence)
  Galactic DM at the Sun’s position – our DM!
  Mass measurement (if not too heavy)
Indirect detection (decay, annihilation XS)
  High-energy cosmic-rays, g-rays, neutrinos, etc.
  Over-dense regions, annihilation signal  n2
  Challenging backgrounds
Accelerator searches (production XS)
  Missing transverse energy, monojets, etc.
  Good place to look for particles…
  Mass measurement poor, at least initially
  Can it establish that new particle is the DM?

## Slide 3: WIMP-NUCLEUS ELASTIC SCATTERING RATES
The ‘spherical cow’ galactic model
DM halo is 3-dimensional, stationary, with no lumps
Isothermal sphere with density profile r ∝ r −2
Local density r0 ~ 0.3 GeV/cm3 (~1/pint for 100 GeV WIMPs)
Maxwellian (truncated) velocity distribution, f(v)
  Characteristic velocity v0=220 km/s
  Escape velocity vesc=544 km/s
  Earth velocity vE=230 km/s
~ few keV
Nuclear recoil spectrum [events/kg/day/keV]

## Slide 4: TWO-PHASE XENON TPC
S1: prompt scintillation signal
  Light yield: ~60 ph/keV (ER, 0 field)
  Scintillation light: 178 nm (VUV)
  Nuclear recoil threshold ~5 keV
S2: delayed ionisation signal
  Electroluminescence in vapour phase
  Sensitive to single ionisation electrons
  Nuclear recoil threshold ~1 keV
S1+S2 event by event
  ER/NR discrimination (>99.5% rejection)
  mm vertex resolution + high density: self-shielding of external backgrounds
LXe is the leading WIMP target:
  Scalar WIMP-nucleon scattering rate dR/dE~A2, broad mass coverage (>5 GeV)
  Odd-neutron isotopes (129Xe, 131Xe) enable SD sensitivity; target exchange possible
  No damaging intrinsic nasties (127Xe short-lived, 85Kr removable, 136Xe 2nbb ok)

## Slide 5
Searches for RARE and LOW ENERGY events: a very challenging combination
THE NOBLE LIQUID XENON
single scatters
<5 keVee

## Slide 6: ZEPLIN  LUX  LZ
Next-generation LXe experiment
building on LUX & ZEPLIN programmes
Route to detection & study: a progressive programme
  ZEPLIN pioneered two-phase Xe for WIMP searches (3.9x10-8 pb/n)
  LUX is present world leader in sensitivity (7.6x10-10 pb/n, and ongoing)
  LZ expected sensitivity: ~2x10-12 pb/n with 3-year run
Experimental approach: a low risk but aggressive programme
  Internal bk-free strategy (self-shielding, modest discrimination assumed)
  Two-phase Xe technology: high readiness level
  Some infrastructure inherited from LUX
LZ will provide exciting physics opportunities for light & heavy WIMPs (GeV-TeV): since we do not know what BSM physics looks like!
6
6 kg LXe fid 100 kg 6,000 kg
ZEPLIN-III LUX LZ

## Slide 7: LZ DETECTOR(S)
LUX
water tank
HV umbilical
Gd-loaded
liquid scintillator
veto detector
low-bk cryostat
LXe ‘skin’
detector
LXe HX
LXe TPC

## Slide 8
The 8-m diameter LUX water tank (to contain LZ), Davis Campus, 4850-ft u/g level,
Sanford Underground Research Facility

## Slide 9: THE LZ TPC
TPC PARAMETERS
  1.5 m diameter/length (3x LUX)
  7 tonne active LXe mass (28x LUX)
  2x 241 3-inch PMTs (4x LUX)
  Highly reflective PTFE field cage
  100 kV cathode HV (10x LUX)
  Electron lifetime 3 ms (3x LUX)
PHYSICS PARAMETERS
5.8 keVr S1 threshold (4.5 keVr LUX)
0.7 kV/cm drift field, 99.5% ER/NR disc.
(already surpassed in LUX at 0.2 kV/cm)
TPC CALIBRATION
ER: Dispersed sources: Kr-83m, CH3T
NR: AmBe, YBe, D-D generator

## Slide 10: LZ IN DAVIS CAMPUS

## Slide 11: IMPORTANT BACKGROUNDS
Neutrons and gamma-rays from internal radioactivity
  Die out very quickly into xenon target, leaving ~6-tonne fiducial
  Layered, near-hermetic detector strategy plus self-shielding and accurate 3D position reconstruction are extremely effective
PMTs +
Cryostat
PMTs +
Cryostat

## Slide 12: INTRINSIC BACKGROUNDS
Intrinsic electron backgrounds
  Controlled with modest discrimination (99.5%) – already achieved in LUX
    85Kr: require <0.02 ppt Kr (best LUX production batch ~0.2 ppt)
    214Pb: require <0.6 mBq radon in active volume (cf. ~mBq in Borexino, SNO)
    2nbb from 136Xe dominates only >20 keVee (signal acceptance <6 keVee)

## Slide 13: DOMINANT BACKGROUNDS
Solar pp n-e elastic scattering is dominant e-recoil background
  1.5 events in 1,000 live days x 6,000 kg (99.5% discrimination, 50% acceptance)
CNS is dominant nuclear recoil background
  8B solar neutrinos: significant number of events, but ~0 above 6 keVr threshold
  Small background from atmospheric and diffuse supernova neutrinos
  0.26 events in 1,000 live days x 6,000 kg (50% acceptance)
8B
DSNB
Atm
hep
Strigari 2009
D. Malling, Brown

## Slide 14: LZ SENSITIVITY
Snowmass Community Summer Study 2013 CF1: WIMP Dark Matter Detection

## Slide 15: PROGRAMME STATUS
Conceptual design nearly completed
Construction from 2015/16
Operation from 2018
DOE/NSF experiment down-selection imminent in US
Substantial support from South Dakota Science & Technology Authority
Endorsed by DMUK consortium in the UK

## Slide 16: LZ COLLABORATION
University of Alabama
Brown University
University of California, Berkeley
University of California, Davis
University of California, Santa Barbara
Case Western Reserve University
Daresbury Laboratory
Edinburgh University
Imperial College London
MEPHI-Moscow, Russia
Lawrence Berkeley National Laboratory
Lawrence Livermore National Laboratory
LIP-Coimbra, Portugal
University of Maryland
University of Oxford
Rutherford Appleton Laboratory
University of Rochester
Sheffield University
SLAC National Accelerator Laboratory
SD School of Mines & Technology
University of South Dakota
Texas A&M University
University College London
Washington University
University of Wisconsin
Yale University
US (17) + UK (7) + PT (1) + RU (1)