## Slide 1: First Years of Running for the LHCb Calorimeter System
Pascal Perret
LPC Clermont
On behalf LHCb Collaboration
2 June 2014

## Slide 2: The LHCb detector
A single-arm forward spectrometer:
  Covers ~4% of the solid angle, but captures ~30% of the heavy quark production cross-section
  Precision measurements in beauty and charm sectors
LHCb region
2 < η < 5
ATLAS & CMS
region |η| < 2.5
~20m
~10m
10 – 250 mrad
10 – 300 mrad

## Slide 3: The LHCb detector

## Slide 4: The LHCb detector
TT
Si
Muon
MWPCGEM
HCAL
ECAL
RICH2
Outer Tracker straw Tubes
Magnet
RICH1
VELO&PU
Si
Inner Tracker
Si
p
p
[The LHCb Detector at the LHC, JINST 3 (2008) S08005]
PS+SPD

## Slide 5: The LHCb calorimeters
PS
SPD
ECAL
HCAL
Inner Outer Middle
region
ECAL (inner modules): σ(E)/E ~ 8.2% /√E + 0.9%
[JINST 3 (2008) S08005,
LHCb calorimeters", TDR, CERN/LHCC/2000-0036 LHCb TDR 2]
Calorimeter system :
L0 trigger on high ET e / γ / π0 and hadron
Precise energy measurement of e and γ
Particle Identification: e / γ / h (contributes to µ PID)

## Slide 6: LHCb trigger
  Level-0 trigger: hardware
    4 μs latency @ 40MHz
    “Moderate” ET/pT threshold:
      Typically
        ET(e/γ)>2.7 GeV
        ET(h)>3.6 GeV
        pT(μ)>1.4 GeV/c
  HLT trigger: software
    ~30000 tasks in parallel on ~1500 nodes
  Storage rate: 5 kHz
  Combined efficiency (L0+HLT):
    ~90 % for di-muon channels
    ~30 % for multi-body hadronic final states

## Slide 7: LHCb operation
2012 | 8 TeV | 2.1 fb-1
2011 | 7 TeV | 1.1 fb-1
2010 | 7 TeV | 0.038 fb-1
2010
2011
2012
Semi-continuous (automatic) adjustment of offset of colliding beams allows luminosity to be levelled
4x1032cm-2s-1
Design:
2x1032cm-2s-1
High Efficiency!
LHC
Detectors all with >~99% active channels
(operation)>94%
~98% are good data!
    4 times more collisions per crossing than in the design!!!
15 h!

## Slide 8: LHCb Calorimeter System
  40 MHz trigger on energetic e, π0, γ, h
  Distance to i.p. ~13 m
  Solid angle coverage 300x250 mrad
  Four sub-detectors: SPD,PS,ECAL,HCAL
    Independently retractable halves
  Granularity:
    SPD, PS, ECAL:
      6016 cells: 3 zones 4x4; 6x6 and 12x12 cm2
    HCAL: 1488 cells: 13x13 and 26x26 cm2
Y~7m
X~8.5m
Z~2.7m
HCAL
ECAL
PS/SPD
120 mm
40
60 mm

## Slide 9: LHCb Calorimeter System
Y~7m
X~8.5m
Z~2.7m
HCAL
ECAL
PS/SPD
120 mm
40
60 mm
HCAL
ECAL
PS/SPD
  40 MHz trigger on energetic e, π0, γ, h
  Distance to i.p. ~13 m
  Solid angle coverage 300x250 mrad
  Four sub-detectors: SPD,PS,ECAL,HCAL
    Independently retractable halves
  Granularity:
    SPD, PS, ECAL:
      6016 cells: 3 zones 4x4; 6x6 and 12x12 cm2
    HCAL: 1488 cells: 13x13 and 26x26 cm2

## Slide 10: LHCb Calorimeter System
HCAL
ECAL
PS/SPD
  40 MHz trigger on energetic e, π0, γ, h
  Distance to i.p. ~13 m
  Solid angle coverage 300x250 mrad
  Four sub-detectors: SPD,PS,ECAL,HCAL
    Independently retractable halves
  Granularity:
    SPD, PS, ECAL:
      6016 cells: 3 zones 4x4; 6x6 and 12x12 cm2
    HCAL: 1488 cells: 13x13 and 26x26 cm2
  Detection
    Sandwich of scintillator/lead (iron for HCAL)
    WLS fibres are used to collect the light read out thanks to photomultipliers (PMT)
      Multianode PMT (64) for SPD & PS
    Cost effective

## Slide 11: SPD (Scintillator Pad Detector) and PS (Preshower)
8 m
4 m
    Scintillator Pad – 2.5X0 lead – Scintillator Pad
      15/15/15 mm thick;
      WLS fibres are used to collect the light
      Signal read by 64-channel MAPMT
      Average light yield: ~20 p.e/MIP
      PS: 10 bits – dynamic range: 0.1-100 MIPs
      SPD: 1 bit

## Slide 12: ECAL
Inner
Module 9 cells: 4x4 cm2
Middle
Module 4 cells: 6x6 cm2
Outer
Module 1 cell: 12x12 cm2
3312 shashlik modules with 25 X0 Pb
  Electromagnetic Calorimeter (ECAL):
    66 layers of 2mm Pb/ 4mm scintillator
    Light collected through WLS fibres bunch
      Moliere radius: 3.5 cm
      Longitudinal size: 25X0, 1.1 I,
      Average light yield: ~3000 p.e/GeV
      Dynamic range: 10 ÷ 12 GeV of transverse energy (E(max, GeV)=7 + 10 /sin(θ))
      Energy resolution (beam tests)
      σ(E)/E = (8 ÷ 10)% /√E  0.9%

## Slide 13: HCAL
52 modules with longitudinal tiles
  Hadronic Calorimeter (HCAL):
    26x2 horizontal modules
      The same design as in ATLAS TileCal
      interleaving Sc tiles and iron plates parallel to the beam axis. Volume ratio Fe:Sc = 5.58:1
      Longitudinal size: 5.6 I
        Mostly used as a trigger device!
      Average light yield: ~105 p.e/GeV
      Dynamic range: 15 GeV of ET (now 30 GeV)
      Energy resolution (beam tests)
      σ(E)/E = (69  5)% /√E  (9  2)%
      moderate resolution is sufficient
6mm master, 4mm spacer / 3mm scintillator

## Slide 14: Calorimeter functionalities
    PS/SPD: PID for L0 electron and photon trigger
      electron, photon/pion separation by PS
      photon/MIP separation by SPD
      Charged multiplicity by SPD
    ECAL
      ET of electrons, photons and π0 for L0 trigger (Bd → K* ee, B0 → K* , )
      Reconstruction of π0 and prompt γ offline (+ PS)
      Particle ID (+ PS)
    HCAL: ET of hadrons, ET for L0 trigger
      ~ 500 kHz (out of ~1 MHz)
SPD/PS/ECAL/HCAL in coincidence
SPD | PS | ECAL | HCAL | 
1 | 1 | 1 | 0 | e
0 | 1 | 1 | 0 | 
1 | 0 | 0 | 1 | h
1 | 0 | 0 | 0 | µ

## Slide 15: Calibration
  SPD: [LHCb-PUB-2011-024]
  Threshold set at ~0.5 MIP
  Binary detector: no straight MIP calibration
    Tracks pointing to given cell are extrapolated
    Collect data at different thresholds and get efficiency to MIP by comparing with theoretical value
Theoretical efficiency
ε = Landau x Poisson
Energy loss
Fluctuations of nphe at photocathode.
~95% efficient for MIPs
SPD efficiency as a function of threshold
    Provide a resolution in the MIP position smaller than 5%

## Slide 16: Calibration
PS
  MIP signal set at ~10 ADC count (10 bits – dynamic range: 0.1-100 MIPs)
    Use any reconstructed track which extrapolation hits the Preshower
    MIP signal is fitted (LandauGauss to account for photostatistics resolution) and fixed to a given number of ADC counts
      ~5% precision level
µ: 10.58 ± 0.03
σ: 0.93 ± 0.02
µ: 10.41 ± 0.03
σ: 0.90 ± 0.02
µ: 10.87 ± 0.03
σ: 0.83 ± 0.02
OUTER
MIDDLE
INNER
2011 data Preliminary

## Slide 17: Calibration
ECAL: fine absolute calibration using reconstructed p0 peak
  Iterative procedure by p0 mass peak fitting
    Find the coefficient which would move the measured mass closer to the p0 nominal one:  = Mnom/Mmeas = 135 MeV / Mmeas
    Repeat for each cell (6096)
    Iterate until stable: 5-6 iterations
  ~1-2% precision
    ~100M events needed
      ~200 pb-1 (~1month)
Absolute
calibration iterations
Initial calibration value
Final calibration value
2011 data (June)
Preliminary
0 selection cuts:
No SPD hit
pT()>300 MeV
EPS<10 MeV
(only ECAL calibration)
pT (0)>800 MeV

## Slide 18: Calibration
ECAL calibration with electrons
  Comparison of the electron momentum measured in the tracking system with its energy measured by the ECAL and PS
      Electrons from conversion selected with RichDllE and loose electron id.
    Used to monitor ageing with applying ageing trend corrections every 40 pb-1 (not enough statistics to apply p0 method).
E/p for electrons in ECAL
E/p for hadrons in ECAL
2011 data
E/p
HV corrections
Annealing
after one month

## Slide 19: Calibration
  Two ~ 10 mCi 137Cs source used:
    1 per each detector half
      Driven by hydraulic system
      Similar to the ATLAS TileCal one
  Each source propagates consecutively through 26 HCAL modules
    average velocity of about 20–40 cm/s.
    System of dedicated integrators measures PM anode currents every 5 ms
    Absolute normalization ~10%, dominated by the uncertainty in the source activity
    Cell to cell intercalibration better than 4%
    Calibration done regularly during Technical Stops
    LED monitoring system is used to control HCAL response during data taking.
HCAL calibration done with 137Cs source:
Radioactive source
2 dead cells

## Slide 20: Detector ageing
  Combination of several effects:
    Scintillator ageing due to radiations (~0.25 Mrad /year);
      Plastic tiles become less and less transparent
      Proportional to particule flux (neutral + charged)
    PMT ageing as a function of the integrated current (PMT dynode)
      Depends upon cell size and location (up to 100C)
  These are well known unavoidable effects …
    On the trigger rate, on detector performances, etc
L0Hadron/L0muon-dimuon trigger rate
L0electron/photon / L0muon-dimuon trigger rate
0 mass as a function of time (recorded luminosity)
Regular calibration!

## Slide 21: Calibration
Towards an automatic (online) calibration for RUN 2
  Based on LED and raw ocupancy
  The method is very promising: ~1% could be achieved
      A first look was done at 2012 collection for ECAL, HCAL and PS
    Adjust PMT HV on a fill basis
    Obtain a stable trigger
Precision reached with 1 hour data taking

## Slide 22: Performances: Electron PID
  Based on difference between likehood of the (electron) signal and background
    Fully based on data distributions
      Signal : electrons/positrons from g conversions
      Background : hadrons from D0  Kp
Mis_ID rate ~5%
for electron eff 90%
Combined Calo Delta Log –Likelihood
__ e from  → e+e-
__ hadrons from D0
Electron efficiency
misID rate (%)
Electron efficiency(%)
misID rate (%)
Momentum (GeV/c)
Momentum (GeV/c)
__  log > 1
__  log > 0
__  log > 2
__  log > 3
From B+ J/ K
+ RICH information:
Mis_ID rate <2%
for electron eff >97%

## Slide 23: Performances: 0 reconstruction
  Low energy 0 : resolved pair of g:  ~ 8 MeV/c2
  High energy 0 (pT > 2 GeV/c):
D0K+-0 (resolved 0)
D0K+-0 (merged 0)
=17.4 MeV/c2
=32.2 MeV/c2
Resolved pair of well separated photons
      Photons that cannot be resolved as a pair of clusters within ECAL granularity

## Slide 24: Performances: Radiative decays
  Theory
      Predictions for BR suffer from large uncertainties from hadronic form factors
        B0 → K*  = (4.31.4)x10-5 ; Bs →   = (4.31.4)x10-5
      Ratio of BR and direct CP asymmetries are better known
  LHCb measurements (1 fb-1) [NP B 867 (2012) 1]
  RBR = 1.23  0.06  0.04  0.10(fs/fd)
    Th: 1.0  0.2
  ACP(B0 → K* ) =
  (0.8  1.7  0.9)%
    Th: (-0.61  0.43)%
  WB measurements
N B0 → K*  = 5279  93
N Bs →   = 691  36
B0 → K* 
Bs →  
Invariant mass resolution: ~92 MeV/c2
BR(Bs →  ) = (3.5  0.4)x10-5
    No sizeable deviation from SM

## Slide 25: LHCb calorimeter upgrade
Running at ~2x1033cm-2s-1 (instead of 4x1032cm-2s-1) @ √s =14 TeV
  After LS2: ~2019
Full software trigger
  DAQ @ 40MHz
    Change in the readout electronics
  Lower PMT gain
    Higher luminosity
    Ageing
  New electronics under development : 5 times more gain
    See poster session
  PS and SPD shall be removed (mainly contribute to L0 trigger)
LHCb upgrade PID TDR: CERN/LHCC 2013-022
    LHCb Upgrade LoI: CERN-LHCC-2011-001
    LHCb Upgrade Framework TDR: CERN-LHCC-2012-007

## Slide 26: Summary & Conclusion
  The calorimeters are running smoothly!
    O(10-3) dead channels
  and performing well:
    Trigger capabilities: hadron, electron, photon
      Key role in the trigger system
    Energy resolution
      Important measurements achieved:
        b → s  (B0 → K* , Bs →  ), etc.
  Significant ageing (PMT, scintillators) … as expected
    Under control thanks to “frequent calibrations”
    New calibration procedure for RUN 2
      Automation of HV PMT adjustment procedures after each fill
  Calorimeter (LHCb) upgrade to run at L ~2x1033cm-2s-1 > 2020
  Many other LHCb talks & posters @ TIPP
    Trigger, VELO, RICH, SciFi, etc.

## Slide 27: Thank you!

## Slide 28: The LHCb detector
Excellent muon identication  = 97%, misid 2%
σ(E)/E ~ 70%/√E  10%
σ(E)/E ~ 10%/√E  1% σm~90 MeV for B0K*
σm~8 MeV for B+J/K+, 25 MeV for B µ+µ-
(k  k) 90% for (k  ) <10%
~20 µm IP resolution at PT > 2 GeV
p
p
Great Vertex Resolution! Primary/secondary separation, proper time resolution.
Excellent momentum and mass resolution.
Outstanding PID (K-π) and μ reconstruction.
Dedicated Trigger system for B and C!

## Slide 29: The readout system
192 ECAL FEB
54 HCAL FEB
12-bit ADC
100 PS/SPD FEB
10-bit ADC
40 MHz
1 MHz
1 MHz
40 MHz
40 MHz
40 MHz
32 channels
64 channels

## Slide 30: ECAL ageing
After calibration (preliminary, 2011 data):
103
April May June July August
2012

## Slide 31: HCAL ageing
Longitudinal dose in HCAL, cell closest to the beam
0 1 2 3 4 5
HCAL tile row
  137Cs source
    Allow to separate the light yield degradation from the PMT gain loss
    Radiation damage of tiles and fibers
The hadronic shower maximum lays ~ within the tile row 0; the dose in the row 5 is much less. Radiation damage of scintillator tiles and fibers can therefore manifest itself as a decrease of relative response of upstream rows (0, 1) with respect to row 5.

## Slide 32: HCAL ageing
    Radiation damage of tiles and fibers
      30-Aug vs 29-Mar (758 pb-1)
Further decrease in the centre
At low doses, it develops ~linearly in time
Row4/R5
Row0/R5
Row1/R5
Row2/R5
Row3/R5

## Slide 33: HCAL ageing
    PMT ageing
      The anode currents of the HCAL PMTs are continuously monitored with integrators of the source calibration system
      In 2011, at L=3.5∙1032/cm2/s, PMT anode current was significant, up to 35μA in the HCAL centre. The integrated anode currents are up to 100C
      x5 times more current than for ECAL
      In 2012, the PMT gain has been reduced by a factor 2 to reduce the ageing rate

## Slide 34: HCAL ageing
  HCAL HV corrections
    Results of Cs calibrations at TS is used as a starting point, then LED-based corrections
      Precision of corrections is limited by:
        annealing during TS (and faster ageing afterwards)
        A model to account for plastic ageing has been used >August 2012
          uncertainty in the “plastic ageing” prediction – non linearity, annealing
sum/sumref, 56 central cells
shutdown 137Cs calibration
TS1, 137Cs calibration
TS2, 137Cs calibration
TS3, 137Cs calibration
LED-based HV corrections (17)
Cs calibrations (3)

## Slide 35: Neutral clusters
Energy deposits in ECAL cells are clusterized applying a 3x3 cell pattern around local maxima
  Photon PID based on probability density functions
    Track – ECAL cluster anti-coincidence
    ECAL shower shape
    PS energy
  Neutral pions
    Mostly reconstructed as a resolved pair of well separated photons
      Mass resolution of ~8 MeV/c2 (low transverse energy 0 )
    For high energy 0 (pT > 2 GeV/c):
      A large fraction of the pairs of photons cannot be resolved as a pair of clusters within ECAL granularity: merged 0
        Specific procedure: consists in spliting each single Ecal clusters into two interleaved 3x3 subclusters built around the two highest deposits of the original cluster. Iterative procedure for the sharing of the energy of the common cells based on the expected transversal shape of photon showers.
      Mass resolution of ~20 MeV/c2

## Slide 36: LHCb upgrade
    2013: R&D, technology choices, preparation of sub-system TDRs
    2014: funding, procurements
    2015-2019: construction and installation

## Slide 37: Performance under irradiation
Assuming L=2x1032cm-2s-1, 107s/year
ECAL
  0.25 Mrad/year close to the beam pipe
    Fast variation with distance from beam pipe
      Middle & outer section: 0.02 Mrad/year
    The radiation affects a small part of ECAL
  Modules irradiated at LIL with ~10 rad/s for a total dose of 5 Mrad
    Scintillator and WLS fiber degradation (and annealing) effects studied
    Simulation used to estimate the degradation on resolution:
    Constant term degrades from 0.8% to 1.5% with 2.2 Mrad
TDR

## Slide 38: Performance under irradiation
Assuming L=2x1032cm-2s-1, 107s/year
HCAL
  50 krad/year close to the beam pipe
    Fast variation with distance from beam pipe
      Down by a factor 2 for cells second closest The radiation affects a small part of HCAL
  Modules irradiated at Serpukhov with ~70 krad/day for 25 days (80 to 1500 krad)
    Scintillator and WLS fiber degradation (and annealing) effects studied
      Simulation used to estimate the degradation on resolution
    Constant term degrades from 10% to ~12% with 0.5 Mrad in the inner most modules (negligible for next to central modules)
TDR
2011 measurements (1fb-1)
HCAL front: ~30 krad
HCAL back:~3krad

## Slide 39: HCAL ageing
Light yield degradation map (front tile)
HCAL front dose ~100 krad
Degradation ~20-25% at the center
From TDR (100 krad ):
Tile light yield degradation ~ 5-10%
Fibre attenuation increases by ~10-20%
TDR
__ Non irradiated fibre
--- 50 krad/year (10y)
…. 100 krad/year (10y