## Slide 1: The RICH detectors of LHCb and the proposed upgrade
Antonis Papanestis
On behalf of the LHCb RICH collaboration

## Slide 2: Outline
The LHCb experiment
The LHCb RICH detectors
  Description
  Operation
  Alignment and Calibration
  Performance
  Physics examples
LHCb Upgrade
Conclusions

## Slide 3: The LHCb experiment
Probing New Physics in CP violation and rare decays of b and c quarks
Single arm spectrometer with:
Excellent vertexing
Excellent PID
Efficient trigger and tracking
RICH 1
RICH 2

## Slide 4: LHCb event
23 sep 2010 19:49:24
Run 79646 Event 143858637

## Slide 5: The LHCb RICH detectors
RICH 2
Acceptance 15-120 mrad
RICH 1
Acceptance 25-300 mrad
Note Scale Difference
2 Detectors
3 Radiators
~7 m
CF4 gas
300 mrad
120 mrad
Side view
Top view
Flat mirrors
Spherical mirrors

## Slide 6: RICH1 Mirrors and Aerogel
Aerogel is inside a gas tight box flushed with CO2 to avoid performance degradation from exposure to C4F10
Carbon fibre mirrors for low material budget
~0.5 m

## Slide 7: RICH 2 entry and exit windows

## Slide 8: Photon Detectors
Main features of Pixel-HPD:
Quartz window with thin S20 pK
Cross-focussing optics (tetrode structure):
  De-magnification by ~5
  Active diameter 75mm
   484 tubes for overall RICH system
  Up to 20 kV operating voltage (~5000 e– [eq. Si])
  Low noise (~140 e- RMS)
3232 pixel sensor array (0.5mm0.5mm each)
Encapsulated binary electronics readout chip
Schematic
view

## Slide 9: RICH 1 & 2 Hitmap
From Online Monitor.
RED histograms for reference

## Slide 10: Magnetic field corrections
HPD image distortion due to magnetic field
Projection of test pattern with and without magnetic field to extract correction parameters
RICH-1
s=0.5mm
RICH-2
s=0.47mm

## Slide 11: Anode image fitting
Position of the photocathode image on the anode can change due to charging effects.
Anode images are cleaned and a Sobel filter is used to detect the edge.
Automated procedure, updates the position of the photo-cathode centre in Conditions Database

## Slide 12: Cherenkov angle resolution
 | Data | MC | Unit
Aerogel | 5.0 | 4.4 | mrad
C4F10 | 1.62 | 1.53 | mrad
CF4 | 0.68 | 0.68 | mrad

## Slide 13: Number of detected photons
Physics event: D0→K-π+
Two event types
“Light” Event: pp→ppµ+µ-
Radiator | Npe from data |  | Npe Simulation
 | D0→K-π+ | pp→ppµ+µ- | 
Aerogel | 5.0±3.0 | 4.3±0.9 | 6.8±0.3
C4F10 | 20.4±0.1 | 24.5±0.3 | 29.5±0.5
CF4 | 15.8±0.1 | 17.6±0.2 | 23.3±0.5

## Slide 14: Using isolated rings
Cherenkov angle vs momentum in RICH1

## Slide 15: C4F10 Gas Composition

## Slide 16: PID algorithm
Consider all photons and all tracks and all radiators at once and maximise likelihood function:
Take all PIDs to be pions
  Estimate background parameter bpixel per HPD
Calculate likelihood of given pixel distribution.
Iterate
  Change PID hypothesis one track at a time
  Recalculate likelihood
  Choose change that had biggest impact
  Assign new PID to that track
Until no significant improvement is found
As signal photons are now identified better, update background estimate and start a 2nd (and usually final) iteration.

## Slide 17: PID Performance
PID performance evaluated from data
  Genuine p/K/p samples identified from kinematics only
Data
Monte-Carlo

## Slide 18: CP violation in B0(s)
First observation of CP violation in the decays of Bs mesons
(arXIV 1304.6173; Phys.Rev.Lett 110 ,221601(2013))

## Slide 19: CP violation in B0(s)
Where
and
Correction for production and detection asymmetries
World’s best
First observation
10.5 s
6.5 s
41420±300 events
1065±55 events

## Slide 20: LHCb Upgrade
Change opto-electronic chain:
Photon detectors
Front-end electronics
DAQ
RICH optics and mechanics:
Modify RICH1 optics
Optimise for available space.
Remove aerogel radiator
40 MHz readout rate
  up to 2×1033cm-2s-1
@
Goal: collect 50 fb-1
Consequence: run at Linst up to 2×1033cm-2s-1
Approach: remove trigger limitations and readout detector @ 40 MHz
  Current max trigger rate of 1.1 MHz limits the efficiency of hadronic channels

## Slide 21: New RICH 1 layout
Present
Upgraded
Hit distribution on photon detectors.
Reduced peak occupancy for upgrade geometry

## Slide 22: New photo-electronic chain
Baseline option: 64 pixels MaPMT
+ custom FE chip (CLARO8)
+ digital board + GBTs
TORCH - a Cherenkov based Time-of-Flight Detector by Euan Cowie (Thu 17:10)

## Slide 23: Conclusions
LHCb has recorded 3 fb-1 in 2010-2012, running in conditions well above the original specifications, at 90% efficiency, producing a number of world first and world best measurements.
The LHCb RICH detectors have been operating in a difficult environment of high track multiplicity and form an essential part of the experiment. There are advanced plans to use the RICH detector in the LHCb trigger for the LHC Run2.
After careful alignment and calibration, the performance of the RICH detectors has reached the levels expected from MC simulations. This is due to:
  Excellent photo-detectors.
  Very stable optical system.
  Well controlled gas radiators.
The LHCb RICH upgrade is progressing well and is on schedule for installation in 2018.
Performance of the LHCb RICH detector at LHCb;
Eur. Phys. J. C (2013) 73:2431

## Slide 24: The END

## Slide 25: CF4 Scintillation Quenched using CO2
Inefficiency is calculated from lab measurements
“Extra” photons from scintillation were saturating data bandwidth

## Slide 26: CF4 Ref Index calibration

## Slide 27: Time alignment
Both RICH detectors are time aligned to less than 1 ns

## Slide 28: LHCb luminosity
LHCb was designed to run at μ~0.5 and nb~2600 ⇒ Linst~2×1032cm-2s-1
In 2012 LHCb runs with μ~1.7 and nb~1300 ⇒ Linst~4×1032cm-2s-1
μ=0.4
μ=2.7
design
1 fb-1
2011 data
2010 data
2 fb-1
2012 data
Automatic luminosity levelling

## Slide 29: RICH 1 MDCS
Correcting for the magnetic distortions
RICH1
Pixels (0.5 mm)

## Slide 30: RICH 2 MDCS
A temporary setup, using commercial projector was used in 2008 to project a static, reproducible grid of light spots onto the photon detector plane,
The raw spot images were analysed to calculate the centre of gravity for precision comparison between measurements:

## Slide 31: RICH 1 Tight space, low mass
Spherical Mirrors Lightweight carbon fibre mirrors 1.5% radiation length
VELO Exit Window 2mm aluminium.. Sealed to gas enclosure. No RICH entrance window.
Photon detector plane 14 by 7 Hybrid Photon Detectors (HPDs)
RICH1 Exit Window Carbon fibre & PMMI foam
Sealed direct to the beampipe.
4m

## Slide 32: HPDs in magnetic field
0 G
B║ 30 G
B┴ 50 G
Test pattern measurements with locally shielded HPD
Magnetic distortions

## Slide 33: Event snapshot 1

## Slide 34: Event snapshot 2

## Slide 35: RICH 2 Huge volume, very precise
8m
Magnetic Shields protect the HPD planes
Flat Mirrors each made from 20 square glass segments
HPD planes of 9 by 16 HPDs
Gas Enclosure Contains CF4 gas radiator and the optical system
Spherical Mirrors each made from 21 glass hexagonal segments
RICH2 entrance / exit windows carbon fibre and foam sandwich

## Slide 36: The readout chain
HPD column assembly
All HPDs arranged in columns with ancillary front-end electronics
LV & HV boards power the HPDs
“Level-0” board passes triggered data to the “Level-1” off-detector board via an ~100m optical link
Level-1 board receives and zero-suppresses the data and passes to the DAQ