## Slide 1: AMKID and ALMA Large Submillimeter Instruments in Atacama desert
A. Baryshev
SRON/Kepteyn Astronomical Institute/RuG

## Slide 2: Why far-infared submillimeter astronomy
Orion
Optical
Far infrared

## Slide 3: A lot of chemical information in spectral lines
Orion spectrum by Hershel HIFI
Sugar – yes!, coffee – Not yet

## Slide 4: Star formation
And much much more

## Slide 5
Atakama large millimeter submillimeter array (ALMA)

## Slide 6: ALMA Frequency bands, athmosphere

## Slide 7: ALMA project
Initial project
  Europe (ESO+Spain) + North America (NRAO+Canada) + Chile
  50 12-m antennas at 5000-m in the Atacama desert in Chile
  antenna baselines = 150 m to 18 km (reconfigurable)
  4 receiver bands around 100, 250, 325, and 650 GHz (first light)
    DSB/2SB receivers
    Dual polarization
    Wide band IF (4-12 GHz)
    Cryogenic temperatures
  possibility to expand to 10 bands over 30 GHz to 1 THz
  Wide band IF (4-12 GHz) 6 Mb/s average data rates (60 Mb/s peak)
After Japan has joined in 2004
  additional 4 12-m + 12 7-m antennas (compact array)
  additional correlator
  receiver bands around 150 and 450 GHz (+ possibly 850 GHz)
1200 M$ (Y2K)

## Slide 8
The ALMA Site

## Slide 15: The ALMA Site
Shaman
Building activity

## Slide 16: ALMA Configurations
18 km Maximum Baseline
150 m Maximum Baseline

## Slide 17: Operation Support Facility
between San Pedro de Atacama and the ALMA site
  2900 m altitude, private road to ALMA site (under construction)
array operations, including
  final integration of the antennas before transport to site
  maintenance and repair (not on site due to altitude)
To AOS (43km)
OSF Site (15km)

## Slide 18: ALMA Transporter

## Slide 19: Lore en Otto

## Slide 20: 4 telescope types

## Slide 21: ALMA Antennas
JP
US
EU
12 m, 0.5 deg/sec rotation, 1.5 degree switch, 25 micron shape accuracy, 15 micron phase stability

## Slide 22: ALMA heterodyne receiver technology
Front-end
Sky object
Telescope
Detector chip
SIS mixer

## Slide 23: Achter elke telescoop:1 Cryostaat
1 m diameter, ~ 65 cm hoog
Plek voor 10 ontvangers
Koelen tot 4 K

## Slide 24: Cryostat met banden 3 tot 10

## Slide 25: Baseline receivers

## Slide 26: ALMA Band 9 design
field-replaceable unit
  “core” of a heterodyne front end
  “plug-and-play” in the cryostat
solid-state broad-band tunable LO
  mm-wave (100 GHz) power amplifiers in warm structure
  cold frequency multipliers to operating frequency
low-noise mixers at 4K
  DSB SIS mixers
focal plane optics
low-noise IF amplifier chain
  1 cryogenic + 1 warm amplifier
rigid structure
monitor and control electronics
2 linearly polarized channels

## Slide 27: SIS Mixer
Simple construction,
Easy to assemble

## Slide 28: SIS Technology
SIS Junctions (TU Delft)
THz SIS mixers
  quantum-limited sensitivities
  600-720 GHz bandwidth
    LO tuning range
  4-12 GHz IF bandwidth
    4-8 GHz in HIFI
SIS junctions (TU Delft)
  Nb SIS technology
  optimized fabrication
    larger quantities
    improved pattern accuracy
    1 µm structures are 1 µm
waveguide device mounts
  optimized for series production
corrugated horn antennas (RPG)
  commercial product
  100 µm structures +/- 5 µm

## Slide 29: ALMA BAND 9

## Slide 30: ALMA band 9, performance of almost all 73 receivers

## Slide 31
Recente observation: Super Nova 1987A

## Slide 32: How to do large scale mapping
APEX telescope

## Slide 33: Detectors
MKID: superconducting pair breaking detector
antenna determines RF-band
resonator determines KID-readout frequency
detector + multiplexing filter in one structure
Light
Dark
Cooper Pairs: Quasiparticles:
Inductance iωL(Psky) Resistance R(Psky)
2Δ
h
Zs = R + iωL

## Slide 34: Hybrid KIDs
Photon noise limited at P>100 fW
APEX loading: 3-10 pW

## Slide 35: AMKID Specifications
HFA
LFA
dual color APEX direct detection camera
  LFA: 347 GHz ( 34 GHz width, from 330 to 364 GHz / HP width)
  HFA: 850 GHz (100 GHz width, from 800 to 900 GHz / HP width)
squared field of view: > 15 x 15 arcmin2
number of pixels
  pixel spacing 1 Fλ
  hexagonal arrangement
   3520 pixel in LFA
   21600 pixel in HFA
detectors operating with sensitivities dominated by the sky background
good system stability that allows mapping of extended structures
cooling:
  two 4K pulse-tube closed cycle systems
  He 10 sorption cooler (<300 mK)
MPIfR, SRON, NOVA, TUD

## Slide 37: Draft sensitivities
B. Sybthorpe

## Slide 38: Optics layout
dominated by the space available within the APEX Cassegrain cabin
fully reflective optics  no losses due to imperfect anti-reflection coating and absorption
four imaging mirrors (M3, M4, M5 und M6)
two “flat” mirrors (FM1 und FM2)
  FM2 is used to compensate for aberration („glasses“ for the dewar-optics) and therefore has also a slightly structured surface.
magnification : ~ 4
size of the dewar-window: approx. 150 x 150 mm2

## Slide 39: cabin layout
beam-path
M3
telescope Focal-plane
1250 mm
FM1
FM2
M4
8-channel readout
temperature monitoring
IF power supply
window
baffling structure (4K)
pulse-tube cooler
H10 cooler
detectors
M5
M6

## Slide 40: Concept prove at APEX
PKS0537-441
PMNJ0210
J2253+161
APEX test-camera @ 345GHz
wet-dewar
He4+He3 cooler
hold-time 24h @ 250 mK
16 pixel
results of one observing night in August 2011
mean sensitivity: 220 mJy √s

## Slide 42: King test cryostat
Started ~Oct 2012 – working June-July 2013…

## Slide 43: Optics Box

## Slide 45: Final integration

## Slide 46: Cryostat overvew

## Slide 47: Dark Tests

## Slide 48
Responce
NEP
Responce
AIV on latest chips

## Slide 49: Outlook
Atlasgal
installation at APEX in Nov/ Dec 2013 done
Upgrade of chips 1 Jan - 26 May 2014 complete
Commisioning / Science operations August/September 2014
Good science till 2017 inclusive