## Slide 1: Firmware development and testing of the ATLAS IBL Readout Driver card
Shaw-Pin Chen, University of Washington
on behalf of the ATLAS IBL DAQ group
TIPP2014, Amsterdam, 2nd-6th of June 2014
TIPP2014, Amsterdam
Page 1 of 22
Shaw-Pin Chen, University of Washington

## Slide 2: The Insertable-B Layer
The successfully installed (May 2014) new inner layer of the ATLAS Pixel detector at the LHC at CERN
Higher luminosity and closer to interaction point → higher occupancy expected
Existing Pixel FE inefficient for IBL readout
New FEs (FE-I4) with larger active area and higher readout speed
New Readout Drivers and Back of Crate Cards
TIPP2014, Amsterdam
Page 2 of 22
Shaw-Pin Chen, University of Washington
Details on IBL covered in Cecile Lapoire’s talk
Notes: FE-I4 functions highly integrated: 8b/10b encoded data at rate of 160 Mbit/s or more
New optical-electrical communication board and readout processors are built
Motivations for new readout electronics

## Slide 3: Trigger DAQ
Based on the VMEx64 Pixel TDAQ
On-detector (staves)
Optical communication to off-detector (ROD/BOC)
TTC Interface Module (TIM)
VME-crate cards (TIM/ROD /BOC)
New FitServer (for calibration)
Readout Subsystem (ROS) with Readout Buffer INput (ROBIN) cards
S-Link: CERN’s data transmission protocol
TIPP2014, Amsterdam
Page 3 of 22
Shaw-Pin Chen, University of Washington
BOC-RODs
FE-I4
Sensor
IBL Staves
LVL 1
Accept
Level 1 Trigger
ROS
Level 2 Farm
Region of
Interest
(ROI)
req.
ROI data
Event Builder
Event
Filter (Level 3)
“raw data”
Mass Storage
S-Links
Fit Server
Details on IBL BOC covered in Marius Wensing’s talk
Notes: Motivation for the upgrade
Only IBL shown here. There are other ATLAS sub detectors
New calibration approach move the time consuming processes externally

## Slide 4: ROD-BOC Communication
TIPP2014, Amsterdam
Page 4 of 22
Shaw-Pin Chen, University of Washington
32x FE
IBL Stave
IBL BOC
IBL ROD
32 RX channels @ 160 Mbit/s
16 cmd channels @ 40 MHz
TX
ROD Bus @ 40 MHz
Control
Data Processing
96-bit data RX @ 80 MHz
4 S-Links @40 MHz
Notes: ROD control path and data path, will talk a little bit more on data path and process flow later
16 serial command lines at 40 MHz
Each S-Link off to ROS transmits at 5.12 Gbit/s

## Slide 5: ATLAS IBL ROD Card
FE control and readout
Fast histogramming for FEs
Main Components:
  1 Master FPGA
  2 Slave FPGA
  1 PRM FPGA
2 SSRAMs,1 DDR2 per slave
32 FE data processing
PowerPC controller
Upgrades for Pixel Layer 1 & 2
15 productions cards ready (RevC and RevD)
TIPP2014, Amsterdam
Page 5 of 22
Shaw-Pin Chen, University of Washington
Slave
Slave
Master /PPC
Ethernet
Ethernet
Ethernet
Notes: High level, non real-time and real time lower level
PPC drives the ROD bus, config FE, slave, scan
PRM
26 RODs for Layer 2 and 38 for Layer 1.
1 ROD-BOC for DBM

## Slide 6: Detector Calibration
TIPP2014, Amsterdam
Page 6 of 22
Shaw-Pin Chen, University of Washington
Set uniform readout threshold for all channels
Find and reject noisy readout cells
Max. hit rate of 85 MHz by serializing 8 FE-I4s.
Histograms stored and updated in external SSRAMs @ 50 MHz (speed upgrade in progress)
Histograms transfer: SSRAMs → dual DMA → DDR2 → MicroBlaze TCP/IP transfer → Gbit Ethernet → FitServer
Notes: Calibration & data taking shares most of the data processing path
Update SSRAM in a pipelined fashion
Theoretically SSRAM can run at above 200 MHz.

## Slide 7: ROD Data Processing
Modular VHDL Firmware based on Pixel ROD
  Internalized many discrete FIFOs and memory
Real-time @ 80 MHz
De-randomizing FIFOs
FE service records
Error checking
Busy handling
Generate S-Link data
Readout link test data
TIPP2014, Amsterdam
Page 7 of 22
Shaw-Pin Chen, University of Washington
FE0
FE1
FEn
Gather Data & Event Building
Frontend Event
Event
Info
. . .
Frontend Data
S-Link Headers
S-Link Trailers
Trailer
Data Record
Service Record
Data Header
Notes: S-Link header and trailer formats are specific using control words.

## Slide 8: IBL ROD Control & Data Flow
TIPP2014, Amsterdam
Page 8 of 22
Shaw-Pin Chen, University of Washington
“Half Slave” inside ROD Slave
Data Router
Store or forward S-Link data, decode detector hits
Event Builder
Distribute event information, check event IDs, process data errors, generate S-Link data, provide S-Link test data
Event Processor
Builds event and synchronization information
PowerPC
Calibration scan, ROD bus control
TTC
Interface
Module
ROD Master
Slave Busy
Master Busy
Trigger Processor
software
triggers
TTC triggers
Collect triggers and event descriptions from TIM for data taking or PPC for calibration
Histogrammer
Build histogrammers for scanned pixels during calibration
S-Link
Fit Server
Formatter 1
Formatter 2
Gather 4 FE data, disable links, runtime errors, data in chip order
FE Data
FE Command Processor
Generate serial frontend-specific fast and slow commands
FEs

## Slide 9
ROD Slave Event Fragment Builder
Event Header FIFO
mem
Fragment Generator
To Router
Formatter
Data (link 0-3)
Event ID checker
Error detector
Data formatter
Event data decoder
Error Word
FIFO B
Event Data Count FIFO B
Event ID FIFO B
Event Data FIFO B
Play2
pop
Event ID checker
Error detector
Data formatter
Error Word
FIFO A
Event Data Count FIFO A
Event ID FIFO A
mem
Play1
pop
Event Data FIFO A
Formatter
Data (link 4-7)
Event Data from Master
S-Link headers + FE data + S-Link trailers
TIPP2014, Amsterdam
Page 9 of 22
Shaw-Pin Chen, University of Washington

## Slide 10: Data path simulation with realistic FE-I4 Model
HDL model from the FE-I4 developers
Service records and allows hits injection
Accelerated ROD data path firmware development and greatly reduced debugging time
TIPP2014, Amsterdam
Page 10 of 22
Shaw-Pin Chen, University of Washington
“realistic” FE-I4B
cdr_8b10b_decode
rx_fifo
Mux_BOC2ROD
ROD Slave
S-Link0
S-Link1
Half_Slave0
Half_Slave1
register
FEI4 pack
ROD Slave pack
configuration,
triggers,
charge injection
Event ID,
register R/W
Simplified BOC
Notes: Motivation!!
The model is black box, which excludes many IO pads for convenience but it is very real
Custom inject digital TOT to desired pixels (in parallel!)
Correct S-Link data, error handling functionality, etc

## Slide 11
TIPP2014, Amsterdam
Page 11 of 22
Shaw-Pin Chen, University of Washington
Simulation Results
FE-I4 model configured
Output with injected hits
Decoded 8b/10b idle signal
S-Link data
to the Router
Extracted hit
Info for the Histogrammer

## Slide 12
TIPP2014, Amsterdam
Page 12 of 22
Shaw-Pin Chen, University of Washington
Simulation Results cont.
event counter reset
external trigger
TOT injections and self-triggering
L1A triggers through serial cmd

## Slide 13: Hardware Readout Chain Tests
TIM – ROD – BOC – S-Link – ROBIN
Two sources of data are used:
  ROD slave-generated readout link test data to ROS
  Triggers to all 32 FE emulators on each BOC, process event on ROD, and send to ROS
ROD can process all FE data at trigger rate of 200 KHz
  No data corruption at ROS
  ROBIN buffer becomes full quickly
  IBL expect to run at 100 kHz
Successfully triggered 16 million emulated events at 50 kHz without data corruption at ROS
TIPP2014, Amsterdam
Page 13 of 22
Shaw-Pin Chen, University of Washington
Notes: Tested at CERN, majority of the IBL TDAQ Level 1 components
Significance of these for the integration test (nothing changed in the ROS)

## Slide 14: Calibration Scan Results
TIPP2014, Amsterdam
Page 14 of 22
Shaw-Pin Chen, University of Washington
Digital scan, 100 triggers, 1/8 mask
Analog scan, 100 triggers, 8/8 mask
Notes: Histograms generated, transferred to FitServer Farm, downloaded from the FitServer
Mask stepping and color correspondence
analog scan process as well as digital scan process

## Slide 15: Summary
New FPGA-based IBL RODs are commissioned for the IBL
Higher bandwidth and integration
Data taking and calibration functions in place
Realistic FE model used in data path firmware development
ROD data taking functionality verified via ROS test.
Near future developments:
  Develop built-in tests for IBL ROD firmware
  Integration of Pixel readout into IBL ROD
TIPP2014, Amsterdam
Page 15 of 22
Shaw-Pin Chen, University of Washington
Notes: Foresaw bandwidth limitation of the Pixel ROD for higher luminosity run.
The link bandwidth is proportional to the product of occupancy and trigger rate of the front-end devices.
Developments to be carried out by LBNL and Washington groups

## Slide 16: Thank you for your attention!
TIPP2014, Amsterdam
Page 16 of 22
Shaw-Pin Chen, University of Washington
Notes: Questions?

## Slide 17: Backup
TIPP2014, Amsterdam
Page 17 of 22
Shaw-Pin Chen, University of Washington

## Slide 18
TIPP2014, Amsterdam
Page 18 of 22
Shaw-Pin Chen, University of Washington
Old vs New ROD
 | Pixel ROD | IBL ROD
FPGAs | 1 Master + 8 Formatter + 1 EFB + 1 Router + 1 PRM | 1 Master + 2 Slaves + 1 PRM
Control | Master DSP + 4 Slave DSP | Embedded PPC & MicroBlaze
Memory Components | Many External | Mostly Internal to FPGA except SSRAMs + DDR2s
Data RX rate from BOC | 40 MHz (all channels enabled) | 80 MHz

## Slide 19
TIPP2014, Amsterdam
Page 19 of 22
Shaw-Pin Chen, University of Washington
Pixel FE-I3 vs IBL FE-I4
 | FE-I3 (requires MCC) | FE-I4
Pixel Size | 50 um x 400 um | 50 um x 250 um
Pixels/chip | 2880 | 26880
Active area | ~75% | ~90%
Serial data out | 40 Mbit/s | 160 Mbit/s

## Slide 20
TIPP2014, Amsterdam
Page 20 of 22
Shaw-Pin Chen, University of Washington
Data Path FW Structure

## Slide 21
TIPP2014, Amsterdam
Page 21 of 22
Shaw-Pin Chen, University of Washington
Slave Busy Logic
S-Links back pressure
overflows in Formatters
overflows in EFBs
force inputs
busy masks
slave busy_n
edge counters
Register busy histograms readout
overflows in Routers

## Slide 22
TIPP2014, Amsterdam
Page 22 of 22
Shaw-Pin Chen, University of Washington
ROD Slave Router Block
S-Link FIFO
To S-Link
To Histogrammer
hit data extraction
Histo FIFO A
Histo FIFO B
pop
FIFO
hit valid
row (9)
col (7)
chip (3)
ToT (4)
24
24
k_word +
data (32)
calibration mode
k_word
33
register
chip_ID (3)
EFB data (32)
row+1