## Slide 1
Towards the integration of the Micro Vertex Detector in the PANDA experiment
Daniela Calvo
INFN – Sezione di Torino
on behalf of the PANDA MVD group
PANDA Collaboration
TIPP’14 - International Conference on Technology and Instrumentation in Particle Physics
2-6 June 2014, Amsterdam, The Netherlands

## Slide 2
Overview
Introduction
Pixel and strip modules
Readout architecture
Service integration
Detector prototypes
Conclusions

## Slide 3
Introduction

## Slide 4
The PANDA experiment
TARGET SPECTROMETER
FORWARD SPECTROMETER
Solenoid
Dipole
Muon ID
RICH
DIRC
Vertex
Central Tracker
Electromag. Calorimeters
Muon
Range System
Drift Chambers
Target
  PANDA is a fixed target experiment with frozen hydrogen pellet and heavier nuclear targets (N, Ne, Ar…)
p beam
Hadron spectroscopy
In-medium effects
Hypernuclear physics
Charmed hadrons
4 p acceptance
High spatial and momentum resolution
No hardware trigger

## Slide 5
The Micro Vertex Detector
Tasks
It must combine good space resolution with accurate time-tagging
Main functions
  Primary vertex reconstruction
  Identification of the secondary vertices (c of some hundreds of m)
  Improvement in momentum resolution
  Support PID of low momentum particles by energy loss measurement

## Slide 6
The Micro Vertex Detector
10.3 M (pixel channels) – active area: 0.106 m2
162 k (strip channels) – active area: 0.494 m2
4 barrels
Two inner layers: silicon hybrid pixel
Two outer layers: double-sided silicon strips
6 forward disks
Four disks: hybrid pixel detectors
Two last disks: mixed pixel and strips
Good spatial resolution (some tens of mm in rf, better than 100 mm along z)
Time resolution < 10 ns
Continuous readout at 2 x 107 interactions /s (clock @160 MHz)
Limited material budget X/Xo ≤ 1 % / layer
Radiation tolerance ˂ 1014 n 1 MeV eq cm-2
Provide at least four hits per track
Room temperature operation
Routing and services only in the backward region

## Slide 7
Pixel and Strip Modules

## Slide 8
Hybrid epitaxial pixels
810 readout chips / 176 sensors
Layout based on a basic unit corresponding to a readout chip size
Modules are built by tiling from two to six units
Standard hybrid technology
Epitaxial Silicon material
Pixel cell size: 100mm x 100mm x 100mm
repi ~ k∙cm
rCz ~ 20-50 m∙cm
ASIC in 130 nm CMOS tecnology
Triggerless
dE/dx using Time over Threshold technique
Wafer from ITME, pixel sensor from FBK

## Slide 9
Pixel modules
Pixel disk
Pixel stave
Total power 94 W
Cooling pipe
diameter 2 mm (Ni-Co alloy)
4 mm carbon foam
Cooling flow 0,3 l/m
Inlet temperature: 18.5 °C
Th. conductivity = 50 W/m∙K

## Slide 10
Double-sided silicon strips
3112 readout chips / 296 sensors
Rectangular (512 x 896 strips) and squared (512 x 512 strips) sensors;
stereo angle: 90°, pitch: 65 mm
Trapezoidal (768 x 768 strips) sensors; stereo angle: 15°, pitch: 45 mm
285 mm thickness (FZ silicon wafer)
Readout every second strip
CiS Erfurt
Radiation damage test using 14 MeV proton beam @ Bonn

## Slide 11
Strip staves
Sandwich structure of carbon fiber
(200 mm) and Rohacell (2 mm)
Up to 18 W dissipated on one stave
Embedded cooling pipe in Ni-Co alloy
(2 mm diameter, 80 mm wall thickness)
POCO HTC around the cooling pipe
Characterization of the PANDA MVD Trapezoidal Silicon Strip Sensor and their First Operation in a Proton Beam
Poster presented by D. Deermann

## Slide 12
The Micro Vertex Detector
Two halves arranged around the beam-target pipes
suspended to the central tracker support
Reconstructed D± mass
Reconstructed D± decay length
pp → D± → k- p + p + k + p - p -

## Slide 13
Readout architecture

## Slide 14
Pixel detector architecture
ToPix
Epitaxial silicon sensor
Hybrid
Pixel module
Power lines
DC-DC converter
HV Power supply
LV Power supply
e-links
Computer node
GBT
Optical fibres
MVD Multiplexer Board
SODA
Optical fibre
Optical fibres

## Slide 15
ToPix
Pixel matrix: 110 x 116
Size (to be optimized):
11.2 mm x 14.8 mm
dE/dx measurement: ToT,
12 bits dynamic range
Maximum input charge: 50 fC
Detector type: n and p
Noise floor: < 200 electrons
Input clock frequency: 160 MHz
Time resolution: ~ 6 ns
Power consumption: ≤ 0.8 W/cm2
Maximum event rate: 6.1 x 106
Total ionizing dose: < 100 kGy
Data rate per chip:
up to ~ 450 Mb/s
Output bandwidth: 2 x 320 Mb/s
Supply voltage: 1.2 V
Columns divided in 8 regions with 7 double columns each
FIFO in the end of column and region control

## Slide 16
ToPix_v4
ASIC size: 3 mm x 6 mm
130 nm CMOS technology
Pixel matrix: 640 cells, 2x2x128 and 2x2x32 columns
Input clock frequency: 160 MHz
Compatible with the sensor of previous version (ToPix_v3)
Hamming encoding and TMR pixel logic protection
Leading and trailing edge registers withDICE -protected latches
SEU protected EoC
Serial data output (SDR and DDR)
GBT compatible SLVS I/O
640 pixel DACs completely linear
Easy calibration
Measured perfomance @ 160 MHz clock

## Slide 17
Hybrid for the pixel module
Hybrid structure for 6 readout chips
Size: 67.9 mm x 11.9 mm
15 mm Al thickness
75 mm kapton thickness
60 mm track width, 60 mm spacing
For each chip:
  3 differential pairs in daisy chain
  4 direct differential pairs
27 differential pairs in total
~ 100 ohm differential impedance
12 smd capacitors
Total jitter vs data rate
UI
Link diretto LVDS
Link diretto SLVS
Daisy chain lunga
Daisy chain corta
long
short
direct
direct

## Slide 18
Signal transmission
Total Jitter
1 m and 1.5 m long aluminum strip prototypes
straight coverless
Technology based on laminated aluminum on kapton, reliable for bonding, produced @ CERN according to our design
18 differential pairs
u
c
SLVS signals

## Slide 19
Hybrid and cable
hybrid
1.5 m long cable
To oscilloscope
PRBS from
pulse generator
SLVS signals

## Slide 20
Strip detector architecture
Power lines
DC-DC converter
HV Power supply
LV Power supply
e-links
Computer node
GBT
Optical fibres
MVD Multiplexer Board
SODA
Optical fibre
Optical fibres
Double-sided silicon
strip detector
Hybrid flex adapter
PASTA
PASTA
PASTA
PASTA
PASTA
PASTA
MDC
MDC
MDC
MDC

## Slide 21
PASTA concept
64 channel, 4.2 x 5 mm2 , self triggered chip
110 nm CMOS technology
Input capacitance: < 50 fF
Dynamic range: < 50 fC
Power consumption: < 4 mW/ch
Channel pitch: 60 mm
Radiation protection: 100 KGy
Dynamic range: 8 bit
Amplification and discrimination
Time interpolation, Wilkinson ADC
Control charging and initiate storing
Handling configuration and channel data

## Slide 22
Full hybrid PCB
Folding of PCB around the stave to connect n-side and p-side r/o
Reduced scale prototype

## Slide 23
MVD service integration

## Slide 24
DC-DC s
GBTs
MVD
2840 mm
MVD services integration
In & Out fittings from front side
360
Cooling tube embedded in an aluminum bar
DC-DC circuit system composed of 3 sets of twin layers of boards, arranged around the beam pipe
2112 DC-DC circuits (CERN)
24 twin cooling bars equipped with 88 circuits each
168 GBT circuits (CERN)
12 cooling bars equipped with 14 circuits each
Thermal simulations in progress

## Slide 25
Integration in PANDA
2840
Backward Calorimeter
MVD
MVD Services
Beam line pump

## Slide 26
Detector prototypes

## Slide 27
Detector prototypes
Flex-PCB and 3.5 cm x 3.5 cm PANDA fullsize strip sensor (+APV25 chips)
Test @ COSY in 2014
Single chip pixel assembly
ToPix_3 prototype and the custom epitaxial silicon (ITME) sensor (FBK), 640 pixels arranged in long and short columns
Cz thinning + Bump bonding @ IZM (Berlin) using Sn-Pb bumps.
  Yield of the tested assemblies :
  ~ 99.5 %
The thin Cz layer is the ohmic contact for the sensor biasing.

## Slide 28
Detector prototypes
BEAM

## Slide 29
Conclusions
Challenging integration of the MVD in PANDA.
The work is in progress on the service side
and
for both pixel and strip readout the custom developments are ongoing.
The prototype results support our study and design.

## Slide 30
SPARES

## Slide 31
MDC - Module Data Concentrator
Time ordered hit packets (Hit Ring-Buffer)
Cluster-centroids and –sums after the 1d-clustering (Cluster Correlation Processor)
2d-hit points after the CCP
Buffering by FIFOs

## Slide 32
MVD services integration
GBT circuits support structure is composed by two halves around the beam pipe
168 GBT circuits (CERN)
12 cooling bars equipped with 14 circuits each
Thermal simulations ongoing
  Water as cooling fluid at 18 °C inlet
Cooling tube embedded into a aluminum bar
In & Out fittings from front side
680