HARPO
(Hermetic ARgon POlarimeter)
A gas detector concept for photon detection and polarimetry in the MeV-GeV range
LLR (CNRS, École Polytechnique)/
Irfu (CEA Saclay)
funded by French ANR and Labex P2IO
TIPP 2014, Amsterdam
Philippe GROS
LLR, École polytechnique

---
Outline
- Science case
- Proposed detector: TPC
- Results with a demonstrator
- Status and outlook

---
Science case
Gamma astronomy

---
Science Case
Gamma telescopes performance
COS-B (1975-1982)
70MeV - 5GeV

---
Science Case
Gamma telescopes performance
EGRET (1991-2000)
271 sources>100MeV

---
Science Case
Gamma telescopes performance
Fermi (2008-)
1873 sources>100MeV

---
Science Case
Gamma telescopes performance
Comptel (1991-2000)
63 sources 1-30MeV

---
Science Case
Gamma telescopes performance
- There is important progress in gamma ray telescope at high energy (>100MeV)
- Still a big performance gap at lower energy

---
Time Projection Chamber (TPC)
- photons are converted in the gas
- produced electrons ionise the gas
- ionisation electrons drift along E field
- electrons are amplified and mesured on the xy-readout plane
- time gives a measure of the z coordinate
  - t0 from external trigger
  - drift velocity
e+
e-
E
readout plane
drift volume
Z
Y
X

---
TPC Characteristics
- A gaseous 3D tracking detector
  - Often used in particle physics
  - High spatial resolution (<1mm), excellent tracking
  - Low multiple scattering => tracking even for low momentum tracks
- “Thin” active target
  - sensitivity proportional to mass, not surface
  - Polarisation information accessible (thick detector, e.g. W/Si excluded)

---
Expected Performance
- Angular resolution
  - limited by multiple scattering above 100MeV
  - limited by the unknown recoil nucleus momentum below 100MeV
  - only multiple scattering for triplet conversion, but very low efficiency
- Up to 1 order of magnitude better than Fermi!

---
Polarimetry
2 %pi {d %sigma} over {d %phi} = %sigma_{tot} ( 1 - PA cos 2 %phi )
- Multiple scattering dilutes the polarisation modulation
- In converters, it is very quickly lost
- In Argon at 5 bar:
  (resolution 1mm, 1m3,
  Crab-like, 1 year, exposure=efficiency=1)
  Polarisation asymmetry A~15%
  Polarisation resolution ~ 1%
D. Bernard,
NIM A 701 (2013) 225
%phi [rad]
raw MC
with multiple scattering

---
HARPO Demonstrator
- Purpose
  - Assess challenges
  - Demonstrate performance in test beam
- Realisation
  - 30cm cubic TPC
  - Ar/iC4H10 95/5 up to 5bar
  - micromegas+2GEM
  - 2x288 strips readout (x&y), ~0.5mm wide
  - AFTER readout electronics,
    511 time bins, up to 50MHz
  - trigger: 6 scintillators

---
HARPO Demonstrator
scintillators
micromegas +GEM
readout strips
field cage

---
Amplification
Micromegas+GEM
- Limited gain with micromegas only
- Micromegas + 2GEM, produced at CERN
  - characterised at 1 bar, with 55Fe source
Ettrans
Main, µM only
Main, µM+1GEM
Escape, µM+1GEM
GEMb
µM
cathode
GEMt
γ
γ
γ
Fe55
2mm
2mm
2mm
#events

---
Micromegas + GEM
Characterisation
- Many field parameters
- Gain factorisation:
- Factorisation well understood (collection and extraction efficiencies)
- Effective gains up to a few 10,000
matrix{ {} # g_{µM}(V_{mesh}) font sans {T}{}_{µM}(color red {E_{trans}^{b}}) ## {} times {} # font sans {E}{}_{GEM}(color red {E_{trans}^{b}}) g_{GEM}^{b}(V_{GEM}^{b}) font sans {C}{}_{GEM}(color blue {E_{trans}^{t}}) ## {} times {} # font sans {E}{}_{GEM}(color blue {E_{trans}^{t}}) g_{GEM}^{t}(V_{GEM}^{b}) bold {font sans {C}{}_{GEM}(color green {bold E_{drift}^{t}})} }
(1)
(2)

---
Cosmic Ray Test
- Simple scintillator coincidence trigger
  - top/bottom coincidence
- Pressure from 0.5 to 2 bar
- Two planes readout
  - X and Time (Z)
  - Y and Time (Z)
- Track reconstruction and matching

---
Raw data, X strips Y strips
Reconstructed tracks

---
Characterisation with traversing cosmic rays
- Charge distribution from through tracks
  - easy access to drift velocity, gain and gas quality
electron absorption
total charge [ADC]
time [30ns bins]
Length / Vdrift
total charge deposit / track

---
Gain in cosmic run
- Preliminary gain study
  - compatible with test box results
  - data to be processed to optimize field configuration

---
Status and Outlook
- Status
  - Encouraging simulations
  - Operational demonstrator
  - Scheduled test in polarised photon beam (NewSUBARU)
- Outlook
  - Upcoming beam test for concept validation
  - High pressure operation improvements (small gap)
  - Developments for space operation:
    trigger, gas stability, radiation hard electronics

---
Dreaming of the future
10MeV photon
100MeV photon
3m

---
Backup

---
Space Challenges
- Trigger
  - heavy cosmic ray background (mostly protons)
  - non directional signal
  - self triggered TPC (AGET electronics)?
  - scintillators/silicon for T0
- Gas stability
  - maintained purity over several month/years
  - closed circuit purification loop?
- Radiation hard electronics

---
Gain micromegas + GEM
absolute GEM gain measured up to ~10 (limited by dynamic range of ADC)
Maximum gain ~30 (extrapolated)
Micromegas gain up to ~2000
Total gain up to ~40,000

---
Track matching

---
Science case example:
Blazars
- Separating processes
  - Leptonic synchrotron self Compton (SSC)
  - Hadronic proton synchrotron
- Polarisation can give the answer
  - no difference in X
  - visible in gamma
1MeV
1GeV
H. Zhang and M. Böttcher,
A.P. J. 774, 18 (2013)

---
Polarimetry
- Polarimetry capabilities depend on many parameters
  - energy, exposure, detector size, gas pressure...
- A simple example was used
  - Crab-like source, 1 year
  - size=1m3, resolution=1mm
  - exposure fraction=1, efficiency=1

---
Expected sensitivity
- At lower energies
  - E<~100MeV
  - up to 2 orders of magnitude improvement
- Higher energy
  - E>100MeV
  - Limited by low cross-section
  - still better than FERMI up to 400MeV
D. Bernard,
NIM A 701 (2013) 225
FERMI pass7
liquid
10bar
1bar
heavy
background
limited
statistics