## Slide 1
Status of the Fluka-based CALET simulation
Paolo Maestro
CALET Modeling & simulation meeting
GSFC 23-25/05/2012

## Slide 2: Outline
Upgrade to Fluka 2011.2 from Fluka 2008.3
Geometry, beam particles, physical processes
Data output: unified data format
First test of MC production in GRID.
On-going studies using Fluka simulated data:
  Benchmark tests with nuclei, electrons and protons to compare Fluka, Epics and Geant4 (see F. Palma’s presentation).
  Particle identification capability with CHD. Measurements of CR secondary nuclei (e.g.: B/C, see S. Bonechi’s talk).
  e/p discrimination (see my talk).
100 GeV e-

## Slide 3: Geometry
CHD
IMC
TASC
Text card (calet.geo) with geometry description is used as input by Fluka. Definition of shapes and dimensions of each region, volumes position in space, material assignment to volumes.
flukaGUI is a tool to visualize the implemented geometry and debug the text card, and inspect the USRBIN standard output files generated during a simulation.
No support structure for CHD, IMC and TASC is implemented at the moment. Need info from CAD
Detector | # layers | segmentation | Material | Segment size (mm) | Density g/cm3
CHD | 2 layers | 14 paddles/layer | PVT (C9H10) | 32x10x448 | 1.032
IMC (absorber) | 7 layers |  | W | 3: 448x448x0.7 2: 384x384x0.7 2: 320x320x3.5 | 19.32
IMC (active) | 8 layers | 448 Scifi/layer | Polystyrene(C8H8) | 1x1x448 | 1.035
TASC | 12 layers | 16 crystals/layer | PbWO4 | 20x20x320 | 8.30

## Slide 4: Particles source
Particles: electron, positron, photons, nuclei (A and Z can be set by the user)
Energy/momentum options:
- Fixed kinetic energy or momentum
- Random extraction in a user-defined energy range: uniform or from a power-law spectrum
Possible implementation of spectral features (e.g. for CR electrons)
Spatial distribution of the particle beam:
- fixed incidence point
- uniform generation inside a rectangular XY area placed at a given Z
- uniform generation on a sphere
Beam direction: - fixed (user defines the X and Y cosines)
- isotropic generation on a sphere for acceptance study
  In the particle generator, it is possible to define and set some acceptance criteria for events generated on a sphere, in order to reduce the simulation time avoiding propagation of particles with generated position/direction not satisfying the criteria. Keep track of the number of rejected particles.
  IETYPE particle crossing 1- bottom IMC layer
  2- top and bottom IMC layers,
  3- top CHD,
  4- (top CHD && bottom IMC) OR (bottom IMC && bottom TASC)

## Slide 5: Physical processes
In a Fluka simulation with option CALORIMETRY/PRECISION activated:
All e.m. processes ON
Detailed photoelectric edge treatment and fluorescence photons activated
Low energy neutron transport on down to thermal energies included
Particle transport threshold set at 100 keV, except for e+ e- and gamma @ 1 keV
Multiple scattering threshold at minimum allowed energy, for both primary and secondary charged particles
Delta ray production ON with threshold 100 keV
Accurate treatment of multiple Coulomb scattering and ionization fluctuations for hadrons/muons (to handle some challenging problems such as electron backscattering and energy deposition in thin layers even in the few keV energy range)
Heavy particle e+/e- pair production activated with full explicit production
Heavy particle bremsstrahlung activated with explicit photon production above 300 keV
Muon photonuclear interactions activated with explicit generation secondaries
Heavy fragment transport activated
Hadron inelastic nuclear interactions. The FLUKA hadron-nucleon interaction models are based on resonance production and decay below 5 GeV/c (PEANUT package), and on the Dual Parton Model (DPM) above (<20 TeV).
Nucleus (Ions)-Nucleus interactions are treated through interfaces to external event generators
5 GeV/n - 10 PeV: DPMJET-III
0.1 - 5 GeV/n: modified RQMD
Transport time cutoff for neutrons set to 1000 ns to discard thermal neutrons in showers

## Slide 6: Fluka Data output
Fluka provides standard binary output files.
- Flexible (user may choose which quantity to score, in which region, for all particles or only a given type).
- Formatted in a compact array, they are written during simulation and must be post-processed by the user with standard Fortran routines.
File types implemented for Calet simulation:
EVENTBIN: scores energy or star densities in a binning structure independent from the geometry, and prints the binning output after each "event”. Used for energy deposited in CHD paddles, IMC fibers and TASC crystals, event-by-event.
EVENTDAT: prints event by event the scored star production and/or energy deposition in each region, and the total energy balance, energy leaking out of TASC from bottom and lateral sides for both neutral and charged particles
USERDUMP a user-defined collision file. It stores:
- parameters of the primary particle (type, energy, generation position and direction)
- first interaction point (hadronic inelastic collisions for p, nuclei, pair production for e.m. showers)
- each backscattered particle track (kinetic energy, direction, particle type, age, deposited energy,
entrance point, direction, generation number) crossing CHD if it or its daughters deposit
some energy in CHD.
- energy transported by neutral and charged particles leaking off of the instrument

## Slide 7: From Fluka output to unified TTree format
After the simulation, the standard output files are processed by a C++ program which reads the arrays stored in the binary files and writes the information in a ROOT TTree, and then in a TFile.
The conversion program is based on 3 libraries:
- libReadCalet containing the definition of the formats of the different Fluka binary files.
General purpose library independent on the specific application (i.e. detector geometry).
- libMCEvent contains the definition of the classes written in the ROOT TTree.
Unified data format provided by JC, equivalent to Level-2 data (as defined in DPAP)
- libCaletDB to convert volumes ID in Fluka to real enumeration (Layer#, Fiber#, Log#, coordinates,etc.)
Information stored in the TTree:
- collection of hits (CHD, IMC, TASC) from EVENTBIN are written in TClonesArray of
TEnergyDeposit* objects contained in TMCEvent class.
- Primary particle parameters and first interaction point from USERDUMP are written in
TincidentParticle.
- Albedo particle tracks crossing CHD stored in USERDUMP are written in a TClonesArray
of TParticleEnergyDeposit* objects contained in TMCEvent class.
- Energy balance in the detectors (deposited energy, e.m. energy, energy leaking out, transported by
neutron, gamma etc.) from EVENTDAT are written in fENOut, FECOut and fEBalance arrays of
TMCEvent class.

## Slide 8: First test using FLUKA CALET MC in GRID
I got a GRID certificate and register in GLAST VO.
I developed:
  scripts and C++ programs to write automatically FLUKA cards, copy software packages to the GRID and submit jobs.
  scripts to retrieve and store simulated data.
Production period: ~ 20 days in Dec. 2011.
~20000 jobs submitted.
~2.3×106 events produced.
Inefficiency due to the grid infrastructure (no. produced/requested events) ~10%
Isotropic generation
Power-law spectrum E>1 TeV