## Slide 1
Status of H- / H+ source for ELENA
Cosy‘s „IBA source I“ for negative and positive ions
14. 6. 2012 | Ralf Gebel

## Slide 2
Ion sources at COSY
The ELENA source
Preparations
Status and outlook
Discussion
Outline

## Slide 3
The COSY facility
Polarized p-, d- beams up to 3.7 GeV/c phase-space cooling
PAX

## Slide 4
The COSY injector with ion sources
Wien filter
Lamb shift
BR
3 operational ion sources @ 4.5 keV/u (CBS incl. a Cs+ source @ ~45 keV)

## Slide 5
2 identical set-ups
Installation of unpolarized ion sources
AEA/IBA injector for H- and D-
Connection to LEBT

## Slide 6
Verified for H- and D- at COSY
At Cosy in operation from 1996 to 2003: ~ 10000 h
IBA‘s ion source specification
Ion source body
Specs from the IBA brochure

## Slide 7
Filament
PM decapole
Magnetic filter
Puller electrode
The negative ion source

## Slide 8
Filament holder
Extraction PM decapole
Isolator
Beam line
The positive ion source

## Slide 9
Schematic view of the source

## Slide 10
Arc Current 30 – 40 A
Arc Voltage 100 – 120 V
Gas Flow < 0.1 mbar ℓs-1
Bias Voltage 2.0 – 2.4 V
Bias Current 1.0 – 2.5 A
Filament Current 45 - 55 A / filament
Beam Current H- 5 – 8 mA
D- 1 – 3 mA
Beam Energy 25 keV H- / D-
Electron trap current 25 – 30 mA
Divergence (1/e half angle) 15 mrad
Emittance (normalized rms) <0.1mmmrad
Modifications:
High Voltage Transistor Switches
High Voltage Terminal
Puller (extraction electrode)
Rc
30kV
40mA
HV PS
Puller
Arc PS
Puller PS
Filament PS
3 Filaments
Electron
suppressor
Plasma
grid
Cusp
body
Ion Source Power Supply
Mains
Electron
Sup. PS
High Voltage
Transformer
Local Control
System
To External
Control System
Optic fiber
link
Safety Cabinet
19" Cabinet
(ref. to H.V.)
Tube used
for output cables
HTS
HTS
Arrangement of power converters

## Slide 11
Replacement of high voltage transistor switches
  Push-pull switches (or full bridge) from Behlke
  Fixed pulse width?
Investigate the need for
  buncher
  post acceleration
Modification for pulsed operation

## Slide 12
Investigations for negative and positive ions
Use a negative ion source with stripper
Test operation of IBA source for proton delivery
Post acceleration / Drift tube or „Tandem“ operation
Vacuum separation
Negative and positive ions

## Slide 13
Horizontal injection
  Length > 2 m
  Vacuum separation might be an issue
Vertical injection
  Small footprint
  Virtually no limit for drifts and vacuum separation
  Needs 90° deflector for 100 keV beams
Optional ion source arrangement

## Slide 14
Cs+ source
Part of the
COSY
Pol. Ions Source
-> available
spare parts and
prototypes
A „100 keV“ ion source at COSY

## Slide 15
Faraday cage for use at the polarized ion source
High voltage cabinet for the (Cs+ ) source

## Slide 16
Vacuum system
Diagnostics for:
Current
Profiles
Viewer
-> for commissioning
Test bench for ion sources

## Slide 17
Preparation for the source
Vacuum chamber and floor space preparation
Transformer and power supplies
Parts and boxes #1

## Slide 18
Preparation for the source
90° deflector
100 kV Isolator and ion source parts
Parts and boxes #2

## Slide 19
Refurbishment started
Floor space and infrastructure is prepared
Identification and preparation of components
  Ion source parts
  Chambers, isolators …
  Vacuum pumps, valves ...
  Power supplies (JEMA, FuG etc. )
  Control system (Siemens PLC)
  Documentation …
Status

## Slide 20
Fix final configuration and parameter ranges
Install refurbished source on test bench
  Check performance for pos. and neg. ions in 2012
Design and realization of the final set-up (100 keV, vert. or horiz.)
Outlook