## Slide 1
Test bench for Linac4 commissioning at 30-50-100 MeV
JB Lallement
Linac4 BCC meeting – 14/06/2012

## Slide 2
L4 Commissioning
The Linac4 commissioning will be divided into several stages :
Structure | Commissioning
Ion Source | Diagnostic tank and emittance meter.
LEBT | 
RFQ | 3 MeV test bench – Straight and spectrometer lines.
MEBT | 
DTL 1 | 
DTL 2-3 | 50-100 MeV test bench
CCDTL | 
PIMS | L4Z – Permanent diagnostics
TL | Permanent diagnostics – LBE/LBS

## Slide 3
Planning
The test bench will be used for :
  Commissioning of DTL tanks 2-3
  Commissioning of CCDTL.
30-50 MeV Dec 2013.
100 MeV March 2014.
Test bench equipment available 3 month in advance for surface assembly, alignment & tunnel assembly !

## Slide 4
Layout
Tank 1
Tank 2
Tank 3
Test bench
CCDTL
…
CCDTL
Test bench
In both cases, the test bench
is located after the intertank !
Dump
EMQ
EMQ
235.5 mm
100 mm
105 mm
105 mm
563 mm
450 mm
700 mm
950 mm
273 mm
BSM
Pick Up
SEMGrid / WS
Steerers
2645.5 mm
Aperture radius :
20 mm up to 2nd EMQ
30 mm up to dump.
BCT
2 Pick-ups for Time Of Flight.
1 BCT for transmission.
3 Profile monitors for emittance reconstruction.
Bunch Shape Monitor.
2 EMQs (L4 spares).
2 Steerers (L4 spares).

## Slide 5
Time of flight
Not possible to install a spectrometer inside the high energy part of the tunnel.
Time of flight using 3 BPMs : 1 intertank and 2 on the test bench.
TOF measurements will be calibrated during the 3 MeV commissioning.
Will be used to set phase and voltage of the cavities.
Chart: Tscope (°)
With PUs 1&2

## Slide 6
Time of flight
Not possible to install a spectrometer inside the high energy part of the tunnel.
Time of flight using 3 BPMs : 1 intertank and 2 on the test bench.
TOF measurements will be calibrated during the 3 MeV commissioning.
Will be used to set phase and voltage of the cavities.
with ΔL = 1 mm & Δt = 1°, and L 2.5 m
With PUs 1&3
Chart: Tscope (°)

## Slide 7
Emittance Reconstruction (1)
Emittance reconstruction using the 3 profiles method.
3 profile monitors (WS or SG) required at appropriate location :
  60° phase advance between the monitor.
Can be confirmed with the 3 quad settings method.
Chart: Z (m)
Example at 30 MeV for horizontal plane.

## Slide 8
Emittance Reconstruction (2)
Chart: Z (m)

## Slide 9
Emittance Reconstruction (3)
Forward method needed for an accurate emittance reconstruction, depending on space charge effects.
  Classic 3 monitor method.
  Iterative process with multi-particle tracking codes.
Examples : 30 and 50 MeV… @ 30 MeV, the beam is debunched…
30 MeV | Ref. Beam | Emit. Recons. | Forward Meth
Alpha X | 1.21 | 1.29 | 1.21
Beta X | 0.49 mm/mrad | 0.49 mm/mrad | 0.49 mm/mrad
ϵ X Norm. RMS | 0.28 mm.mrad | 0.28 mm.mrad | 0.28 mm.mrad
50 MeV | Ref. Beam | Emit. Recons. | Forward Meth
Alpha Y | 2.77 | 0.97 | 2.69
Beta Y | 1.69 mm/mrad | 0.67 mm/mrad | 1.62 mm/mrad
ϵ Y Norm. RMS | 0.29 mm.mrad | 0.33 mm.mrad | 0.30 mm.mrad

## Slide 10
Emittance Reconstruction (4)
50 MeV | Ref. Beam | Emit. Recons. | Forward Meth
Alpha Y | 2.77 | 0.97 | 2.69
Beta Y | 1.69 mm/mrad | 0.67 mm/mrad | 1.62 mm/mrad
ϵ Y Norm. RMS | 0.29 mm.mrad | 0.33 mm.mrad | 0.30 mm.mrad

## Slide 11
Emittance Reconstruction (4)
Beam sizes at profile monitors:
RMS Beam sizes (mm) |  | Monitor 1 |  | Monitor 2 |  | Monitor 3 | 
30 MeV | X/y | 1.31 | 1.73 | 0.69 | 2.95 | 1.63 | 4.69
 | Y/x | 1.28 | 1.59 | 0.79 | 2.65 | 1.49 | 4.18
50 MeV | X/y | 1.37 | 1.66 | 0.51 | 2.85 | 1.78 | 4.71
 | Y/x | 1.23 | 1.26 | 0.73 | 2.00 | 1.40 | 3.37
100 MeV | X/y | 0.92 | 3.68 | 0.54 | 5.10 | 1.26 | 7.14
 | Y/x | 0.94 | 2.72 | 0.61 | 3.45 | 1.20 | 4.56
Simulations of the emit. reconstruction done with:
Wire Scanner 0.1 mm wire spacing and 40 µ width.
SEM Grids 0.4 mm wire spacing and 40 µ width.
Noise and background added

## Slide 12
Conclusion / Discussion
All the test bench devices ready and available in Sept.- Oct. 2013.
What can be re-use from 3 MeV test bench?
Compatibility with Installation of CCDTL 3 and PIMS 4 ?
Magnets : We will use the L4 spares (2 EMQ & 2 correctors).
Diagnostic list :
  3 Profile monitors with 0.4 mm min resolution (use of the L4T ?).
  2 Pick-Ups compatible for 30-100 MeV (3 MeV spares…).
  1 BCT (the one from the 3 MeV TB…).
  The BSM.
Permanent cabling will be re-used!