## Slide 1
A Look into the Future
K Hanke / CERN

## Slide 2
upgrade of rings and
extraction / transfer from
1.4 GeV to 2.0 GeV and
increased intensity
replace main power supply,
number of smaller power
supplies, magnets, kickers,
etc.
Scope of the Upgrade
upgrade of the injection
from 50 MeV protons to
160 MeV H- and increased
intensity
re-build injection line for
160 MeV
replace injection septum by
stripping foil
injection bumps
diagnostics
…
160 MeV
2 GeV

## Slide 3
Upgrade of the Injection for Linac4
why re-building the injection region?
increased energy from 50 MeV to 160 MeV with Linac4
reduce space-charge effects at PSB injection
injection of H- ions rather than protons
significantly reduce injection losses (at the moment about 50% of the beam is lost on the injection septum!)
more flexibility in tailoring emittances by transverse phase space painting

## Slide 4
Present Multiturn Injection
horiz. beam momentum
horiz. co-ordinate
septum
closed orbit at injection (t1)
PSB closed orbit
closed orbit
after one turn (t2)
closed orbit after
second turn (t3)
etc.
as this process takes place, subsequent linac
beam “slices” are injected, with increasing
oscillation amplitude around the instantaneous
closed orbit (“horizontal stacking”)
beamlets are now “polygons”, as they
have undergone several cuts
they spiral up around the (moving)
closed orbit, leading to a density
distribution which is dense in the core
and less dense in the outer part
1
3
2
4
5
6
7

## Slide 5
Charge Exchange Injection Principle

## Slide 6
Remove obsolete BI.DIS Pb
New BI.SMV, 4 mm thick septum and 70 mm horizontal aperture for ~165 mrad @ 160 MeV with associated new pulse generator.
~0.36 Tm required from BI.BVT for ~175 mrad @ 160 MeV
Modify BI.DIS for 4.3 mrad @ 160 MeV
Performance increase of 1.9 in ∫B•dl of
BI.DVT30, BI.QNO30, BI.QNO40, BI.DVT40.
Injection Line for 160 MeV H-
W. Weterings

## Slide 7
new distributor
Injection Line Hardware
new vertical septum

## Slide 8
BSW1 Septa
BSW2 Merging Dipoles
Stripping Foil System
&
Beam Observation
Vacuum manifold
BSW 3 & 4 Dipoles
Existing PSB Dipole Magnets
Internal H0 Dump
3D Layout of new Injection Region
W. Weterings

## Slide 9
Present and Future Injection Region
B. Goddard

## Slide 10
from the closing remarks of
Review on PSB 160 MeV H- Injection
9-10 November 2011
“The world’s most complex ring injection system is about to become more complex…”
“But if anyone can do it, CERN can”

## Slide 11
Upgrade of the Booster to 2 GeV
study launched following Chamonix 2010
 feasibility, cost & time lines confirmed
RCS alternative studied following Chx. 2011
Booster option retained
3rd energy upgrade:
from 800 MeV to 1 GeV (1988)
from 1 GeV to 1.4 GeV (1999)
from 1.4 GeV to 2.0 GeV (LS2)
- no technical showstoppers identified
however a number of equipment and
systems need to be changed or upgraded
- high-impact items: MPS, RF, kickers, septa, …

## Slide 12
Expected Performance Gain with 2 GeV
LASLETT TUNE SHIFT
if we assume that:
the optics at the PS injection remains the same
the bunch length does not change

## Slide 13
Booster spare magnet undergoing stress tests
Main Magnets
main magnets can operate at field levels 30% higher than today
modifications needed:
- shimming
- retaining plates
- cooling circuits
Booster 2 GeV Upgrade: Magnets

## Slide 14
Reference
magnet
Ring 2&3
GND
MPS B
2500V
5500A
QFO
600V
450A
QDE
600V
450A
GND
MPS A
2500V
5500A
64 BHZ
Rings 1&4
128 QFO
Rings
1,2,3&4
64 QDE
Rings
1,2,3&4
64 BHZ
Rings 2&3
Reference
magnet
Ring 1&4
Ring 1 B-filed
measurement
Ring 2 B-filed
measurement
Main Power Supply
present converter cannot deliver more than 1.4 GeV
POPS-type converter proposed (capacitor bank)
divide machine in 2 circuits (inner and outer rings)
will make R 1+4 trim power supply obsolete
new building needed
Booster 2 GeV Upgrade: Power

## Slide 15
Booster 2 GeV Upgrade: RF System
Finemet cavity test installation in the PSB
complete upgrade of the Booster high-level
RF to new Finemet cavities
development of a prototype system (collaboration
with KEK-RF team)
installation of a first test cavity
in PSB during winter stop 2011-2012
upgrade program for the LL RF
M. Paoluzzi

## Slide 16
first beam captured and accelerated
26 April 2012

## Slide 17
Booster 2 GeV Upgrade: Other items
safety
vacuum
controls
dump and beam stopper
electrical installations
cooling and ventilation
transport and handling
civil engineering
beam dynamics
instrumentation
extraction and transfer to PS
radiological protection
interlocks
commissioning
survey
almost a new machine

## Slide 18
1972
Many thanks for your attention
and for your support during
the years to come!