## Slide 1
Measurement of elastic scattering with ALFA
– and the many steps before
Sune Jakobsen
On behalf of the ATLAS collaboration
Low-X 2012

## Slide 2
Measurement of elastic scattering with ALFA
Low-X 2012
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Sune Jakobsen
ALFA Installation Triggering Beam based alignment β* = 90 m campaign 2011 Summary and plans for 2012
Agenda
ALFA detector system
Triggering of ATLAS by ALFA
Beam based alignment (scraping)
β* = 90 m campaign 2011- determination of total cross section
Summary and plans for 2012
2/18
Installation of ALFA in 2011

## Slide 3
Measurement of elastic scattering with ALFA
Low-X 2012
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Absolute Luminosity For ATLAS - ALFA
Sune Jakobsen
Beam pipe
Beam pipe
Approach the beam to few mm with Roman Pot
Only used in dedicated high β* runs
3/18
ALFA Installation Triggering Beam based alignment β* = 90 m campaign 2011 Summary and plans for 2012

## Slide 4
Measurement of elastic scattering with ALFA
Low-X 2012
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Sune Jakobsen
ALFA detector
500 µm scintillating fibers
Aluminum coating
4/18
ALFA Installation Triggering Beam based alignment β* = 90 m campaign 2011 Summary and plans for 2012

## Slide 5
Measurement of elastic scattering with ALFA
Low-X 2012
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Sune Jakobsen
ALFA detector
Main detector
Main detector plan
Staggering of plans
4/18
ALFA Installation Triggering Beam based alignment β* = 90 m campaign 2011 Summary and plans for 2012

## Slide 6
Measurement of elastic scattering with ALFA
Low-X 2012
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Sune Jakobsen
ALFA detector
Main detector
Overlap detector
Overlap detector plan
Overlap detector principle on slide 15
4/18
ALFA Installation Triggering Beam based alignment β* = 90 m campaign 2011 Summary and plans for 2012

## Slide 7
Measurement of elastic scattering with ALFA
Low-X 2012
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Sune Jakobsen
ALFA detector
Main detector
Overlap detector
Fiber connector
MultiAnode PhotoMultiplier Tube (MAPMT)
64 individual channels
MAPMT channel
4/18
ALFA Installation Triggering Beam based alignment β* = 90 m campaign 2011 Summary and plans for 2012

## Slide 8
Measurement of elastic scattering with ALFA
Low-X 2012
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Sune Jakobsen
ALFA detector
Main detector
Main trigger tiles
Overlap trigger tiles
Overlap detector
Fiber connector
Main trigger scintillator tile
Overlap trigger scintillator tiles
4/18
ALFA Installation Triggering Beam based alignment β* = 90 m campaign 2011 Summary and plans for 2012

## Slide 9
Measurement of elastic scattering with ALFA
Low-X 2012
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Sune Jakobsen
ALFA detector
Main detector
Main trigger tiles
Overlap trigger tiles
Overlap detector
Fiber connector
Main trigger scintillator tile
Overlap trigger scintillator tiles
Trigger fiber connector
4/18
ALFA Installation Triggering Beam based alignment β* = 90 m campaign 2011 Summary and plans for 2012

## Slide 10
Measurement of elastic scattering with ALFA
Low-X 2012
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Sune Jakobsen
ALFA Roman Pot
Separates the detector from the ultra high beam vacuum
Ferrite
Roman Pot window
Room for overlap detectors + trigger
Wall in front of the main detector
Secondary vacuum inside (detector side) to keep window flat
Window thickness 200 µm
5/18
ALFA Installation Triggering Beam based alignment β* = 90 m campaign 2011 Summary and plans for 2012

## Slide 11
Measurement of elastic scattering with ALFA
Low-X 2012
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Station installation in LHC
Sune Jakobsen
6/18
Palfinger with ALFA station
Positioning of the station on the foot
Bake out equipment installed on the ALFA stations and the beam pipe
ALFA Installation Triggering Beam based alignment β* = 90 m campaign 2011 Summary and plans for 2012

## Slide 12
Measurement of elastic scattering with ALFA
Low-X 2012
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Detector installation
Sune Jakobsen
7/18
All detectors installed without problems
Custom made tools used
Very delicate due to gaps between detector and Roman Pots of about 100-200 µm
Detector on lifting table
ALFA Installation Triggering Beam based alignment β* = 90 m campaign 2011 Summary and plans for 2012

## Slide 13
Measurement of elastic scattering with ALFA
Low-X 2012
8/18
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Sune Jakobsen
Survey in LHC to calibrate movement system
ALFA Installation Triggering Beam based alignment β* = 90 m campaign 2011 Summary and plans for 2012

## Slide 14
Measurement of elastic scattering with ALFA
Low-X 2012
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Delay of ALFA trigger signals
Sune Jakobsen
9/18
The particles have to travel 240 m (~800 ns) from the interaction point before reaching ALFA.
The trigger signals has to travel back to ATLAS.
Special air-core cables used with signal speed of 91 % c.
Signals arrives 500 ns later the normal ATLAS triggers, so a special latency/buffer setting has to be used when ALFA is included in the global ATLAS trigger.
Lemo cable
Air-core cable
ALFA Installation Triggering Beam based alignment β* = 90 m campaign 2011 Summary and plans for 2012

## Slide 15
Measurement of elastic scattering with ALFA
Low-X 2012
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Current logic for main triggers
Sune Jakobsen
10/18
ALFA Installation Triggering Beam based alignment β* = 90 m campaign 2011 Summary and plans for 2012

## Slide 16
Measurement of elastic scattering with ALFA
Low-X 2012
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Sune Jakobsen
Current logic for main triggers
10/18
ALFA Installation Triggering Beam based alignment β* = 90 m campaign 2011 Summary and plans for 2012

## Slide 17
Measurement of elastic scattering with ALFA
Low-X 2012
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Sune Jakobsen
IP
B7L1U
B7L1L
A7L1U
A7L1L
A7R1U
A7R1L
B7R1U
B7R1L
Beam pipe
Elastics15 (B7L1U or A7L1U) and (A7R1L or B7R1L)
Elastics18 (B7L1L or A7L1L) and (A7R1U or B7R1U)
Single_Diffraction5 B7L1U and A7L1U
Single_Diffraction6 A7R1L and B7R1L
Single_Diffraction7 B7L1L and A7L1L
Single_Diffraction8 A7R1U and B7R1U
or
or
Examples of Look-Up-Tables
11/18
ALFA Installation Triggering Beam based alignment β* = 90 m campaign 2011 Summary and plans for 2012

## Slide 18
Measurement of elastic scattering with ALFA
Low-X 2012
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Sune Jakobsen
IP
B7L1U
B7L1L
A7L1U
A7L1L
A7R1U
A7R1L
B7R1U
B7R1L
Beam pipe
Elastics15 (B7L1U or A7L1U) and (A7R1L or B7R1L)
Elastics18 (B7L1L or A7L1L) and (A7R1U or B7R1U)
Single_Diffraction5 B7L1U and A7L1U
Single_Diffraction6 A7R1L and B7R1L
Single_Diffraction7 B7L1L and A7L1L
Single_Diffraction8 A7R1U and B7R1U
or
or
Examples of Look-Up-Tables
11/18
ALFA Installation Triggering Beam based alignment β* = 90 m campaign 2011 Summary and plans for 2012

## Slide 19
Measurement of elastic scattering with ALFA
Low-X 2012
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Sune Jakobsen
IP
B7L1U
B7L1L
A7L1U
A7L1L
A7R1U
A7R1L
B7R1U
B7R1L
Beam pipe
Elastics15 (B7L1U or A7L1U) and (A7R1L or B7R1L)
Elastics18 (B7L1L or A7L1L) and (A7R1U or B7R1U)
Single_Diffraction5 B7L1U and A7L1U
Single_Diffraction6 A7R1L and B7R1L
Single_Diffraction7 B7L1L and A7L1L
Single_Diffraction8 A7R1U and B7R1U
Examples of Look-Up-Tables
11/18
ALFA Installation Triggering Beam based alignment β* = 90 m campaign 2011 Summary and plans for 2012

## Slide 20
Measurement of elastic scattering with ALFA
Low-X 2012
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Sune Jakobsen
IP
B7L1U
B7L1L
A7L1U
A7L1L
A7R1U
A7R1L
B7R1U
B7R1L
Beam pipe
Elastics15 (B7L1U or A7L1U) and (A7R1L or B7R1L)
Elastics18 (B7L1L or A7L1L) and (A7R1U or B7R1U)
Single_Diffraction5 B7L1U and A7L1U
Single_Diffraction6 A7R1L and B7R1L
Single_Diffraction7 B7L1L and A7L1L
Single_Diffraction8 A7R1U and B7R1U
Examples of Look-Up-Tables
11/18
ALFA Installation Triggering Beam based alignment β* = 90 m campaign 2011 Summary and plans for 2012

## Slide 21
Measurement of elastic scattering with ALFA
Low-X 2012
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Sune Jakobsen
IP
B7L1U
B7L1L
A7L1U
A7L1L
A7R1U
A7R1L
B7R1U
B7R1L
Beam pipe
Elastics15 (B7L1U or A7L1U) and (A7R1L or B7R1L)
Elastics18 (B7L1L or A7L1L) and (A7R1U or B7R1U)
Single_Diffraction5 B7L1U and A7L1U
Single_Diffraction6 A7R1L and B7R1L
Single_Diffraction7 B7L1L and A7L1L
Single_Diffraction8 A7R1U and B7R1U
Examples of Look-Up-Tables
11/18
ALFA Installation Triggering Beam based alignment β* = 90 m campaign 2011 Summary and plans for 2012

## Slide 22
Measurement of elastic scattering with ALFA
Low-X 2012
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Sune Jakobsen
IP
B7L1U
B7L1L
A7L1U
A7L1L
A7R1U
A7R1L
B7R1U
B7R1L
Beam pipe
Elastics15 (B7L1U or A7L1U) and (A7R1L or B7R1L)
Elastics18 (B7L1L or A7L1L) and (A7R1U or B7R1U)
Single_Diffraction5 B7L1U and A7L1U
Single_Diffraction6 A7R1L and B7R1L
Single_Diffraction7 B7L1L and A7L1L
Single_Diffraction8 A7R1U and B7R1U
Examples of Look-Up-Tables
11/18
ALFA Installation Triggering Beam based alignment β* = 90 m campaign 2011 Summary and plans for 2012

## Slide 23
Measurement of elastic scattering with ALFA
Low-X 2012
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Beam based alignment (scraping)
Sune Jakobsen
Beam pipe
12/18
Beam loss monitor
Primary collimator
ALFA Roman Pot
Goal: Find accurately the beam center relative to the Roman Pots. This allows positioning of the Roman Pots very close to and symmetric around the beam center.
Position primary collimators at a well-defined position around 4 sigma.
Move in very slowly Roman Pots until they touch the beam.
Stop by BLM signal (or very high trigger rate).
Halo
ALFA Installation Triggering Beam based alignment β* = 90 m campaign 2011 Summary and plans for 2012

## Slide 24
Track pattern for only elastic candidates
Track pattern before cuts
Simulated track pattern for elastic
Measurement of elastic scattering with ALFA
Low-X 2012
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Data taking at 90 m beta* optics
Sune Jakobsen
Goal:
Physics data to determine total cross section.
Roman Pot position:
6.5 nominal sigma (about 9 real sigma to detector edge).
Beam intensity:
1 bunch of 7E10 colliding.
13 bunches of 1E10 colliding.
1 bunch of 7E10 none-colliding.
13/18
ALFA Installation Triggering Beam based alignment β* = 90 m campaign 2011 Summary and plans for 2012

## Slide 25
Measurement of elastic scattering with ALFA
Low-X 2012
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Observations on beam quality from ALFA triggers
Sune Jakobsen
14/18
Elastic triggers
Any ALFA triggers from BC1 (large colliding bunch)
Single diffraction triggers
Any ALFA trigger from colliding bunches
Any ALFA trigger not from any bunches (after 5 BC)
Any ALFA trigger up to 5 BC after a bunch
Any ALFA trigger from none colliding bunches
About 1.4 M elastic like triggers.
About 2 M single diffractive like triggers (after pre-scale).
Only about 15 % of the “Any ALFA” triggers is from the large colliding bunch.
About 18 % of the “Any ALFA” triggers is not associated with any bunch.
About 12 % of “Any ALFA” triggers is from none colliding bunches.
ALFA Installation Triggering Beam based alignment β* = 90 m campaign 2011 Summary and plans for 2012

## Slide 26
Measurement of elastic scattering with ALFA
Low-X 2012
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Detector alignment
Relative distance of the upper and lower Roman Pot is determined using particles passing both the upper an lower “overlap detector”
The global alignment of the all detectors is made using the distribution of elastic tracks in each detector.
Sune Jakobsen
15/18
Reconstructed distance for (left) the first station from the IP and (right) the second station from the IP.
Beam
Halo
ALFA Installation Triggering Beam based alignment β* = 90 m campaign 2011 Summary and plans for 2012

## Slide 27
Measurement of elastic scattering with ALFA
Low-X 2012
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
90 m β* optics - correlations – evidence of elastic events
Sune Jakobsen
<=
Reconstructed scattering angle correlation between left and right side for elastic candidates - Vertical
=>
Reconstructed scattering angle correlation between left and right side for elastic candidates - Horizontal
<=
Reconstructed scattering angle correlation between vertical and horizontal planes combining the left and right arm of ALFA
16/18
Analysis still ongoing to publish t-spectrum and total cross section.
ALFA Installation Triggering Beam based alignment β* = 90 m campaign 2011 Summary and plans for 2012

## Slide 28
Measurement of elastic scattering with ALFA
Low-X 2012
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Summary and plans for 2012
Elastic event data for determination of the total cross section was successfully taking with a special β* = 90 m optics .
2012: Repeat total cross section measurement with β* = 90 m optics at = 8 TeV.
2012: Use the ALFA detectors for diffractive physics measurements at β* = 90 m.
Sune Jakobsen
2012 main goal: Using β* = 500-1000 m optics to try to probe the Coulomb-Nuclear interference region for luminosity and total cross section determination at = 8 TeV.
17/18
The ALFA detector system was installed in the winter shutdown 2010-2011 and is now fully integrated in ATLAS including common triggering (with special latency setting).
The Roman Pots has been aligned online with beam based alignment and offline using the distribution of elastic events and the measured relative distance of the detectors.
Correlations of scattering angles shown – Analysis to get t-spectrum and total cross section on-going.
ALFA Installation Triggering Beam based alignment β* = 90 m campaign 2011 Summary and plans for 2012
Simulated spectrum
β* = 90 m in 2011
Hope for β* = 500-1000 m in 2012

## Slide 29
Measurement of elastic scattering with ALFA
Low-X 2012
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Sune Jakobsen
18/18
Thanks for your attention
ALFA Installation Triggering Beam based alignment β* = 90 m campaign 2011 Summary and plans for 2012