## Slide 1: LOFT Project Introduction
P. Azzarello, E. Bozzo, F. Cadoux, Y. Favre, M. Pohl

## Slide 2: LOFT
ESA M-class mission candidate
Science: X-ray transients (BH etc.)
Currently in assessment phase
Study lead: SRON (NL), CAP Genève
Downselection mid 2013
Phase A/B 2013-15
Phase C/D 2015-20
Flight ~2022

## Slide 3: Top level science goals

## Slide 4: Top level science goals (2)

## Slide 5: LAD panel and module
LAD contains 6 panels, 90×343 cm2 each
Panel contains 21 modules, 29×49 cm2 each
Module contains 16 × (silicon drift detector + FEE) + n collimators + 1 MBEE
Notes: Module: 29x49 cm2
Panel: 90x343 cm2

## Slide 6: Silicon Drift Detector
Few channels/surface
3D readout, HV along sensor
Low input C, low noise
Design property of INFN for ALICE
Manufacturers:
  Canberra (for LHC)
  FBK Trento
  CSEM

## Slide 7: Some numbers
SDD dimensions: 120.84 × 72.50 × 0.45 mm3
Active area: 108.52 × 70 mm2
Pitch: 970 µm
16 channels/ASIC
7×2 ASICs/sensor
112×2 readout channels per sensor
LAD = 15 m2, ~2000 sensors
Industrial collaboration mandatory

## Slide 8: Electronic noise
Total noise requirement: <260 eV @ 6 keV for 2-anode events at EOL <200 eV @ 6 keV for 1-anode events at EOL <2 keV @ 30 keV for 2-anode events at EOL
Goal: <200 eV @ 6 keV for 2-anode events at EOL <160 eV @ 6 keV for 1-anode events at EOL
Implies electronic noise ~17 e- shared between SDD and ASIC

## Slide 9: FEE Functionality and AIV
Interface with SDD
  SDD Anode readout (ASIC): bond length
  SDD power supply (HV, MV), wrap-around cable
Interface with MBEE:
  Interface with HV, MV, digital voltage
  Digital lines
  Temperature sensor
  …

## Slide 10: Design study (FEE / MBEE)
In this design MBEE is 183mm × 297mm Alternative: split MBEE
F. Cadoux

## Slide 11: LAD module: lower side
(proposal from MSSL)

## Slide 12: FEE Prototyping
Mechanical model FEE+SDD, for thermal and vibration tests (F. Cadoux):
  Low temperature conditions (operating temperature from -60°C to -30°C), while the assembly will be done at 20°C.
  Board material, glue
FEE hybrid (Y. Favre):
  Bread board 1 using existing material, XDXL ASIC under study in Italy: test board enabling sensor readout, with the right mechanical design.
  Bread board 2 using the same board geometry, with the real LAD ASIC, produced by CNES: accommodate and evaluate final ASIC
To test the board design, thermal and vibration tests are foreseen.

## Slide 13: Breadboard with XDXL ASIC

## Slide 14: MBEE
Processing pipeline per detector half

## Slide 15: LAD data handling
MBEE: module back-end electronics
PBEE: panel back-end electronics
DHU: data handling unit

## Slide 16: SDD environment test plan
Vacuum test: test the vacuum operation compliance of the SDD detectors (high voltage on surface)
50 MeV proton irradiation test: confirm test results on leakage current achieved on the ALICE detector using a FBK detector prototype; verify X- ray spectroscopy performance after proton irradiation (DPNC, PSI)
5 MeV proton irradiation test: 5 MeV protons will stop in the center of the detector, where charge transfer occurs: verify both NIEL effects and impacts on the CTE (Charge Transfer Efficiency) (DPNC, PSI)

## Slide 17: SDD environment test plan
Soft proton irradiation test: soft (< 400 keV) protons will stop at the Si-SiO2 interface in the detector, where surface leakage current generation occurs: verify the level of leakage current increase, and possible effects on the oxide.
Debris irradiation test: a few micrometeorites and/or debris are expected to impact on the detectors in orbit; little is known about their effect on the detector functionalities.

## Slide 18: Preliminary test at PSI
Alice SDD D4 detector
50 MeV proton beam
Step | Flux (p/cm2/s) | Actual step fluence (p/cm2) | Total fluence after step completion (p/cm2) | Corresponding to
1 | 1·105 | 6.50·106 | 6.50·106 | half of the minimum
2 | 1·105 | 6.70·106 | 1.32·107 | 600 km 0° inclination
3 | 1·105 | 3.24·107 | 4.60·107 | 600 km 2.5° inclination
4 | 1·105 | 1.50·108 | 1.96·108 | 600 km 5° inclination
5 | 2·105 | 2.30·109 | 2.52·109 | 13 times the maximum

## Slide 19: Leakage currents, temp. corrected

## Slide 20: SDD measurements @Trieste
Chart: UP-half. U_bias=2370V; U_return=45 (50)V; U_grid=20V;

## Slide 21: Schedule
Assessment phase:
  Soft protons (with energy < 1 MeV): data still to be analyzed.
  Tests with 5 and 50 MeV protons on FBK sensor to be done in August at PSI.
  Complete sensor development plan with CSEM
  Complete FEE bread-board design
  Complete module level AIV plan
Down selection of M3 missions by ESA in 2013  Definition phase