## Slide 1: Field Error Tolerances for Triplet Quadrupoles of the HL-LHC Lattice V3.01 Option 4444
Yuri Nosochkov
Y. Cai, Y. Jiao, M-H. Wang (SLAC)
S. Fartoukh, M. Giovannozzi, R. de Maria, E. McIntosh (CERN)
HL-LHC Task 2.3 General Meeting
CERN, 20 June 2012

## Slide 2: Outline
Perform scaling of the measured field of the nominal LHC inner triplet (IT) quadrupoles to large aperture IT quadrupoles in the HL-LHC lattice.
Determine dynamic aperture (DA) sensitivity to the IT field errors in the HL-LHC lattice using long term tracking.
Specify field error tolerances for large aperture IT quadrupoles based on the DA sensitivities.
Lattice: HL-LHC V3.01, collision option “4444” with b*=15/15 cm at IP1 and IP5, Nb-Ti superconducting IT quadrupoles with 120 mm coil diameter and 120 T/m gradient, 7 TeV beam energy.
Code: SixTrack.

## Slide 3: Impact of low-b*
The HL-LHC V3.01 collision lattice has lower than nominal b* at IP1 (ATLAS) and IP5 (CMS) crossing points resulting in higher b-functions (~1/b*) in the IT quadrupoles. Large aperture IT quadrupoles with coil diameter of 120-150 mm are proposed to accommodate a larger beam size. A dedicated large b-modulation in the adjacent arcs is used for local cancelation of the IT non-linear chromaticity.
Impact: High b-functions in the triplet and adjacent arcs amplify the effects of IT errors and sextupole aberrations causing reduction of dynamic aperture. Crossing angle orbit in the IT quadrupoles further amplifies the field errors. New tolerances on the triplet field errors need to be specified for an acceptable DA in collision.

## Slide 4: Beta functions: Nominal LHC versus V3.01 “4444”
Nominal LHC
b* = 55/55 cm
V3.01 “4444”
b* = 15/15 cm
bmax~ 4.5km
bmax~ 21.5km
Dedicated b modulation in arcs 81,12,45,56 for IR chromaticity correction
IP5
IP1

## Slide 5: Interaction Region: Nominal LHC versus V3.01 “4444”
L*=23 m
LFFS=268m
Triplet
Separation dipoles D1/2
Matching section Q4/5/6
Proposed large aperture superconducting triplet quadrupoles Q1,Q2,Q3.
This study: coil diameter dc = 120 mm.
Nominal LHC
b* = 55/55 cm
V3.01 “4444”
b* = 15/15 cm
bmax~ 4.5km
bmax~ 21.5km

## Slide 6: Achromatic Telescopic System (ATS) for the HL-LHC
High peak beta functions in the IT quadrupoles (bmax ~ 1/b*) result in high IT chromaticity which requires strong correcting sextupoles. A dedicated b-modulation is created in the arcs adjacent to IP1 and IP5 in order to raise beta functions at the sextupoles (bsext ~ 1/b*) and increase their effect without exceeding their field limit. These sextupoles are arranged in -I pairs to cancel their geometric aberrations, and have a proper phase advance relative to the triplets for a localized correction of non-linear IT chromaticity.
IP1
IP1
Arc 81
Arc 81
Arc 12
Arc 12
barc ~ 700 m
b*=15/15cm
V3.01 “4444”

## Slide 7: Path to the new IT field error tolerances
Follow the method described in the “Phase-1” upgrade lattice study (“LHC Project Report 40” by B. Holzer).
The target minimum DA is 12-13 s when the IT multipole field correction , arc errors and correction are included. In this case, field errors are not included in the D1, D2 separation dipoles and Q4 quadrupoles (future study).
Start with the measured multipole field coefficients for the nominal IT quadrupoles.
Scale the measured field coefficients to the new reference radius (r0 = 50 mm) and new IT quadrupole coil diameter (dc = 120 mm). Name this table “target3”. Verify dynamic aperture (expected to be small due to high IT beta in the HL-LHC V3.01).
Scale the “target3” coefficients with the peak IT beta function in the HL-LHC V3.01 (bmax ~ 21.5 km). This will reduce the coefficients. Name this table “target31”.
If the “target31” minimum DA > 13 s, then relax the coefficients by scanning them between “target31” and “target3” values.
Scan the field coefficients individually to determine DA sensitivities.
Obtain tolerances by scaling all the coefficients according to their individual sensitivities until the target minimum DA is reached.

## Slide 8: Multipole field scaling in a SC quadrupole
where n=2 is for a quadrupole, etc. B2 is the main quadrupole field at r0
Note: the an,bn coefficients are defined in 10-4 units.
The an and bn values are split in two components: the “uncertainty” term (deviation from systematic) and the “random” term. Their values in the field error tables represent Gaussian sigmas for generating random errors.
Scaling with reference radius r0 does not affect dynamic aperture. Nominal r0 = 17 mm → new IT quad r0 = 50 mm.
Scaling with coil diameter dc in a SC quad (B. Bellesia, et al., Phys. Rev. ST-AB 10, 062401 (2007)). Nominal dc = 70 mm → new IT quad dc = 120 mm.
Scaling with peak IT beta function bmax to keep the IT non-linear resonance driving terms constant (S. Fartoukh, SLHC Project Report 0038). Nominal bmax = 4.5 km → new bmax = 21.5 km.

## Slide 9: Multipole field correctors in the triplet
a3, b3, a4, b4, b6 correctors
IP
The a3, b3, a4, b4, b6 correctors compensate non-linear effects from the corresponding terms of the IT field. Tolerances on these terms are expected to be relaxed.
The newest a5, b5, a6 correctors are not included in this study.
The IP optics is anti-symmetric, hence the correctors sample both x and y large betas

## Slide 10: SixTrack tracking set-up
100,000 turns
60 random error seeds for final tracking, 20 seeds for multipole coefficient scans
30 particle pairs per amplitude step (2s)
11 angles
7 TeV beam energy
initial Dp/p = 2.7e-4
tune = 62.31, 60.32
normalized emittance = 3.75 mm-rad
IT multipole field correctors to compensate a3, b3, a4, b4, b6 terms are included
(IT correctors for a5, b5, a6 terms have been added to the latest HL-LHC version, but not included in this study)
Arc errors and correction are included
No field errors in D1, D2 separation dipoles and Q4 quadrupoles (future study)

## Slide 11: Measured field error table for the nominal IT quadrupole MQXB with dc=70 mm at r0=17 mm
skew | uncertainty | rms |  | normal | uncertainty | rms
a3 | 0.5235 | 0.6354 |  | b3 | 0.4135 | 0.7873
a4 | 0.4432 | 0.3883 |  | b4 | 0.1552 | 0.1563
a5 | 0.0874 | 0.1423 |  | b5 | 0.1142 | 0.2171
a6 | 0.2306 | 0.2637 |  | b6 | 0.2098 | 0.3088
a7 | 0.0254 | 0.0411 |  | b7 | 0.0311 | 0.0374
a8 | 0.0140 | 0.0280 |  | b8 | 0.0060 | 0.0096
a9 | 0.0127 | 0.0078 |  | b9 | 0.0085 | 0.0116
a10 | 0.0094 | 0.0179 |  | b10 | 0.0303 | 0.0086
a11 | 0.0046 | 0.0028 |  | b11 | 0.0084 | 0.0106
(G.V. Velev et al., IEEE Trans. Appl. Supercond., 17, 1109-1112 (2007))

## Slide 12: Field error table “target3” scaled from the measured table to r0=50 mm and dc=120 mm
skew | uncertainty | rms |  | normal | uncertainty | rms
a3 | 0.5239 | 0.6359 |  | b3 | 0.4139 | 0.7879
a4 | 0.7611 | 0.6667 |  | b4 | 0.2664 | 0.2683
a5 | 0.2574 | 0.4191 |  | b5 | 0.3365 | 0.6396
a6 | 1.1655 | 1.3328 |  | b6 | 1.0603 | 1.5608
a7 | 0.2203 | 0.3564 |  | b7 | 0.2701 | 0.3244
a8 | 0.2087 | 0.4162 |  | b8 | 0.0889 | 0.1423
a9 | 0.3238 | 0.2003 |  | b9 | 0.2165 | 0.2971
a10 | 0.4137 | 0.7838 |  | b10 | 1.3256 | 0.3755
a11 | 0.3457 | 0.2116 |  | b11 | 0.6340 | 0.7965
a12 | 0.1863 | 0.1863 |  | b12 | 0.1863 | 0.1863
a13 | 0.1164 | 0.1164 |  | b13 | 0.2328 | 0.1164
a14 | 0.4366 | 0.1455 |  | b14 | 0.5821 | 0.1455
These values should be achievable in the magnet design.
Values for n = 12,13,14 are added from table “ITD1_errortable_v2” (SLHC Project Report 0040).

## Slide 13: Dynamic aperture for the field error table “target3”
DAmin = 5.07s
Angle [degree]
The line represents the average aperture for 60 seeds and the error bars show the spread between the minimum and maximum aperture for 11 x-y angles
Aperture is too small

## Slide 14: Field error table “target31” scaled from table “target3” to bmax = 21.5 km
skew | uncertainty | rms |  | normal | uncertainty | rms
a3 | 0.05016 | 0.06089 |  | b3 | 0.03963 | 0.07545
a4 | 0.03334 | 0.02920 |  | b4 | 0.01167 | 0.01175
a5 | 0.00516 | 0.00840 |  | b5 | 0.00674 | 0.01281
a6 | 0.01069 | 0.01223 |  | b6 | 0.00972 | 0.01431
a7 | 0.00092 | 0.00150 |  | b7 | 0.00113 | 0.00137
a8 | 0.00042 | 0.00080 |  | b8 | 0.00015 | 0.00027
a9 | 0.00029 | 0.00019 |  | b9 | 0.00019 | 0.00024
a10 | 0.00018 | 0.00030 |  | b10 | 0.00054 | 0.00018
a11 | 0.00007 | 0.00007 |  | b11 | 0.00015 | 0.00015
a12 | 0.000016 | 0.000016 |  | b12 | 0.000016 | 0.000016
a13 | 0.000004 | 0.000004 |  | b13 | 0.000009 | 0.000004
a14 | 0.000008 | 0.000003 |  | b14 | 0.000010 | 0.000003
Coefficients are significantly reduced
(too small for realistic magnet design)

## Slide 15: Dynamic aperture for the field error table “target31”
The minimum DA is large (close to DA without IT errors).
The coefficients can be relaxed to reduce DAmin to 12-13s.
DAmin = 14.94s
Angle [degree]

## Slide 16: Individual scan of an “random” coefficients
Each coefficient is scanned between “target31” and “target3” values while all other coefficients are fixed at “target31” values.
The DA is not sensitive to the corrected a3, a4 terms.
The strongest effects are from a6, a10 terms.

## Slide 17: Individual scan of bn “random” coefficients
The b3, b4 terms are well corrected, but the b6 still affects the DA.
“DA cut” will be used later to set the coefficients for about equal impact on DA.

## Slide 18: Individual scan of an “uncertainty” coefficients
The a3, a4 terms are well corrected.
Overall, a smaller impact on DA compared to effect of “random” an.

## Slide 19: Individual scan of bn “uncertainty” coefficients
The b3, b4, b6 terms are well corrected.
High order terms are still important.

## Slide 20: Final field scaling for the target DA
We construct the tolerances, where the effects of individual coefficients on DA are about equal. This is done by setting to the values corresponding to the same DA in the individual scans using “DA cut”. The target DA is reached when the DA cut is 14.8s.
target
aperture
“target31”

## Slide 21: Tolerance table “target39” at r0=50 mm
skew | uncertainty | rms |  | normal | uncertainty | rms
a3 | 0.28701 | 0.34839 |  | b3 | 0.22675 | 0.43166
a4 | 0.39722 | 0.34797 |  | b4 | 0.13905 | 0.14002
a5 | 0.13129 | 0.02945 |  | b5 | 0.09018 | 0.07111
a6 | 0.41458 | 0.02698 |  | b6 | 0.53501 | 0.38921
a7 | 0.11063 | 0.02557 |  | b7 | 0.01031 | 0.01215
a8 | 0.10452 | 0.00820 |  | b8 | 0.02766 | 0.00557
a9 | 0.15817 | 0.01044 |  | b9 | 0.00911 | 0.00844
a10 | 0.09435 | 0.00924 |  | b10 | 0.01872 | 0.00674
a11 | 0.07756 | 0.00700 |  | b11 | 0.00820 | 0.00998
a12 | 0.05541 | 0.00354 |  | b12 | 0.00456 | 0.00363
a13 | 0.03679 | 0.00442 |  | b13 | 0.00396 | 0.00268
a14 | 0.01892 | 0.00364 |  | b14 | 0.00611 | 0.00364
The least sensitive terms could be set to large “target3” values. But in the above table “target39” we intentionally limited them to a mid-value between the “target3” and “target31” settings in order to help relaxing the other tighter terms. As an alternative, we also constructed the table “target36”, where the non-sensitive terms are set to “target3” values at the expense of somewhat tighter other tolerances.

## Slide 22: Comparison of “target3”, “target31” and “target39” tables (normalized to “target3” values)
22

## Slide 23: Dynamic aperture for tolerance table “target39”
DAmin = 12.35s
Angle [degree]

## Slide 24: Summary
DA sensitivity to individual multipole field errors in the large aperture IT quadrupoles of the HL-LHC V3.01 lattice (option “4444”) have been determined using long-term tracking in SixTrack.
The setting for the IT field error tolerances have been obtained based on analytical scaling for the new IT coil diameter and peak beta functions, and taking into account the DA sensitivity to individual multipole coefficients.
The obtained tolerances may be too tight – further optimization is needed.
This work was presented at IPAC’12, paper MOPPC020.
Next steps
Try to relax the tolerances towards the field error estimate presented by E. Todesco (E.T.) at the Hi-Lumi & LARP Collaboration Meeting, 7 June 2012:
  Set the least sensitive coefficients to the E.T. estimate – verify DA.
  Assume a5, b5, a6 terms are corrected – set to 20% of the E.T. estimate (to simulate the correction without actual correctors in tracking).
  Reduce the target minimum DA to 11s to loosen the tolerances.

## Slide 25: Back-up slides

## Slide 26: Field error table from presentation by E. Todesco
``REVIEW OF ESTIMATES OF RANDOM COMPONENTS IN THE INNER TRIPLET’’
E. Todesco, Hi-Lumi and LARP Collaboration Meeting, CERN, June 7, 2012

## Slide 27: Tolerance table “target39” scaled to r0=40 mm
skew | uncertainty | rms |  | normal | uncertainty | rms
a3 | 0.22961 | 0.27871 |  | b3 | 0.18140 | 0.34533
a4 | 0.25422 | 0.22270 |  | b4 | 0.08899 | 0.08961
a5 | 0.06722 | 0.01508 |  | b5 | 0.04617 | 0.03641
a6 | 0.16981 | 0.01105 |  | b6 | 0.21914 | 0.15942
a7 | 0.03625 | 0.00838 |  | b7 | 0.00338 | 0.00398
a8 | 0.02740 | 0.00215 |  | b8 | 0.00725 | 0.00146
a9 | 0.03317 | 0.00219 |  | b9 | 0.00191 | 0.00177
a10 | 0.01583 | 0.00155 |  | b10 | 0.00314 | 0.00113
a11 | 0.01041 | 0.00094 |  | b11 | 0.00110 | 0.00134
a12 | 0.00595 | 0.00038 |  | b12 | 0.00049 | 0.00039
a13 | 0.00316 | 0.00038 |  | b13 | 0.00034 | 0.00023
a14 | 0.00130 | 0.00025 |  | b14 | 0.00042 | 0.00025

## Slide 28: Field error table “target3” scaled to r0=40 mm
skew | uncertainty | rms |  | normal | uncertainty | rms
a3 | 0.4191 | 0.5087 |  | b3 | 0.3311 | 0.6303
a4 | 0.4871 | 0.4267 |  | b4 | 0.1705 | 0.1717
a5 | 0.1318 | 0.2146 |  | b5 | 0.1723 | 0.3275
a6 | 0.4774 | 0.5459 |  | b6 | 0.4343 | 0.6393
a7 | 0.0722 | 0.1168 |  | b7 | 0.0885 | 0.1063
a8 | 0.0547 | 0.1091 |  | b8 | 0.0233 | 0.0373
a9 | 0.0679 | 0.0420 |  | b9 | 0.0454 | 0.0623
a10 | 0.0694 | 0.1315 |  | b10 | 0.2224 | 0.0630
a11 | 0.0464 | 0.0284 |  | b11 | 0.0851 | 0.1069
a12 | 0.0200 | 0.0200 |  | b12 | 0.0200 | 0.0200
a13 | 0.0100 | 0.0100 |  | b13 | 0.0200 | 0.0100
a14 | 0.0300 | 0.0100 |  | b14 | 0.0400 | 0.0100