## Slide 1
RAL Site Networking
Robin Tasker
20 June 2012

## Slide 2
RAL Core Network
Looking Back
Tier 1 – Tier 2 via JANET
This traffic by-passes the RAL site Firewall via the Lightpath Router to the SAR
Issue on LR-SAR connection started mid December 2011
Transient problem, very difficult to diagnose with no consistent pattern
A matter of following the evidence BUT lack of resilience makes testing hard
All optics, the fibre on the path and the 10G line cards in the SAR and LR have been replaced
The problem is now resolved AND the entire infrastructure is changing
Tier 1
Centre
SAR
LR
FW
A
JANET
CERN
RAL Site

## Slide 3
RAL Core Network
Future Planning – Current Status
RAL was connected at 2*20G to the JANET core at Reading (Primary) and London (Secondary)
The physical offsite path has been moved to provide geographic resilience
The RAL connection to JANET is now operational at 2*30G with the option of 2*40G
The RAL Core Network is being refurbished in 3 Phases:
Phase 1:
  The SAR and LR routers are now replaced in a fully path and geographic resilient configuration operating at 80G around the network core
Phase 2:
  An internal “distribution fabric” is now introduced to provide internal resilience with an associated connection policy
Phase 3:
  The “security layer” will be replaced through this FY and in FY2013/14
As a part of JANET SIX, JANET are considering the use or Atlas and R89 to host RNEP equipment. For RAL this would add great JANET resilience into the infrastructure

## Slide 4
SAR
UKLR
F/W
A
Janet Primary
Janet Secondary
OPN Primary
OPN Secondary
RAL Core Network Implementation Plan
PoP and Internal Distribution Starting Point
Tier 1
BCE Access
Border Controller
VPN

## Slide 5
SAR
UKLR
F/W
A
Tier 1
Janet Primary
Janet Secondary
OPN Primary
OPN Secondary
S1
S2
VPN
BCE Access
Border Controller
R2
R4
R3
R1
RAL Core Network Implementation Plan
PoP Stage One (22 May 2012)
80G Core Network ring
Internal Distribution

## Slide 6
Janet Primary
Janet Secondary
F/W
A
UKLR
OPN Primary
OPN Secondary
S1
S2
Tier 1
VPN
BCE Access
Border Controller
R2
R4
R3
R1
RAL Core Network Implementation Plan
PoP Stage Two (Tuesday 19 June)

## Slide 7
T1
A
S1
S2
Tier 1
VPN
Janet Primary
Janet Secondary
OPN Primary
OPN Secondary
BCE Access
Border Controller
R2
R4
R3
R1
RAL Core Network Implementation Plan
PoP Stage Three (from Tuesday 3 July)
F/W
40G uplinks to core
10G uplinks to Internal Distribution

## Slide 8
T1
F/W
A
S1
S2
Tier 1
VPN
Janet Primary
Janet Secondary
OPN Primary
OPN Secondary
BCE Access
Border Controller
R2
R4
R3
R1
RAL Core Network Implementation Plan
PoP and Internal Distribution Complete

## Slide 9
T1
F/W
A
S1
S2
Tier 1
VPN
Janet Primary
Janet Secondary
OPN Primary
OPN Secondary
BCE Access
Border Controller
R2
R4
R3
R1
RAL Core Network Implementation Plan
Security Layer Scope