## Slide 1: Control Systems Under Attack !?
…about the Cyber-Security
of modern Control Systems
Dr. Stefan Lüders (CERN Computer Security Officer) Openlab Summer Student Lectures
July 23rd 2012

## Slide 2: Security in a Nutshell
Security is as good as the weakest link:
  Attacker chooses the time, place, method
  Defender needs to protect against all possible attacks (currently known, and those yet to be discovered)
  Security is a system property (not a feature)
  Security is a permanent process (not a product)
  Security cannot be proven (phase-space-problem)
Security is difficult to achieve, and only to 100%-ε.
  At CERN, every single computing resource owner defines ε !!!
BTW: Security is not a synonym for safety.

## Slide 3: Security in a Nutshell
Security is as good as the weakest link:
  Attacker chooses the time, place, method
  Defender needs to protect against all possible attacks (currently known, and those yet to be discovered)
  Security is a system property (not a feature)
  Security is a permanent process (not a product)
  Security cannot be proven (phase-space-problem)
Security is difficult to achieve, and only to 100%-ε.
  At CERN, every single computing resource owner defines ε !!!
BTW: Security is not a synonym for safety.
YOU are responsible for securing your services & systems:
  As user, developer, system expert or administrator
  As a project manager or line manager
  As part of the CERN or your experiment hierarchy

## Slide 4: Warm-Up: A small quiz
  What links to www.ebay.com?
http://www.ebay.com\cgi-bin\login?ds=1%204324@%31%33%37 %2e%31%33%38%2e%31%33%37%2e%31%37%37/p?uh3f223d
http://www.ebaỵ.com/ws/eBayISAPI.dll?SignIn
http://scgi.ebay.com/ws/eBayISAPI.dll?RegisterEnterInfo&siteid=0& co_partnerid=2&usage=0&ru=http%3A%2F%2Fwww.ebay.com&rafId=0 &encRafId=default
http://secure-ebay.com




This IS Not EVEN obvious
FOR professionals!

## Slide 5: “Control Systems” in a Nutshell
Process Control System (PCS)
Safety System

## Slide 6: Roadmap for Today

## Slide 7: “Control Systems” go “IT”...
In the past, PCS were
  largely proprietary
  stand-alone & interconnected using proprietary networks only
  accessed via modems, if at all
  using own standards, technologies & means
Today, PCS
  base on custom-of-the-shelf hardware and software (“office IT”)
  are highly inter-connected
  determine & impact widely on our daily life
Notes: 7

## Slide 8: (R)Evolution: The Past

## Slide 9: (R)Evolution: Today

## Slide 10: Control Systems for Living
…in the electricity sector
…in the oil & gas sector
…in the water & waste sector
…in the chemical and pharmaceutical industry
…in the transport sector
…for production:
  e.g. cars, planes, clothes, news
…in supermarkets
  e.g. scales, fridges
…for facility management
  electricity, water, C&V
…for accelerator controls
COBB County Electric, Georgia
Middle European Raw Oil, Czech Republic
Athens Water Supply & Sewage
Merck Sharp & Dohme, Ireland
CCTV Control Room, UK
Reuters TV Master Control Room
CERN Control Centre
The claimed No. 1 goal for cyber-security in the 21st century:
Critical Infrastructure Protection (CIP)

## Slide 11: This is how PCS can look like
Controller
Connections to sensors & actuators
Sensors & actuators
Controller

## Slide 12: PCS omitted security aspects!
In the past, PCS security was
  hidden (“security through obscurity”)
  never a real concern
  a target for nerds
Today,
  Same “office IT”-risks inherent in PCS (TCP/IP, Windows PCs, WWW & mail, C++, …)
  Same “office IT”-attackers targeting PCS (viruses/worms, saboteurs, attacker, stupidity, …)
Notes: 12

## Slide 13: Why worry? The Risk Equation
Threat
× Vulnerability
× Consequence
Risk =

## Slide 14: Who is the threat?
Attacks performed by…
  Disgruntled (ex-)employees or saboteurs
  Attackers and terrorists, but also since “Stuxnet”: (Western) countries (step-by-step instructions on BlackHat conferences; freeware hacking tools for “Script Kiddies”)
  Trojans, viruses, worms, …
Lack of robustness & lots of stupidity
  Mal-configured or broken devices flood the network
  Developer / operator “finger trouble”
Lack of procedures
  Flawed updates or patches provided by third parties
  Inappropriate test & maintenance rules / procedures

## Slide 15: Damage by Insiders?

## Slide 16: Damage by Attacker?

## Slide 17: Damage due to CI No-P?

## Slide 18: Natanz, we have a problem.

## Slide 19: Stuxnet
  SCADA PC infected via USB stick with 4(!) zero-day exploits (worth $100k-500k)
  Hide, spread & listen
  Look for STEP7. If so, BINGO Replace S7 drivers to hide & start exploiting
  Fingerprint PLC
  If right configuration, download additional code (Insider knowledge necessary!!!)
  Vary rotational speed of centrifuges to wear them out. GAME OVER.
  Lots of hype in media (“First Cyberwar”) but just logical consequence of the past
  Nothing new, apart from level of sophistication
  Stay tuned for similar attacks!!!!
Notes: Short version of the next three slides.

## Slide 20: The Workings of Stuxnet (I)
  An infected USB stick was infiltrated into the plant either by malicious act or through social engineering.
  Once inserted into a Windows PC, the stick tried to compromize the O/S with up to 4(!) zero-day exploits (worth >$100k).
  There were 4-5 evolutions starting 6/2009.
  Infected 100.000 PCs (60% Iran,10% Indonesia).
  Using “rootkit” technologies and two stolen certificates, it hid from being detected.
  It tried to infect other hosts and establish a P2P connection “home”.
So far, nothing new:
A standard, but expensive virus!

## Slide 21: The Workings of Stuxnet (II)
  Stuxnet then checked the local configuration looking for the presence of Siemens PCS7/STEP7/WINCC SCADA software.
  If so, it copied itself into the local STEP7 project folder (to propagate further).
  It replaced the S7 communication libraries (DLLs) used for exchanging data with a PLC.
  Stuxnet can now manipulate values to be send to the PLC or displayed by the SCADA.
  If not, Stuxnet got idle and would expire on 2012/06/24.
Stuxnet is now the “Man in the Middle” controlling the communication between SCADA & PLC.

## Slide 22: The Workings of Stuxnet (III)
  Next, Stuxnet was “fingerprinting” connected PLCs.
  If right PLC configuration, it downloaded/replaced code between 17 and 32 FBs & DBs.
The “Man in the Middle” made everything looked fine at the SCADA level…
This code varied the rotational speed of the centrifuges over months wearing them out and inhibiting uranium enrichment.

## Slide 23: Stuxnet was not the first one!

## Slide 24: Smart Meters: Nothing Learned?
  Use case:
  Measuring your consumption at home
  Online with the grid: Optimizing the power usage
  Publicly accessible, off-the-shelf, open networks
Risks:
  Exploitation of meter vulnerabilities: registration process, firmware, data, …
  Loss of confidentiality: customer data available to others
  Loss of integrity: manipulation of reading data
  Loss of availability: data not available in a timely manner
  Misuse as attack platform
courtesy of M. Tritschler (KEMA)

## Slide 25: Smart Meters: Nothing Learned?
  Use case:
  Measuring your consumption at home
  Online with the grid: Optimizing the power usage
  Publicly accessible, off-the-shelf, open networks
Risks:
  Exploitation of meter vulnerabilities: registration process, firmware, data, …
  Loss of confidentiality: customer data available to others
  Loss of integrity: manipulation of reading data
  Loss of availability: data not available in a timely manner
  Misuse as attack platform
courtesy of M. Tritschler (KEMA)
We had this before :
Modems in the 80’s
Windows PCs in the 90’s (before XP SP2)

## Slide 26: Why care?

## Slide 27: Mitigation: Today’s Cacophony
Using “office-IT” must also mean using “office-security technology”:
  Apply same security measures
  Inherent differences need to be taken care of separately
  Defence-in-Depth as a basis
  Influence your vendor!!!
Too many stakeholders:
  A cacophony in standards & guidelines
  A cacophony in interest
  No real directions by legislators
Notes: 27

## Slide 28: Myths about Cyber-Security
"The firewall makes you secure..."
"Network security, that's it !"
"Everything can be solved by technique !"
"More and better gadgets can solve security problems..."
"You are secure if attackers can’t get in..."
"You can keep hackers out..."
"Field devices can't be hacked..."
"IDSs can identify possible control system attacks..."
"Encryption protects you..."
"VPNs protect you..."

## Slide 29: Ground Rules for Cyber-Security
Segregate networks
Control (remote) access
Increase robustness
Patch, patch, patch!!!
Review development life-cycle
Deepen collaboration & policies
“Defence-in-Depth” protection on every layer:
device/hardware/network firmware/operating systems/network protocols software/applications user/integrator/developer/vendor

## Slide 30: Ground Rules for Cyber-Security
Segregate networks
Control (remote) access
Increase robustness
Patch, patch, patch!!!
Review development life-cycle
Deepen collaboration & policies
“Defence-in-Depth” protection on every layer:
device/hardware/network firmware/operating systems/network protocols software/applications user/integrator/developer/vendor
Control Systems use COTS IT hard/software.
Control System Cyber-Security must employ/allow for COTS IT security measures, too!

## Slide 31: Damage due to Interconnectivity?

## Slide 32: Network Segregation at CERN
Different networks for different purposes:
  …for accelerator operations
  …and for experiments
  Campus network for office computing
  Additional protective measures where needed (“VPNs”, ACLs, …)
Restrictions on Controls Networks:
  Assignment of responsibilities and usage of authorization procedures
  No Internet, no (GPRS) modems, no wireless access points or laptops
  Controlled inter-communication between networks
  Blocked incoming emails & control over visible web pages
  Controlled remote access, e.g. for maintenance, development & testing
  Traffic monitoring & intrusion detection at the gates

## Slide 33: Damage by Viruses & Worms?

## Slide 34: Patch, Patch, Patch!!!
but problematic:
  Compliance statement needed (vendor-side testing)
  Integrator might decline responsibility if PCS is touched
  PCS might need to be re-certified (e.g. SILx)
  True impact on PCS unknown: thorough on-site testing!
  Difficult (impossible?) to patch embedded devices!
CERN delegates patching:
  Passing flexibility and responsibility to the experts
  They decide when to install what on which control PC
  NOT patching is NOT an option, but delays are tolerated
  Running up-to-date anti-virus software and local firewalls is a must
  However, processes are still not optimal: Applications still depend too much on the O/S!
Prompt patching essential…

## Slide 35: Patch, Patch, Patch!!!
but problematic:
  Compliance statement needed (vendor-side testing)
  Integrator might decline responsibility if PCS is touched
  PCS might need to be re-certified (e.g. SILx)
  True impact on PCS unknown: thorough on-site testing!
  Difficult (impossible?) to patch embedded devices!
CERN delegates patching:
  Passing flexibility and responsibility to the experts
  They decide when to install what on which control PC
  NOT patching is NOT an option, but delays are tolerated
  Running up-to-date anti-virus software and local firewalls is a must
  However, processes are still not optimal: Applications still depend too much on the O/S!
Prompt patching essential…
Review you PCS.
How can you make patching easier/quicker? Do you have test systems in place?

## Slide 36: Damage due to Openness?

## Slide 37: Apply the Rule of Least Privilege
Can’t follow the “Rule of Least Privilege”:
  Default passwords still widely used – not incentive/force to change
  Backdoors might be present – not communicated to user
  Still need for shared accounts instead of personal accounts
  No modern access protection for PLCs and field devices like certificates, challenge/response, granular access control, … (The RUN-P key switch disappeared again from Siemens S7-400 PLCs)
  Difficult to integrate into standard IdM: OIM, FIM, LDAP/AD/Kerberos
  Cacophony of different solutions for remote access: Is this user or vendor driven???
CERN uses PVSS (ETM/Siemens):
  Full integration with CERN SSO/AD/LDAP (i.e. central IdP)
  Multi-factor to come (SmartChip certificates, mobile apps, Yubikeys)
  More difficult with home-grown SCADA software 

## Slide 38: Apply the Rule of Least Privilege
Can’t follow the “Rule of Least Privilege”:
  Default passwords still widely used – not incentive/force to change
  Backdoors might be present – not communicated to user
  Still need for shared accounts instead of personal accounts
  No modern access protection for PLCs and field devices like certificates, challenge/response, granular access control, … (The RUN-P key switch disappeared again from Siemens S7-400 PLCs)
  Difficult to integrate into standard IdM: OIM, FIM, LDAP/AD/Kerberos
  Cacophony of different solutions for remote access: Is this user or vendor driven???
CERN uses PVSS (ETM/Siemens):
  Full integration with CERN SSO/AD/LDAP (i.e. central IdM)
  Multi-factor to come (SmartChip certificates, mobile apps, Yubikeys)
  More difficult with home-grown SCADA software 
Review & restrict access rights. Access should be personalized. Keep passwords secret! Ask your vendor of default/hidden accounts.

## Slide 39: Damage due to lack of resilience?
CERN 2007

## Slide 40: Robustify!
Many PLCs, etc. are completely unprotected:
  Legacy & even today’s systems fail basic security scans (nmap, Nessus).
  No firewall, no anti-virus, nothing.
  Wrong defaults: everything should be disabled, first.
  Violating standards: They fulfill use-cases, but not abuse-cases.
  No data sheets of default configuration, open ports, default accounts.
  There is no certification. Nothing mandatory. (INL & Wurldtech/Archilles procedures & results are proprietary to vendors)
Understanding is the key at CERN:
  Building asset inventory & understanding dependencies
  Running vulnerability tools on everything
  Applying “Security Baselines” i.e. a contract on security with recommendations for configuration settings, protective means, procedures & training

## Slide 41: Robustify!
Many PLCs, etc. are completely unprotected:
  Legacy & even today’s systems fail basic security scans (nmap, Nessus).
  No firewall, no anti-virus, nothing.
  Wrong defaults: everything should be disabled, first.
  Violating standards: They fulfill use-cases, but not abuse-cases.
  No data sheets of default configuration, open ports, default accounts.
  There is no certification. Nothing mandatory. (INL & Wurldtech/Archilles procedures & results are proprietary to vendors)
Understanding is the key at CERN:
  Building asset inventory & understanding dependencies
  Running vulnerability tools on everything
  Applying “Security Baselines” i.e. a contract on security with recommendations for configuration settings, protective means, procedures & training
Review you field devices.
Scan them (if not in production ;-). Return failing ones to your vendor!

## Slide 42: Damage due missing procedures?
A Boeing 777 uses similar technologies to Process Control Systems

## Slide 43: Review Development Life-Cycle
Reviewing procedures for
  ...development of hardware & applications
  ...system testing
  ...deployment
  ...operations
  ...maintenance & bug fixing
  Use of software versioning systems, configuration management, and integration frameworks (e.g. Git)
Protecting operations
  Keeping development separated from operations (eventually debugging might need access to full hardware)
  Avoiding online changes for the sake of safe operations: Online changes must be authorized

## Slide 44: Damage due to Unawareness?

## Slide 45: This is a People Problem! (I)
Bringing together experts:
  Control system experts know their systems by heart – but IT concepts?
  IT people (should) know IT security – but don’t know controls!
  Synergy between both is often poorly/not really exploited!
Openly discuss vulnerabilities:
  Attackers are better networked than we are! Attackers know of vuln’s probably long before we do.
  “Responsible disclosure” also for PCS vulnerabilities.
  Create “SCADA_BugTraq” (ideally join BugTraq, CVE, & Co.).
  Deploy/train CERT/CSIRTs to understand PCS.
  More activism of the vendors needed (outside standardization bodies)!

## Slide 46: This is a People Problem! (II)
CERN aims to for a “change of culture” & “a new mind set”
  Basic awareness training to everyone, esp. newcomers
  Every owner of a computer account must follow an online security course every 3 years.
  Provisioning of static code analyzers
  Dedicated training on secure development (Java, C/C++, Perl, Python, PHP, web, ...)
  Baselines & consulting
  The Security Team as facilitator and enabler: Making security part of the overall.

## Slide 47: This is a People Problem! (II)
CERN aims to for a “change of culture” & “a new mind set”
  Basic awareness training to everyone, esp. newcomers
  Every owner of a computer account must follow an online security course every 3 years.
  Provisioning of static code analyzers
  Dedicated training on secure development (Java, C/C++, Perl, Python, PHP, web, ...)
  Baselines & consulting
  The Security Team as facilitator and enabler: Making security part of the overall.
Communication is the key.
Bring together experts. Change the culture & the mind set.
Make “security” part of the overall!

## Slide 48: Today’s only(?) regulation
NIST 800-53 & 53A
  Help to identify, control, mitigate risks to information and information systems
  Recommendations and guidelines for selecting and specifying safeguards & countermeasures
  Foundation for risk assessment
  …how does this apply to PCS (e.g. NIST SP800-82)?
http://csrc.nist.gov/publications/drafts/800-82/draft_sp800-82-fpd.pdf

## Slide 49: (Too) Many Standards...? (I)

## Slide 50: (Too) Many Standards...? (II)
  “Good Practice Guidelines Parts 1-7” U.K. Centre for the Protection of National Infrastructure (CPNI) http://www.cpni.gov.uk/Products/guidelines.aspx
  “Manufacturing and Control Systems Security” ANSI/ISA SP99 TR99.00.01-04 http://www.isa.org/MSTemplate.cfm?MicrositeID=988& CommitteeID=6821
  “Guide to SCADA and Industrial Control Systems Security” NIST SP800-82 http://csrc.nist.gov/publications/drafts/800-82/draft_sp800-82-fpd.pdf
  “Critical Infrastructure Protection CIP-002 to CIP-009” U.S. Federal Energy Regulatory Commission (FERC) http://www.nerc.com/page.php?cid=2%7C20
  “Information Technology ― Security Techniques” ISO/IEC 27001:2005 and following
  Plus standards of: American Gas Association (AGA) Int’l Society for Pharmaceutical Engineering (ISPE) U.S. Chemical Industry (CIDX) Norwegian Oil Industry Association (OLF) German Federal Association of the Gas and Water Industries ...

## Slide 51: (Too) Many Standards...? (II)
  “Good Practice Guidelines Parts 1-7” U.K. Centre for the Protection of National Infrastructure (CPNI) http://www.cpni.gov.uk/Products/guidelines.aspx
  “Manufacturing and Control Systems Security” ANSI/ISA SP99 TR99.00.01-04 http://www.isa.org/MSTemplate.cfm?MicrositeID=988& CommitteeID=6821
  “Guide to SCADA and Industrial Control Systems Security” NIST SP800-82 http://csrc.nist.gov/publications/drafts/800-82/draft_sp800-82-fpd.pdf
  “Critical Infrastructure Protection CIP-002 to CIP-009” U.S. Federal Energy Regulatory Commission (FERC) http://www.nerc.com/page.php?cid=2%7C20
  “Information Technology ― Security Techniques” ISO/IEC 27001:2005 and following
  Plus standards of: American Gas Association (AGA) Int’l Society for Pharmaceutical Engineering (ISPE) U.S. Chemical Industry (CIDX) Norwegian Oil Industry Association (OLF) German Federal Association of the Gas and Water Industries ...
Pick one. It doesn’t really matter which one. Apply its recommendations. Note down where you can’t.
Cross-check with a second one.
http://www.msisac.org/scada

## Slide 52: Some keyplayers…
  Government Initiatives:
  Global Key Players:
  Mixed Communities:
  (This list is not intended to be complete.)
EuroSCSIE

## Slide 53: Stuxnet: Protective Measures (I)
  Deploy a Defense-in-Depth protection
  Establish security cells on your network
  Forbid usage of USB keys or use Epoxy ; restrict usage of CDs, open shares & DFS
  Teach your experts about “Social Engineering”
  Screen your experts: alcohol/drugs, financial, psychological/social/family, …
  Patch, patch, patch… …and run up-to-date antivirus software (wouldn’t have helped here )
Apply Defense-in-Depth!!! …and follow a standard.

## Slide 54: Stuxnet: Protective Measures (II)
  Scan you PLCs on vulnerabilities & robustness
  Lock down the PLC configuration: Enable firewall, disable unneeded services
  Enable PLC intrusion detection
Talk to your vendor!
Accept the residual risk.

## Slide 55: Summary
PCS are (still) not designed to be secure. They fulfill use-cases but not abuse cases.
Defence-in-Depth is the key. Protective means must be applied on every layer. Control System Cyber-Security should align with IT security.
Patch procedures, access protection, robustness, security certification & documentation
need significant improvement.
Open communication, e.g. on vuln’s, is essential.
Get your vendors/integrators/IT people on board.
There was (is?) lots of hype on PCS security since Stuxnet. Many vendors quickly rolled out “security solutions”. Assess first. Choose a standard and apply.

## Slide 56: Thanks a lot !