## Slide 2: HFM Test Station Main Cryostat
Arnaud Vande Craen (TE-MSC)
EUCARD : HFM Collaboration Meeting – LASA Milano

## Slide 3: Summary
Introduction
Design
Status
Conclusion

## Slide 4: Introduction

## Slide 5: Overview
Vertical cryostat
  “Claudet bath” principle
  Few cryogenic connections
4 parts
  Vacuum vessel
  Helium vessel
  Thermal shield
  Insert
Support structure in pit
Courtesy P. Minginette

## Slide 6: Integration
Exhaust line
  Burst disc
  DN 300
Current leads
  20 kA
  10 kA
Jumper
Courtesy P. Minginette

## Slide 7: Design

## Slide 8: Vacuum vessel
Dimensions
  4.6 m height
  2.3 m diameter
  4.8 tons
Stainless steel
Conical cover
3 supports
Static vacuum
Courtesy P. Minginette

## Slide 9: Helium vessel
Neck
  3 mm thick
  1.6 m diameter
  1.6 m long
Lower volume
  6 mm thick
  1.5 m diameter
  2.5 m long
Max pressure : 4 bar
Heat exchanger
  30 x U shape
  OFE Copper
  Cooling power ≈ 100 W @ 1.9K (1.5 day Cool-Down)
    (25W nom, ; 40W dyn. )
Courtesy P. Minginette

## Slide 10: Thermal shield
Actively cooled
Supported from above
Stainless steel structure
Copper
  Sheet
  Pipe
Courtesy P. Minginette

## Slide 11: Insert
Top plate
  Current leads
    20 kA
    10 kA
  Instrumentation
Radiative screens
Lambda plate
  Lambda valve
  Splices
  Instrumentation
Mechanical support
  Lambda plate
  Magnet (15 tons)
Courtesy P. Minginette

## Slide 12: Status

## Slide 13: Vacuum vessel
Design : Finished
Call for tender :
  Answers received
  Selection in progress
Order : October
Delivery : 6 months after order (May ?)

## Slide 14: Helium vessel
Design : October
Call for tender : November
Order : December
Delivery : 6-7 months after order (August ?)

## Slide 15: Thermal shield and Insert
Thermal Shield
  Design in progress
  Construction in the shadow of helium vessel
Insert
  Design in progress
  Construction at CERN

## Slide 16: Conclusion

## Slide 17: Conclusion
Design well advanced
Components at CERN for next summer
Assembly phase to be planned (during LS1)
  Assembly of the cryostat
  Connection to other components

## Slide 18: Acknowledgment
M. Bajko (TE-TF)
V. Benda (TE-CRG)
G. De Rijk (TE-MSC)
C. Giloux (TE-TF)
P. Minginette (EN-MME)
V. Parma (TE-MSC)
P. Perret (EN-MME)
P. Viret (TE-TF)

## Slide 19: Grazie !