## Slide 1: Communications Services
CERN Data Center Network Changes and Evolution
David Gutiérrez
Co-autors: Carles Kishimoto, Edoardo Martelli
Communication Services / Engineering
www.cern.ch/it

## Slide 2: Outline
High performance Brocade routers
External connectivity and Firewall system
Network Architecture for Wigner
1
2010
2011
2012
2013
1
2
3

## Slide 3: Data Center Network 2010
2010
2011
2012
Brocade deployment
100Gbps tests
100Gbps deployment
Force10
Force10 | 
LCG non-blocking Fabric | 2.88 Tbps
Routers | 24
Linecards | 248
10Gbps Ports | 1100
100Gbps Ports | N/A
2
Data Center | 
Racks | 841
Systems | 11,320
Cores | 57,651
Raw HDD (TiB) | 61,137
1G NICs | 15,703
10G NICs | 390
ToR Switches | 584
Consumption DC | 2.44 MW
ToR: Top of the Rack

## Slide 4: DC Network 2010
Tier1s
Active
Firewall
LCG
CORE
GPN
Passive
Firewall
Backbone
Distribution
Access ToR sw
CPU, Disk, Tapes
Border routers
Force10 router
Switching fabric
0.96 Tbps
Switching fabric
2.88 Tbps
Aggregated 10Gbps links
AFS, Mail, Web, …
. . .
3
LCG: LHC Computing Grid GPN: General Purpose Network ToR: Top of the Rack
10Gbps link
Notes: 3

## Slide 5: 10Gbps Aggregation issues
Hashing is decoupled from link capacity
Flow based hashing
Potential network traffic polarization
Manageability
10G
10G
LACP
4x10G
4
LAG: Link AGgregation ECMP: Equal Cost MultiPath

## Slide 6: 100Gbps fat router interconnects
Technology upgrade where needed
Performance and fairness tests
  100GBase-LR10 CFP (SMF up to 2Km)
Testing 100GbE WAN to:
  Lyon (RENATER) ~120 km
  Amsterdam (AMSIX) ~1650 km
5

## Slide 7: Migration in images
6

## Slide 8: DC Network today
Tier1s
Active
Firewall
LCG
CORE
GPN
Passive
Firewall
Backbone
Distribution
Access ToR sw
CPU, Disk, Tapes
Border routers
Brocade router
Aggregated 10Gbps Links
AFS, Mail, Web
100Gbps Link
LHCONE
7
. . .
Switching fabric
1.36 Tbps
Switching fabric
5.28 Tbps
Notes: 7

## Slide 9: Data Center Network today
2013
2012
8
Data Center | 2010 | 2012
Power | 2.9 MW | 3.5MW*
Racks | 841 | 1070
Systems | 11,320 | 12,483
Cores | 57,651 | 68,385
Raw HDD (TiB) | 61,137 | 97,698
1G NICs | 15,703 | 16,026
10G NICs | 390 | 1,912
ToR Switches | 584 | 662
Consumption | 2.44 MW | 2.8MW
Data Center L3 Switch | Brocade
LCG non-blocking Fabric | 5.28 Tbps
Routers | 22
Linecards | 230
10Gbps Ports | 1,280
100Gbps Ports | 60
Data Center L2 Switch | HP
1Gbps Ports | 22,776
10Gbps Ports | 4,284
MLXe32 Technical Specs | #
Non-blocking Fabric | 15 Tbps
Linecards | 32
10Gbps Ports | 256
100Gbps Ports | 32

## Slide 10: Outline
High performance Brocade routers
External connectivity
Network Architecture for Wigner
2010
2011
2012
2013
2
3
9

## Slide 11: External connectivity changes
Active
Firewall
CORE
Passive
Firewall
LCG
GPN
EXTNET
Internet
Internet2
US Peers
Géant2
CIXP
10
LHCOPN
LHCONE
CIXP: Cern Internet eXchange Point

## Slide 12: Firewall System Active-Passive
Géant2
Active
Firewall
CORE
Passive
Firewall
LCG
GPN
EXTNET
Internet
Internet2
US Peers
CIXP
11
LHCONE
LHCOPN
Shared with SWITCH
12Gbps
3.8Gbps
1Gbps
20Gbps
20Gbps
30Gbps
6Gpbs Stateful
130Gbps
20Gbps

## Slide 13: Firewall System Active-Active
Active
Firewall
CORE
Active
Firewall
LCG
GPN
EXTNET
Internet
Internet2
US Peers
Géant2
CIXP
12
LHCONE
LHCOPN
Shared with SWITCH
12Gbps
3.8Gbps
1Gbps
20Gbps
20Gbps
130Gbps
30Gbps
6Gpbs Stateful
30Gbps
10Gpbs Stateful
RENATER
2Gbps
40Gbps

## Slide 14: Outline
High performance Brocade routers
External connectivity
Network Architecture for Wigner
2010
2011
2012
2013
3
13

## Slide 15: LCG Resources
Geneva Building 513
Firewall
Internet/
GeantIP/
Esnet/I2
Budapest Wigner
Wigner Core
Network
LCG
CERN Core
Network
GPN
LCG
2x100Gbps
14

## Slide 16: Autonomous Operation
Geneva Building 513
Firewall
Internet/
GeantIP/
Esnet/I2
Budapest Wigner
Wigner Core
Network
LCG
CERN Core
Network
GPN
LCG
GPN
Firewall
Internet/
HU access
AS198797
188.185.0.0/16
2001:1459::/32
dns
radius
ntp
dhcp
2x100Gbps
15

## Slide 17: LHCOPN and LHCONE traffic
Geneva Building 513
Firewall
Internet/
GeantIP/
Esnet/I2
Budapest Wigner
Wigner Core
Network
LCG
CERN Core
Network
GPN
LCG
GPN
Firewall
Internet/
HU access
AS198797
188.185.0.0/16
dns
radius
ntp
dhcp
LHCOPN
LHCONE
16
MPLS
BGP
MPLS
BGP
MPLS
MPLS
MPLS: MultiProtocol Label Switching
2001:1459::/32

## Slide 18: Wigner in numbers
Wigner Data Center | 2013 | 2014
Power | ~900KW | ~1200KW
Racks | 90 | 120
Routers | 6 | 10+Firewall
100Gbps ports | 18 | 18
Switches | 140 | 210
Servers | ~1200 | ~1800
L2 Switch | 2013 | 2014
1Gbps ports | 3072 | 4608
10Gbps ports | 528 | 792
17

## Slide 19
Thank you for your attention
Questions?