## Slide 1: Can the development from Dubna be applied for an effective high energy high current charge breeder ?
Evgeny E. Donets
Laboratory of High Energy Physics,
Joint Institute for Nuclear Research,
Dubna, Russia
edonets@jinr.ru
for the JINR ESIS group
HIE-EBIS Workshop
CERN, October 16-17, 2012

## Slide 2
B = 3.3 T Q- = 10 nC, E_e=8 KeV; J_e=300 A/cm^2; (Krion-2)
B = 6.0 T Q- = 50 nC E_e=25 KeV, J_e=2000 A/cm^2
(expected Krion-6T)
= 3.0 1011 e.ch.
B = 9.0 T Q- = 150 nC E_e=70 KeV, J_e=12000 A/cm^2 ????
.

## Slide 5
Krion-2 installation on HV terminal of LU-20 (Nuclotron run 2010

## Slide 6
EBIS in the electron reflex mode of operation

## Slide 7
3 mm
1 mm
0.2 mm
Experimental conditions in ionization region (110 cm length): Drift tube temperature 4.2 K , Vacuum P < 10-12 torr, B_max= 3.3 T; IrCr cathode 1-2 mm diameter; e-gun Pierce type, I_emiss.~8-12 mA.
e-string: J= 100 - 270 [A/cm2], ( 5x1011 e/cm3 ) . Number of reflections 100 - 300.
Q_e_total=10^11 e, Consumption power P=50 W!
(Q_e_total=10^11 e in EBIS: P=10 kW )
Total length of the drift tube structure 1.2 m

## Slide 8
3 mm
1 mm
0.2 mm
3 temperature terminals : room (anodes), 78 K 3+3 drift tube sections
( injection of neutrals: gases, Ferrocene, Au (evaporation from tungsten wire)),
Ionization region 110 cm , 26 separated druft tubes – 4.2 K.
Cryopumping only ! Works excellent. Turbopumps are not used during operation
(60 days or more). 5-6 days of anodes (mainly) outgassing by e-beam/string after beginning is enough .
Total length of the drift tube structure 1.2 m

## Slide 9
3 mm
1 mm
0.2 mm
1) NO any “MEMORY” effect was observed in 4.2 K drift tube sections!
2) Xe remnants were observed: localization 78 K drift tubes in injection region. Xe and more heavy gases (Rn) are partially frosen at 78 K,
and then could decopule drift tube wall under bombardment by other neutrals/ions of new working element.
Total length of the drift tube structure 1.2 m

## Slide 10: WHY REFLEX MODE?
TO REDUCE CONSUMPTION POWER,
SAVING ALL OTHER
EBIS ADVANTAGES

## Slide 11
Q-(e-ch./m) EBIS ESIS
1011 10 KW 50 W (Krion-2)
1012 200 KW 200 W (expected
Krion-6T)
1013 5000 KW 2 KW (expected
Krion –Tubular)

## Slide 12
EBIS

## Slide 13
Electron string is formed in nonlinear process via strong instability of trapped electrons and exists as a dynamic equilibrium of injecting and loosing electrons.
Nonlinear development and partial saturation
(self-suppression) of various intabilities:
Two beam instability (with l=1,2... in linear perturbation theory);
Initial stage of Virtual cathode formation with loss of low energy tail.
Not squeezed state; no low energy electrons.
work is in progress

## Slide 14
84Kr18+

## Slide 20
(190 ms), 150 µA
, 120 µA
8 µs
E=4.5KeV(Einj)+1.1KeV(Vstr)
124Xe42+ procuded with Krion-2 ESIS

## Slide 21: Charge state distribution of Ar ions after 500 ms confinement in an electron string space.
IAr16+ = 200 A in 8 s
I(Fe24+) = 150 A in 8 s
Charge state distribution of Fe ions after 1100 ms confinement in space of an electron string.

## Slide 22: Ion-ion cooling

## Slide 23
TOF spectra just after Au injection

## Slide 25
Au TOF spectra, mean q Au = 50.2+
Ionization time Ti = 700 ms

## Slide 26
Au TOF spectra, mean q Au = 50.2+

## Slide 27
Au TOF spectra, mean q Au = 50.2+

## Slide 28
Au TOF spectra, mean q Au = 50.2+

## Slide 29
GAS PULSE INJECTION FOR PRODUCTION OF HIGHLY CHARGED IONS
Ion-ion cooling of highly charged ions in ESIS
The Ion-ion cooling with use of C and O coolant ions produced at gas pulse injection permits to increase the Au51+ion yield
by factor 2.
The intensity of Au51+ ions at ion-ion cooling was 108 per pulse.
Ion charge state spectrum after 1,1 s of confinement.
Au ion yield & ion spectra
(qAu = 50.2) for various injection time
of coolant (CO) gas. Ti =700 ms -ionization time,
red – cooling gas injection time Tc = 150 ms,
magenta - Tc = 450 ms,
blue - Tc = 550 ms,
green - Tc = 650 ms.

## Slide 30: Total Kr27+ ion pulse without ion-ion cooling -(blue) and with use of (CH4) ion-ion cooling - red.

## Slide 31: Preliminary results on ion-ion cooling
Ion-ion cooling effectively works: it allows to reduce ion losses considerably, approaching to the natural limit of trap capacity.
Further plans.
Towards Au69+ intense beams
(with new 6T Krion-6T source):
cooling by the ions (Ar8+ ?) to avoid charge exchange with neutrals of coolant gas,
produced at separate drift tube space of ESIS.

## Slide 32: Experimental set-up for pulse injection of methane into Krion-2 ESIS (schematic drawing).
1) Gas injection section (78 K)
2) Drift tube sections at 4.2 K
6) Methane freezing-evaporation cell.
7) The cell rod, covered with aluminized Mylar or graphite.
10) Copper wire, connected to 4.2 K terminal.
11), 12), 13), 14) Elements of the system for isolation of 1014 molecules of methane.
11CH4
12CH4
3.2 cm3
2000 cm3
P1 = 338 Tor
P2 = 0.54 Tor
P3= 8.7·10-4 Tor
i.e. app. 1014 in 3.2 cm3

## Slide 33: Cryogenic cell for pulse injection of gases (schematic view)

## Slide 34: Pulse injection of Argon into the electron string.
3 ms
E.D. Donets 12.09.2011

## Slide 37: Superconducting test coil (L=19 cm, 32 layers of SC wire) : preparation for testing in a liquid helium.

## Slide 38: SC solenoid: 1.2 m length, 22 layers; technology was elaborated and manufacturing has been done in ESIS group (VBLHEP,JINR)

## Slide 39
Magnetic field versus electron current: expected and experimental data. Latest reached point: 105 A – 5.44 T (04.10.2012)

## Slide 40: SC solenoid inside of Krion-6T ESIS (left); test assembling of the quench protection system (right).

## Slide 41: Nearest future plans:
1) First e-string tests are planned in October 2012.
2) Then, basic studies on e-string and heavy ion production in new range of relevant parameters (electron energy up to 25 KeV, confining magnetic field up to 6 T, et cetera)…
3) … towards Au65+ ÷Au69+ beams production for their possible acceleration on existing LU-20/Nuclotron facility (LU-20 accepts ions with charge state to mass ratio > 1/3) in 2013?

## Slide 42
Thank you for your attention!

## Slide 43
TUBULAR ELECTRON STRING ION SOURCE
1-electron gun, 2- superconducting solenoid, 3-cryo-cooler, 4- reflector electrode,
5- thermal shielding at temperature of 40 К.

## Slide 44
ION OPTICAL SYSTEM
 The method of the off–axis TESIS ion extraction was proposed to get TESIS beam emittance comparable with ESIS one.
OPERA 3D simulation of the ion optic system and the ion off-axis extraction channel.
The extracted ion beam has an ellipsoidal shape (Δri, Δyi are radial and azimuthal directions)
Δri= 2 mm, Δyi=8 mm.
Normolized radial εr-n and azimuthal εφ-n emittances of the extracted ion beam:
εr-n βi∙Δri2/4ρi 0,05πmmmrad,
εφ-nβi∙Δri∙Δyi/4ρi0,15πmmmrad.
The radial and azimuthal emittances of the ion beam accelerated to energy of eUac =25∙Z keV
εr5 πmmmrad and εφ20 πmmmrad.