## Slide 1: HIE-ISOLDE linac upgrade
D. Voulot, BE/OP, CERN
On behalf of Matthew Alexander Fraser; Fredrik Wenander; Brennan Goddard and the HIE-ISOLDE project team
The REX and ISOLDE facilities
HIE-ISOLDE linac
HEBT and experimental stations
Beam characteristics

## Slide 2
ISOLDE overview

## Slide 3
REXEBIS
Experiments
REXTRAP
MASS SEPARATOR
7-GAP RESONATORS
IH
RFQ
9-GAP RESONATOR
3.0 MeV/u
2.2 MeV/u
1.2 MeV/u
0.3 MeV/u
ISOLDE beam
60 keV
Rebuncher
Optional stripper
REX-Isolde overview
* 6 cavities
* 300 keV/u to 3 MeV/u
* longitudinal accumulation and bunching
* transverse phase space cooling
* charge breeding
* 1+ ions to n+

## Slide 4
RFQ
IHS
7GP
9GP
5keV/u
300keV/u
1.2MeV/u
2.2MeV/u
3MeV/u
3m
Linac:
Length 11 m
Freq. 101 MHz (202 MHz for the 9GP)
Duty cycle 1ms 100 Hz (10%)
Energy max. 3 MeV/u
A/q 2.0 - 4.5
Trans. 90% (lower for highly charged beams)
REX linac

## Slide 6: ISOLDE Statistics 2011
ISOLDE Shifts (8h):
  Scheduled: 471.5
  Delivered: 329.5 (+134 for machine development and test)
  REX-ISOLDE: 147 (45%)

## Slide 7: HIE-ISOLDE
A general upgrade of ISOLDE: High Intensity and Energy
  High intensity: upgrade of target area, separators and charge breeder (design study)
  High energy: HIE-LINAC
    R&D activities for the linac (started in 2008)
    Approved CERN project 2010
    5.5 MeV/u (stage 1) 2015 / 10 MeV/u (stage 2) 2016-2018
    36.5 MCHF, 50% financed through external collaboration

## Slide 8: Motivations
Superconducting linac => “array of small independent resonating cavities, equipped with their own small RF amplifier “
  -> No high power amplifier (< 10W of RF diss. In the cavity)
  -> High accelerating gradient (6 MV/m)
  -> Short + independent cavities = high flexibility
  -> CW operation

## Slide 9: SC quarter-wave cavities
Low b
Highb
f (MHz) | 101.28 | 101.28
b 0 | 6.3% | 10.3%
Gradient Ea (MV/m) | 6 | 6
Inner Cond. Diam (mm) | 50 | 90
Outer Cond Diam (mm) | 195 | 300
Mechanical Length (mm) | 215 | 320
Gap length (mm) | 50 | 85
Beam Apert. Diam. (mm) | 20 | 20
Rsh/Q (Ohm) | 564 | 548
Q0 min for 6 MV/m at 7W | 3.2 108 | 5 108
TTF max | 0.85 | 0.9
No. of cavities | 12 | 20

## Slide 10
Vacuum vessel
QWR
Liq. He reservoir
Focusing solenoid
Supporting frame
Beam
Tuning plates
HIE High-beta Cryomodule

## Slide 11
16 m
HIE linac (Stage 2b)
12 low-beta cavities
20 high-beta cavities
39.6 MV accelerating voltage

## Slide 12: Energy RANGE: STAGE 1
A/q =4.5
W = 5.5 MeV/u
βγ = 0.109
A/q = 2.5
W = 8.8 MeV/u
βγ = 0.136
A/q =4.5
W = 2.8 MeV/u
βγ = 0.0773
A/q = 2.5
W = 3.0 MeV/u
βγ = 0.080
0.3 MeV/u
1.2 MeV/u
2.25 MeV/u
2.8 - 3.0 MeV/u

## Slide 13: Energy RANGE: STAGE 2a
A/q =4.5
W = 9.3 MeV/u
βγ = 0.140
A/q = 2.5
W = 14.5 MeV/u
βγ = 0.177
A/q =4.5
W = 2.8 MeV/u
βγ = 0.0773
A/q = 2.5
W = 3.0 MeV/u
βγ = 0.080
0.3 MeV/u
1.2 MeV/u
2.25 MeV/u
2.8 - 3.0 MeV/u

## Slide 14: Energy RANGE: STAGE 2b
2.5 < A/q < 4.5
W = 1.2 MeV/u
βγ = 0.051
0.3 MeV/u
1.2 MeV/u

## Slide 15: Energy RANGE: STAGE 2b
2.5 < A/q < 4.5
W = 1.2 MeV/u
βγ = 0.051
A/q = 4.5
W = 10.2 MeV/u
βγ = 0.147
A/q = 4.5
W = 16.8 MeV/u
βγ = 0.187
Highest rigidity:
W = 10 MeV/u
A/q = 4.5
Bρ = 2 Tm
0.3 MeV/u
1.2 MeV/u

## Slide 16: HIE-REX Cavity: Nb sputtered on Cu

## Slide 17: Beam characteristics
Characteristic | Value (for A/q = 4.5)
Particle type | Heavy (radioactive) ions (A < 238)
Mass-to-charge state (A/q) acceptance | 2.5 < A/q < 4.5
Transverse emittance (normalised) (mm.mrad) | 0.07 (rms) and 0.3 (90%)
Longitudinal emittance (π ns keV/u) | 0.35 (rms) and 1.5 (86%)
Energy (MeV/u) | 0.3 – 10
Average Beam Current | ~ few particle per sec – 1 nA
Maximum rigidity (T.m) | 2.05
Macro-pulse length (ms) | < 2
Repetition rate (Hz) | < 50

## Slide 18: REX time structure
Protons from PSB
RIBs released from ISOL target
Accumulation/cooling/macro bunching (up to 100 Hz)
Charge breeding
Duty cycle of linac matched to charge breeder/ion source
μ
μ
Micro-bunching of EBIS beam pulse by RFQ at 101.28 MHz

## Slide 19: Chopper-buncher
Goal: increase natural bunch spacing from ~10 ns (101.28 MHz) to ~100 ns for physics with TOF systems
Multi-harmonic pre-buncher operating at f0/10 to ‘squeeze’ several bunches in one
Beam chopper (meandering line or sine-wave) pulsed in phase with the beam to remove particles from empty bunches

## Slide 20: High Energy Transfer lines and experimental stations

## Slide 24: HIE Schedule

## Slide 25: TSR@ISOLDE
Heavy-Ion Storage Ring + HIE-ISOLDE
  No background
  No energy straggling
  Cold beam/Smaller beamsize
  Reduced dead time/CW beam
Approved by research board May 2012
Aiming for start-up in 2015 as an experiment, integration as CERN facility towards 2018
TSR at MPIK Heidelberg
Possible TSR installation

## Slide 26: Spare slides

## Slide 27: Diagnostic box
TYPE IV
Collimator slit
Type 2
FC
Scanning slit
Silicon
detector
Stripping
foils

## Slide 28: Magnets – present designs

## Slide 29: Slow extraction
normal extraction, 14N4+, measured in front of linac
Slow extraction, 108Sn, measured at Miniball
Bunched beam = high instantaneous rate -> dead time
Good signal to noise ratio

## Slide 30: REX beam collection 2001-2012
6He 8,9,11Li 10,11,12Be 10C 17F 21,24,25,26,27,28,29,30Na 28,29,30,31,32Mg 44Ar 61,62,63Mn 61,62Fe 66,68Ni 67,68,69,70,71,73Cu 72,74,76,78,80Zn 70Se 72,88,92,94,96Kr 93,95,97,99Rb 96,98Sr 100,102,104,122,123,124,126,128Cd 108In 106,107,108,109,110Sn 138,140,142,144Xe 140,142,148Ba 140Nd 148Pm 140,142,153Sm 156Eu 182,184,186,188Hg 186,188,190,192,194,196,198Pb 196,198,200,202,206Po 202,204,208,220,221Rn 224Ra
>100 radioactive isotopes of 31 elements
A selection of stable elements charge bred