## Slide 1
Charge breeding at REX-ISOLDE
HIE-EBIS workshop 16-17/10 2012
Fredrik Wenander
CERN

## Slide 2
KoRIA
* ECRIS and EBIS
* Design
REX-ISOLDE, CERN
* EBIS/ECRIS
* Operation/Stopped
SPES, LNL
* ECRIS
* Design
CARIBU, ANL
* ECRIS/EBIS
* Operation/Commissioning
TRIAC, JAERI
* ECRIS
* Stopped
Charge breeders for RIBs worldwide
SPIRAL/SPIRAL2
* ECRIS
* Design
VECC
* ECRIS
* Commissioning
ARIEL, TRIUMF
* EBIS?
* Planning
TITAN, TRIUMF
* EBIT
* Operational
ISAC, TRIUMF
* ECRIS
* Operation
ReA, MSU
* EBIT
* Commissioning
EURISOL, Europe
* EBIS/ECRIS
* Design

## Slide 3
Radioactive nuclei: main interest for nuclear physics
Proton dripline
Neutron
dripline
Potential and delivered beams
To this date:
~6000 nuclei believed to ‘exist’
~3000 different nuclides experimentally observed
Less than 10% stable
32 different radioactive elements for physics
~100 isotopes accelerated
~100 beam times
radioactive
stable
REX-ISOLDE beams

## Slide 4
REX-ISOLDE
Post accelerator to 3 MeV/u
Room temperature Linac
First experiment 2001

## Slide 5
Ion mass | 4 to >250 | He to >U
Intensity | few to >1E11 ions/s | Large dynamic range
Charge | 1+ | Some (undesired) 2+, 3+,…
Energy | 30 to 60 keV | 
Energy spread | few eV | 
Temporal structure | quasi-cw | Proton impact every n*1.2 s
ISOL beam parameters
Release curve
Semi-continuous
depending on release
properties and ionization time
typical tens ms to minutes
(r=rise, f=fast, s=slow)
8Li (T1/2 = 840 ms) produced by target fragmentation of tantalum foils
Extra

## Slide 6
See also http://ie.lbl.gov/isoexpl/charthlp.htm
ISOL beam parameters
Transverse emittance | 10-50 mm mrad | 90% at 60 keV
Half-life | >10 ms | Limited by ISOL-system
Selection | Not necessarily isobarically clean | Use e.g. resonant ionizing laser ion source
ISOL magnet
selects A/Q (Q=1)
Z
resonant laser separation
N

## Slide 7
0 | Achievable A/Q (3<A/Q<4.5)
1 | High breeding efficiency rare radionuclides limit machine contamination chain of machines
2 | Short breeding / confinement time handle short-lived ions
3 | Clean extracted beams
4 | High ion throughput capacity
5 | Good beam-quality (large α, small trans, small Eextr) good trapping efficiency high linac/separator transmission  good mass separation
6 | Easy handling and reliable to be used in an accelerator chain on a production basis
Breeder criteria
ionization
Checklist for ‘normal’ breeder design
target ion source
separation
breeding
acceleration
detector
CB delay
For HIE-EBIS tougher requirements

## Slide 8
Beam out of REXTRAP
* Bunching: few us
* Transverse emittance: ~30 -> ~10  mm.mrad at 30 keV
* Et~10 eVus
EBIS
injection
works
Non-cooled
Cooled
NB! Usually not isobarically cleaned

## Slide 9
* Only 15 min delivered beam for 24 h beam time ->
+ excellent signal-to-noise ration
- high instantaneous rates (DAQ dead-time, pile-up)
=> implement slow (ms) extraction
REXEBIS extraction times
Self extraction, 14N4+
measured before Linac
FWHM~25 us
* Beam pulse can be extended from 25 us to >400 us FWHM
(pulse length limited by Linac RF duty cycle to 800 us, from 2015 2 ms)
* Mass and q dependent – no standard settings
(need TOF from experiment for tuning)
Slow extraction, 190Pb44+ measured with Miniball detector
500 us FWHM
t (us)
See Andrey’s presentation

## Slide 10
Beam contamination
Can’t see the trees for the forest
Beam impurities:
a. isobaric contamination
from ISOL-target
Remember: often deal with <1E4 pps => 1.7 fA
What’s problem?

## Slide 11
Molecular beams
The idea
1. Use chemical properties to separate isobars e.g. 96Rb from 96Sr
2. Create a molecular sideband (96Sr19F+) with gas leak at ISOL-target
3. Molecular ions are extracted and selected in the separator (A=115 selection)
4. Keep molecules inside trap, break them in EBIS
5. Charge breed as usual and obtain clean 96Sr
All elements ionized by the ISOLDE 1+ source
96Sr19F+ 115In+
A/q=115
ISOLDE separator
Trap
EBIS
F
REX separator
96Sr27+ A/q=3.556 115In32+ A/q=3.594 115In33+ A/q=3.484
3.54 <A/q< 3.58
REX linac
Double separation
Benefit from larger Ie

## Slide 12
A/q-resolution ~150
Mass separator
After REXEBIS
A/q < 4.5
Emittance ~10-25 mm mrad (95%) @ 20 kV
E < 50 eV*q ?
Energy of 5 keV/u (determined by RFQ)
Nier-spectrometer
Even so, some A/Q contaminants difficult to resolve
7Be3+ from 14N6+ R=450
18F9+ from 12C6+ R=19200

## Slide 13
Clean beam?
Extracted beams from REXEBIS as function of A/q showing residual gas peaks and charge bred 129Cs. The blue trace is with and the red trace without 129Cs being injected.
residual gases in CB
Iresidual  0->1+ Pres gas
Isotope toolbox turns 10

## Slide 14
* C, O, Ne and Ar partial pressures around 310-12, 210-12, 510-12 and 410-13 mbar
How pure is the beam really?
12C3+
16O4+
20Ne5+
40Ar10+
21Ne5+
22Ne5+
40Ar9+
47Ti11+?
60Ni14+?
90Zr21+?
A/q=4.24
Isotope A/q Z Origin
17O 4.250 8 residual gas
21Ne 4.2 10 buffer gas
38Ar 4.222 18 residual gas
47Ti 4.272 22 drift tubes
51V 4.25 23 NEG strips
63Cu 4.2 29 anode and collector
80Kr, 84Kr 4.21, 4.2 36 residual gas
94Zr 4.272 40 NEG strips
139La 4.212 57 cathode
Other elements that can be present at other A/q are:
He, C, N residual gases
B cathode
Fe NEG strips, stainless steel
Ni stainless steel
Cr stainless steel
Mo stainless steel

## Slide 15
Continuous injection ‘accu’ mode
Local ion source
+ Collect ions continuously => no Penning trap needed
+ Adapted to ISOL ion sources
+ Shorter cycle times
* Na+, K+, Rb+, SrF+ from both local
ion source and from ISOLDE target
* CW operation even used for a run
96Sr(F) - continuous injection into EBIS
* CW beam from the RFQ cooler:
EBIS efficiency alone of 5% for
87Rb17+, Tbreed = 29 ms
* Some problems...

## Slide 16
In-trap decay
Be
Tested first time at REX-ISOLDE with 61Mn (T1/2=675 ms; 1.7x106 atoms/s)
Ttrap Tbreed Result
200-1100 ms 28 ms no Fe detected at Miniball
300-1100 ms 298 ms 57(7)% Fe detected agrees with predictions
In-EBIS decay
Benefit from increased:
1. radial holding voltage
2. higher electron beam
β±-decay

## Slide 17
Hot spots in REX
40-70%
Losses, in percent of the ISOLDE beam
5-10%
35-40%
2-5%
1-2%
ISOLDE
* Class C Lab
* Handle 100 LA
Radiation / contamination

## Slide 18
* Two separators (GPS and HRS) in parallel
* ~180 shifts scheduled 2012
* In between stable beams from EBIS for:
calibration of detector setups
machine development (beam diagnostics tests, Linac, controls upgrades)
* Running from beginning of April to mid December
* Scheduled 2 weeks machine stop if requested
Consequences of a breakdown
-> cancelled run
(not less statistics but no measurement)
ISOLDE schedule
Red boundary = REX run
Purple = REX setup

## Slide 19
Beam zapping with REX
Beams to the Miniball experiment from ISOLDE target #433, Aug/Sep 2010
REX used to be difficult to setup
Since 2010 improved scalability and reproducibility
At least 16 changes in 15 days!

## Slide 20
1. REX breeder system is working extremely well!
2. Penning trap complicates things but: can be used for isobaric mass separation
crucial for injection into a storage ring after the post-accelerator
3. Effort presently put on Linac energy upgrade
4. Future serious challenges for REXEBIS breeder upgrade
Conclusions

## Slide 22
Bunched beam : high instantaneous rate !
  deadtime …
Good signal/background …
1 shift at REX
=
19 min actual measuring time
Trapping
Charge Breeding
Post Acceleration
Time Structure
EBIS
REX
TRAP
Slide borrowed from J. van de Walle