## Slide 1: WATCHMAN: A Field Demonstration of Remote Reactor Monitoring
Adam Bernstein for the WATCHMAN Collaboration
Simulation courtesy G. Jocher/J Learned, U Hawaii
This work was performed under the auspices of the U.S. Department of Energy by Lawrence Livermore National Laboratory under contract DE-AC52-07NA27344. Lawrence Livermore National Security, LLC
Global reactor antineutrino fluxes

## Slide 2: Outline
A one-page nonproliferation tutorial
Antineutrinos and nonproliferation
The WATCHMAN project
The apparently unique advantages of the Boulby Mine
Nonproliferation, Technology and Fundamental Science

## Slide 3
The IAEA Safeguards regime monitors the flow of fissile material through the nuclear fuel cycle in 170 countries
Weapons production
Generic fuel cycle
IAEA goal – detect diversion
of fissile material from peaceful
to military programs
Goal for antineutrino measurements - track fissile inventories in operating reactors
t

## Slide 4: Monitoring nuclear reactors with antineutrinos
Detected rates are quite reasonable
Reactors emit huge numbers of antineutrinos
6 antineutrinos per fission from beta decay of daughters
1021 fissions per second in a 3,000-MWt reactor
1017 antineutrinos per square meter per second at 25-m standoff
6,000 events per ton per day with a perfect detector
600 events per ton per day with a simple detector (e.g., SONGS1)
About 1022 antineutrinos are emitted per second from a typical PWR unattenuated and in all directions
Example: detector total footprint with shielding is 2.5 meter on a side at 25-m standoff from a 3-GWt reactor

## Slide 5: Our LLNL/SNL collaboration has helped create the field of applied antineutrino physics for nonproliferation
Determine reactor on/off status within 5 hours with 99.9% C.L.
Measure thermal power to 3% in one week
Sensitivity to 70 kg switch in U/PU: known power and initial fuel content
In 2012, IAEA released an official report endorsing continued research into several reactor monitoring applications – including long range reactor monitoring

## Slide 6: Cross-border reactor monitoring is going on right now – but only for GWt reactors and with a technology that is difficult to scale
1000 tonnes scintillator 1000 m depth
Per month:
16 reactor antineutrinos
1 background event
From 130 GWt of reactors
~3% of signal from South Korean reactors @ 400 km standoff
The KamLAND detector

## Slide 7: 10 MWt reactors at a distance are a very hard problem
Goal | Detector mass | standoff | Required reduction in bg rate relative to KamLAND
16 events in 1 year from a 10 MWt reactor, ( 25% accurate thermal power) | 10 kiloton | ~40 km | 10x
 | 1 Megaton | ~400 km | 100x
Global reactor antineutrino fluxes
http://arxiv.org/abs/0908.4338
Science & Global Security, 18:127–192, 2010
Gadolinium-doped (light) water appears to be the most viable option for scaling to the largest sizes

## Slide 8: Advantages of antineutrino detection for remote discovery and monitoring of reactors
  Cross border detection – ultimate limit is perhaps ~800 km
  Continuous surveillance
  Constraints on power and plutonium production rate
  With long range capability, no cueing information required
  Eventually: Reactor localization with improved directionality or spectral measurement
8
My own guess at the most likely use: cooperative deployment to confirm absence of reactors in a prescribed wide area

## Slide 9: The WATCHMAN (Water Cherenkov Monitor for Antineutrinos) Collaboration
UC Davis
UC Berkeley
UC Irvine
U of Hawaii
Hawaii Pacific University
Virginia Tech.
Current Phase: Two U.S. National Laboratories, 6 Universities, 4 M$, 2.25 years

## Slide 10: WATCHMAN is now in its first phase in the United States
Overall Project Goal: demonstrate sensitivity to reactor antineutrinos using a gadolinium-doped (light) water detector at 0.1-1 kilometer standoff from a 10-150 MWt US research reactor, or 10-20 kilometers from a 3000 MWt scale US commercial power reactor.
Kiloton scale detector
Research or power reactor
//
0.1 - 25 km standoff
100-1000 meters overburden
First Phase, 2012-2014:
identify site
measure backgrounds
develop a design envelope for the detector
//

## Slide 11: Complementary activities worldwide (OK mostly in Japan)
- HyperKamiokande
560,000 ton multipurpose water detector being planned by Japan
Time scale: ~12 years
Interest in U.S. science community in participation will lead to further R&D in this area
Gd an option but not guaranteed
Our demonstration would give strong confidence for exercising the Gd option
EGADS- 200 ton deeply buried detector to evaluate Gd-doped antineutrino detection
  backgrounds
  materials
  energy thresholds
This detector volume is too small for direct demonstration of sensitivity

## Slide 12: Antineutrino signal and background
Backgrounds:
Real antineutrinos
Random event pair coincidences
Muon induced high energy neutrons
Long-lived (~ 1 sec) radionuclide decays
n
(100-200 MeV)
n
n
m
m
9Li
b
Signal in 1 kiloton of water
n
e
p
 ~ 8 MeV
511 keV
511 keV
e+
Gd
t ~ 30 ms
prompt e+ signal + n capture on Gd
Exactly two Cerenkov flashes
within ~100 microseconds
Within a cubic meter voxel
‘The antineutrino heartbeat’

## Slide 13: Step 1: What are the backgrounds ?
Shallow Depths (100-600 meters): not well known, measure as a function of overburden at a US facility (Kimballton)
Boulby: (1 km) reasonable extrapolations from past and ongoing experiments (KamLAND, Soudan mine water detector)
high energy neutron
spectrometer
radionuclide detector
(Water doped with gadolinium)

## Slide 14: Step 2: Choose a location
Detect as few as ~1 but no greater than 10 signal events per day.
Three sigma detection of the presence of the reactor in <~1 month.
  For 1 signal event per day  tolerable background is 2 events per day.
  Greater standoff can be compensated by greater overburden
Overburden:
  Existing overburden preferred (cost savings)
Reactor Power:
  A small reactor is preferred, (greater similarity with the ultimate intended use)

## Slide 15: A shallow site: Oak Ridge High Flux Isotope Reactor, 100 m depth
1000 ton det. target mass
Power = 85 MWth
S = 13 events per day
B = 164 events per day
10 days ON and OFF to detect @ 3 sigma
Main problem: excavation costs are high

## Slide 16: A deep site: the Boulby mine, 1000 meter depth
20 kilometer radius
S~B = 0.9 events per day
20 days (ON and OFF) to detect @ 3 sigma
(S = 0.7 events per day)
30 days
25 kilometer radius
1000 ton detector target mass
Power = 1570 MWth (2 cores)
16

## Slide 17: Why is Boulby an interesting site ?
Event rate meets our detection goal
Depth suppresses most backgrounds
Relatively large standoff provides a convincing demonstration
Mature, well-run, well supported underground science infrastructure
Excavation costs lower than ‘greenfield’ options
Recent mine activity allows for larger cavern (15x15x15 m)
International cooperative deployment underscores and reinforces nonproliferation commitments of all participants
World-class science and a path towards very large detectors
17

## Slide 18: A shot of the scientific bow: WATCHMAN will also be one of the world’s largest supernova watch detectors
A 1000 ton detector even with moderate overburden (few 100 m.w.e.) could detect ~700 events from a supernova at the galactic center. Any detector capable of detecting reactor antineutrinos can do this by default (SN antineutrinos are higher energy and easier to detect).
WATCHMAN would see antineutrinos from a supernova like 1987a, shown here in the visible
Pre-1987
1987

## Slide 19: Nonproliferation, Technical and Scientific objectives are all met with this proposal
First ever demonstration of sensitivity to reactor antineutrinos at appreciable standoff from a reactor using a gadolinium-doped water detector – probably the only scalable technology choice
A concrete example to policy makers of a reliable low event rate antineutrino-based measurement system, with unambiguous detection of only a few events per day
Detection efficiencies and backgrounds for large Gd-WCD detectors
Well-benchmarked detector and background simulation tools
Experience with gadolinium-doped water handling, purification monitoring in order to scale to next generation experiment
Now:
Core-collapse supernovae in this galaxy
Eventually ?
Megaparsec supernovae detection
Diffuse supernova neutrino detection
proton decay
long baseline neutrino CP phase and mass-hierarchy experiments
60 km standoff mass hierarchy measurements at reactors
Nonproliferation
Technology
Fundamental Physics

## Slide 20: Conclusions
Antineutrino detectors deployed a few hundred meters from reactors detect operational status, thermal power and Pu production
Attempts at the far more ambitious long-range capability are underway in both the nonproliferation and scientific communities
WATCHMAN aims to meet a nonproliferation need and become a source of interesting science and detector technology for the neutrino community

## Slide 21: Backup slides

## Slide 22: Applied Antineutrino Physics – a growing global community with strong ties to Dark Matter and Neutrino Science

## Slide 23: Map of US Power Reactors

## Slide 24: Map of US Reactors + Active Mines

## Slide 25: Perry Nuclear Generating Station
Perry Reactor Nuclear Generating Station to IMB cavern in the Fairport Salt Mine (Ohio)
1570 m.w.e.
cavity was 18m x 17m x 22.5m
~13 km standoff
3875 MWth
Pros
Existing cavern in active mine.
Large depth for low background.
Cons
Large stand-off will give low signal rate (0.5-1.0 per day).
Old cavern likely to require renovation.

## Slide 26: What will we actually measure at shallow depths
The energy spectrum of muogenic fast neutrons as a function of depth below the Earth’s surface
  Allows us to model double-neutron antineutrino-like backgrounds in a kiloton scale detector
The rate of muogenic radionuclides such as 9Li
  Allows us to set an upper limit on the contamination of our signal by these antineutrino-like backgrounds

## Slide 27: Fast Neutron Spectrometer
Plastic scintillator/Gd doped paint detectors sandwich ~4 tons of lead.
Direct interaction with scintillator for E < ~100 MeV.
Neutron multiplication off of the lead for E > ~50 MeV.
Expect 3000-5000 events per month at 100 m.w.e.

## Slide 28: Fast Neutron Spectrometer – muon veto on platform
Detector + muon veto + data acquisition and peripherals are less than 9 tons.
Platform will be standard trailer outfitted with power and AC.

## Slide 29: Radionuclide Background Detector
3.5x3.5 meter detector with 1.5x1.5 meter active inner volume.
Four optically segmented volumes with 0.1% GdCl3 doping.
Three inner volumes define a muon ‘telescope’
The central volume is the search region.
The outer volume is the muon/neutron veto.

## Slide 30: Background Measurements at the Kimbleton Underground Research Facility
Drive in access
Can deploy from 100 feet to 1400 feet of overburden
Use of the same detector at multiple depths ensures reliable comparison of results
First-ever continuous measurement as a function of depth

## Slide 31: A groundswell of experimental activity worldwide

## Slide 32: WATCHMAN has five phases – Phase I (two years) currently funded
Phase | Activity
I | Siting and Scoping, including site identification and detailed estimates of signal, background, required overburden and total project cost, and experimental measurement of backgrounds
 |  Sponsor approval of large detector
II | Design and site licensing
III | Construction
IV | Deployment
V | Data-taking and demonstration to end users