## Slide 1: LIU Beam Studies Review SPS Session
28-Aug-2012

## Slide 2: Q20 instability improvement
TMCI
  threshold expected at 3.5e11 for low vert chroma
  Up to 4e11 no TMCI observed
  Gives margin to reach HL LHC intensities
Space charge:
  For Q26 with chroma 0.25 can go up in single bunch intensity but struggling with losses due to TMCI
  Similar brightness, but better losses for Q20
  Slightly smaller tune spread for Q20 due to larger dispersion
  With Q20 can also go up in intensity with lower chroma
Ecloud
  Not limited at present, but more margin for Q20 (simulation)
  Could help for 25 ns beam
Longitudinal
  Threshold decreases with energy, controlled blowup
  Need less blow up for Q20
  Could also get in trouble at injection with more intensity from PS

## Slide 3: Q20 to LHC and studies left
Bunch length at extraction
  need more voltage
  For given emittance longer bunches – capture i n LHC
  Gvie bunch length, smaller long em – IBS in LHC
Longitudinal beam quality at flattop
  For Q20 slightly unstable without blow up
Need to study 25 ns beam for Q20 this year
Short bunches at LHC
  Bunch lenght growth for short bunches 1.45 ns
  Longer bunches in LHC 1.7, no capture losses, less bunch len growth
Final steps to make Q20 operational
  Probe cycle, extraction settings verification, transverse blow up, tails, SPS LLRF
Studies left for 2012
  Tails and transverse emittance for 50 ns
  25 ns with Q20 optics
  Single bunch high int for SC and TMCI
  Ions with Q20, IBS and SC

## Slide 4: Q20 discussion
Dampers: this degree of freedom should be taken into account and properly designed intabilities can be suppressed, does not appear in all machines! Proper parameter place to be chosen, chroma! - High bandwidth FB is addressed in SPS
Optimisation for IBS growth, in LHC we can do batch by batch blowup and decouple the machines; from MD it seems we don’t need batch by batch blowup for these intensities
Same long emitt as for Q26, we would try to work with same bunch length – was motivated by capture losses which were not seen in MD, could optimise bunch length, more difficult if we need the same long emittance
From LHC the limit is capture voltage, should not go to limit of 8 MV; bunches come always with smaller dp/p but same bunch length so we don’t need more voltage
For MD no setting in LHC had to be changed apart from transfer line settings
IBS: what is smaller in emittance at LHC collision has faster lumi decay at present operation – no big deal now

## Slide 5: Ecloud lessons from 2012 studies
25 ns beam, nominal intensity
  No emittance growth with 4 batches as seen in 2000, (with low chroma settings)
  In 2000 pos tuen shift (ecload), 2012 negative (impedance?)
  High chroma needed in 2000 for stability, no degradation in 2012 even with low chroma
  Only other observalbe is pressure rise, smaller by 10e4 than 2002
25 ns, ultimate intensity
  For higher int ecloud can reach non conditioned areas – pressure rise, tried with radial steering, seems to confirm, more tests
  Conditioning observed with a few hours on thes e intensities
  By moving the beam 1 cm clearly see effect even with 50 ns beam on pressure rise by factor 10 – expected by simulations
Coating:
  MBA less critical than MBB (risetime, flux, central density) with 25ns

## Slide 6: Ecloud lessons from 2012 studies
Bunch intensity dependence
  MBA less critical
  Ecload in central region not increasing with intensity (consistent with model)
Dynamic pressure rise
  Why do we observe a dynamic rise on coated chambers?
  Comes only from stainless steel part of machine
How to learn more about ecloud?
  Data logging
  Microwave transmission technique: send EM wave through pipe and detect phase modulation by ecloud, further increased bandwidth, quantitative estimations of e densities and finally online monitoring, shielded pick up with remote data acquistion to get ecloud decay time

## Slide 7: Ecloud studies left and after LS1
Still to be done this year
  25 ns ultimate int
  Incoherent effects, coast at 26 GeV for some minutes
  Srubbing in machine and lab
    Copper
    Stainless steel
    Analyse dark layer on chambers
  Repeat solenoid experiment
  Scrubbing localisation
In LS1:
  Crucial to preserve vacuum
  After LS1 scrubbing run with long 40 s cycle
  Two fully coated cells to be installed, remove aC coated drift with STSt
  After LS1 profit of high brightness RF schemes in PS

## Slide 8: Ecloud discussion
Decision about coating or scrubbing, asymptotic value of SEY, still correct? - in lab still like this, but the vacuum situation is different in machine and lab, chemical reaction different, startup after LS1 crucial
Vac quality during LS1 very important, need to know how much time needed for scrubbing, presently consider 2 weeks?
aC coating or not depends on (Bren’s summary):
  does aC work as a mitigation? Present answer is yes.
  is present SPS performance with well-scrubbed machine acceptable for today's and tomorrow's beams? Less obvious, but present performance with 50 ns excellent and nominal 25 ns promising - can we extrapolate easily to HL-LHC regime?
  can we quickly scrub SPS back to 'acceptable' situation after a long shutdown? This remains to be demonstrated - do we need reference measurements end 2012 to compare with 2014 startup?
Possible minimum of ecloud with bunch intensity, when losing ecloud in centre your are losing nonlinearity, so could be misleading that it is beneficial - see clearly also in LHC that we are dependent on central density
What do you expect for LHC 25 ns beam – emittance growth

## Slide 9: Longitudinal instability studies in 2012
LHC beam quality in Q26:
  Unstable bunches at flat bottom for N > 1.5 1011
  Batch 4 spends no time at flat bottom  unstable at the end of ramp or flat top
  Enhanced instabilities due to increased spread of incoming bunches
  Solutions:
    Take out the dips in the 200 MHz RF voltage program (done)
    Introduce more time at flat bottom after the 4th injection (longer FB)
    Increase emittance blow-up in the PS (3x4.5 kV)  more stable in PS 
    less spread of bunch parameters at injection in the SPS
  Cost: more losses - about 1 %
  Q20 (still better with longer FB)
Longitudinal impedance identification using long injected bunches (~25 ns) with
RF off :
  Measurements as in the past (1997,2001,2007…) of the beam spectrum
  show a high mode amplitude at 1.4 GHz  low Q impedance to be identified

## Slide 10: Longitudinal instability studies in 2012
Longitudinal instability thresholds measured at flat bottom and flat top in
single RF:
  Single bunch (εL~0.28 – 0.32 eVs):
  Flat bottom: Loss of Landau damping due to injection V mismatch – stable
  with low (matched) capture voltage > 1.4x1011
  Flat top: - Nth~1x1011 p
  Single50 ns LHC batch:
  Flat bottom: 1.5x1011 < Nth < 1.8x1011 p/b  similar to single bunch
  Flat top: Nth< 0.4x1011  stronger effect of beam loading at 800 MHz RF (?)
50 ns LHC beam Q20
  Np~(1.5 - 1.6)x1011 p/b on flat top
  Stable beam on FB
  Acceptable beam parameters at extraction (bunch length) – injected to LHC
  Scaling of bunch length/stability between Q20 and Q26 as expected
  More possibilities with upgraded 200 MHz RF (LS2)

## Slide 11
MDs:
  High intensity 50&25 ns beam in Q20  operational. And Q26?
  (losses increased in the first test)
  Study (thresholds) of single and multi-bunch instability at injection
  for Q26 and during ramp for Q20 and Q26 in a single and double RF systems
  Reference impedance measurements from quadrupole
  frequency shift at injection and stable phase shift (? – more difficult)
Simulations:
  Identify the impedance from comparison with
  measurements done with long (RF off) and short (RF on) bunches
  Reproduce the measured thresholds for single bunches (PL on/off)
Longitudinal instability plans for 2012/13

## Slide 12
Long. instability: Questions to be answered
Requirements for the 800 MHz system:
  2nd cavity operational (idle at the moment) – more voltage and better
  control
  FB and FF for phase and voltage control under strong beam loading for the
  two cavities (work in progress)
  Phase calibration (now based on bunch shape/stability)
What else do we need to know to estimate performance after LIU:
  Impedance source of longitudinal instabilities  measurements of HOMs
  in the 200 MHz and 800 MHz TW RF systems in labs (spares, not fully
  equipped) and in situ (tunnel) during LS1 (F. Caspers, E. Montesinos + new
  fellow/PhD student)
  1.4 GHz
  Complete impedance model

## Slide 13: Long. Instability Discussion
Instability seen in single RF, single batch - should be seen for single bunch as well which is not the case
The more un-uniform the beam from the PS, the more unstable the beam in the SPS at FT because blow-up becomes more difficult
In MD found that voltage dips are also important and allow for blow-up due to mismatch
Also parameter in LLRF found to become more independent from PS beam quality

## Slide 14: High bandwidth damper - MD studies in 2012
Synchronized excitation signal to the bunch.
Established method by which time aligning can be performed quickly and reproducibly, using variable delay line.
Excited the beam with band-filtered random noise.
Excited beam to instability, different modes.

## Slide 15
High bandwidth damper - 2012 MD slots
With LARP:
  LARP meeting in Frascati 14-16 November 2012
  1st slot: Beginning of October or before above November LARP meeting: fine timing, excitation of bunch in a train
  2nd slot: As late as possible, weeks 47 and 48 after LARP meeting: tests of new hardware for “demonstrator” to close FB loop
Further:
  One dedicated MD with bunch trains at 25 ns
  MDs to check the developed hardware orbit compensation (Urs Wehrle)
  Note: any MDs next year (26 GeV) would be extremely useful (consolidated Hardware) for extended demonstrator tests and prototype specification.

## Slide 16: Addressing the specific questions…
Which studies will still require significant MD time before LS1?
  List of topics given above
Is any study presently limited by instrumentation or diagnostics? Any improvement possible before LS1?
  Limited by speed of HW development and availability, rather than intrinsic SPS instrumentation
Is any study strongly relying on the installation and test of new hardware before LS1?
  Yes – the single bunch ‘demonstrator’ studies require the HW for the feedback processing channel to be available…tight for end 2012
How can we optimize the use of the remaining available MD time? Do we need to request for more?
  The timing of the MD is most critical – as late as possible
Which are the main motivations why we could benefit from the extension of the MD run into 2013?
  Would be very useful indeed, as HW will arrive very late in the year. Increase time for measurement, reduce risk of missing deadline, …

## Slide 17: Damper discussion
MD time really dedicated ?
  means 25 ns cycle but no coast SPS, 12 b would be fine
  No HI beam next year, which are the CNGS and TOF like beams
  Two issues, RP and 80 Mhz in PS
  Probably not highest intensity needed for this MD
Behaviour of damper for higher number of bunches could be different, should be tested as high as possible
  Not possible this year
  Impo effort in parallel going on in simulations
In what optics
  Q20 - so what to dump?
  Can go to higher intensities
  Should keep Q26
Still don’t know if PS damper effective at high energy, since beam is not unstable
  Have to understand if damper from today is enough or more bandwidth needed
  Mode 0 damping at 0.2 chroma
  Going to try at high energy but was designed for inj oscillations