Review of CTF3 optics
Ben Constance
30th January 2013

---
Outline
- Maximising CTF3 performance requires good control of optics
- Transverse matching for emittance preservation
- Dispersion control
  - Large energy spread of a few percent
  - Big beams in dispersive regions threaten losses
- Isochronicity to limit energy variation effects on power produced
  - Short bunches
  - Control of beam phase
- Performing campaign of transverse linear optics verification
  - Will describe technique for optics measurements
  - Discuss machine sections in turn
CLIC Workshop 30th January 2013
1

---
Transverse phase space painting
- CTF3 optics are designed in and referenced against MAD-X
- Pair of corrector magnets used to ‘paint’ a phase space ellipse
  - Ideally, correctors separated by a drift space
- Linear combination of kicks produces orbits with desired x, x’
  - Orbits behave as macroparticles, ensemble simulates beam
  - Orbits uniformly distributed in normalised phase space
- Ellipse is painted to match the design (MAD-X) phase space
2

---
Transverse phase space painting
- ‘Star’ pattern painted to maximise signal to noise
  - Difference of two orbits separated by 180 deg. phase adv.
  - Beam drifts thus cancelled
  - Use an average over typically 5 difference orbits
- Repeat measurement with multiple ellipses
  - Increase the ‘emittance’ of the painted ‘beam’
  - Combine ellipses, reducing sensitivity to drifts further
3

---
Evolution of painted ellipse
- Aim to measure matrix M
  - Know phase space painted at downstream corrector
  - Want to observe how the ellipse evolves at the BPM P1
  - This requires knowledge of position and angle at P1
  - Assume matrix N from MAD-X, reconstruct using P1 & P2
4

---
Reconstruct transfer matrix with
symplectic fit
MATLAB non-linear fitting code (fmincon). Solve for M:
- Where for the N difference orbits:
- And the symplectic constraint is applied:
5

---
Example data
- Example of reconstructed ellipse in TL2 BPM
  - Blue – data and symplectic fit
  - Dashed and solid red – original and modified MAD-X
6

---
CTF3
7

---
Delay loop optics measurements
- Good agreement with MAD-X for horizontal optics
- However, large discrepancy in the vertical plane
  - Lead to suspect modelling of dipole edge focussing
  - Developed an iterative optimisation routine in MATLAB
  - Reconciled with measurements by optimising dipole FINT
8

---
Delay loop vertical measurements
9

---
TL2 optics measurements
- Disagreement with MAD-X for both vertical and horizontal optics
- Suggests problem with quadrupole position and/or calibration
  - Confirmed positions are accurate during shutdown
  - Able to reconcile model by fitting selected quadrupole strengths and focussing due to vertical dogleg dipoles
  - Fits agreed to within a few percent for majority of magnets
  - One doublet with 25% error
- Optics to be rematched and exercise repeated after restart
10

---
TL2 horizontal measurements
11

---
TL2 vertical measurements
12

---
Summary
- Optics verification part of consolidation of CTF3 operation
- Confident of linac, TL1 and combiner ring MAD-X models
- Error in model of delay loop dipole edge focussing corrected
- Error in TL2 optics found
  - Model parameters fitted to measurements
  - New model to be confirmed with further data
13