## Slide 1: FEL activities and plans at SINAP
Gu Qiang
For the FEL team
Shanghai INstitute of Applied Physics (SINAP)

## Slide 2: Outline
FEL roadmap at SINAP
SDUV-FEL facility
  Linac
  FEL experiments
XFEL facility
  x-ray FEL facility (test facility)
  Hard x-ray FEL facility
Summary

## Slide 3: Roadmap of Shanghai FELs
Soft X-ray FEL
SDUV-FEL
Hard X-ray FEL
Conceptual design
Cons., Comm., Operation
100
10
0.1
nm
Desi.
Beamline, User?
Cons.
Comm.
1000
2009
2008
2011
2012
2013
2015
2019
2020
2014
2010
2016
2017
2018
SASE, HGHG,
EEGH, CHGHG
Gun
Comm.
Linac
Comm.
FEL
experiments

## Slide 4: The Shanghai Deep Ultra-Violet FEL project
High Gain FEL test facility, since 2000.
  Being carried out by Shanghai Institute of Applied Physics in cooperation with
  Institute of High Energy Physics
  NSRL, Univ. of Science and Technology of China
  Accelerator Lab. of Tsinghua University
Fund partially supported by
  Chinese Academy of Sciences (CAS)
  Ministry of Science and Technology of China (MOST)
  National Natural Science Foundation of China (NSF)
Goal
  HGHG at the very first stage
  EEHG, CHGHG & new operation scheme of the high gain FEL

## Slide 5: The linac
2009.4~2011.6
2011.8~2012.4

## Slide 6: Beam parameters
 | 2009.4~2011.6 | 2011.8~2012.4
Beam energy (MeV) | 130 | 190
Energy spread(%) | 0.3 | 0.2
Bunch charge (nC) | 0.2 | 0.2
Beam current (A) | 100 | 100
Global norm. emittance (umrad) | ~4 | ~3

## Slide 7: Milestones of FEL experiments
2009.09~12: SASE experiment
2010.01~03: Seeded FEL Installations
2010.05: Seeded FEL experiments start
2010.05.17: HGHG signal
2010.05.23: First Echo signal (‘double-peak’)
2010.07~08: Install. for high harmonics EEHG
2010.12: HGHG saturation
2011.04: EEHG amplification
2011.08~ 2012.4 : Cascaded HGHG

## Slide 8: HGHG principle
L.H. Yu, PRA 44, 5178 (1991)

## Slide 9
Linac
Exit
Mod1
Mod2
Radiator
EMU100
PMU20
Seed
ODS2
DS1
DS2
HGHG
ODS1
ODS=Optical Diagnostics Station

## Slide 10: Widely-tunable and fully-coherent HGHG FEL
Paper submitted to PRL
Notes: 10

## Slide 11: EEHG principle
G. Stupakov, PRL 102, 074801 (2009)

## Slide 12
Linac
Exit
Mod1
Mod2
Radiator
EMU100
PMU20
Seed1
Seed2
ODS=Optical Diagnostics Station
ODS2
DS1
DS2
ODS1
EEHG
Notes: 12

## Slide 13
First lasing of EEHG FEL
FEL profile
Gain curves
Spectrum
Experiments
Simulation
Nature Photonics 2012.105

## Slide 14: Future work on SDUV-FEL facility
Linac
  Install a new photocathode RF gun from Tsinghua University
  Install a new klystron (E3730A)
FEL experiments
  CHGHG
  Polarizing experiment with cross undulator
  ……

## Slide 15: Soft X-ray FEL project
Parameters | Value | Unit
Output Wavelength | 8.8 | nm
Bunch charge | 0.5 | nC
Energy | 0.84 | GeV
Energy spread | 0.1 | %
Norm. emittance | 2.5 | mm.mrad
Pulse length | 1. | ps
Peak current | ~0.5 | kA
Rep. rate | 10 | Hz
Proof test for the fully coherent X-ray FEL operation scheme
R&D on key components and technology
Test facility for the hard X-ray FEL in China for the future

## Slide 16: FEL scheme
Seed laser
798nm
1st stage
798nm =》44nm
FEL
Diag.
2nd stage
44nm =》8.8nm
84m
Seed laser
266nm
1st stage
266nm =》44nm
FEL
Diag.
2nd stage
44nm =》8.8nm
84m
CHGHG
EEHG+
HGHG

## Slide 17: Layout of Linac

## Slide 18: Layout of the RF system
 | S-band | S-band | S-band | C-band | X-band | unit
No. of sets | 1(+1) | 2 | 3 | 4 | 1 | 
frequency | 2.856 | 2.856 | 2.856 | 5.712 | 11.424 | GHz
Kly. power | 50 | 80 | 80 | 50 | 50 | MW
Repetition rate | 10 | 10 | 10 | 10 | 10 | Hz
No. of acc. structure | 1(2) | 1 | 2 | 2 | 1 | 
Gradient | 120 | 25 | 18 | 40 | 25 | MV/m
SLED | No | No | No | Yes | No | 

## Slide 19: Longitudinal jitter budget
 | error | dE(%) | dI(%) | dt(fs)
inj_arr | 0.25ps | 0.0308 | 6.6666 | 10.3842
inj_Q | 5% | 0.0304 | 1.5227 | 23.5803
L1_pha | 0.09deg | 0.0614 | 3.2216 | 88.1103
L1_volt | 0.04% | 0.0216 | 0.0277 | 31.51897
Lx_pha | 0.4deg | 4.97E-03 | 6.2115 | 6.571162
Lx_volt | 0.1% | 8.7E-03 | 0.1438 | 12.64579
L2_pha | 0.09deg | 2.64E-03 | 0.1528 | 2.113066
L2_volt | 0.04% | 0.016 | 0.0664 | 10.23434
L3_pha | 0.18deg | 0.0482 | 1.72E-13 | 4.64E-06
L3_volt | 0.04% | 0.0199 | 4.05E-14 | 1.58E-06
BC1_R56 | 0.02% | 8.88E-03 | 0.1268 | 16.03079
BC2_R56 | 0.02% | 2.76E-03 | 0.0212 | -4.99334
total |  | 0.0963 | 9.79 | 100

## Slide 20: Beam break-up study

## Slide 21: R&D of key components

## Slide 22: Schedule of the soft x-ray FEL
2013.2, Approval of the feasibility study
2013.3, Approval of the preliminary study
2013.7, Ground breaking
2014.7, Utility installation starts
2014.10, Linac installation starts
2015.3, Linac commissioning starts
2015.12, First Lasing

## Slide 23: Compact hard X-ray FEL
Compact XFEL
580m

## Slide 24: Main parameters of the compact hard X-ray FEL
Parameters | Value | Unit
Output Wavelength | 0.1 | nm
Bunch charge | 250 | pC
Energy | 6.4 | GeV
Normalized emittance | 0.4 | mm.mrad
Energy spread (sliced) | 0.01% | 
Pulse length (Full) | 100 | fs
Peak current | 3 | kA
Rep. rate | 60 | Hz
FEL parameter | 3.41*10-4 | 
Peak power | 10 | GW
Peak brightness | 2*1033 | 
3D gain length | 2.156 | m
Saturation length | 50 | m

## Slide 25: Preliminary design of the linac
40MV/m, 0deg
20MV/m
-27.5deg
-47mm
21.5MV/m
0deg
1.5m,
0.005GeV
0.1%
25A
280m,
6.4GeV
0.050%
4000A
-8mm
15m,
0.125GeV
0.15%
100MV/m
30deg
57MV/m
180deg
40MV/m
-15deg
36m,
0.321GeV
1.92%
90m,
1.194GeV
0.522%
60m,
0.321GeV
1.92%
500A
115m,
1.194GeV
0.522%
4000A
L0(s)
L1(s)
Gun
BC1
L2(c)
BC2
L3(c)
X
 | S-band | S-band | S-band | C-band | X-band | unit
No. of sets | 1 | 2 | 2 | 44 | 1 | 
frequency | 2.856 | 2.856 | 2.856 | 5.712 | 11.424 | GHz
Kly. power | 50 | 80 | 80 | 50 | 50 | MW
No. of acc. structure | 1 | 1 | 2 | 2 | 1 | 
Gradient | 120 | 25 | 18 | 40 | 57 | MV/m
SLED | No | No | No | Yes | Yes | 

## Slide 26: Summary
In SINAP we are conducting an ambitious and systematic strategy on FELs in response of the rapidly growing demands for the next generation coherent photon source.
R&Ds on key FEL concepts and technologies are well integrated in the SDUV-FEL test facilities.
SDUV-FEL experiments: ongoing, and many interesting results are coming out.
SXFEL: funded, design studies under way, construction will begin at middle 2013 and complete expected in 2015.
Welcome to IPAC2013 in Shanghai!

## Slide 27: Thank you for your attention

## Slide 28: Cascaded HGHG
2-Stage cascade HGHG
Courtesy of L.H.Yu

## Slide 29: The two-stage cascaded HGHG FEL
CH01
CV01
B15-18
Q19
CH19
CV19
CH04
CV04
Q16
Q13
Q14
Q15
DS1-1
B3
Q18
Q17
DS1-2
B4-B7
Q30
UDR
Q20
CH20
CV20
Q21
CH21
CV21
Q22
CH22
CV22
Q23
CH23
CV23
Q24
CH24
CV24
PMU
sRad
B8
CH02
CV02
Q1-1
Q1-2
Q1-3
ADC-2
ADC-1
MC3-C
MC3-A
SeedInj-1
SeedInj-2
MC3-B
MC3-D
MC5-B
MC5-A
MC5-C
MC5-D
BPM4
BPM5
UN-POP3/4
UN-POP9/10
UNPRF0
ADC-POP2
ADC-POP1
UN-POP1/2
UN-POP5/6
UN-POP7/8
UN-POP11/12
CCD Motor
UNPRF1
UNPRF2
UNPRF3
UNPRF4
Coll.1
Coll.2
UNPRF5
UNPRF6
UNPRF7
CBPM
MOD2
Delay Line
B19-B21
DS2
B22-B24
B9
Stage-1
Stage-2

## Slide 30: Preliminary result
Radiation from 1st stage
Radiation from 2nd stage
Notes: 30