## Slide 1: TRAINING COURSE on radiation dosimetry
Quantities and units in radiation dosimetry
Marco SILARI, CERN
1th Annual ARDENT Workshop, Vienna, 20-23 November 2012

## Slide 2
1895
Discovery of X rays
Wilhelm C. Röntgen
1897
“Discovery” of the electron
J.J. Thompson
1897
First treatment of tissue with X rays
Leopold Freund
The beginnings of modern physics and of medical physics

## Slide 3
Henri Becquerel (1852-1908)
1896
Discovery of natural
radioactivity
Marie Curie Pierre Curie
(1867 – 1934) (1859 – 1906)
1898
Discovery of polonium and radium
Thesis of Mme. Curie – 1904
α, β, γ in magnetic field
Hundred years ago
The beginnings of modern physics and of medical physics

## Slide 4
1911: first practical application of a radioisotope (as radiotracer) by G. de Hevesy, a young Hungarian student working with naturally radioactive materials in Manchester
1924: de Hevesy, who had become a physician, used radioactive isotopes of lead as tracers in bone studies
First practical application of a radioisotope

## Slide 5
James Chadwick
(1891 – 1974)
1932
Discovery of the neutron
Cyclotron + neutrons = first attempt of radiation therapy with fast neutrons at LBL (R. Stone and J. Lawrence, 1938)
The beginnings of modern physics and of medical physics

## Slide 6
Directly ionizing radiation:
fast charged particles (e.g., electrons, protons, alpha particles), which deliver their energy to matter directly, through many small Coulomb-force interactions along the particle’s track
Indirectly ionizing radiation:
X- or g-rays photons or neutrons (i.e., uncharged particles), which first transfer their energy to charged particles in the matter through which they pass in a relatively few large interactions, or cause nuclear reactions
The resulting fast charged particles then in turn deliver the energy in matter
The deposition of energy in matter by indirectly ionizing radiation is a two-step process
photon  electron
neutron  proton or recoiling nuclei
Directly and indirectly ionizing radiation

## Slide 7
Why is radiation dosimetry important?
Unique effects of interaction of ionizing radiation with matter
Biological systems (humans in particular) are particularly susceptible to damage by ionizing radiation
The expenditure of a trivial amount of energy (~4 J/kg or Gy) to the whole body is likely to cause death
Even if this amount of energy can only raise the gross temperature by about 0.001 °C
This is because of the ability of ionizing radiation to impart their energy to individual atoms and molecules
The resulting high local concentration of absorbed energy can kill a cell either directly or through the formation of highly reactive chemical species such as free radicals (atom or compound in which there is an unpaired electron, such as H or CH3) in the water medium that constitutes the bulk of the biological material
Main aim of dosimetry = measurement of the absorbed dose (energy/mass)
Notes: Ionizing radiation can also produce gross changes, either desirable or deleterious, in organic compounds by breaking molecular bonds, or in crystalline materials by causing defects in the lattice structure. Even steel can be damaged by large fluxes of fast neutrons, suffering embrittlement and possible fracture under mechanical stress (e.g., ITER)

## Slide 8
delta rays
Ionization event (formation of water radicals)
Light damage - reparable
Clustered damage - irreparable
Water radicals attack the DNA
The mean diffusion distance of OH radicals before they react is only 2-3 nm
OH•
e-
Primary particle track
Courtesy R. Schulte
DNA damage

## Slide 9
Radiobiological effectiveness (RBE)

## Slide 10
P
How many rays (i.e. photons or particles) will strike a point P in radiation field?
The answer is zero, since a point has no cross-sectional area with which the rays can collide
So: how can we describe the radiation field at P?
The random nature of radiation
Associate some nonzero volume to the point P
Simplest volume is a sphere centered at P (it presents the same cross-sectional area to rays incident from all directions)
How large should this imaginary sphere be?
  It depends on whether the physical quantities we wish to define w.r.t. the radiation field are:
    Stochastic
    Non-stochastic

## Slide 11
Stochastic quantity
Its values occur randomly and cannot be predicted. However, the probability of any particular value is determined by a probability distribution
It is defined for finite (i.e. non-infinitesimal) domains only. Its values vary discontinuously in space and time, and it is meaningless to speak of a gradient or rate of change
In principle, its values can each be measured with an arbitrarily small error
The expectation value Ne of a stochastic quantity is the mean of its measured values N as the number n of observations approaches
as

## Slide 12
For given conditions its value can, in principle, be predicted by calculations
It is, in general, a “point function” defined for infinitesimal volumes; hence it is a continuous and differentiable function of space and time, and one may speak of its spatial gradient and time rate of change
Its value is equal to, or based upon, the expectation value of a related stochastic quantity, if one exists. Although non-stochastic quantities in general need not be related to stochastic quantities, they are so related in the context of ionizing radiation
Non-stochastic quantity

## Slide 13
The volume of the imaginary sphere surrounding P may be small but must be finite if dealing with stochastic quantities
This volume may be infinitesimal, dV, in reference to non-stochastic quantities
Likewise the great-circle area da and contained mass dm, as well as the irradiation time dt may be expressed as infinitesimal with non-stochastic quantities
Most common and useful quantities for describing radiation fields and their interaction with matter are non-stochastic
Stochastic quantities are mostly involved with microdosimetry (the determination of energy spent in a small but finite volume)  next year workshop at the Politecnico of Milano, October 2013
Microdosimetry is of particular interest in relation to biological cell damage  T. Waker’s lecture
Stochastic and non-stochastic quantities

## Slide 14
In general a “constant” radiation field is random w.r.t. how many rays or particles arrive at a given point per unit area and time interval
The number of rays or particles observed (counted by a detector) in repetitions of the measurement follows a Poisson distribution, which can be approximated by a Gaussian for large number of events
Standard deviation σ of a single random measurement N relative to :
= expectation value of the number of rays detected per measurement
Percent standard deviation S:
=
A single measurement N has 68.3% chance of lying within ±σ of Ne, 95.5% chance of lying within ±2σ of Ne and 99.7% chance within ±3σ
(Remember that as )
Counting statistics

## Slide 15
Quantities describing the radiation field (e.g., fluence)
Quantities describing the medium with which the radiation field interacts (e.g., stopping power)
Dosimetric quantity =
= quantity describing the field x constant of the medium
Radiation fields can be described by a set of non-stochastic quantities
Radiation dosimetry
In radiation dosimetry we have:

## Slide 16
= expectation value of the number of rays or particles striking a finite sphere surrounding point P during a time interval from a starting time t0 to a later time t
The sphere around P is reduced to an infinitesimal with great-circle area da
( m-2 or cm-2)
FLUENCE at a point P
Fluence

## Slide 17
FLUX DENSITY OR FLUENCE RATE at a point P
( m-2 s-1 or cm-2 s-1)
is the increment of fluence during the infinitesimal time interval dt at time t
may be defined for all values of t through the interval from t0 (for which = 0) to t = tmax (for which = max). Then at some time t within the interval t0  t:
Flux density or fluence rate

## Slide 18
The fluence at P for the time interval t0  t1
For a time-independent radiation field, = constant and
It is important to note that:
and express the sum of rays or particles incident from all directions, and irrespective of their quantum or kinetic energies  basic information
a radiation field is often composed of various components (e.g., photons, neutrons, charged particles), which are – as far as possible – measured separately, as their interaction with matter are fundamentally different
Fluence and fluence rate

## Slide 19
The energy fluence sums the energy of all individual rays or particles
R = expectation value of the total energy (exclusive of rest-mass energy) carried by all the Ne rays striking a finite sphere surrounding point P during a time interval from t0 to t
The sphere around P is reduced to an infinitesimal with great-circle area da
(J m-2 or erg cm-2)
R = E Ne
1 eV = 1.602 x 10-19 J
Energy fluence
For the special case where only a single energy E of rays is present:
Notes: Individual particle or photon energies are usually given in keV or MeV, which is the kinetic energy acquired by a single charged particle in falling through a potential difference of one thousand or one million volts

## Slide 20
may be defined for all values of t through the interval from t0 (for which=0) to t = tmax (for which = max). Then at some time t within the interval t0  t:
ENERGY FLUX DENSITY OR ENERGY FLUENCE RATE at a point P
= increment of energy fluence during the infinitesimal time interval dt at time t
(J m-2 s-1 or erg cm-2 s-1)
Energy flux density or energy fluence rate

## Slide 21
and for constant
Similarly to what written above for the fluence rate:
For monoenergetic rays of energy E (for whichthe energy flux density may be related to the flux density by:
Energy fluence and energy fluence rate

## Slide 22
Differential distributions versus energy and angle of incidence
Most radiation interactions are dependent upon the energy of the ray as well as its type, and the sensitivity of radiation detectors typically depends on the direction of incidence of the rays striking it
The radiation field must usually be described in terms of its energy and angular distributions
In principle one could measure the fluence rate at any time t and point P as a function of kinetic energy or quantum energy E and of the polar angles of incidence θ and β, to obtain the differential fluence rate:
θ, β, E) (m-2 s-1 sr-1 eV-1)
(According to the energy range, one uses keV-1 or MeV-1 instead of eV-1)
Notes: Polar coordinates. The element of solid angle is
Polar coordinates. The element of solid angle is 𝑑Ω

## Slide 23
Number of rays per unit time having energies between E and E + dE which pass through the element of solid angle dΩ at the given angles θ and β before striking the small sphere centered at P, per unit great-circle area of the sphere:
θ, β, E) dΩ dE (m-2 s-1 or cm-2 s-1)
Integrating over all angles and energies, one obtains the flux density :
=
(m-2 s-1 or cm-2 s-1)
Similar expressions are valid for the energy fluence rate, fluence and energy fluence
Differential distributions versus energy and angle of incidence

## Slide 24
Simpler and more useful differential distributions of fluence, fluence rate, energy fluence and energy fluence rate are those which are functions of only one of the variables θ, β or E
When E is the chosen variable, the resulting differential distribution is called the energy spectrum of the quantity
For example:
Energy spectrum of the fluence rate summed over all directions, E):
=
(m-2 s-1 keV-1 or cm-2 s-1 keV-1)
and integrating over all energies of the rays gives of course
Energy spectra

## Slide 25
Energy spectra
E
E’
0
0
E1
E2
E’

## Slide 26
Flat spectrum of photon fluence rate versus photon energy E
Corresponding spectrum of energy fluence rate ’(E)
’(E) = E
Energy spectra
Example

## Slide 27
=
The component of the fluence rate consisting of the particles of all energies arriving at P through the annulus lying between the two polar angles θ1 and θ2 is:
If the radiation field is symmetrical w.r.t. the vertical axis z, it can be described in terms of the differential distribution of e.g. the fluence rate as a function of polar angle θ
If
is expressed e.g. in m-2 s-1 radian-1
Angular distributions

## Slide 28
Differential distribution of fluence rate per unit solid angle, for particles of all energies:
(m-2 s-1 sr-1)
and integrating over all directions:
=
For a field that is symmetrical about the z-axis, is independent of β, and integrating the previous expression over all β–values:
= 2
Angular distributions

## Slide 29
PLANAR FLUENCE: the number of particles crossing a fixed plane in either direction (=summed by scalar addition) per unit area of the plane
θ = angle of incidence of rays or particles on surface da
If the angular distribution of the rays or particles is isotropic:
= 1/2
If the radiation field is unidirectional:
Planar fluence
P
da
P
da

## Slide 30
Planar fluence
Particles scattered through the same angle q
Spherical and flat detectors of equal cross-sectional areas
No of scattered particles striking spherical detector = (1/cos q) x no of particles striking flat detector
Same fluence
Notes: This increase in fluence by the (1/cos θ) factor contributes to an effect sometimes seen in broad-beam geometry, in which the fluence behind an attenuation layer can be greater that that incident on it

## Slide 31
In radiation dosimetry three non-stochastic quantities describe the interaction of a radiation field with matter:
the kerma K, describing the first step in energy dissipation by indirectly ionizing radiation = energy transfer to charged particles
the absorbed dose D, describing the energy imparted to matter by all kinds of ionizing radiations, but delivered by the charged particles
the exposure X, which describes x- and g-fields in terms of their ability to ionize air
  A related quantity is the mean energy expended per ion par production in a gas,
Interaction of ionizing radiation with matter

## Slide 32
Uncharged ionizing radiation lose their energy in relatively few large interactions, whereas charged particles typically undergo many small collisions, losing their kinetic energy gradually
An uncharged particle has no limiting range in matter, beyond which it cannot go
Charge particles encounter such a range limit as they run out of kinetic energy
For comparable energies, uncharged particles penetrate much farther through matter, on the average, than charged particles, although this difference gradually decreases at energies above 1 MeV
Interaction of ionizing radiation with matter

## Slide 33
Total coefficients for attenuation, energy transfer and energy absorption
Total mass attenuation coefficient for g-ray interactions (neglecting photonuclear reactions):
photoelectric effect
Compton effect
Rayleigh scattering
pair production
(cm2 g-1 or m2 kg-1)
mass attenuation coefficient
σ = cross section
NA = Avogadro’s constant (6.022·1023 mol-1)
A = atomic weight
Notes: NOTE: while 𝜇/𝜌 and 𝜇tr/𝜌 are based only on the hν and Z actually present at the point of photon interaction, 𝜇en/𝜌 must also be based on an assumption about the medium through which the secondary electrons pass in slowing down. Usually the interaction point is assumed to be surrounded by the same homogenous medium, at least to a distance equal to the max electron range. Exception: near an interface between two media

## Slide 34
Mass energy-transfer coefficient
Mass energy-absorption coefficient
average fraction of secondary electron energy lost in radiative interactions (bremsstrahlung and β+ annihilation)
For low Z and low hν, g  0
= fraction of energy of incident particles transferred to kinetic energy of secondary particles
For photons:
Total coefficients for attenuation, energy transfer and energy absorption
Notes: NOTE: while / and tr/ are based only on the hν and Z actually present at the point of photon interaction, en/ must also be based on an assumption about the medium through which the secondary electrons pass in slowing down. Usually the interaction point is assumed to be surrounded by the same homogenous medium, at least to a distance equal to the max electron range. Exception: near an interface between two media
NOTE: while 𝜇/𝜌 and 𝜇tr/𝜌 are based only on the hν and Z actually present at the point of photon interaction, 𝜇en/𝜌 must also be based on an assumption about the medium through which the secondary electrons pass in slowing down. Usually the interaction point is assumed to be surrounded by the same homogenous medium, at least to a distance equal to the max electron range. Exception: near an interface between two media

## Slide 35
Example: mass attenuation coefficient for soft tissue (Z = 7)
Total coefficients for attenuation, energy transfer and energy absorption

## Slide 36
Exponential attenuation of uncharged ionizing radiation (g and neutrons)
m = linear attenuation coefficient
(narrow beam) (cm-1 or m-1)
1/m = mean free path = average distance a single particle travels in a medium before interacting
A distance of 3/m reduces the beam intensity to 5%, 5/m to <1%
= probability of interaction in an infinitesimal thickness
Notes: Uncharged ionizing radiation lose their energy in relatively few large interactions, whereas charged particles typically undergo many small collisions, losing their kinetic energy gradually
An uncharged particle has no limiting range in matter, beyond which it cannot go; charge particle encounter such a range limit as they run out of kinetic energy
For comparable energies, uncharged particles penetrate much farther through matter, on the average, than charged particles, although this difference gradually decreases at energies above 1 MeV

## Slide 37
Stopping power and LET
dE = energy lost by the particle in path-length
dE = energy locally imparted to the medium in collision events
= cut-off on energy of d-rays
The expression “locally” can be more or less restrictive

## Slide 38
In broad-beam geometry, the effective attenuation coefficient m’ > m
Narrow- and broad-beam attenuation
Strictly speaking, exponential attenuation is only observed for a monoenergetic beam of identical uncharged particles that are absorbed without producing scattered secondary radiation
Notes: The value of attenuation coefficient includes the partial coefficients for all types of interactions by the primary particles, since a particle ceases to be primary when it undergoes its first interaction of any kind
The value of attenuation coefficient 𝜇 includes the partial coefficients for all types of interactions by the primary particles, since a particle ceases to be primary when it undergoes its first interaction of any kind

## Slide 39
Two methods to achieve narrow-beam attenuation:
Discrimination against all scattered and secondary particles that reach the detector
(on the basis of particle energy, penetrating ability, direction, etc)
Narrow-beam geometry, which prevents any scattered or secondary particle from reaching the detector
Narrow-beam geometry

## Slide 40
For narrow-beam geometry B = 1
For broad-beam geometry B > 1
B is a function of radiation type and energy, attenuation medium and depth, geometry and measured quantity (e.g. energy fluence, kerma, dose)
For example, for energy fluence :
= unattenuated primary energy fluence
= total energy fluence at the detector behind a medium thickness L
= narrow-beam attenuation coefficient
The build-up factor

## Slide 41
No attenuation between source and detector
phantom
L = 0
for most broad-beam geometries,
except when detector on phantom surface
Here > and > 1
is called backscatter factor
For 60Co photons on a water phantom = 1.06 for tissue dose
The build-up factor

## Slide 42
- +
where:
= radiant energy of uncharged particles entering the volume V
= radiant energy of uncharged particles leaving V, except that which originated from radioactive losses of kinetic energy by charged particles while in V
= net energy derived from rest mass in V (m E positive, E m negative)
The energy transferred is a stochastic quantity defined as:
The radiant energy is the energy of particles (except rest energy) emitted, transferred or received
The energy transferred is just the kinetic energy received by charged particles in V (regardless of where or how they in turn spend that energy)
Energy transferred
Notes: Radiative losses = conversion of charged-particle kinetic energy to photon energy, through either bremsstrahlung x-ray production or in-flight annihilation of positrons

## Slide 43
Kerma (Kinetic Energy Released to Matter)
Relevant only for indirectly ionizing radiation (photons and neutrons)
= expectation value of the energy transferred in the finite volume V (the sum of the initial kinetic energies of all charged particles produced by the indirectly ionizing particles in V)
= expectation value for the infinitesimal volume dv at point P
dm = mass of dv
(Gy) (1 Gy = 1 J/kg = 100 rad)
The average value of K in a volume V of mass m is /m

## Slide 44
For monoenergetic photons, the kerma is related to the energy fluence by:
is the linear energy-transfer coefficient (m-1 or cm-1) and / is the mass energy-transfer coefficient (function of the photon energy E and atomic number Z of the medium)
For a spectrum of photons:
differential distribution of photon energy fluence
/ are numerical values tabulated for selected photon energies and materials
(Gy)
Relation of kerma to energy fluence for photons

## Slide 45
Average value of / for the spectrum :
Relation of kerma to energy fluence for photons

## Slide 46
Neutron fields are usually described in terms of flux density (or fluence) instead of energy flux density (or energy fluence)
Kerma factor (Fn)E,Z:
and:
For neutrons with energy spectrum [cm-2 MeV-1] of particle fluence:
(Gy)
(Gy cm2)
(Gy)
are numerical values tabulated for selected neutron energies and materials
Relation of kerma to fluence for neutrons

## Slide 47
Average value of Fn for a neutron spectrum :
Kerma factors are used to convert dose or kerma measured in a tissue-equivalent material to absorbed dose or kerma in tissue the correction to be applied is the ratio of the kerma factors
Relation of kerma to fluence for neutrons

## Slide 48
For photons, the kerma consists of energy transferred to electrons and positrons per unit mass of medium
K = Kc + Kr
Kc = collision kerma = energy spent by the electrons in collisions (ionization and excitation in or near the electron track)
Kr = radiative kerma = energy spent by the electrons in radiative-type interactions or by positrons through in-flight annihilation
For neutrons, the resulting charged particles are protons and heavier recoiling nuclei:
Kr << Kc  K = Kc
Components of kerma

## Slide 49
+
The net energy transferred is a stochastic quantity defined for a volume V as:
= radiant energy emitted as radiative losses by the charged particles which originated in the volume V, regardless of where the radiative loss event occur
and K include energy that goes to radiative losses
and Kc do not include such losses
Net energy transferred

## Slide 50
= expectation value of the net energy transferred to charged particles per unit mass at the point of interest, excluding both the radiative-loss energy and the energy passed from one charged particle to another.
Average value of collision kerma throughout a volume of mass m:
For monoenergetic photons, Kc is related to the energy fluence via the mass energy-absorption coefficient / :
Collision kerma Kc
(similarly to
)

## Slide 51
For a low-Z medium and small photon energy E (small radiative losses):
/
Kc K
Percentage by which / is less than
Collision kerma Kc
And similar as seen above for an energy spectrum

## Slide 52
Kerma rate at point P and time t
(Gy s-1 or Gy h-1)
Integrated kerma between times t0 and t1:
and for constant kerma rate:
Kerma rate

## Slide 53
+ +
where:
= radiant energy of uncharged particles entering the volume V
= radiant energy of all uncharged radiation leaving V
= radiant energy of the charged particles entering V
= radiant energy of the charged particles leaving V
= net energy derived from rest mass in V
(m  E positive, E  m negative)
The energy imparted is a stochastic quantity defined as:
Energy imparted

## Slide 54
Absorbed dose and dose rate
The absorbed dose is relevant to all types of ionizing radiation fields and to any ionizing radiation source distributed within an absorbing medium
= expectation value of the energy imparted in the finite volume V during a given time interval
d = expectation value of the energy imparted in an infinitesimal volume dV at point P
dm = mass of dV
D is the expectation value of the energy imparted to matter per unit mass at point P
(Gy)
Average absorbed dose in a volume of mass m:
Notes: D represent the energy per unit mass which remains in the matter at P to produce any effect attributable to the radiation.
If D = 0 there can be no radiation effect.
Thus, the absorbed dose is the most important quantity in radiological physics.

## Slide 55
Energy imparted, energy transferred and net energy transferred
Compton interaction followed by bremsstrahlung emission
+ +
+
- +
The energy transferred is just the kinetic energy received by charged particles in V (regardless of where or how they in turn spend that energy)
Notes: = radiant energy of uncharged particles leaving V, except that which originated from radioactive losses of kinetic energy by charged particles while in V
= radiant energy emitted as radiative losses by the charged particles which originated in the volume V, regardless of where the radiative loss event occur
(𝑅_𝑜𝑢𝑡 )𝑢_^𝑛𝑜𝑛𝑟 = radiant energy of uncharged particles leaving V, except that which originated from radioactive losses of kinetic energy by charged particles while in V
〖𝑅′〗_𝑢 = radiant energy emitted as radiative losses by the charged particles which originated in the volume V, regardless of where the radiative loss event occur

## Slide 56
Example involving g-ray emission, pair production and β+annihilation
g-ray emitted by a radioactive atom
Energy imparted, energy transferred and net energy transferred
= net energy derived from rest mass in V (m E positive, E m negative)

## Slide 57
Only defined for x-ray and g-ray photons
= absolute value of the total charge of the ions of one sign produced in air when all the electrons and positrons liberated by photons in air of mass are completely stopped in air
the ionization arising from the absorption of bremsstrahlung emitted by the electrons is not to be included in (only relevant at high energies)
(C/kg)
The exposure X
Notes: The ionization arising from the absorption of bremsstrahlung emitted by the electrons is not to be included in (only relevant at high energies).
A part for this difference, the exposure X coincides with the ionization equivalent to kerma in air
The ionization arising from the absorption of bremsstrahlung emitted by the electrons is not to be included in 𝑑𝑄 (only relevant at high energies).
A part for this difference, the exposure X coincides with the ionization equivalent to kerma in air

## Slide 58
Relation of exposure X to energy fluence
The exposure X is the ionization equivalent of the collision kerma in air, for x- and g-rays
Exposure X at a point P due to an energy fluence of monoenergetic photons of energy E:
1 R (roentgen) is the exposure that produces in air one esu of charge of either sign per 0.001293 g of air (the mass contained in 1 cm3 at 760 Torr and 0°C)
1 R = 2.58 x 10-4 C kg-1
(C kg-1)

## Slide 59
Exposure occurring between times t0 and t1:
(C kg-1 s-1 or R s-1)
Exposure rate
For a photon spectrum with energy fluence :

## Slide 60
Characterization of x- or g-fields by the exposure X
The energy fluence is proportional to X for any given photon energy or spectrum
Air is similar to soft tissue (muscle) in effective atomic number, so that it is “tissue-equivalent” w.r.t. x- or g-ray energy absorption
If one is interested in the effect of x- or g-radiation in tissue, air may be substituted as a reference medium in a measuring instrument
X α
Kc in muscle α
/
for E = 4 keV – 10 MeV

## Slide 61
Charged-particle and radiation equilibrium
Generally, the transfer of energy (kerma) from a photon beam to charged particles at a particular location does not lead to the absorption of energy by the medium (absorbed dose) at the same location
(e.g., a 10 MeV electron has a range in water of about 5 cm)
All energy transferred by photons to electrons is deposited in M D = K
Electrons originates outside M but deposit part of their energy in M D > K
Electrons originates in M but deposit part of their energy outside M D < K
If (b) and (c) compensate each otherCPE D = K

## Slide 62
Radiation equilibrium
Sketch courtesy M. Kissick
and
Radiation equilibrium
Medium of homogeneous atomic composition
Medium of homogeneous density
Radioactive source uniformly distributed
No electric and magnetic fields present to perturb the charged-particle paths
The dimensions of the volume are much larger than the mean free path of the radiation
= mean free path of the photons
r = radius to the edge of the volume

## Slide 63
Charged-particle equilibrium
+
Charged-particle equilibrium
Medium of homogeneous atomic composition
Medium of homogeneous density
Radioactive source uniformly distributed
No inhomogeneous electric and magnetic fields present
The dimensions of the volume are much larger than the mean free path of the secondary charged-particles

## Slide 64
Photon energy (MeV)
bone
air
muscle
Charged-particle and radiation equilibrium
Conversion coefficients from energy fluence to absorbed dose
(for CPE and negligible radiative losses)

## Slide 65
Charged-particle equilibrium
β = D / Kc
if radiative losses are negligible
Notes: As a high-energy photon beam penetrates the medium, collisional kerma is maximal at the surface of the irradiated material because photon fluence is greatest at the surface. Initially, the charged particle fluence, and hence the absorbed dose, increases as a function of depth until the depth of dose maximum (zmax) is attained. This build-up of absorbed dose is responsible for the skin sparing effect in the case of high energy photon beams. However, in practice the surface dose is small but does not equal zero, because of the electron contamination in the beam due to photon interactions in the media upstream from the phantom or due to charged particles generated in the accelerator head and beam modifying devices.

## Slide 66
Depth in medium
K0
Relative energy per unit mass
Point at which CPE exists
Transient charged-particle equilibrium
B = build-up factor
m = attenuation coefficient
Build-up region
TCPE region
Notes: In the more realistic situation, however, due to photon attenuation and scattering in the medium, a region of TCPE occurs, where there exists an essentially constant relation between collisional kerma and absorbed dose. This relation is practically constant since, in high energy photon beams, the average energy of the generated electrons and hence their range, do not change appreciably with depth in the medium.
Kerma stays slightly lower than absorbed dose, since the secondary charged particles that contribute to kerma at a given depth x also contribute to dose at depth x + dx

## Slide 67
Compton
Charged-particle equilibrium
Radiative losses are negligible (and K = Kc) for low energy photons and neutrons (secondaries are protons and nuclei)
CPE exists (no CP enter or exit)
hn’’ is included in K
hn’’ in not included in D and Kc
D = Kc < K
K – D = Kr
If the electron would not radiate part of its energy Kr = 0
In carbon, water, air and other low-Z media, Kr = K - Kc < 1% for photons up to 3 MeV

## Slide 68
Dose, kerma and collision kerma
(a.u.)
Depth (a.u.)
Uncollimated beam of high-energy photons impinging perpendicularly on a semi-infinite slab of absorbing material
For e.g. 6 MeV photons on Al:
=
At the surface:
Notes: The maximum of dose occurs at the point where the increment of dose deposited by the electrons equal the increment of the attenuation of the primaries

## Slide 69
Dosimetry fundamentals
CPE
TCPE
For photons
For neutrons
CPE
TCPE
CPE
CPE
m’ is the common slope of the K, D and Kc curves
is the mean distance the secondary charged particles carry they kinetic energy in the direction of the primary rays while depositing it as dose

## Slide 70
Relating absorbed dose D in air to exposure X for x- or g-fields
CPE
J/kg
J/kg
C/kg
34 J/C
If D is in Gy and X is in Roentgen, remembering that:
and 1 R = 2.58 x 10-4 C kg-1

## Slide 71
Bibliography
F. H. Attix, Introduction to radiological physics and radiation dosimetry, Wiley-VCH (2004)
International Commission on Radiation Units and Measurements, ICRU Report 33, Radiation quantities and units (1980)
F.H. Attix , W.C. Roesch and E. Tochilin, Radiation dosimetry, 2nd edition, Vols. I-III, Academic Press (1966-1969)
In Italian
M. Pelliccioni, Elementi di dosimetria delle radiazioni, ENEA (1983)
R.F. Laitano, Fondamenti di dosimetria delle radiazioni ionizzanti, 2a edizione, ENEA (2011)