## Slide 1: Machine protection aspects of injection and extraction for the CLIC DR
R. Apsimon

## Slide 2: Failure modes
Fast failures
  Particles hit aperture within few turns
    E.g. injection and extraction kicker failures
  Passive protection needed (collimators, absorbers)
Slow failures
  Failure slow enough to abort/dump beam before it hits aperture
    E.g. magnet power supply failure
  Use extraction system to remove beam

## Slide 3: Injection kicker failure modes
Inductive adder level failure
  20 levels: supply ~700V each
  Consider up to 3 levels failing simultaneously
    Assumed to be caused by failure of FETs on level
    ~8σ event, so realistic worst-case scenario.
Total inductive adder failure
    Likely to be due to a trigger timing error
    ALL particles considered dangerous and hit aperture shortly downstream of injection
    Injection collimator designed to capture full 6σ beam (+ tolerances)

## Slide 4: Collimator considerations [1]
Number of σ that can pass through aperture
Region | A1/2 (mm) | H-plane | V-plane | H-plane | V-plane
LSS | 12 | ≥13.3 | ≥65.3 |  | 
Arc | 20 | ≥33.7 | ≥126.1 |  | 
 |  | Injection cell |  | Extraction cell | 
1st quad | 20 | 17.1 | 246.5 | 17.1 | 246.5
Septum | - | 7.1 | 242.7 | 9.3 | 110.8
Kicker | 12 | 9.9 | 263.0 | 8.7 | 119.9
δ = alignment tolerance = 2mm
A1/2 = physical half-aperture
Acceptance calculations at injection emittance

## Slide 5: Collimation considerations [2]
Beam aperture critical in injection/extraction regions
  Use absorbers to protect septa (fixed position)
  Collimators to protect rest of machine (moveable)
Collimation scheme depends on whether septa are in vacuum or not

## Slide 6: Septa in vacuum: H-plane
Red: kicker Orange: quads in injection cell
Blue: septum edge Brown: quads in matching cell
Purple: stored beam Green: Injected beam (total kicker failure)
Dark green: region of beam removed by first collimator

## Slide 7: Septa not in vacuum: H-plane
Red: kicker Orange: quads in injection cell
Blue: septum edge Brown: quads in matching cell
Purple: stored beam Green: Injected beam (total kicker failure)
Dark green: region of beam removed by first collimator

## Slide 8: Comments on collimator plots
Beam envelope
  6σ envelope ± 2mm tolerance
First collimator
  Needed to stop particles hitting aperture before reaching second collimator
Second collimator
  Designed to completely capture beam for total kicker failure

## Slide 9: Injection/extraction parameters
 | Septa in vacuum | Septa not in vacuum
Kicker parameters |  | 
Aperture | 12 mm | 12 mm
Voltage | ±12.5 kV | ±12.5kV
Kicker length | 2.43 m | 2.58 m
Thin septum parameters |  | 
Gap field | 0.2T | 0.2T
Length | 0.87 m | 0.85 m
Thick septum parameters |  | 
Gap field | 1T | 1T
Length | 2.02 m | 1.99 m
Inj/ext cell length | 7.90 m | 9.36 m
Matching cell length | 2.39 m | 3.09 m
Total length | 10.29 m | 12.45 m

## Slide 10: Comparison of schemes
Septa in vacuum
    Smaller beams; good aperture clearance
    >4 m reduction in total length of DR
      This is almost entirely drift length
Septa not in vacuum
    Efficient collimation

## Slide 11: Tracking simulations
Tracking done for failure of 3 inductive adder levels
  1000 particles for 100 turns
    Uniform random number generators: 6σ ± 2mm phase space
    Polar coordinates to create oval beams
  340 “dangerous” particles
    Exceed 6σ ± 2mm phase space of nominal orbit
Turn number | % absorbed
At injection | 37.4%
1 turn | 52.1%
2 turns | 92.4%
3 turns | 95.9%
4 turns | 97.4%
10 turns | 99.1%
All particles captured by absorbers + collimators; no losses in kickers or elsewhere.
Remaining 0.9% of particles on edge of phase space limit and survive for many turns.

## Slide 12: Phase space: no collimation
Phase space plot at second injection collimator

## Slide 13: Phase space coverage: 1 turn
Blue: phase space of nominal orbit
Green: Phase space of poorly injected beam (3 levels failed) without collimation
Red: Phase space of poorly injected beam (3 levels failed) with collimation
Black: Phase space confined by collimation

## Slide 14: Phase space coverage: 2 turns
Blue: phase space of nominal orbit
Green: Phase space of poorly injected beam (3 levels failed) without collimation
Red: Phase space of poorly injected beam (3 levels failed) with collimation
Black: Phase space confined by collimation

## Slide 15: Phase space coverage: 3 turns
Blue: phase space of nominal orbit
Green: Phase space of poorly injected beam (3 levels failed) without collimation
Red: Phase space of poorly injected beam (3 levels failed) with collimation
Black: Phase space confined by collimation

## Slide 16: Phase space coverage: 4 turns
Blue: phase space of nominal orbit
Green: Phase space of poorly injected beam (3 levels failed) without collimation
Red: Phase space of poorly injected beam (3 levels failed) with collimation
Black: Phase space confined by collimation

## Slide 17: Dump system considerations
Latency
  How many turns before beam can be dumped?
Location and space constraints

## Slide 18: Breakdown of latency
Signal time of flight to dump kicker
    ~1μs
Latency of electronics
    <1μs
Kicker rise time
    ~700ns
Time for 1 turn of ring (circumference: 400-450m)
    1.3-1.5μs
~2-3 turns of ring required to dump beam

## Slide 19: Location + space constraints
Avoid
  Regions with synchrotron radiation
  High dispersion regions
    Near injection or extraction only suitable places.
Dedicated dump cell?
  Would add ~10m in each straight section
    Unacceptable increase in length
  Can extraction cell be used as dump system?

## Slide 20: Technical challenges
Kicker must fire in two modes
  Extraction mode (±12.5kV)
  Dump mode (±17.5kV)
    Need to extract beam with injection emittance
Separate dumped beam from extracted

## Slide 21: How to achieve 2 kicker modes
Separate inductive adder into 2 banks of levels
  “Bank 1” contains 20 levels
  “Bank 2” contains 8-10 levels
  Extraction trigger discharges Bank 1
  Dump trigger discharges Banks 1 and 2

## Slide 22: Kicker triggering
Bank 1
Bank 2
Trigger select
“Extract”
Bank 1
Bank 2
Trigger select
“Dump”

## Slide 23: Consideration of damping time [1]
Time needed to damp beam:
  Injection: 54 μm rad (x), 1.3 μm rad (y)
  Extraction: 500 nm rad (x), 5 nm rad (y)
  Equilibrium: 470 nm rad (x), 4.8 nm rad (y)

## Slide 24: Consideration of damping time [2]
~8.5 damping times to reach design
  17ms (injection period 20ms)
How long to charge inductive adder?
  Currently unknown, estimate ~90% at injection
    Add levels in Bank 2 to compensate missing charge?
    Reduce storage time by ~1 damping time?
      4% increase in extraction emittance; acceptable?

## Slide 25: Kicker failure modes
Extraction mode
  Both banks fire: beam dumped → safe
  Bank 1 fires: beam extracted → safe
  Bank 2 fires: beam absorbed by septum absorber and collimator → safe
  Neither bank fires: beam remains in ring
Dump mode
  Both banks fire: beam dumped → safe
  Bank 1 fires: beam extracted → NOT SAFE
  Bank 2 fires: beam absorbed by septum absorber and collimator → safe
  Neither bank fires: beam remains in ring

## Slide 26: Separate ext and dump beams
Start of extraction line
  Kicker gives larger deflection to dumped beam
  Use defocussing quad to further separate beams
Septum magnet to separate ext and dump lines
  Use same septa design as in extraction system

## Slide 27: Current design: h-plane

## Slide 28: Comments on design
Septa in vacuum?
  Easier if extraction septa NOT in vacuum
    More lever-arm; less length needed to separate beams
    Twiss parameters more controllable
Final quad needed in dump line
  Control spot size at dump block

## Slide 29: Radiation length
Need minimum 5 rad. lengths for 2.86 GeV e-
  Use 10 rad. lengths for dump block
  Use 5 rad. lengths for absorbers and collimators
Material | Density (kg m-3) | Radiation length (m)
Beryllium | 1.84 X 103 | 0.353
Carbon | 2.25 X 103 | 0.188
Titanium | 4.50 X 103 | 0.036
Copper | 8.93 X 103 | 0.014
Tungsten | 19.3 X 103 | 0.0035
Higher density means more back scattering, but shorter radiation length

## Slide 30: Material choice
In DR, space is limited
  short radiation length and low back-scattering
    Use titanium: ~20cm for collimators and absorbers
Dump block
  Space not limited
    Use carbon for dump block
    Surround block in higher mass material (e.g. lead) to contain radiation.