## Slide 1: Step IV & VI: Local Flux Return

## Slide 2: Outline
Introduction and Concept
Shielding efficiency
Extension to Step VI
Effect on beam
Forces

## Slide 3: Local Flux Return
Explore shielding options
  Initially only for Step IV, but should also work for Step VI (or upgradable)
What has been done so far?
  general concept
  performance Step IV&VI (all cases)
  effect of shielding on field of MICE
  individual components
    walls, Q9, floor, …
However, there are many things which have not been done so far…

## Slide 4: Concept
To get good shielding horizontally: need continuous steel in azimuthal direction
Geometry
  Tube of radius 1.2 m
  wall thickness 10 cm
  azimuthally -50..50°
  weight: 30t
1.5 m
2 m
R1.2
(Note: not to scale)

## Slide 5: Magnetization In Shield
Wall thickness: 10 cm
r = 1.2 m

## Slide 6: Initial Situation
Peak: 550 Gauss at r=1.5m
Average: ~ 300 Gauss

## Slide 7: Shielding Efficiency
r = 1.5 m
B < 15 Gauss (1.5 mT)
Step IV, 240 MeV/c, flip

## Slide 8: Development of Fringe Field
r = 2 m

## Slide 9: Development of Fringe Field
r = 3 m

## Slide 10: Development of Fringe Field
r = 4 m

## Slide 11: Fringe Field
Vertical Position: 0.75m

## Slide 12: Options for Extension Step VI
MICE Step VI: significantly larger in diameter
  Coupling coils
  RF waveguides
Adaption of scheme possible?
Ideally:
  single scheme for both scenarios
  Or: possibility of modification

## Slide 13: Extension to Step VI
Required: closed iron surface in long. direction

## Slide 14: Geometry
4 m
5.6 m
t=0.1m
t=0.3m
r=1.8m
r=1.2m
100°
Weight: 130t
(both halfs)

## Slide 15: Geometry
CC
CC
Spectrometer
Spectrometer

## Slide 16: Geometry
Outside faces removed

## Slide 17: 200 MeV Flip Mode
r=2.5m
Peak: 5.8 mT
Average: 3 mT?

## Slide 18: MICE Step VI – Option 2
Gap in radial direction
  still continuous flux return path in longitudinal direction
Shield at different radii
  azimuthal angles must match
  overlap seems not necessary
Allows feed-in/out of tracker wiring?

## Slide 19: MICE Step VI – Option 2

## Slide 20: Additional Iron Structures
Additions:
  ‘Virostek’ shields
  TOF cage
  Quad Q9 (simplified)
  Floor
Field reductions due to shield
  Q9: 63 to 36 mT
  Walls: 150 mT to 12 mT
Shield
Floor

## Slide 21: Effect on Field in Channel
1
2
3
R0.2

## Slide 22: Variation of Bz
ΔB with respect to Bz at θ=0°
θ

## Slide 23: Unwanted Multipole Components
Additional hor. field introduced by shield
5 mT @ r=150mm

## Slide 24: Unwanted Multipole Components
Caused by uncorrected
coil currents
2D Simulation

## Slide 25: 3D Field Correction

## Slide 26: Forces
Forces on shield under quench conditions
  Normal operation: no longitudinal force on proposed shield
  Cases studied: Step IV
    1. one tracker solenoid switched off
    2. one focusing coil switched off
Coil forces
Forces evaluated in Opera/VectorFields
  Maxwell stress tensor
  (virtual work gives identical results within simulation accuracy)
  Field evaluation: Mesh = nodal, coil = integral

## Slide 27: Forces on Shield
 | Hor. Force [kN] | Long. Force [N]
200 MeV Flip One tracker inactive | -13.6 | 73
200 MeV Sol One tracker inactive | -9.3 | 70
200 MeV One FC inactive | -30 | -8
Reference 200 MeV Flip | -30 | -158
Reference 200 MeV Solenoid | -13 | -143

## Slide 28: Coil Forces Step VI
 | No Iron | Iron | Change
FC1 | -3367202 | -3410424 | 1.012836
CC | -203400 | -379805 | 1.867281
FC2 | 3235323 | 3294357 | 1.018247
FC3 | -3281620 | -3339131 | 1.017525
Match 1 | -190322 | -199323 | 1.047294
Match 2 | -49992 | -51374 | 1.027644
End1 | -851298 | -850645 | 0.999233
Spect. Sol | -29037 | -14438 | 0.497228
End2 | 1400771 | 1407749 | 1.004982
Force in Newton

## Slide 29: Radial Field CC
Iron
No Iron

## Slide 30: Radial Field CC
F = (JxB)*V
Field difference (radial): 10 mT, J=115 A/mm2
V=(2*pi*0.8)*0.25*0.1
F=140 kN
r [m]
z [m]

## Slide 31: Step VI Force on CC
Add ‘nose’ to shield
Force (Opera 3D):
198 kN (97% of TRD)

## Slide 32: Engineering
Courtesy of Jason Tarrant, STFC
BNL engineering effort to look into practical design and manufacturing
Present estimate: Full design 1st week January
Procurement: 4 months

## Slide 33: Geometric Freedom

## Slide 34: Conclusion
Conceptual design of local flux return
  reduces stray field in hall significantly (factor 30)
  shield: about 30t of iron (130t for Step VI)
  force on shield manageable
Effect on beam
Effect on other iron structures in hall
  Q9, floor, walls
Extension to Step VI possible
  includes solution for natural breaks in shield for wire feed-in/out
Engineering

## Slide 35: Additional Slides

## Slide 36: Simulation Details
Finite element simulations
  Opera from VectorFields/Cobham
  Comsol Multiphysics
Iron
  AISI 1010 steel
  BH curve: Opera/VF
(Benchmarking)

## Slide 37: 3D Field Correction

## Slide 38: Quad Q9
Shield: 36 mT (average)
No Shield: 62mT

## Slide 39: Walls
Shield: 12 mT (peak)
No Shield: 150 mT (peak)
Reduction of factor 10+