## Slide 1
The LHC future:
the CMS perspective
T.Camporesi, CERN
LISHEP 2013

## Slide 2: LHC prediction trustfulness
2010: 0.04 fb-1
  7 TeV
  Commissioning
2011: 6.1 fb-1 (exp 5)
  7 TeV
  … exploring the limits
2012: 23.3 fb-1 (exp 20)
  8 TeV
  … production
…. We better take seriously the LHC predictions….

## Slide 3: LHC plans

## Slide 4: Map into CMS space

## Slide 5: A comment about statistics
Stat. halving time Assuming flat lumi accumulation
Flat lumi accumulation is probably not the right assumption: trigger selection can influence stats for specific searches/measurements

## Slide 6: The accelerator complex
What we know
What to expect

## Slide 7: Performance from injectors 2012
Bunch spacing [ns] | Protons per bunch [ppb] | Norm. emittance H&V [microns] Exit SPS
50 | 1.7 x 1011 | 1.8
25 | 1.2 x 1011 | 2.7
Design report with 25 ns:
1.15 x 1011 ppb
Normalized emittance 3.75 microns

## Slide 8: Radiation effects (SEU ++)
~3 dumps per fb-1
2012
~12 dumps per fb-1
2011
2011/12 xMasBreak ‘Early’ Relocation + Additional Shielding + Equipment Upgrades
Several shielding campaigns prior the 2011 Run + Relocations ‘on the fly’ + Equipment Upgrades
< 0.5 dump per fb-1
>LS1 (nominal -> ultimate)
R2E-Project aiming for …
2012 SEE Failure Analysis
Equipment relocations @ 4 LHC Points (>100 Racks, >60 weeks of work)
Additional shielding
Critical system upgrades (QPS, FGC)

## Slide 9: 25 ns & electron cloud
Typical e– densities: ne=1010–1012 m–3 (~a few nC/m)
Typical e– energies: <~ 200 eV (with significant fluctuations)

## Slide 10
10
Warp and Posinst have been further integrated, enabling fully self-consistent simulation of e-cloud effects: build-up & beam dynamics
CERN SPS
at injection (26 GeV)
Turn 1
Turn 500
Miguel Furman ECLOUD12

## Slide 11: Electron cloud: consequences
Possible consequences:
  single-bunch instability
  multi-bunch instability
  emittance growth
  gas desorption from chamber walls
  excessive energy deposition on the chamber walls (important for the LHC in the cold sectors)
  particle losses, interference with diagnostics,…
In summary: the EC is a consequence of the interplay between the beam and the vacuum chamber “rich physics”
  many possible ingredients: bunch intensity, bunch shape, beam loss rate, fill pattern, photoelectric yield, photon reflectivity, SEY, vacuum pressure, vacuum chamber size and geometry, …
Defense: design (saw-tooth pattern on the beam screen inside the cold arcs, NEG coatings, solenoids, etc.)
Electron bombardment of a surface has been proven to reduce drastically the secondary electron yield of a material.
This technique, known as scrubbing, provides a mean to suppress electron cloud build-up and its undesired effects

## Slide 12: The 2012 25 ns scrubbing
  Reconstructed comparing heat load meas. and PyECLOUD sims.
  3.5 days of scrubbing with 25ns beams at 450GeV (6 - 9 Dec. 2012):
  Regularly filling the ring with up to 2748b. per beam (up to 2.7x1014 p)
  Scrubbing effects in the arcs:
  Quite rapid conditioning observed in the first stages
  The SEY evolution significantly slows down during the last scrubbing fills (more than expected by estimates from lab. measurements and simulations)

## Slide 13: 25 ns & electron cloud
There is a change of mode of operation with 25 ns. Electron cloud free environment after scrubbing at 450 GeV seem not be reachable in acceptable time.
Personal convinction: Need to ramp and scrub
Operation with high heat load and electron cloud density (with blow-up) seems to be unavoidable with a corresponding slow intensity ramp-up.
2015: SEY etc. will be reset - initial conditioning will be required
  FROM LHC OPS: Will need to start with 50 ns and only later to move to 25 ns to recover vacuum, cryogenics, UFOs conditions we were used in 2012.

## Slide 14: Beam from injectors LS1 to LS2
 |  | Bunch intensity [1011 p/b] | Emittance,[mm.mrad] | Into collisions
25 ns ~nominal | 2760 | 1.15 | 2.8 | 3.75
25 ns BCMS | 2520 | 1.15 | 1.4 | 1.9
50 ns | 1380 | 1.65 | 1.7 | 2.3
50 ns BCMS | 1260 | 1.6 | 1.2 | 1.6
BCMS = Batch Compression and (bunch) Merging and (bunch) Splittings
Batch compression & triple splitting in PS
Rende Steerenberg, Gianluigi Arduini, Theodoros Argyropoulos, Hannes Bartosik, Thomas Bohl, Karel Cornelis, Heiko Damerau, Alan Findlay, Roland Garoby, Brennan Goddard, Simone Gilardoni, Steve Hancock, Klaus Hanke, Wolfgang Höfle, Giovanni Iadarola, Elias Metral, Bettina Mikulec, Yannis Papaphilippou, Giovanni Rumolo, Elena Shaposhnikova,…

## Slide 15: 50 versus 25 ns
 | 50 ns | 25 ns
GOOD | Lower total beam current Higher bunch intensity Lower emittance | Lower pile-up
BAD | High pile-up Need to level Pile-up stays high High bunch intensity – instabilities… | More long range collisions: larger crossing angle; higher beta* Higher emittance Electron cloud: need for scrubbing; emittance blow-up; Higher UFO rate Higher injected bunch train intensity Higher total beam current
Expect to move to 25 ns because of pile up…

## Slide 16: b* reach at 6.5 TeV

## Slide 17: Potential performance
 | Number of bunches | Ib LHC FT[1e11] | beta*X beta*sep Xangle | Emit LHC [um] | Peak Lumi [cm-2s-1] | ~Pile-up | Int. Lumi per year [fb-1]
25 ns | 2760 | 1.15 | 55/43/189 | 3.75 | 9.2e33 | 21 | ~24
25 ns low emit | 2320 | 1.15 | 45/43/149 | 1.9 | 1.5e34 | 42 | ~40
50 ns | 1380 | 1.65 | 42/43/136 | 2.5 | 1.6e34 level to 0.9e34 | 74 level to 40 | ~45*
50 ns low emit | 1260 | 1.6 | 38/43/115 | 1.6 | 2.2e34 level to 0.9e34 | 109 level to 40 | ~45*
6.5 TeV
1.1 ns bunch length
150 days proton physics, HF = 0.2
85 mb visible cross-section
* different operational model – caveat - unproven
All numbers approximate

## Slide 18: HL -LHC
This is a new regime: Phase 1 detectors were designed to handle between 1 and 2 1034 Hz/cm2

## Slide 19: The CMS view point
The short term challenges
The upgrade program:
Phase 1
Phase 2 ( HL LHC)

## Slide 20: HLT : challenges for 2015
2012: 8 TeV HLT s ∼0.09 μb
  PU=25, small dependence on PU
8 TeV→ 14TeV  rates double
  Average output rate of ~ 1.2kHz at 1034cm-2s-1 if menu untouched.
To keep the present acceptance:
  Improve HLT object reconstruction
    Allowing tighter cuts
  Reconsider strategies
    More cross triggers
  Will need more CPU
    e.g. to extend PF usage
    Particularly if PU <> grows above 25
20
σHLT≈ 0.09μb

## Slide 21: The Tier-0 Today
Many improvements
  But reco time is still non-linear with instantaneous luminosity
Preparing for both extremes of 25 and 50 ns bunch spacing
  Goal is to keep the physics performance the same as run1.
    Our physics projections are made with that assumption.
7500
35
Off the chart:
Start of record fill
21

## Slide 22: 50 ns spacing is too hard…
Projecting ahead
  Would need a factor of 10 reduction in cpu time per event to maintain our current perfromance at highest projected luminosities
  Realistically?
    Could conceivably foresee factor of 2 reduction in cpu time per event
      We already gained factor of 3 in early 2012
18000
80
70
60
50
10000
40
90
100
125
150
175
7500
Points measured from current
release as run on high PU MC
Previous slide
22
Peak lumi X 1033 Hz/cm2
50 ns and ultimate lumi need major upgrade of computing resources and SW improvements/sacrifices

## Slide 23: CMS upgrade program

## Slide 24: Detector upgraded in LS1
DT sector collectors
HF PMT
ME4 endcap muons
ME1 FE electronics
Cold trackrer operation
New beampipe

## Slide 25: Short term (LS1)
Completion of staged projects:
  Completion of muon coverage
  Implement Cold tracker operation
Fix problems detected in first LHC run
  HF, Cerenkov light from PMT windows: replace PMTs with new thinner window and multianode PMTs
  Replace HPD for HO with Si-PM (unforeseen instability of HPDs at fields lower than 3 T)
  Consolidation of DT front-end fiber readout (sector collector)off-cavern: allows intervention and easy reconfiguration for trigger upgrade +new front-end theta trigger board ( FPGA based)
Prepare for future upgrades :
  New smaller diameter beam-pipe ( necessary if wanting to install new pixel in extended end of year shutdown)
  Optical splitting of calorimeter trigger lines+ new optical output for muon trigger ( to allow parallel commissioning of trigger upgrade –mTCA based- during LHC operation in 2014-2015)
  Install new HF backend electronics (mTCA to replace VME) : first step of full HCAL upgrade
See Gilvan
See Gilvan
See Gilvan

## Slide 26: LS1 Muon Upgrades
Target Rate 5 kHz
Trigger performance: significantly lower threshold for same rate
CSC and RPC: ME4/2 (1.25<|η|<1.8)
More hits, lower rates
CSC: ME1/1 (2.1<|η|<2.4) new digital boards and trigger cards : higher strip granularity
Electronics reliability
DT: new trigger readout board and relocation of sector collector from UXC55 to USC55 (new optical links)

## Slide 27: Medium term (LS1 to LS2): pixel
Features of New Design
Robust design: 4 barrel layers and 3 endcap disks at each end
Smaller inner radius (new beampipe), large outer
New readout chip with expanded buffers,
embedded digitization and high speed data link
Reduced mass with 2-phase CO2 cooling, electronics moved to high eta, DC-DC converters
Ready to install by end of 2016

## Slide 28: Upgraded Pixel tracking
6
Tracking efficiency for tt ̄ sample with ROC data losses.  pions etc. (hadronic interactions)
current detector
upgrade detector
0 PU
25 PU
50 PU
100 PU
Fake Rate= 6% (h=0, 100PU)
Fake Rate= 2% (h=0, 100PU)
better 0 PU
Current Pixel front end designed to handle 1034... Beyond the FE buffer structure does not keep up

## Slide 29: Upgrade: Pixel b-tagging
b-jet efficiency
~ 1.3x better
@ 10-2 udg-rej.
current
upgrade
Primary vertex resolution improved by gain factor ~1.5 - 2

## Slide 30: Pixel upgrade: use case H→4ℓ
Event selection: (as 2012 analysis)
events with ≥ 4 isolated leptons
2 leptons with pT>17 GeV and 8GeV
same 2 leptons with Npixhit >2
e-reconst. PF and h<2.5, pT>7GeV
m-reconst. PF and h<2.4, pT>5GeV
leptons from primary vertex SIP3D< 4
40 GeV < MZ1 < 120 GeV
12 GeV < MZ2 < 120 GeV
pT(l) >10,20 GeV & M4l >100 GeV
Significant gain in signal reconstruction efficiency:
H 4m +41%
H 2m2e +48%
H 4e +51%
Conclusion:
Upgrade detector provides physics reach as current detector with 40-50% more efficiency.

## Slide 31
9
Event selection:
events with ≥ 2 leptons + ≥ 2 jets
pT>20 GeV for leptons & jets
H with highest pT combination
Z with hightest pT combination
75 GeV < MZ < 105 GeV
pT >100 GeV for both H & Z
H & Z back to back: Df < 2.9
CSV tag on both b-jets
light jet rejection 0.1% (HE) & 1% (LE)
Both lepton channels (mm, ee) show gain of 65% in signal efficiency for upgraded system.
HLT Trigger with 3 out of 4 hits from upgraded pixel for muons may benefit significantly.
Upgrade pixel system will lead to considerable increased sensitivity in this channel.
Z  m+m-
Pixel upgrade:ZH  ℓ+ℓ-+2 b-jets

## Slide 32: LS1 to LS2: HCAl
HB/HE: replace HPD with SIPMs
Improved S/N and depth segmentation
Improved calibration, bkg & PU suppression, EM isolation (analysis and trigger)
Install front-end electronics in LS2
Paramount to maintain efficient Particle flow
approach in high pileup environment
See detailed presentation this afternoon: here only a summary

## Slide 33: L1 Trigger Upgrade

## Slide 34: Longer term: LS3,HL-LHC
Si –trackers to be replaced: tracker in L1 trigger
Endcap calorimeters very likely to need replacement/upgrades (assessing longevity)
Muon chambers: the detectors themselves should still be ok. Issue will be trigger ( and possibly readout)
Physics needs & performance: being assessed

## Slide 35: HL-LHC /LS3
Need stepping up R&D and design effort in the next 2 years: if we want to be ready for installation in 2022 we need to have clear ideas ( read TR-level) of what to build by end 2014.
0th order: need a detector with the same performance as today: hence require replacement of components rad damaged
But running at lumi of 5 1034 (pileup ≳ 100) will require substantially improved detector

## Slide 36: Challenges of HL HLC
5 1034 Hz/cm2 luminosities challenges for CMS
  Trigger: studying of having Tracker in L1 trigger to provide parameters of tracks with Pt >2 GeV ( including estimate of vertex!) to correlate with other trigger info at first level
  Exploring what would be needed to have 1 MHz L1 trigger ( and longer L1 trigger decision latency)
  Particle flow : will need high calorimetric granularity
  In forward region will need to have ways to estimate vertex origin of physics objects ( thinking about VBF like tagging) : looking into what VERY forward tracking and fast timing devices could do.

## Slide 37
1033
1035
1032 cm-2 s-1
1034

## Slide 38: Preview ( special fill ): what we learned
Reconstruction algorithms are such that one can assume that with
a working detector (this implies major upgrades for LS3!)
adequate granularity
one can cope with extreme conditions… Heavy ion running an additional proof.
We know that today trigger systems will be inadequate.

## Slide 39: LS3: Tracker trigger
Tracker stubs to be correlated with Muon stubs: allows to reduce by factor muon trigger rate at the ‘useful’ Pt thresholds
Present trigger rates flattens out at Pt ≳ 30 GeV
Simulation confirmed by special fill at high lumi

## Slide 40: VERY forward tracking (CMS study)
Courtesy of S. Mersi
Good resolution in Z0 reco down to h=4
Muon pT
100 GeV/c
10 GeV/c
1 GeV/c
Resolution < 1mm for pT>10 GeV/c down to h=4
s(dZ0)1 mm
Beneficial to VBF tagging as it provides coverage for Barrel/Endcap service cracks

## Slide 41: D0 and Pt resol VFPIXEL
Muon pT
100 GeV/c
10 GeV/c
1 GeV/c

## Slide 42: Fast timing: needs
For a luminous region distributed over ~ 10cm, collisions will be distributed over ~ 300ps
The TOF at the Calorimeter at h ~ 0 depends on the time of the specific collision
At Larger values of h the TOF depends both on the time and position of the specific collision

## Slide 43: A dream for the moment
Consider (for example) an EM pre-shower with 10~20ps (i.e few mm resolution in Z position) TOF resolution for MIP’s and g
  Tracking identifies Z location of interesting collision (high Pt)
  Preshower could deliver (TOF, h, f) of cluster (can be a EM shower or cluster of jet particles) from that collision
  Could imagine to correlate at trigger level Preshower(TOF, h, f), Calorimeter(E,h, f) and Tracking (Pt, Z vtx) info
  At analysis level use Z location and time to select calorimeter clusters associated to interesting collision
Could result in similar effective pile-up conditions comparable to what we are handling today
  ! ! Neutral hadrons will need special attention ! !

## Slide 44: An issue
At the time of LS2 the detector will have components ( e.g. forward calorimeters) whose manipulation might be rendered very difficult by the radiation problems.
This and the space constraints in the experimental hall can become a significant constraint of what can be done…and extensive study need to be done and possibly non trivial tooling developed. E.g. HF calorimeter (300 tons object) on the + side of the experiment cannot be moved as a single piece ( crane can handle 80 tons at most) … and its wedges will be radioactive to a level that dismantling into manageable units might be a real challenge

## Slide 45: Summary
CMS has been successful in exploiting the first LHC run and has a clear plan to maintain its excellent performance after LS1
A new era where commissioning of new components will happen in parallel to LHC operation will start after LS1
The experience from the past shows that we must have a clear idea of the CMS phase 2 detector within 2014, if we want to have it ready by LS3
In some areas ( e.g. calorimeters able to withstand a factor 10 of radiation compared to the first LHC phase, tracker/triggering, Very forward tracking…) vigorous R&D is necessary
The potential of High Luminosity LHC will be exploited only if we start preparing for it NOW

## Slide 46: Backup

## Slide 47: Fast timing: state of the art
Current state of the art for large scale systems is ~75ps: ALICE TOF
Fast RPCs (small prototypes) : 60 ps
Current State of the Art is 100~120ps for demonstrator TOF PET Calorimeter detectors
The goal of 10~20ps Calorimeter TOF resolution is beyond the current state of the art, and clearly ambitious
But so were many of today’s features of LHC detectors 10 years before beams….
Need to engage stakeholders : CERN, HEP laboratories, Universities into a focused R&D effort… and practical re-use of technology immediately obvious: PET scan.

## Slide 48: Muon hit rates – simulated, endcap
Curves w/wo neutron hits
  Slow n capture
   N*
   de-excitation g
   electrons
Highest rate/area in ME1/1
  Up to 10 kHz/cm2 at 1E35
High total rates in ME4/2
  Large area
ME1/1
ME1/2
ME1/3
ME2/2
ME2/1
ME3/2
ME3/1
ME4/2
ME4/1
CMS IN 2002/007

## Slide 49: HPD gain drifts

## Slide 50: HCAL doses after 500 fb-1

## Slide 51: Depth segmentation

## Slide 52: P flow with HCAl upgrade
Barrel
Endcap
Std pFlow @50 ns
Std pFlow @25 ns
pFlow(HCAL upgade) @25 ns
<Pileup>= 50

## Slide 53
4
Parameter of Pixel System
# layers (tracking points)
beam pipe radius (outer)
innermost layer radius
outermost layer radius
pixel size (r-phi x z)
In-time pixel threshold
pixel resolution (r-phi x z)
cooling
material budget X/X0 (h=0)
material budget X/X0 (h=1.6)
pixel data readout speed
1st layer module link rate (100%)
ROC pixel rate cabability
control & ROC programming
Present
3
29.8 mm
44 mm
102 mm
100m x 150m
3400 e
13m x 25m
C6F14 (monophase)
6%
40%
40MHz (analog coded)
13 M pixel/sec
~120 MHz/cm2
TTC & 40MHz I2C
Upgrade
4
22.5 mm (LS1)
29.5 mm
160 mm
100m x 150m
1800 e
13m x 25m (or better)
CO2 (biphase)
5.5%
20%
400Mb/sec (digital)
52 M pixel/sec
~580 MHz/cm2
TTC & 40MHz I2C
Pixel Parameters: Present & Upgrade

## Slide 54: Calorimeter trigger upgrade

## Slide 55: Muon trigger upgrade

## Slide 56: Fast timing practical interest

## Slide 57: Data parking: a + for next year
Parked data includes Core (will ‘reprocess’ only ‘parked’ with final ali/calib): i.e. 75% is Core and 25% new triggers

## Slide 58: VBF tags

## Slide 59: Higgs couplings

## Slide 60: Material budget VFWD pixel