## Slide 1: LAGUNA/LBNO WP4: secondary beam line status report
M. Calviani, P. Velten, A. Ferrari, I. Efthymiopoulos, C. Lazaridis (CERN)
+ M. Zito, V. Galymov (CEA), A. Rubbia, S. Murphy, S. Di Luise (ETHZ)
LAGUNA/LBNO DS meeting --- 20/09/2012

## Slide 2: Organization of the WG and activities
Started in April 2012 and focused (for the moment) on:
  Agreement on the main physics parameters
  Optimization of beam/target optimization
  Started analysing potential configurations of horn
  Muons in the ND and configuration of the decay pipe
CERN-oriented meetings held on a monthly basis to discuss the activities within the sub-WG
  Steering the activities on the LAGUNA/LBNO secondary beam line
Recently we have enlarged the participation to external members working on some aspects of the beam line in other institutes
  Important input from the experiment!

## Slide 3: Summary
Target optimization and potential cooling configuration
Horn/reflector studies
Decay pipe main parameters
Muon fluence in ND
On-going work

## Slide 4: Physics optimization
Quite some effort was spent in clarifying the main driving parameter of the beam line optimization
As the phase-space for the physics goal is very broad --- we would need the highest fluence in the range of the two first oscillatory peaks
1st peak == [3÷6] GeV
2nd peak == [1.2÷1.8] GeV
Maximize the total (peak1+peak2)
peak1/total ~ 0.5

## Slide 5: Neutrino production target optimization (1/2)
CNGS case:
  Ep = [20÷50] GeV
     q < 20 mrad
LAGUNA/LBNO:
  Ep = [2÷10] GeV
     q < 70/100 mrad
Objective:
  Produce as many p+ as possible in the required energy range
  Optimize their collection via magnetic horns (large angles)

## Slide 6: Neutrino production target optimization (2/2)

## Slide 7: Target optimization: target/beam radius
Maximum yield for a rT=4-6(8) mm
  Beam 1s =1-2 mm
Larger radiuses:
  Advantage for low energy p+
  Reduction of thermal stresses on target
  Optics?

## Slide 8: Energy dep and peak temperature
Evaluation:
  400 GeV/c
  Adiabatic, 7*1013 p/pulse
Peak DT/pulse comparable to CNGS case
  helped by larger beam size
4 mm radius
2.5 mm FWHM
Max DT~650 K
(450 K for 8 mm radius case)
Target outside horn is a major advantage
  Degree of freedom in target/horn design
  No problem of target/horn heat & electrical insulation
  Set as a design constraint
50 GeV (2 MW) phase will (probably) need a new optimization
Detailed studies to be conducted

## Slide 9: Ideas on target cooling and constraints
Target cooling possibilities for 750 kW phase
  Radiation cooling (a-la-CNGS)
  Forced He cooling and radiation cooling
  Target should be operating at 700/800 ºC
Radiation damage of graphite
  Expected ~0.3 DPA/y @750 kW
  At 600-1000 °C: dimension change and thermal conductivity are minimized
  Also reduce H embrittlement

## Slide 10: Summary on target optimization
Proposed configuration:
  Length: 130 cm
  Radius: 4-6 mm (8 mm possible)
  No segmentation
  Material: carbon @ r=1.85 g/cm3
  Target outside horn (or downstream part in “contact”)
Stresses and heat evacuation to be studied in detail as a function of the general design of target area
Is there already a constraint from the beam optics point of view?
target
horn

## Slide 11: Horn/reflector studies
Initially started by optimizing relative element position and currents
  “standard” shape optimized for a 50 GeV primary beam (parabolic shapes)
Attempts to vary the inner conductor shapes (“vast” amount of degree of freedoms)
dTH
dHR
IH
IR

## Slide 12: Horn/reflector studies
Effect of relative distance between target/horn
Both peaks optimization
Effect of relative distance between horn/reflector
Optimal horn configuration:
dTH=0 cm
IH=220 kA
Optimal reflector configuration:
dHR=10 m
IR=220 kA

## Slide 13: Horn/reflector shape studies
Different approaches are also done by scanning the phase space of inner conductor shapes
Example of scanning Bezier curve parameters for the horn design
Single parabola
Bezier
Single neck, fixed diameter
Double neck, different aperture for improved focusing
Bezier  improved fluence and improved balance!

## Slide 14: Decay pipe
200 m
400 m
600 m
r=150 cm
2x
Higher nm fluence for longer DP (~saturation for r>1.5m)
DP length partly imposed by the m fluence in the ND!
... And by costs!
Potential DP configuration
rDP=1.5 m, LDP ≤300 m
CNGS
rDP=1.2 m, LDP=1100 m

## Slide 15: Muons in the near detector and constrains
The m fluence (background for the experiment) in the ND is an issue which might contribute driving the
  HS design, DP length and ND distance from TS
In iron, dE/dx|m ~1.6 GeV/m  16 GeV/10m
In molasses, dE/dX|m~460 MeV/m  ~50 GeV/100m
HS in the present simulation setup:
  5 m carbon core
  12.5(17.5) m Fe shielding around
  WANF: 4x4.5x36 m3 + toroidal magnet (12 T*m, 10 m long, 6 m diameter)
17.5 meters
5 m
Fe
C
Hadron absorber ~15 m long
Molasses assumed ~2.4 g/cm3

## Slide 16: m± fluence in the ND
ND 500 m
ND 800 m
350 m
At 500 m from TS
  106 m/cm2/pulse
At 800 m
  ~100 m/cm2/pulse
  ~105 m/m2/1013 p+
Possible solutions being investigated:
  Reduction of primary beam energy to 350 GeV (equiv. to ~30 m of Fe)
  Massive increase of DP Fe blocks – costs?
  ND further away (much also deeper…)
    TOSCA was at ~700 m from m pit (1800 m from TS)  2.5 m/m2/1013 p+

## Slide 17: On-going work
Main medium-term objectives:
  Definition of an updated set of parameters for the installation
  Definition of a new “reference” neutrino fluence in the ND/FD
FLUKA modelling of target area based on a “chase” design
Energy deposition analysis
  750 kW/400 GeV/c and 2 MW/50 GeV/c beam
First radioprotection assessment of the area (with DGS/RP?)
  Prompt dose rate around TS (access/electronics?)
  Activation around the TS (+DP/HS)
  Air activation
Hadron absorber initial design
  Baseline design -- 2 MW beam

## Slide 18: Potential configuration
Initial configuration for preliminary evaluation
He container (?)
<30 meters
target
horn
reflector
DP collimator (Fe) – reduce load on structural part of DP
Concrete/Molasse
Concrete/Molasse
Air volume for structural support services
~3.5 m Fe
Movable steel plates
Movable concrete blocks
~4/5 m concrete
Primary beam zone
Decay pipe (DP)
baffle
Beam window (He-jet cooled)
Target station surface or underground building & services

## Slide 19
Marco.Calviani@cern.ch