## Slide 1: WP9.4 Summary
AIDA WP9.4 meeting

## Slide 2: Baseline vs. Advanced Deliverable
Baseline
Deliverable
Two orthogonal layers of u-strips
HPK SiLC sensors
AVP25 based hybrid
Provide precise entry point to calorimeter
Advanced Deliverable
Integration with CaloDAQ
Deliverable 2nd QT 2014
Ultra-light strip layer of thin sensors (230 um)
Conventional mechanics
Demonstrator of ILD silicon tracker
Integrated PA or 2D-Poly silicon or short strip sensors.
APV25 based hybrid
Light mechanics with embedded Fiber Optic Sensors
Integration with caloDAQ
Offline software
Offline Software
No deadline

## Slide 3: Schedule of yesterdays session

## Slide 4: Advanced deliverable

## Slide 5: ON Semiconductor
ON Semiconductor: 6” wafers
 stepping mask projection machines,
 the stitching technique is needed
„little“ problem with funding – delay
 problem with purchase 6“ P-type HiRes wafers  big lead time (Topsil)  received just recently
Purchase full ingot  big lead time  costly
 as a result we have quite good portfolio of wafers 6“: P-type, N-type, 300 micrometers thick.
Rushing with design – changing every day!! (not vaste time with details)

## Slide 6
Wafer layout
Strip layout
Sensor design

## Slide 7: Charge-Division Concept in ustrip Sensors (1)
Charge division used in wire chambers to determine the coordinate along the sensing wire.
Same concept with conventional microstrips with slightly resistive electrodes (doped polysilicon)

## Slide 8: Prototypes from CNM
two new prototypes with double-end readout and different resistivity.
Strip:
  length =20 mm
  width =20 um
Pitches:
  Implant=80 um
  readout= 80 um
Electrode:
  R/um = 2.8 Ohms/um
  R/um = 12.2 Ohms/um
Beatle chip

## Slide 9: VERY Preliminary results (1)
Imaging of the SPS beam profile.
Cluster correlation between opposite ends

## Slide 13: SMART Mechanics: Initial proposal
The aim is to manufacture a few ILD FTD support petals, both for real sensor support and thermo- mechanical mock-up
Petals matching the geometry of the 3th FTD geometry has been chosen, being the biggest one
Equiped with CNM manufactured sensors (four inches Wafers) , the structure will be scaled 0.65 :1
Petals mechanical and thermal behavior will be tested
Embeding of FOS sensors for selfmonitoring.

## Slide 14: Demostrator plate demostrator @ DESY
The First step is to manufacture and test this self monitoring structures
This demonstrator is a CFRP plate with ten FBG sensors embedded at a define position, allowing us to measure deformations under Torsion and Flexion loads, and temperature
When a torsion or a flexion load is applied to the sheet, we know from simulations the expected measured value of each sensor.
,
Flexion sensors
Torsion sensors
Top layer
Botton layer

## Slide 15: Demonstrator simulation under flexion loads
15

## Slide 16: Demonstrator simulation under flexion loads
16

## Slide 17: Demonstrator simulation under torsion loads
17

## Slide 18: Baseline deliverable

## Slide 19: Re-using old SiLC Sensors
Large sensor: 95 x 95 mm2
Structures for resolution studies
Specifications:
  Size: 95 x 95 mm2
  Very fine pitch: 50 µm pitch, 12.5 µm width, 1792 strips, 320 µm thickness
  Readout pitch: 150 µm pitch (512 channels), 2 intermediate strips
  Resolution studies have been performed with small structures of same wafer (but on 50 µm pitch)
  Expected resolution: due to analog readout better than 43 µm, due to inter medial strips approx. 15 µm (43/3)

## Slide 20: Recuperation of SiLC Sensors
Sensors glued
With stiff araldite:
Cook in toluene
At 100 degC

## Slide 21: Sensor Performance after disassembly
  IV curves show acceptable behavior
  Sensors are fully depleted at about 50 V
  Sensor on module will be operated at about 70 V-80V

## Slide 22: All components available:
Sensors
FE chips (APV 25 from CMS/Belle II)
Mechanics
Pitch adapters produced at CNM Barcelona

## Slide 23: Module Status
One module (consisting of two orthogonal sensors, FE electronics) fully built and tested
Two further modules to be built within next few weeks
  No problems expected
  Source tests by summer

## Slide 24: Data Acquisition System
Status:
  DAQ system based on APV25 FE chip (developed for CMS), TLU compatible
  Three versions:
    APVDAQ: lab-system for 4 APVs/boards; 1kHz using 1 card
    SiTra DAQ: 16 APVs/board; 3kHz
    Belle II System: 48APVs/board; up to 20kHz
APV25 chips
Front-end hybrids
Rad-hard voltage regulators
Analog level translation, data sparsification and hit time reconstruction
~2m copper cable
Junction box
~10m copper
cable
VME boards

## Slide 25: DAQ Details
Compatibility with (old) EUDET TLU box exists
  Has been used in previous testbeams with EUDET telescope
  offline merging of data streams
Interest to check possibilities with new AIDA TLU

## Slide 26: Status DAQ software
DAQ online software was ported recently from old Labwindows/CVI system to Linux/ROOT-based system
  Basic functionality available
  implementation of sophisticated run modes ongoing (ADC delay scan, calibration scan,…) to be done by the end of the year
  Offers modular system with online DQM
  Dummy EUDAQ producer exists, interface to new software seems to be possible

## Slide 27: Schedule

## Slide 28: Deliverable Month 39
D9.5) Silicon micro-strip ladders: The Silicon micro-strip ladders are installed in front of the Calorimeter stack delivered by WP9.5. The pointing precision and timing performance are characterized. The devices remain available for the study of the calorimeter performance in case of overlapping showers. [month 39: May 2014]

## Slide 29: Deliverable status
Baseline Deliverable
Re-use old SiLC sensors done.
APV25-based front-end done.
Conventional mechanics done.
readout system hardware done.
Offline software done
Online (DAQ) software (re-implementation ongoing)
Integration with common DAQ missing
Advanced Deliverable
  Sensors with integrated PA and/or 2D polysilicon sensors ongoing
  New frontend chip ongoing
  Light mechanics with embedded deformation measurement (fiber bragg sensors) ongoing
  Integration with common DAQ missing

## Slide 30: Summary
WP9.4 (one and only) deliverable will be available in summer this year
  Sensors, FE electronics, mechanics, offline software, DAQ Hardware (mid-size System, prototype of Belle II)
DAQ Software re-implementation ongoing
  Modular design
  Interface to EUDAQ possible
Testbeam in January 2014 at DESY (parasitically with Belle II beam test)
  DAQ software re-implementation finished then
  Common testbeam together with calorimeter has to be scheduled