## Slide 1
CAD Tools for 3D-IC and TSV-based designs
Kholdoun TORKI
Kholdoun.Torki@imag.fr
CMP
46, Avenue Félix Viallet,
38031 Grenoble, France
http://cmp.imag.fr

## Slide 2
Agenda
Introduction
Process overview
3D-IC Design Platform
3D-IC industrial CAD tools
Conclusion

## Slide 3
SiP versus 3D-IC

## Slide 4
Tezzaron Process Flow for TSV and DBI (using Via Middle process)
Starting wafer in 130nm (5 Cu metal layers + 6th Cu metal as DBI)
Source Tezzaron

## Slide 5
Top Tier
(10um thickness)
Bottom Tier
(Handle wafer)
Resulting 2-tier 3D-IC integration TSV and DBI (Via Middle Process)
Bond pad for wire bonding or bump, flip-chip …
Source Tezzaron

## Slide 6
Interconnection Type | Line Width (µm) | Line Thickness (µm) | Line Resistance (Ohm/cm) | Max Length (cm)
Direct Bond Interface (DBI) | 2-100 | 2-100 | 0 | 0
Through Si Via (TSV) | 1-100 | 1-100 | 500-1000 | 5-100
On-Chip | 0.1-2 | 0.1-2 | 100-1000 | 0.1-1.5
Thin-film | 10-25 | 5-8 | 1.25-4 | 20-45
Ceramic | 75-100 | 16-25 | 0.4-0.7 | 20-50
PCB | 60-100 | 30-50 | 0.06-0.08 | 40-70
Shielded Cables | 100-450 | 35-450 | 0.0013-0.033 | 150-500
Interconnections
 | Size | Capacitance | Series Resistance
DBI | 2µ | << | <
TSV | 1. 2µ | 2-3 fF | <1.5 Ω
Interconnections in the 3rd dimension at Tezzaron/GF 130nm

## Slide 7
The more is the Design Automation on the 3rd dimension, the more is the 3D-IC Integration.
2 D
2.5 D
Memory Stack
Simple Imaging Sensor
Pixel Sensor (HEP)
Multi-Processors + Memory
NoC
3 D
Processor + DRAM + RF + MEMS + Optical communication
Design Methodology
System Complexity

## Slide 8
3D-IC Design Platform

## Slide 9
Tezzaron / GlobalFoundries Design Platform
Modular Design Platform. It has all features for full-custom design or semi-custom automatic design.
  PDK : Original PDK from GF + (TSV / DBI) definition from Tezzaron
  Libraries : CORE and IO standard libraries from ARM
  Memory compilers : SPRAM, DPRAM and ROM from ARM
  3D-IC Utilities : Contributions developments embedded in the platform
  Tutorials, User’s setup.
All modules inside the platform refer to a unique variable, making it portable to any site. The installation procedure is straightforward.
Support of CDB and OpenAccess databases.

## Slide 10
assura
calibre
cds_cdb
cds_oa
doc
eldo
hercules
hspice
prep3DLVS
skill
spectre
strmMaptables_ARM
strmMaptables_Encounter
chrt13lprf_DK009_Rev_1D (Version issued in Q1 2011)
calibre:
3DDRC
3DLVS
DRC
FILLDRC
calibreSwitchDef
assura:
FILLDRC
LVS
QRC
hercules:
DRC
LVS
STAR_RCXT
PDK Tezzaron / GlobalFoundries

## Slide 11
DBI (direct bonding interface) cells library. (FermiLab)
3D Pad template compatible with the ARM IO lib. (IPHC)
Preprocessor for 3D LVS / Calibre (NCSU)
Skill program to generate an array of labels (IPHC)
Calibre 3D DRC (Univ. of Bonn)
Dummies filling generator under Assura (CMP)
Basic logic cells and IO pads (FermiLab)
Floor-planning / automatic Place & Route using DBIs, and TSVs (CMP)
Skill program generating automatically sealrings and scribes (FermiLab)
MicroMagic PDK (Tezzaron/NCSU)
Collaborative Work on the Design Platform
HEP labs contributing with Programs, Libraries, and Utilities. All included in the Design Platform

## Slide 12
Virtuoso Layout Editor with 3D layers and verification
TSV
Back Metal
Back Pad
DBI
Assura
Calibre
Virtuoso from Cadence IC 5.1.41

## Slide 13
Virtuoso from Cadence IC 6.1.4
Customized Menu with some utilities

## Slide 14
Libraries from Providers and Users
ARM
GF/TSC
FermiLab
IPHC
Univ. Bonn
NCSU

## Slide 15
Virtuoso / Calibre DRC Interactive Menu
Setting switches
graphically

## Slide 16
Choosing 2D
or 3D LVS
Virtuoso / Calibre LVS Interactive Menu

## Slide 17
3D viewer in Virtuoso Layout
- Graphically Interfaced into Virtuoso.
- Works for both CDB and OA.
- Use a free and open-source VRML viewer.

## Slide 18
IPHC Contribution for 3D-IC IO Libraries
Pad shell containing TSV and DBI allowing the use of the ARM IO libraries in 3D-IC designs

## Slide 19
IPHC Contribution for 3D-IC IO Libraries
Pad shell containing TSV and DBI allowing using the ARM IO libraries in 3D-IC designs

## Slide 20
IPHC Contribution for 3D-IC IO Libraries
Pad shell containing DBI and TSV connecting the pad to the backside bonding pad

## Slide 21
3D-IC Automatic P&R using DBI and TSV
3D Floor-Planning
DBI, TSV, IO placement
System Level Partitioning
Automatic Place & Route
Extraction, Timing Analysis
Physical verification
3D DRC, 3D LVS
Dummies Filling
Final 3D DRC
Design exploration at system level
Design exploration at the physical level
DBI, TSV, and IO placement & optimization
Cells and blocks place & route can be done tier by tier
To be done for each tier, then combined for back-annotation to the 3D top level system
Similar to the full-custom design flow

## Slide 22
Automatic Place & Route with Direct Bond Interface
- Custom scripts allowing routing pins on DBIs.
- The resulting layout is compliant to the Tezzaron DRC, LVS etc …
DBI completely routed down to the
lower metal layer
DBI array generation + P&R

## Slide 23
Saving the floor plan for the bottom tier, and apply it for top tier.
Place & Route taking into account the locations of the DBIs.
The place & route for both tiers is optimal for timing, buffer sizing and power performance.
This results in a “correct-by-construction” design.
Automatic P&R with Direct Bond Interface

## Slide 24
Cadence / Encounter Bump Array Generator

## Slide 25
Cadence / Encounter Signal Bumps Assignment

## Slide 26
Before
Before
After
After
Custom Scripts Enabling Routing on DBIs
Placing logical pins on bumps (DBIs), and extract their location.
Generating Physical pins from these locations.
They can now be used as terminals for routing.

## Slide 27
- DBIs Placement
- TSVs Placement
- Obstructions on TSVs
- Std cells Placement
- Clock Tree Synthesis
Filler Cells Placement
- Clock routing
- Final routing
Automatic P & R Design Flow (From Floor-Plan to Routed Design)

## Slide 28
Clock and all nets routing is enabled on M1-M5

## Slide 29
Cadence is making its 3D-IC design tools available to selected European academic institutions in partnership with the Europractice scheme operated by the UK Science and Technology Facilities Council Rutherford Appleton Laboratory
Proposals are being invited from the existing Europractice/Cadence user base of 378 European academic institutions
These selected early adopters will then be able to more efficiently design 3D-IC systems for their research projects, e.g. in new computer architectures, with the possibility of fabrication via existing broker services offered by CMP (Circuits Multi-Project) in France
Source John McLean
Rutherford Appleton Laboratory

## Slide 30
True 3D Mask Layout Editor
MicroMagic MAX-3D
Technology Files fully supported by Tezzaron

## Slide 31
MicroMagic 3D viewer

## Slide 32
MicroMagic 3D crossection

## Slide 33
Conclusion
A Design Platform resulted from the collaboration.
CMC, CMP, MOSIS, FermiLab, Tezzaron, HEP Labs, NCSU
Industrial CAD vendors just starting addressing the features.
Still awaiting for new CAD tools dedicated to 3D-IC Integration :
+ 3D-IC Partitioning : both at the system level and the floor-planning level.
+ Standard 3D layout editor (i.e. Virtuoso 3D)
+ Sign-off tools for 3D-IC Integration : (3D-DRC, 3D-LVS, 3D-Extration)