## Slide 1: Data Networks
ISOTDAQ 2013
Enrico.Bonaccorsi@cern.ch

## Slide 2: TCP/IP Protocols
Transport
Internet
Network access
Application
Ethernet
Frame Relay
Token Ring
PPP
HTTP
FTP
Telnet
DNS
RIP
SNMP
TCP/IP protocol suite
TCP
UDP
IP
ARP
IGMP
ICMP
17
6
23
20/21
80
520
53
0806
0800
88
01
161/162

## Slide 3: Networks
Networks connect s two or more computers
  Computers can be located anywhere
Networks can be categorized depending on the size:
  Local Area Network
  Metropolitan Area Network
  Wide Area Network

## Slide 4: Protocols
A protocol defines the syntax, semantics, and synchronization of communication
the specified behavior is typically independent of how it is to be implemented
A protocol can therefore be implemented as hardware or software or both

## Slide 5: History and Standards
1969: ARPANET is commisioned by the USA defense department for reasearch into networking
1972: First e-mail program written
  Telnet is specified
1973: Ethernet is outlined
  FTP is specified
1974: TCP is specified
1976: First email sent by Queen Elizabeth
1977: Number of hosts breaks 100
1981: IP Standard is published in RFC 791
1983: TCP/IP becomes the core Internet Protocol
1984: DNS is specified

## Slide 6: RFCs
http://www.ietf.org/
  Large, open, international community of network designers, operators, vendors and researchers concerned with the evolution of the Internet Architecture
  Open to any interested individual
Network managers will readily agree that networks need documentation.
RFCs (Request for Comments) document the functions of the Internet and the protocols that support it
The documentation process start with the Internet Draft

## Slide 7: ISO/OSI
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 8: Network Components
Hosts
Hubs
Switches
Routers

## Slide 9: Local Signaling
Data formatting
Session Handling
Routing
Local Signaling
Local Signialing is not part of the TCP/IP family of protocols, but an IP datagram requires a physical interface to get to the target station
Most popular LAN protocol in use today is Ethernet

## Slide 10: Ethernet
Destination address:
  UNICAST: 00 10 A4 BA 87 5B
  MULTICAST: 01 00 5E 00 00 09
  BROADCAST: FF FF FF FF FF FF
Preamble | Physical Dest. Address | Physical Source Address | Type | Data/Payload | CRC
8Bytes | 6B | 6B | 6B | 46-1500B | 4B

## Slide 11: Internet Protocol
The IP network moves datagrams with the same functionality that the Postal Service delivers letters.
An IP datagram is placed on the network by the source host.
  Letters are deposited in the mailbox by the mailer
The IP network tries to deliver the datagrams, if the necessary physical and logical connections exists
  The postal service tries to deliver the letter if the right trucks, planes, buses, and mail personal exists
IP is connectionless and not reliable
  Just as the postal service, IP make no guarantee of delivery

## Slide 12: IP Addressing
IP Address:
Are 32-bits long
Uniquely identify a particular network interface
Contain two parts
  Network ID or prefix
  Locally administered bits
  137.138.111.12

## Slide 13: Reserved Address
0.0.0.0
  The “unknown” address
127.0.0.1
  The loopback address
255.255.255.255
  The local broadcast address
(all local bits off)
  Our local network
(all local bits on)
  The broadcast address for our local network

## Slide 14: Private Addressing
Can be used by anyone, anywhere
Not routable on the global Internet
Three blocks allocated by RFC 1918
  10.0.0.0/8: About 16 million addresses
  172.16.0.0/12: About 1 million addresses
  192.168.0.0/16: 65.536 addresses

## Slide 15: Address Resolution Protocol
IP address: 10.10.10.10 
 MAC address 00 00 0c 00 23 23
When any system in an IP network begins the process of communicating with another system, a key part of the process is to identify the MAC address that matches the target IP address

## Slide 16: ARP Cache
[lxplus427] ~ $ /sbin/arp -n
Address HWtype HWaddress Flags Mask Iface
137.138.210.193 ether 0A:00:30:89:D2:C1 C eth0
137.138.210.211 ether 00:30:48:F0:DF:BC C eth0
137.138.210.238 ether 00:30:48:F0:E7:CA C eth0
[lxplus427] ~ $

## Slide 17: ARP Restrictions
ARP uses the network broadcast address to find the hardware address of the target host, which is only a concern when the two hosts share the same network and subnet.
Since routers block broadcasts, the ARP requests never leaves the subnet

## Slide 18: ARP Message Fields
0 | 15 | 16 | 31
Hardware Type (16) |  | Protocol Type (16) | 
Hardware Lenght (8) | Protocol Lenght (8) | Operation (16) | 
Source Hardware Address – Sender MAC address |  |  | 
Source Protocol Address – Sender IP address |  |  | 
Target Hardware Address – Receiver MAC address |  |  | 
Target Protocol Address – Receiver IP address |  |  | 

## Slide 19: Prefix Notation
Prefix | Mask | Prefix | Mask | Prefix | Mask
/0 | 0.0.0.0 | /11 | 255.224.0.0 | /22 | 255.255.252.0
/1 | 128.0.0.0 | /12 | 255.240.0.0 | /23 | 255.255.254.0
/2 | 192.0.0.0 | /13 | 255.248.0.0 | /24 | 255.255.255.0
/3 | 224.0.0.0 | /14 | 255.252.0.0 | /25 | 255.255.255.128
/4 | 240.0.0.0 | /15 | 255.254.0.0 | /26 | 255.255.255.192
/5 | 248.0.0.0 | /16 | 255.255.0.0 | /27 | 255.255.255.224
/6 | 252.0.0.0 | /17 | 255.255.128.0 | /28 | 255.255.255.240
/7 | 254.0.0.0 | /18 | 255.255.192.0 | /29 | 255.255.255.248
/8 | 255.0.0.0 | /19 | 255.255.224.0 | /30 | 255.255.255.252
/9 | 255.128.0.0 | /20 | 255.255.240.0 | /31 | 255.255.255.254
/10 | 255.192.0.0 | /21 | 255.255.248.0 | /32 | 255.255.255.255

## Slide 20: IP datagrams
Header must be at least 20 bytes
Header can increase in multiples of 4 bytes
Options (0 or 32 if any)
Source IP Address (32)
Destination IP Address (32)
Time to Live (8)
Identification (16)
Data (varies if any)
Total length (16)
Header Checksum (16)
Protocol (8)
Flags
(3)
Fragment Offset (13)
Type of Service
(8)
Version
(4)
Header
Length (4)
Bit 0
Bit 31
Bit 16
Bit 15
20
bytes

## Slide 21: Fragment Bytes Layout
If the “More” bit is | And the Offset is | Then the datagram is
0 | 0 | Not fragmented
1 | 0 | The first fragment
1 | > 0 | A middle fragment
0 | > 0 | The last fragment
Fragmentation Field Layout (16 Bits)
Reserved | Don’t Fragment | More Fragments | Fragment Offset (13 bits)

## Slide 22: Fragmenting Fragments
Target
Source
4,096
Router
Gateway

## Slide 23: Fragmenting Fragments
Target
Source
1136
Router
Gateway
1480
1480

## Slide 24: Fragmenting Fragments
4,096
552
552
376
552
552
376
552
552
32
Target
Source
Router
Gateway

## Slide 25: Fragmenting Fragments
4,096
552
552
376
552
552
376
552
552
32
4,096
Target
Source
Router
Gateway

## Slide 26: What Is IP Routing?
Host 190.1.10.3
Host 190.1.10.2
Host 190.1.20.2
Host 190.1.20.3
Internet
Router
Routing Table
Network # Interface
190.1.10.0 # 1
190.1.20.0 # 2
0.0.0.0 # 3
#2
#1

## Slide 27: Routing Function
How do routers
know where other
networks are
located?

## Slide 28: Routing Table Basics
Most routing tables contain:
  Destination network address
  Subnet mask
  Cost or metric
  Next hop address or gateway address
  Exit interface

## Slide 29: Routing Table Contents

## Slide 30: Router Routing Table

## Slide 31: Reliable Transport Services
Segments
TCP is connection-oriented and reliable.
UDP is connectionless and unreliable.

## Slide 32: Transport (Host-to-Host) Layer Protocols
Connectionless Protocol
Connection-Oriented Protocol
Data
Setup request
Setup response
Data
Acknowledge
Connection clear
Clear response

## Slide 33: UDP
Not reliable
Connectionless
Provides ports
  Ports identifies the application that send or recieve the data
Checksum is optional
  Reliability reduced even further if it is not used
  Checksum cover also the data field

## Slide 34: UDP Header
Ethernet | IP | UDP | UPD Payload | CRC
14 | 20-60 | 8 | Variable | 4

## Slide 35: UDP Header Layout
UDP Message Length (16)
Destination Port Number (16)
Data (if any)
UDP checksum (16)
Source Port Number (16)
Bit 0
Bit 31
8
bytes
Bit 16
Bit 15

## Slide 36: TCP Header
Ethernet Header | IP | TCP | TCP Payload | Checksum
14 | 20 to 60 | 20 or 24 | Varies (may not exist) | 4

## Slide 37: TCP Header Layout
Options (if any)
Header Length (4)
TCP Checksum (16)
Sequence Number (32)
Data (if any)
Destination Port Number(16)
Acknowledgment Number (32)
Source Port Number (16)
Bit 0
Bit 31
20 bytes
Bit 16
Bit 15
Window Size (16)
Reserved (6)
Code Bits (6)
Urgent Pointer (16)

## Slide 38: TCP Three-Way Handshake
Client port 12288
Server port 21
Host 1
Host 2
SYN
1
2
ACK, SYN
3
ACK
Sequence number = 7577
Acknowledge = 896
Flags = ACK, SYN
Window = 4096
MSS = 1024
Sequence number = 895
Acknowledge = 0
Flags = SYN
Window = 4096
MSS = 1460
Sequence number = 896
Acknowledge = 7578
Flags = ACK
Window = 4096
MSS = 1460

## Slide 39: Example of DAQ Network
Experiment, composed by several sub detectors:
Our data is produced here
Readout boards
Readout boards
Readout boards
Readout boards
Readout boards
Readout boards
Readout boards
10.0.0.10
10.0.0.11
10.0.0.12
10.0.0.13
10.0.0.14
192.168.0.10
192.168.0.14
192.168.0.18
192.168.0.22
192.168.0.26
192.168.0.30
192.168.0.34

## Slide 40: Backup slides

## Slide 41: Step 1: Request for Synchronization

## Slide 42: Step 2: Acknowledgment of the Client Request

## Slide 43: Step 3: Acknowledgment of the Server Request

## Slide 44: Congestion and TCP
Buffer
When a host is congested it sets its window size to 0.
An indication of a network congestion is a large window size and no change in the returned ACK numbers.

## Slide 45: Normal End of the Session
Client port 12288
Server port 21
Host 1
Host 2
ACK, FYN
1
2
ACK
4
ACK
3
ACK, FIN
Sequence number = 900
Acknowledge = 8542
Flags = ACK, FYN
Window = 4096
Sequence number = 8542
Acknowledge = 901
Flags = ACK
Window = 4096
Sequence number = 8542
Acknowledge = 901
Flags = ACK, FIN
Window = 4096
Sequence number = 901
Acknowledge = 8543
Flags = ACK
Window = 4096

## Slide 46: Step 1: Sending a FIN

## Slide 47: Step 2: Acknowledging the FIN

## Slide 48: Step 3: Client Sends a FIN

## Slide 49: Step 4: The Server Acknowledges the FIN

## Slide 50: Reset Session
Client
Server
Reset bit
turned on
X
System failure

## Slide 51: Network Address Translation
Nat includes:
  Static NAT
    Permanent one-to-one mapping
    Allows outbound and inbound sessions
  Dynamic NAT
    Mappings dynamically assigned from pool
    Allow outbound sessions only
  PAT
    One public address serves many internal sessions
    Allows oubound sessions only