## Slide 1: ODR - a non-invasive Beam Size Measurement Technique for CLIC
L. Bobb1, 2, T. Aumeyr1, M. Billing3, E. Bravin2, N. Chritin2, P. Karataev1, T. Lefevre2, S. Mazzoni2
John Adams Institute at Royal Holloway, Egham, Surrey, United Kingdom
CERN European Organisation for Nuclear Research, CERN, Geneva, Switzerland
Cornell University, Ithaca, New York, USA

## Slide 2: Contents
Motivation
Aim
Diffraction Radiation
Experimental preparation for Phase 1
  Simulations
  Vacuum assembly
  Optical system
Future work
  Outlook for Phase 2

## Slide 3: Most recent experiments using Optical Diffraction Radiation (ODR) for beam diagnostics
E. Chiadroni, M. Castellano, A. Cianchi, K. Honkavaara, G. Kube, V. Merlo and F. Stella, “Non-intercepting Electron Beam Transverse Diagnostics with Optical Diffraction Radiation at the DESY FLASH Facility”, Proc. of PAC07, Albuquerque, New Mexico, USA, FRPMN027.
A.H. Lumpkin, W. J. Berg, N. S. Sereno, D. W. Rule and C. –Y. Yao, “Near-field imaging of optical diffraction radiation generated by a 7-GeV electron beam”, Phys. Rev. ST Accel. Beams 10, 022802 (2007).
P. Karataev, S. Araki, R. Hamatsu, H. Hayano, T. Muto, G. Naumenko, A. Potylitsyn, N. Terunuma, J. Urakawa, “Beam-size measurement with Optical Diffraction Radiation at KEK Accelerator Test Facility”, Phys. Rev. Lett. 93, 244802 (2004).
σy = 14 µm measured ATF2@KEK

## Slide 4: Motivation
http://www.clic-study.org/
Section of machine | Beam Energy [GeV] | Beam size [µm] | Requirement
PDR (H/V) | 2.86 | 50/10 | Micron-scale resolution
DR (H/V) |  | 10/1 | 
RTML (H/V) | 2.86 - 9 | 10/1 | 
Drive Beam Accelerator | 2.37 | 50 -100 | Non-invasive measurement
Transverse beam size requirements for the Compact Linear Collider (Table 5.62 CDR Volume 1, 2012):
Baseline high resolution non-interceptive beam profile monitor:
Laser Wire Scanners
S. T. Boogert et al., “Micron-scale laser-wire scanner for the KEK Accelerator Test Facility extraction line”, Phys. Rev. S. T. – Accel. and Beams 13, 122801 (2010)

## Slide 5
 | E (GeV) | σH (µm) | σV (µm)
CesrTA | 2.1 | 320 | ∼9.2
 | 5.3 | 2500 | ∼65
Project aim:
To design and test an instrument to measure on the micron-scale the transverse (vertical) beam size for the Compact Linear Collider (CLIC) using incoherent Diffraction Radiation (DR) at UV/soft X-ray wavelengths.
Our experiment
D. Rubin et al., “CesrTA Layout and Optics”, Proc. of PAC2009, Vancouver, Canada, WE6PFP103, p. 2751.
Cornell Electron Storage Ring Test Accelerator (CesrTA) beam parameters:
http://www.cs.cornell.edu

## Slide 6: Diffraction Radiation
Principle:
Electron bunch moves through a high precision co-planar slit in a conducting screen (Si + Al coating).
Electric field of the electron bunch polarizes atoms of the screen surface.
DR is emitted in two directions:
  along the particle trajectory “Forward Diffraction Radiation” (FDR)
  In the direction of specular reflection “Backward Diffraction Radiation” (BDR)
θ0
θy
e-
DR Angular distribution
Impact parameter:
Generally:
DR intensity ⇧ as slit size ⇩
h

## Slide 7
Vertical Beam Size Measurement using the Optical Diffraction Radiation (ODR) model + Projected Vertical Polarisation Component (PVPC)
P. Karataev et al.
Vertical polarisation component of 3-dimensional (θx, θy, Intensity) DR angular distribution.
PVPC is obtained by integrating over θx to collect more photons.
Visibility (Imin/Imax) of the PVPC is sensitive to vertical beam size σy.

## Slide 8: Phase 1 Experiment Simulations for CesrTA
To compare with TR intensities:
TRmax
Measureable visibility for initial test at parameters:
λ = 200 - 400 nm
a = 0.5, 1 mm
σy = 50 µm

## Slide 9
Beam lifetime and beam jitter
M. Billing, "Introduction to Beam Diagnostics and Instrumentation for Circular Accelerators", AIP Conference Proc. 281, AIP 1993, pg.75 ff.
target slit size [mm] | vertical beam size [µm] | beam lifetime [min]
0.1 | 9.2 | 2.40
0.5 | 30 | 60 (max)
 | 50 | 2.22
1.0 | 50 | 60 (max)
Errors due to beam jitter are reduced by including turn-by-turn vertical position measurements of the bunch in the target aperture.
atarget ≥ 5∙σy,
preferably atarget = 7-10∙σy
Large aperture = low DR intensity
Multiple turns of a single bunch through the target aperture

## Slide 10
Target design
Technical drawings by N. Chritin
Requirements:
High precision slit size
Coplanarity ≤ 10% ∙ λ
High reflectivity at λ
Aperture sizes a:
0.5 mm, 1 mm
Material: Si

## Slide 11
Synchrotron Radiation (SR)
Source of background | Contribution
SR from beamline optics | High
Camera noise | Low
Residual background | 
SR + DR interference
SR suppression
P. Karataev et al., Proc. of EPAC 2004, THPLT067
θ0
θy
e-
Use a mask upstream of target to suppress SR contribution.
E = 2.1 GeV
λ = 400 nm
a = 0.5 mm
Mask
Target
OTR
ODR

## Slide 12
L3 layout @CesrTA
Technical drawings by N. Chritin
Electron beam direction
DR experiment

## Slide 13
Vacuum chamber assembly
Technical drawings by N. Chritin
Simulations by A. Nosych
E-field magnitude of a single bunch pass in time domain (Gaussian bunch, length = [-4s,4s], s = 10mm)
H-field surface tang complex magnitude (Loss map)
Mode Fr = 1.19 GHz, Q = 3309, Ploss = 0.075 W
Total power loss for single bunch = 0.6 W

## Slide 14
Vacuum chamber assembly cont’d
Images taken during assembly at CERN and current testing at Cornell.

## Slide 15
Method of Operation
Alignment of the electron beam with the target aperture:
  BPMs for centering (~10 microns resolution)
  Target imaging to look for OTR from beam halo
  Correlate with BLMs:
DR vertical beam size measurement
Quadrupole
Dipole
Virtual BLMs
Si
1
2
3
4
-400μm off
center
+400μm off
Virtual Detector 3
Virtual Detector 4
Simulations by A. Apyan

## Slide 16
Optical System
Far-field Condition:
 | 2.1 GeV | 5 GeV
200 nm | 0.54 m | 3.18 m
400 nm | 1.08m | 6.37 m
Compact optical system (distance to detector L ≤ ) | Long-range optical system (distance to detector L >> )
Bi-convex lens required with camera in back focal plane. | Far-field zone
Dual purpose: Image target Image DR angular distribution | 
DR observation wavelengths: λ = 200 nm, 400 nm | 
In footprint of target mechanism ( < 1m) | Determined by L and spatial constraints.
Bi-convex lens required with camera in back focal plane. | Far-field zone
Dual purpose: Image target Image DR angular distribution | 
DR observation wavelengths: λ = 200 nm, 400 nm | 
In footprint of target mechanism ( < 1m) | Determined by L and spatial constraints.
given γ and λ:
L = distance from source of DR to detector.
Compact optical system is in the prewave zone
(Pre-wave zone effect in transition and diffraction radiation: Problems and Solutions -P. V. Karataev).

## Slide 17
Phase 2: Micron-scale resolution
E = 5.3 GeV
atarget = 0.2 mm
DR at soft X-ray wavelengths:
  More complex optical system.
  Grazing target tilt angle
Aperture size determined by impact parameter for given wavelength
Main requirement:
Micron-scale resolution
Must use shorter wavelengths
Sensitivity @50 nm ≈ 2x sensitivity @200 nm

## Slide 18
Summary + Conclusion
Acknowledgements
I would like to thank J. Barley, J. Conway, J. Lanzoni, Y. Li, T. O'Connell, M. Palmer, D. Rice, D. Rubin, J. Sexton, C. Strohman and S. Wang (@Cornell) for all technical contributions and advice. In addition, O.R. Jones and H. Schmickler for organisation of the collaboration, A. Apyan, S. Burger, A. Jeff, A. Nosych and S. Vulliez (@CERN).
Simulations have demonstrated the feasibility of vertical beam size measurements at CesrTA. The preliminary phase 1 experiment will take place at the end of December 2012.
The design must account for the experiment location in a circular machine. This introduces some advantages and disadvantages not applicable for linacs.
Preliminary simulations for the phase 2 test aiming for the soft x-ray spectral range have been presented.

## Slide 19
Thank you for your attention
Questions?

## Slide 20
Extra slides

## Slide 21
E-field + B-field magnitude of a single bunch pass in time domain (Gaussian bunch, length = [-4s,4s], s = 10mm)
Higher Order Modes (HOMs)
1.017 GHz
1.26 GHz
1.19 GHz
Ploss_total = 0.6W
Simulations by A. Nosych
H-field surface tang complex magnitude (Loss map)
Fork OUT, Chamber IN
1.017 GHz
1.19 GHz
1.26 GHz

## Slide 22
Feasibility of a ring beam size monitor
LHC also has γ ≈ 4000 (@ E = 4000 GeV)
Using proton beam:
  Reduced SR background
  Larger beam size
Wavelengths in the infrared spectral range
Main requirement:
Non- invasive measurement
Must use large target aperture

## Slide 23
Optical Diffraction Radiation Interference (ODRI)
A. Cianchi et al., Phys. Rev. ST Accel. Beams 14 (10) 102803 (2011)
Aperture sizes | Interference
amask = atarget | Complete destructive interference of FDR + BDR (blue)
amask ≈ 2∙atarget | Measureable interference (green)
amask ≥ 4∙atarget | Negligible interference (red)
E = 2.1 GeV
λ = 400 nm
amask = 2 mm
atarget = 1 mm
σy = 50 µm
Using non-collinear slits (i.e. centres of mask + target do not coincide) allows measurement of beam size, beam offset from the target centre and angular divergence.

## Slide 24
ODR movements
There are 2 stepping motors:
  1x linear movement of the fork
  1x angular movement of the fork
There is 1 DC (+24V) motor that drives a linear movement for the replacement chamber
The linear (stepping) movement of the fork and the linear (DC) movement of the
replacement chamber have to be interlocked one with respect to the other to avoid
collision (see next slide)
Cabling of stepping motors has to be adapted to available driver (unipolar/bipolar)
(tests @ CERN were performed with bipolar driver and cabling)
S. Burger

## Slide 25
Replacement Chamber
(linear movement)
OUT
IN
Burndy 12M
Socket
M
ODR fork
(linear movement)
OUT
IN
OUT switch 5
COM switches 8
IN switch 11
Motor + 9
NO
NO
NO
NC
NO
NC
Stepping switches cabling
Motor - 10
Burndy 4M
Socket
Burndy 4F
Socket
1
2
3
4
1
2
3
4
Interlock ODR movement
Cable
Burndy
4M/F
1 to 1
(as connected with CERN screen
instrumentation ‘standard’ driver)
Stephane.burger@cern.ch
Hardware INTERLOCK logic: ODR fork can not move if replacement chamber not OUT
Replacement chamber can not move if ODR fork not OUT
DC motor
24V
Cornell connection
S. Burger