## Slide 1: Software for Testing the New Injector BLM Electronics
Emmanouil Angelogiannopoulos (BE-BI-SW)
Acknowledgements:
  Maciej Kwiatkowski (BE-BI-BL)
  Stephen Jackson (BE-BI-SW)
  Christos Zamantzas (BE-BI-BL)

## Slide 2: Outline
Motivation for this project
Technical details with examples
Results
Conclusions

## Slide 3: Final System Implementation
Final architecture of the new BLM system:
  Detectors in tunnel
  Acquisition crate (BLEDP)
  VME crate
    Processing electronics (BLEPT)
    FESA server on Linux CPU providing data to clients and dealing with settings and interlocks

## Slide 4: Test System Implementation
VME processing electronics not yet available
Replacing fibre module with Ethernet allows standalone implementation
Nios-II software-implemented CPU allows custom server.
Expert BI software communicates directly with the BLEDP module
Topic of this talk

## Slide 5: Objectives for the Expert Software
Debug and verify the hardware
Further develop the analogue circuits and the final firmware
Assist in the development of the FPGA algorithms to merge the acquired data
User-friendly environment
Real-time data-viewing and parallel logging to files

## Slide 6: Software, Firmware and Hardware Development Phases
Analogue and PCB Design
Protocol and Software
Specification
Nios II firmware development
Testing & Validation
Expert GUI Client

## Slide 7: Two Types of Data Provided
Acquisition data
  8 channels per BLEDP module
  2 measurement methods:
    Low current measurement (in pA)
    High current measurement (in mA)
Status data
  Number of sensors and parameters to be monitored
  Data rate 1s

## Slide 8: Protocol Specification
The protocol for the client-server architecture:
  Header to identify data source, measurement method, continuity problems.
  Header + payload = 32 bit data frame.
  350 data frames packed into data bundle. Size is selected to avoid IP fragmentation.
  Status data buffers.
  4 byte commands.
  Both TCP and UDP can be used.

## Slide 9: Development Phases
Processed data from one channel
Processed data from all eight channels
Raw ADC data from one channel
TCP protocol
16 Mbit/s
128 Mbit/s
UDP protocol
320 Mbit/s
UDP protocol
Type of acquisition data supported by the module:
2. Status Data with 1 Hz frequency interleaving with all the above types.

## Slide 10: Online Panel
The user should set different parameters before starting communication with the module. Most of them are saved from previous sessions on the same computer or have default values.
Acquisition parameters like Data type mode, channel number and acquisition time should always be set manually.
After these steps the acquisition can start and real-time data from the module are plotted in the graph.
It is possible to stop the acquisition at any time.
User can also define Units and Scale in the Y Axis.
The user can also select whether or not to save incoming data to the hard drive. This process is executed in parallel with the real time plotting. It is important for further offline analysis, that will be explained in the next slides.
We can see a video example with real time plotting.

## Slide 11: Online Panel Video

## Slide 12: Offline Panel
Open a file search window to select an acquisition folder from a previous online session.
Mac address of a module.
Different acquisition sessions for this module to select.
Upper graph is the picker. It is plotted from statistics files inside the selected session folder and contains minimum, maximum and average values of the data for each second. The user has to pick a second with the mouse.
The picked second is marked in the upper graph and the data are mined from the corresponding file and then plotted with the desired accuracy in the lower graph.
11/16
A zooming video example follows.

## Slide 13: Offline Panel Video

## Slide 14: Status Panel
Plot selected status packets in these three graphs with 1 Hz update rate: current consumption, high voltage monitoring, temperature and humidity.
In the first graph are plotted acquisition data from the selected channel with 1 Hz update rate also. The plots of the four graphs are aligned.
E.g. Influence of a power supply problem on the measurements can be seen here.
LEDs show status of the power supplies and the calibration relays.
Print in textboxes: values which are plotted and additional like digital potentiometers settings and event counters.

## Slide 15: Conclusion
Direct Ethernet communication allowed a standalone implementation
Collaboration between BL (hardware, firmware) and SW (Expert GUI) sections
Software and the firmware development was split:
  Processed Data from one channel
  Processed data from all 8 channels
  Raw Data from one channel
Expert GUI allowed developing of both firmware and hardware
  Offline data storage allowed detailed analysis of the RT algorithm implemented in the FPGA

## Slide 16
Thank you for your attention!
People involved in the Project:
Christos Zamantzas (BE-BI-BL)
Stephen Jackson (BE-BI-SW)
Analog design: William Viganό (BE-BI-BL)
Firmware design: Marcel Alsdorf, Maciej Kwiatkowski (BE-BI-BL)
Software design: Emmanouil Angelogiannopoulos (BE-BI-SW)