## Slide 1: 120GB-300Gb Optical Interconnect Solutions for Optical backplane and Optical Routers
March, 2013
Presenting: Avner Badihi
TECHNOLOGY
&
MANUFACTURING
XLoom Proprietary and Confidential

## Slide 2: iFlame™ Technology - Platform for Optical Integration
XLoom Proprietary and Confidential
iFlame
Integrated
ROSA & TOSA
Transceivers & Cables
- Ethernet
- InfiniBand
- Inter-Board connections
- Active Optical Cables
Optical Cross-Connect
Mux / Demux
ROADM
AWG
Optical Subsystems
Modules
Subassemblies
- Fibre Channel
- Back plane
Optical Router

## Slide 3: Agenda
XLoom Proprietary and Confidential
Technology Overview
Product Manufacturing and Cost Analysis
Appendix
3

## Slide 4: XLoom Micro-Optical Technology Solves Density, Power and Reach
XLoom Patented Technology
Miniature scale optical-to-electronic conversion
Commercially-available lasers/photodiodes and circuits
Aligned and assembled on the wafer level (6” in process)
Standard semiconductor micromachining processes

## Slide 5: iFlame Technology
XLoom Proprietary and Confidential
Wafer-level assembly – simultaneous alignment of >200 optical chips
Passive Alignment – automation possible
Array Optics – multiple channels assembled simultaneously
Low Profile – multiple environments/applications
5

## Slide 6: iFlame Optical Design
XLoom Proprietary and Confidential
6
Ray-tracing optical design
(sequential analysis, using ZEMAX®)
Acceptance angle > NA of fiber/ VCSELs
Near-field pattern at detector
Example of offset z-focus
Focus on flat mirror
Imaging 1:1

## Slide 7: Light-Coupling Scheme
XLoom Proprietary and Confidential
7
VCSEL/PD
metal traces
reflector bar
reflectors
epoxy
protective cap
fiber
substrate

## Slide 8: Agenda
Technology Overview
Product Manufacturing and Process
Appendix

## Slide 9: Production Plan Processes
Wafer
Preparation
Fiber Ribbon
Preparation
Lens Strip
Preparation
In process testing
Wafer Level Processing
Chip Assembly
In process testing
Flip Chip
Chip Level Processing
XLoom Proprietary and Confidential
9

## Slide 10: Wafer Level Processes
Structure is repeated in 2D on a 6” or 8” wafer
Grooves created at the same time on all devices
Simultaneous alignment of all devices
Lead free (ROHS) SAC Alloy bumps
silicon/glass
V-grooves
grooves
fibers
MT pins
Patterned device wafer ready for saw

## Slide 11: Lens Bars Placement
Lens/Reflectors bars are manufactured separately on in wafer form, cut, and attached to device wafer using an automated machine (passive alignment)

## Slide 12: iFlame Optical Chip Structure
XLoom Proprietary and Confidential
12
VCSEL array
PD array
reflector bar
Mounted VCSELs
seen from optical side

## Slide 13: iFlame 12X10Gb/s Specs
Compliant with 100GbE specifications 802.3ba (100GBASE-SR10 and nPPI)
High Channel Density: 120Gb/s
Operates at 10.3125 Gb/s per channel with 64b/66b coded data
Links up to 100m using OM3 MM fiber and 150m using OM4 MM fiber
0 to 70ºC case temperature operating range
Two Wire Serial (TWS) interface with maskable interrupts for expanded functionality including:
  Individual channel functions: channel disable, squelch disable, and lane polarity inversion
  A/D read back: module temperature and supply voltages, per channel laser current and laser power, and input receiver power
  Status per channel: Tx fault, electrical (transmitter) or optical (receiver) LOS, and alarm flags
XLoom Proprietary and Confidential
13
XLoom Proprietary and Confidential

## Slide 14: iFlame 12X25 / 4X25 Gb/s Specs
FDR & EDR full specifications are not released yet
High Channel Density: up to 300Gb/s
Operates at 25.8 Gb/s per channel .
Links up to 30m using OM3 MM fiber and 100m using OM4 MM fiber
0 to 70ºC case temperature operating range
Bit Error Rate ( BER ) < 10-15
Optical Power 1mW
3 possible configurations
  12x module – Tx, Rx – MPO connector
  QSFP type active cable 4x
  4x module – Tx, Rx – MPO connector
Incircuit flux (optical spot)- <19um
XLoom Proprietary and Confidential
14
XLoom Proprietary and Confidential

## Slide 15
15
XLoom Proprietary and Confidential
Thank You

## Slide 16: iFlame Optical Path
XLoom Proprietary and Confidential
16
Advantages:
Inexpensive (using flexible circuits)
Used widely in the industry
Disadvantages:
Large minimum height is (> 1 cm)
Signal integrity problems at high line rates
iFlame Advantages:
Very high channel density
Potentially very low profiles enabling ultra-small transceivers
Disadvantages:
Difficult technology (in general)
electrical turn
optical turn